## Slide 1
Chris Cianciola,
Deputy Manager
Space Launch System Program
September 17, 2018
NASA’s Space launch system:
Progress Toward Unmatched
Exploration Capability
Notes: Thank-you
SLS represents a significant contribution to our country’s strategic national capabilities in engineering, manufacturing, science, exploration, technology, and soft statecraft skills in peaceful cooperation.
I’d like introduce you today to NASA’s Space Launch System, talk about the design and give you an update on it’s current status.

## Slide 2: NASA’s Exploration plans
NASA’s Gateway
PPE – Habitat – Airlock – Logistics
Notes: It’s been more than 4 decades since we ventured into deep space with humans.
Since the Apollo missions, we’ve been working in low Earth orbit, learning how to conduct long duration operations and learning about humans in space.
NASA is now directed to venture back into deep space with people with the moon as our first stop.
Most recently, in 2017, the President signed National Space Policy Directive 1 calling for NASA to “lead an innovative and sustainable program of exploration with commercial and international partners to enable human expansion across the solar system and to bring back to Earth new knowledge and opportunities. Beginning with missions beyond low-Earth orbit, the United States will lead the return of humans to the Moon for long-term exploration and utilization, followed by human missions to Mars and other destinations.”
NASA is working with domestic and international partners to solve the great challenges of living and working in space farther from Earth, and in the process creating new knowledge that benefits all of humanity and inspires the nation.
Visible here are the elements of our effort – ISS operations with commercial crew logistics, a return to the moon with robotic landers, a Gateway human-tended station, robotic landers and rovers, eventually people, and continued robotic exploration of Mars to inform future crewed missions.
The transportation is a high priority as part of a larger priority – mission success.

## Slide 3: Evolvable capability for deep space
Payload to TLI/Moon
355 ft.
RS-25 Engines
365 ft.
Core Stage
Up to 313ft.
Interstage
Evolved
Boosters
Solid
Rocket
Boosters
Exploration Upper Stage
325 ft.
Orion
Launch Abort System
Launch Vehicle
Stage Adapter
Interim Cryogenic
Propulsion Stage
8.4m Fairing
Long (Up to 90’)
Solid
Rocket
Boosters
Core Stage
Interstage
Exploration Upper Stage
8.4m Fairing
Short (Up to 63’)
Universal
Stage Adapter
Core Stage
Interstage
Exploration Upper Stage
365 ft.
> 45 t (99k lbs)
37–40 t (81k–88k lbs)
34–37 t (74k–81k lbs)
> 26 t (57k lbs)
> 45 t (99k lbs)
SLS Block 2 Cargo
SLS Block 1B Cargo
SLS Block 1B Crew
SLS Block 1 Cargo
SLS Block 2 Crew
RS-25 Engines
SLS Block 1
> 26 t (57k lbs)
5m Class Fairing
(up to 63’)
322 ft.
Universal
Stage Adapter
Notes: This is our transportation – NASA’s Space Launch System.
Why do they look like this?
government exploration role – exploration, complete the missions, bring back knowledge
evolution – budget, challenges
heavy lift – mass volume trip time benefits. SLS will lift more mass and more volume than any other rocket today.
proven technologies w/ prudent upgrades
assured access

## Slide 4: SLS BLOCK 1 CONFIGURATION
Launch Abort System (LAS)
RS-25 Engine (4)
Aerojet Rocketdyne
Service Module (SM)
Spacecraft Adapter
5 Segment Solid Rocket Booster (2)
Northrop Grumman
Interim Cryogenic
Propulsion Stage (ICPS)
Boeing/United Launch Alliance
Encapsulated Service Module (ESM) Panels
Crew Module (CM)
Orion Spacecraft
Lockheed Martin
Launch Vehicle Stage Adapter
Teledyne Brown Engineering
Orion Stage Adapter
Core Stage & Avionics
Boeing
RL10 Engine
Aerojet Rocketdyne
Notes: We are currently building and testing our first Block 1 vehicle for our first flight – Exploration Mission 1.
Visible are the major elements of the EM-1 vehicle – solid rocket boosters, core stage, (engine section, LH tank, intertank, LOX tank, forward skirt) LVSA and ICPS, OSA, and Orion/SM/LAS.
Block 1 will be more capable than any current launch vehicle, able to deliver >26 metric tons (57,320 lb) to the Moon.
Work is well underway on our initial Block 1 configuration, and we are overcoming challenges and making steady progress.
All major hardware for structural testing and for first flight have completed welding or assembly, and all are undergoing installation of insulation, wiring, piping, brackets, and other internal structures.
On our first mission, EM-1, will take the Orion crew vehicle farther into space than humans have ever ventured before.
Block 1 will be the foundation for the development of the future Blocks on the previous chart.

## Slide 5
EXPLORATION MISSION-1 FULL SYSTEMS CHECKOUT PRIOR TO CREWED MISSIONS
Notes: This animation shows the EM-1 trajectory in a looping video.
After one orbit around the Earth, Orion will fly through the Van Allen Radiation Belts, where it will experience high amounts of radiation.
It will take Orion about 4 days to get to the moon.
Tucked into the Orion Stage Adapter – the ring that connects Orion to the SLS – will be 13 secondary payloads/CubeSats.
The CubeSats will deploy after the Orion spacecraft separates from SLS and starts its journey into deep space.
The Orion spacecraft will fly 40,000 miles beyond the moon, farther than we did during Apollo, and spend about 6 days in the vicinity of the moon before beginning the 4-day return to Earth.
Although uncrewed, EM-1 will provide the first integrated test of SLS and Orion, including:
  Assembly, integration and test of SLS and Orion at KSC
  Tanking and countdown operation at KSC LC39
  Test SLS ascent and Orion vehicle performance in lunar distant retrograde orbit (DRO) without crew
  Mission operations
  Deep space navigation
  Flight validation of data systems
  Test deep-space maneuvers
  Test communications and tracking
  Validate re-entry from lunar gravity assist
  Secondary payloads on SLS
  Orion heat shield and reentry
  Landing and recovery operations with Orion

## Slide 6: NASA’s Gateway STEPPING STONE TO THE SOLAR SYSTEM
Notional rendering
Notes: SLS is part of the NASA vision to build a reusable in-space architecture. Effectively a reusable Apollo command and service module with far more capability.
Our initial goal is building a crew-tended “Gateway” spaceport in orbit around the Moon. We’re accelerating to 2022 plans to deliver the first Gateway element.
A power and propulsion element, as well as habitation, airlock and logistics capabilities, will establish the core functionalities of the Gateway.
NASA is looking at commercial and SLS co-manifested payload options to launch the individual Gateway components, and assemble them in space. Gateway is accessible to SLS and major commercial launch vehicles.
The Gateway can operate from a variety of lunar orbits and be moved when the crew is not present – “learning to sail the gravity rivers of the Earth/Moon system.”
The Gateway can contribute to lunar surface activities – robotic landers and eventually humans – and have application to farther destinations in the solar system, including Mars. It serves both a function as training and hardware maturation element as well as operational element needed to send humans beyond low-Earth orbit. Additional opportunity for attached payloads and Earth-observing payloads.
NASA is discussing components that International Space Station partners could potentially provide to the Gateway.
NASA and its partners will use the gateway for deep-space operations including missions to and on the Moon with decreasing reliance on Earth. Using lunar orbit, the agency will develop its exploration systems and gain the experience necessary to extend human presence farther into the solar system than ever before.

## Slide 7: SOLID ROCKET boosterS
Notes: Large image:
Qualification Motor QM-2 test in Promontory, Utah at Northrop Grumman’s facility in June of 2016.
Inset image:
Booster production continues at prime contractor Northrop Grumman’s facilities, where technicians are applying photogrammetric markings on completed segments for the five-segment solid rocket booster motors for the first integrated mission of SLS and Orion.
BASIC
Each booster is 177 feet or 17 stories tall – taller than the Statue of Liberty
Each is 12 feet in diameter.
Each booster burns through 1,385,000 pounds of propellant in two minutes – that’s an average of 5.5 tons of propellant every second.
Each booster’s thrust is greater than 14 four-engine Boeing 747s at full take-off power.
During flight, the temperature of the motor chamber gases reach more than 5,000°F – hot enough to boil steel!
STATUS
Two full-scale static hot-fire tests have been conducted and are paving the way for qualification.
The first test (March 2015) tested the propellant at a temperature of about 90 degrees.
The second test (June 2016) tested the propellant at about 40 degrees
At Northrop Grumman in Utah, all 10 EM-1 motor segments have been cast with propellant and several are completely painted, finished and are awaiting shipment to Kennedy Space Center.
Both nozzles are finished at Northrop Grumman facilities in UT.
At Kennedy, the forward and aft skirts are being refurbished and outfitted for flight. TVC has been installed in the left-hand aft skirt and teams recently completed a hot fire test on an aft skirt pathfinder in preparation for final assembly and checkout.
Upper and lower TVC frames have been installed in the right-hand aft skirt.
Booster separation motors are currently being installed on the left-hand aft skirt.
At Marshall, the avionics recently finished qualification testing and will be tested with vehicle avionics later this year.
Booster segments are now being cast for EM-2.

## Slide 8: ENGINES
Notes: Top Inset Image: EM-1 engines in processing
Bottom inset image: Development test engine with 3-D printed Pogo accumulator
Right Image: RS-25 testing at SSC
BASIC
4 RS-25 engines vs 3 for shuttle, 109% thrust vs 104.5%, new controller and software and nozzle insulation, more than 500,000 lb thrust each, more than 1 million seconds total ground and flight time.
Program starts with 14 flown engines and 2 new serial number engines built from spares.
STATUS
Program has been hot-fire testing the RS-25 engines since 2015 to ensure the engines can perform under the different SLS pre-launch conditions, higher heating environment, and flight thrust profiles, and also to qualify the new EM-1 controllers. More than 20 tests, more than 10,000 seconds hotfire time.
All 4 EM-1 engines processing complete. All 4 EM-1 controllers and all 4 EM-2 controllers green run tested.
Early 2018 testing took the RS-25 to 113% thrust, the highest ever, and it continued to function nominally (with no issues).
Concurrent work is under way on developing a new more affordable, expendable variant of the RS-25 that costs at least 30 percent less and operates at 111% (521,000 lb) thrust. It incorporates new materials and new manufacturing processes, as well as new technology like 3D printing. First test was early 2018 of a 3D printed pogo accumulator on a ground test engine.
New test series began in August that will includes the pogo accumulator plus a new HIP (Hot Isostatic Pressure) – Bonded main combustion chamber that reduces production time and cost.

## Slide 9: CORE STAGE
Notes: Top Inset image: The EM-1 LOX tank is shown here after robotic thermal protection system application. It moved to another area for sensor installation and preparations to be stacked with the completed intertank and forward skirt.
Bottom Inset image:
The intertank is the second core stage test article delivered to Marshall Space Flight Center in Huntsville, Alabama, for structural testing. We got it up here from Michould Assembly Facility earlier this year and we have completed our initial round of tests. We will begin the second round this fall.
Right Image:
The EM-1 liquid hydrogen tank moves into place in Cell P at Michoud Assembly Facility to be primed before thermal protection system application. It’s been insulated and has been undergoing sensor installation.
BASIC
The SLS Core Stage will be the tallest rocket stage ever flown. When completed, the Core Stage will be 212 feet tall (64.6 m) and 27.6 ft. (8.4 m) in diameter.
It will weigh 2.3 million pounds when fueled
The liquid hydrogen tank measures more than 130 feet tall, comprises almost two-thirds of the core stage and holds 537,000 gallons of liquid hydrogen cooled to minus 423 degrees Fahrenheit.
The Core Stage is being built by prime contractor Boeing at Michoud Assembly Facility outside New Orleans, LA, using state-of-the-art manufacturing tools, including the world’s largest friction-stir welding tool, the Vertical Assembly Center.
STATUS
Structural work is complete on the engine section, LH tank, intertank, LOX tank and forward skirt for the 212-foot EM-1 core stage, and all are being outfitted with internal hardware and instrumentation for flight.
SITF-Q completed software testing as part of intertank functional tests in 2018, and forward skirt testing was recently completed to demonstrate the flight computers and other avionics.
Core Stage Pathfinder built in 2017 and barged to Michoud to begin practice operations. Test moves with core stage GSE planned for this year.
B-2 test stand at Stennis Space Center continuing to get ready for core stage green run.
Ground support equipment in testing.

## Slide 10: IN-SPACE STAGE AND ADAPTERS
Notes: Left Image:
Launch Vehicle Stage Adapter after application of foam insulation (thermal protection system) being transported to its final stop at Marshall where it will be outfitted for flight.
Right Image:
Interim Cryogenic Propulsion System and Orion Stage Adapter both in the Space Station Processing Facility at Kennedy Space Center until needed for stacking
BASIC
ICPS fast facts:
Built by Boeing/ULA
Modified Delta Cryogenic Second Stage by lengthening LH2 tank, adding hydrazine bottles for attitude control and minor avionics changes
42’ tall x 16’ wide
Powered by one AR RL-10B-2 engine
24,750 lbs thrust
Operates about 700 seconds
Provides TLI burn for Orion
LVSA fast facts:
Connects core and upper stages
27.5’ long and 27.5’ wide at base, tapers to 5 m at top
Friction-stir welded lightweight aluminum alloy
OSA fast facts:
Connects ICPS and Orion
5’ high, ~18’ diameter
Holds 13 cubesats for EM-1
STATUS:
Integrated Structural Test of upper stage successfully completed in May 2017 at MSFC
  Consisted of test articles of ICPS, LVSA, OSA and FJA
  First major structural test to be completed
ICPS and OSA finished and shipped to EGS in 2017 and 2018
ICPS will remain in Space Station Processing Facility at KSC until needed for stacking
OSA will remain in SSPF until payloads are integrated, then it will be stacked
LVSA recently completed TPS, will soon be integrated with frangible joint assembly
LVSA scheduled to ship on Pegasus at the end of this year

## Slide 11: Avionics/software Development and testing
Notes: Images: Software Integration Lab at MSFC
How do you get nearly 6 million pounds of rocket safely to orbit at 17,500 mph or so? Avionics and software. It’s not as visually impressive as big hardware but every bit as important.
Marshall has developed state of the art tools, facilities and test environments to support development test integration and verification of mission critical human-rated embedded flight software.
SIL can also perform hardware in the loop testing.
Avionics on all SLS components: flight computers in the core stage, engine controllers on four RS-25s, booster avionics, core stage avionics.
Delivered first release of flight software May 2013.
MSFC software team and Systems Integration Lab has “flown” SLS virtually thousands of times in hardware and software testing. They can perform complete range of flight software activities, including requirements development and analysis, software processes and planning, design and development, system integration and development testing, and software verification.
SLS engines and boosters have completed qualification testing, and testing is underway for the core stage. SIL technicians are checking out the avionics systems for the entire rocket to verify they can all “talk to” each other, to Orion, and to ground control computers and give SLS the direction it needs for a successful mission. Almost identical avionics boxes in the lab simulate the flight computers and other avionics in the booster and core stage.

## Slide 12
Notes: SLS Progress video: 2 minutes
Animation: This is the vision. We’re working on.
Video: And this is the reality. We’re a real rocket. There’s a huge amount of work going on all over the country. We are knocking down challenges and working our way to the Launchpad in December 2019. (with 6 months of risk).

## Slide 13
Notes: LAST SLIDE
In conclusion:
SLS represents a significant contribution to our country’s strategic national capabilities in engineering, manufacturing, science, exploration, technology, and soft statecraft skills in peaceful cooperation.
Thanks for your time.
Hope you enjoyed the presentation.
There are multiple ways to follow our progress.

## Slide 14
BACKUP

## Slide 15: ONE LAUNCH, MULTIPLE DISCIPLINES 13 SMALLSATS TO BE DEPLOYED FROM THE ORION STAGE ADAPTER
Notes: NASA’s Super Guppy cargo plane arrives in Huntsville to pick up the Orion Stage Adapter.
Along with Orion, the first SLS launch will carry 13 6U smallsats, representing multiple disciplines and partners. The smallsats will be deployed from the Orion Stage Adapter.
CubeSats flown on EM-1 will provide a unique opportunity for innovative, low-cost research in deep space in a variety of fields.
MOON
• Lunar Flashlight – Jet Propulsion Laboratory, California
Searching for ice deposits and resources on the moon using a laser.
• Lunar IceCube – Morehead State University, Kentucky
Searching for water in all forms and other volatiles on the moon with an Infrared Spectrometer.
• LunaH-Map – Arizona State University, Arizona
Creating higher fidelity maps of near-surface hydrogen in craters and other permanently shadowed regions of the moon’s south pole with neutron spectrometers.
• OMOTENASHI – JAXA/University of Tokyo
Observing the radiation environment and soil mechanics of the moon.
• LunIR – Lockheed Martin, Colorado
Performing advanced infrared imaging of the lunar surface.
SUN
• CuSP – Southwest Research Institute, Texas
Measuring particles and magnetic fields as a space weather station.
ASTEROID
• NEA Scout – Marshall Space Flight Center, Alabama
Traveling by solar sail to a near-Earth asteroid and taking pictures and other characterizations of its surface.
EARTH
• EQUULEUS – JAXA, University of Tokyo
Imaging the earth’s plasmasphere for a better understanding of earth’s radiation environment.
OTHER MISSIONS
• BioSentinel – Ames Research Center, California
Using single-celled yeast to detect, measure, and compare the impact of deep-space radiation on living organisms over a long period of time.
• ArgoMoon – European Space Agency/ASI, ArgoTec, Italy
Observing the Interim Cryogenic Propulsion Stage as it follows its disposal stage with advanced optics and software imaging system.
CENTENNIAL CHALLENGES
  Cislunar Explorers – Cornell University, in Ithaca, New York focused around a water-electrolysis-based propulsion system
  CU-E3 – University of Colorado Boulder, CO; designed for a communications demonstration mission
  Team Miles – Miles Space will demonstrate evolutionary plasma thrusters

## Slide 16
Notes: Deep space human missions are made possible by SLS, Orion and Exploration Ground Systems at Kennedy Space Center. All three programs are represented in our mission patch for EM-1.
Orion and EGS have made a lot of progress. My point is that what we are developing is an exploration architecture that works together.