## Slide 1: Air Quality Forecasts using the NASA GEOS Composition Modeling and Data Assimilation System
K. Emma Knowland
USRA/GESTAR
NASA Global Modeling and Assimilation Office (GMAO)
In collaboration with:
GMAO: Christoph Keller, Lesley Ott, Steven Pawson, Emily Saunders, Brad Weir, Kris Wargan
Atmospheric Chemistry and Dynamics Lab: Bryan Duncan, Melanie Follette-Cook, Junhua Liu, Julie Nicely
9 April 2019

## Slide 2: NASA GMAO global meteorology and chemistry products
GEOS
Forecasting
Reanalysis
GEOS-FP
MERRA-2
GEOS-FPIT
GEOS-CF
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
Research product

## Slide 3: NASA’s composition forecast (GEOS-CF)
Ozone (O3)
Nitrogen Dioxide (NO2)
Fine Particulate Matter (PM2.5)
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
GEOS NWP
GEOS - Chem

## Slide 4: GEOS-Chem is a state-of-the science chemistry model
Tropospheric and Stratospheric full chemistry
250 reactive species, 725 reactions
100+ user/developer groups worldwide
Updated version is released about every year
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov

## Slide 5
GEOS NWP
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
Daily composition forecast
GEOS - CF
One 5-day forecast per day
GEOS - Chem

## Slide 6
GEOS NWP
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
Daily composition forecast
GEOS - CF
One 5-day forecast per day
  1-day hindcast
GEOS - Chem

## Slide 7
GEOS NWP
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
Daily composition forecast
GEOS - CF
One 5-day forecast per day
  1-day hindcast
  5-day forecast
GEOS - Chem

## Slide 8
GEOS NWP
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
Daily composition forecast
GEOS - CF
One 5-day forecast per day
  1-day hindcast
  5-day forecast
  c360 (0.25°, ~25x25 km2) resolution, 72 model layers
  O3, NOx, VOCs, PM ...
  1 January 2018 to NRT
GEOS - Chem

## Slide 9
GEOS NWP
GEOS - Chem
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
  Currently no direct data assimilation of constituents in GEOS-CF
GEOS - CF
Daily composition forecast

## Slide 10
GEOS NWP
GEOS - Chem
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
  Currently no direct data assimilation of constituents in GEOS-CF
  Aerosols constrained by satellite measurements of AOD
  Biomass burning emissions from QFED
GEOS - CF
Daily composition forecast

## Slide 11: Case study: agricultural fires in India
Observation
GEOS-CF
0 +1 +2 +3 +4 +5
MODIS fires Nov 01, 2017
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov

## Slide 12
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
  Currently no direct data assimilation of constituents in GEOS-CF
  Annual emission scale factors based on satellite
  Scale factors applied to emissions for diurnal and weekly variations
GEOS - CF
Daily composition forecast
Observation
GEOS-CF
0 +1 +2 +3 +4 +5

## Slide 13: Toward an air quality modeling system in the NASA GEOS model
GEOS data assimilation system:
 Weather
Aerosols
Fires
GEOS-Chem composition forecast model
Chemical data assimilation: O3, NO2, CO, …
Air Quality Modeling System
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov

## Slide 14
GEOS NWP
GEOS - Chem
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
  Currently no direct data assimilation of constituents in GEOS-CF
  Stratospheric Ozone relaxed to GEOS-FP O3
GEOS - CF
Daily composition forecast

## Slide 15
MERRA-2
GEOS-CF
GEOS FP
O3 in UT is greater in the assimilated products (GEOS FP & MERRA-2)
k.e.knowland@nasa.gov
christoph.keller@nasa.gov
Careful: Large gradient in O3 at UTLS
Flagstaff, Arizona, USA 17 April 2018 18UTC
O3 (ppbv)

## Slide 16: Chemical data assimilation system for reactive gases
Data Assimilation System
CO, NOx, O3
OMI
MOPITT
Weakly coupled; 6 hour assimilation window
GEOS NWP
GEOS - Chem
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
MLS

## Slide 17: Impacts of ozone assimilation are primarily seen in stratosphere
Boulder, 2013-07-25
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov

## Slide 18
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
GEOS CO Simulation
GEOS CO Assimilation
IASI CO Observations
Impacts of CO assimilation:
Aug 2010 Russian Wildfires

## Slide 19: Assimilation of CO reduces low bias relative to surface observations
CO [ppbv]
Control (no assimilation)
With assimilation
Implies significant (~20%) underestimation of CO emissions (?)
Alternatively: CO lifetime too short ( OH)
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov

## Slide 20
Assimilation of NOx and CO exacerbates
tropospheric ozone bias
Ozone [ppbv]
Control (no assimilation)
With multi-species assimilation
Improved diurnal cycle, most likely due to improved afternoon NO2
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov

## Slide 21: Machine learning mechanism for chemistry solver (random forest)
For more info see Christoph Keller’s
Presentation, Thursday 17:45
Room 0.60
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov

## Slide 22: Summary
k.e.knowland@nasa.gov :: christoph.a.keller@nasa.gov
GEOS-CF produces daily global air quality forecasts at 25km (16 miles) horizontal resolution since 1 January 2018
Output available at fluid.nccs.nasa.gov/cf
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov

## Slide 23: Summary
GEOS-CF produces daily global air quality forecasts at 25km (16 miles) horizontal resolution
Output available at fluid.nccs.nasa.gov
Under development:
Assimilation system for trace gases (O3, NOx, CO, & others)
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
k.e.knowland@nasa.gov :: christoph.a.keller@nasa.gov

## Slide 24: Thank you!
k.e.knowland@nasa.gov :: christoph.a.keller@nasa.gov
k.e.knowland@nasa.gov christoph.a.keller@nasa.gov
https:/fluid.nccs.nasa.gov/cf