## Slide 1: Supporting Material for APL’s Interstellar Probe Final Report
December 3, 2019
Rob Stough / XP50
David Hitt / XP50
Barney Holt / ED04
Alan Philips / ED04
Margaret Patrick / ED04

## Slide 2: Data Package Summary
Stage adaptor sizing GR&A and estimated mass
Integrated Stages and adaptors under the 8.4m, short fairing
SLS Block 1B GR&A for C3 estimates
SLS C3 performance with additional upper stages
Representative Trajectory
Supplemental Descriptions

## Slide 3: Star48BV
43.3 inch top interface diameter
Estimated 143.9 inch tall adapter (45. deg angle)
4,772 lb motor total mass (NGIS catalog)
Supporting 22,050 lb payload (design point)
Estimated 121 inches to CG
1821 lb (basic mass) + 328 lb (MGA) = 2149 lb predicted mass

## Slide 4
13.5 m
489 m3

## Slide 5: Star48GXV
49.0 inch top interface diameter
Estimated 141.0 inch tall adapter (45 deg. angle)
Supporting 22,050 lb payload
Estimated 139 inches to CG
1717 lb (basic mass) + 309 lb (MGA) = 2026 lb adapter predicted mass

## Slide 6
12.7 m
452 m3

## Slide 7: Orion 50XL
52.2 inch top interface diameter
Estimated 139.4 inch tall adapter (45. deg angle)
9,494 lb motor total mass (source:NGIS catalog)
Supporting 22,050 lb payload
Estimated 138 inches to CG
1768 lb (basic mass) + 318 lb (MGA) = 2086 lb adapter predicted mass

## Slide 8
12.4 m
441 m3

## Slide 9: Centaur D
NOTE: May require a forward bearing reactor
120.0 inch top interface diameter
Estimated 181.3 inch tall adapter (nozzle clearance)
34,524 lb stage total mass (MSFC internal estimate)
Supporting 22,050 lb payload
Estimated 152 inches to CG
2154 lb (basic mass) + 388 lb (MGA) = 2542 lb adaptor predicted mass

## Slide 10
7.1 m
205 m3

## Slide 11: Atlas V Centaur
NOTE: May require a forward bearing reactor
120.0 inch top interface diameter
Estimated 199.0 inch tall adapter (nozzle clearance)
Estimated 54,665 lb stage (MSFC internal estimate)
Supporting 22,050 lb payload
Estimated 166.5 inches to CG
2550 lb (basic mass) + 459 lb (MGA) = 3009 lb adapter predicted mass

## Slide 12
4.2 m
85 m3

## Slide 13: Castor 30B
95.0 inch estimated top interface diameter
Estimated 139.3 inch tall adapter (nozzle clearance)
30,800 lb motor mass (source:NGIS catalog)
Supporting 22,050 lb payload
Estimated 200 inches to CG
2265 lb (basic mass) + 408 lb (MGA) = 2673 lb adaptor predicted mass

## Slide 14
12.3 m
438 m3

## Slide 15: Castor 30XL
95.0 inch estimated top interface diameter
Estimated 154.0 inch tall adapter (nozzle clearance)
58,217 lb motor total mass (source: NGIS catalog)
Supporting 22,050 lb payload
Estimated 230 inches to CG
2934 lb (basic mass) + 528 lb (MGA) = 3462 lb adapter predicted mass

## Slide 16
10.9 m
374 m3

## Slide 17: Castor 30B – Star 48BV
EUS to Castor 30B
  2703 lb (basic mass) + 486 lb (MGA) = 3189 lb predicted mass
  Dimensions: 139.3 in tall, 331.0 in base, 95.0 in top
  Supporting 63,968 lbs including Castor 30B, Star 48BV, and 10 mt payload
  139.3 in to clear EUS fwd dome, vent valve, and nozzle
Castor 30B to Star 48BV
  302 lb (basic mass) + 55 lb (MGA) = 357 lb predicted mass
  Dimensions: 45.0 in tall, 95.0 in base, 43.3 in top
  Supporting 28,241 lbs including Star 48BV and 10 mt payload
  45.0 in to clear nozzle

## Slide 18
9.8 m
328 m3

## Slide 19: Castor 30XL – Star 48BV
EUS to Castor 30XL
  3470 lb + 625 lb (MGA) = 4095 lb adapter predicted mass
  Dimensions: 154.0 in tall, 331.0 in base, 95.0 in top
  Supporting 85,384 lbs including Castor 30XL, Star 48BV, and 10 mt payload
  154.0 in to clear EUS fwd dome, vent valve, and nozzle
Castor 30XL to Star 48BV
  302 lbs (basic mass) + 55 lb (MGA) = 357 lb adapter predicted mass
  Dimensions: 45.0 in tall, 95.0 in base, 43.3 in top
  Supporting 28,241 lbs including Star 48BV and 10 mt payload
  45.0 in to clear nozzle

## Slide 20
8.3 m
259 m3

## Slide 21: Centaur D – Star 48BV
EUS to Centaur D
  2918 lb (basic mass) + 525 lb (MGA) = 3443 lb adapter predicted mass
  Dimensions: 181.3 in tall, 331.0 in base, 120.0 in top
  Supporting 61,877 lbs including Centaur D, Star 48BV, and 10 mt payload
  181.3 in to clear EUS fwd dome, vent valve, and nozzle
Centaur D to Star 48BV
  439 lb (basic mass) + 79 lb (MGA) = 518 lb adapter predicted mass
  Dimensions: 45.0 in tall, 120.0 in base, 43.3 in top
  Supporting 26,818 lbs including Star 48BV and 10 mt payload
  45.0 in to clear nozzle

## Slide 22
12.8 m
459 m3

## Slide 23: Centaur (Atlas V) – Star 48BV
EUS to Centaur (Atlas V)
  3523 lb (basic mass) + 634 lb (MGA) = 4157 lb adapter predicted mass
  Dimensions: 199.0 in tall, 331.0 in base, 120.0 in top
  Supporting 84,432 lbs including Centaur, Star 48BV, and 10 mt payload
  199.0 in to clear EUS fwd dome, vent valve, and nozzle
Centaur (Atlas V) to Star 48BV
  439 lbs + 79 lb (MGA)= 518 lb adapter predicted mass
  Dimensions: 45.0 in tall, 120.0 in base, 43.3 in top
  Supporting 26,818 lbs including Star 48BV and 10 mt payload
  45.0 in to clear nozzle

## Slide 24
9.9 m
331 m3

## Slide 25: Orion 50XL – Star 48BV
EUS to Orion 50XL
  2172.8 lb (basic mass) + 392 lb (MGA) = 2564 lb adaptor predicted mass
  Dimensions: 139.4 in tall, 331.0 in base, 52.2 in top
  Supporting 36,312 lbs including Orion 50XL, Star 48BV, and 10 mt payload
  139.4 in for 45 degree adapter
Orion 50XL to Star 48BV
  96 lb (basic mass) + 17 lb (MGA)= 113 lb adaptor predicted mass
  Dimensions: 45.0 in tall, 52.2 in base, 43.3 in top
  Supporting 26,818 lbs including Star 48BV and 10 mt payload
  45.0 in to clear nozzle

## Slide 26
9.9 m
328 m3

## Slide 27: Castor 30B – Star 48GXV
EUS to Castor 30B
  2780 lb (basic mass) + 500 lb (MGA) = 3280 lb adapter predicted mass
  Dimensions: 139.3 in tall, 331.0 in base, 95.0 in top
  Supporting Castor 30B, Star 48GXV, and 10 mt payload
  139.3 in to clear EUS fwd dome, vent valve, and nozzle
Castor 30B to Star 48GXV
  318 lb (basic mass) + 57 lb (MGA) = 375 lb adapter predicted mass
  Dimensions: 60.0 in tall, 95.0 in base, 49.0 in top
  Supporting Star 48GXV and 10 mt payload
  60.0 in to clear nozzle

## Slide 28
9.0 m
292 m3

## Slide 29: Castor 30XL – Star 48GXV
EUS to Castor 30XL
  3493 lb (basic mass) + 629 lb (MGA) = 4122 lb adapter predicted mass
  Dimensions: 154.0 in tall, 331.0 in base, 95.0 in top
  Supporting Castor 30XL, Star 48GXV, and 10 mt payload
  154.0 in to clear EUS fwd dome, vent valve, and nozzle
Castor 30XL to Star 48GXV
  318 lb (basic mass) + 57 lb (MGA) = 375 lb adapter predicted mass
  Dimensions: 60.0 in tall, 95.0 in base, 49.0 in top
  Supporting Star 48GXV and 10 mt payload
  60.0 in to clear nozzle

## Slide 30
7.5 m
223 m3

## Slide 31: Centaur D – Star 48GXV
EUS to Centaur D
  3025 lb (basic mass) + 545 lb (MGA) = 3570 lb adapter predicted mass
  Dimensions: 181.3 in tall, 331.0 in base, 120.0 in top
  Supporting Centaur D, Star 48GXV, and 10 mt payload
  181.3 in to clear EUS fwd dome, vent valve, and nozzle
Centaur D to Star 48GXV
  451 lb (basic mass) + 119 lb (MGA) = 532 lb adapter predicted mass
  Dimensions: 60.0 in tall, 120.0 in base, 49.0 in top
  Supporting Star 48GXV and 10 mt payload
  60.0 in to clear nozzle

## Slide 32
12.1 m
425 m3

## Slide 33: Centaur (Atlas V) – Star 48GXV
EUS to Centaur (Atlas V)
  3565 lb (basic mass) + 642 lb (MGA) = 4207 lb adapter predicted mass
  Dimensions: 199.0 in tall, 331.0 in base, 120.0 in top
  Supporting Centaur, Star 48GXV, and 10 mt payload
  199.0 in to clear EUS fwd dome, vent valve, and nozzle
Centaur (Atlas V) to Star 48GXV
  451 lb (basic mass) + 119 lb (MGA) = 532 lb adapter predicted mass
  Dimensions: 60.0 in tall, 120.0 in base, 49.0 in top
  Supporting Star 48GXV and 10 mt payload
  60.0 in to clear nozzle

## Slide 34
9.2 m
298 m3

## Slide 35: Orion 50XL – Star 48GXV
EUS to Orion 50XL
  2499 lb (basic mass) + 450 lb (MGA) = 2949 lb adapter predicted mass
  Dimensions: 139.4 in tall, 331.0 in base, 52.2 in top
  Supporting Orion 50XL, Star 48GXV, and 10 mt payload
  139.4 in for 45 degree adapter
Orion 50XL to Star 48GXV
  125 lb (basic mass) + 23 lb (MGA) = 148 lb adapter predicted mass
  Dimensions: 60.0 in tall, 52.2 in base, 49.0 in top
  Supporting Star 48GXV and 10 mt payload
  60.0 in to clear nozzle

## Slide 36
9.1 m
295 m3

## Slide 37: SLS GR&A for High C3 Performance
B1B Vehicle:
  Expanded look at B1B, B1B with new build RS25s, and B1B BOLE
  Predicted masses for all elements and nominal propulsion performance.
Fairing:
  Keep integrated upper stages and payload within the 8.4m short PLF dynamic envelope
Upper stages:
  All 3rd and 4th stages are encapsulated under the fairing
  Existing stages in production
  FPR (Liquid Stages)
  Propellant Boiloff
  Solid performance nominal
  3rd Stages Assessed:
    Castor 30B (NGIS provided data)
    Castor 30XL (NGIS provided data
    Centaur (Government Estimate)
  4th Stages Assessed:
    Star 48 BV (NGIS provided data)
    Star48 GXV (NGIS provided data)

## Slide 38: Low Range C3 Performance

## Slide 39
Mid-Range C3 Performance

## Slide 40: High Range C3 Performance

## Slide 41: High C3 Representative Trajectory
Core Stage Flight
EUS Parking Orbit (1rev)
EUS Orbit Insertion
EUS Separation
Centaur Burn
EUS Ascent Burn
EUS 2nd Burn
Centaur Separation
Core Stage Separation
EUS Separation
Star48BV Burn

## Slide 42: Supplemental Descriptions
Adaptor Sizing Description:
In support of the interstellar probe study, NASA SLS employed the Advance Concept Office (ACO) to generate estimated masses for the stage adaptors interfacing the various upper stages. The adaptors are sized assuming a maximum payload on top of the last stage on the order of 10t. The adaptors consist of two interface rings with composite face sheets and an aluminum honeycomb core. The composite structure sizing is consistent with NASA CR-1457 and NASA SP-8007 references. After the basic mass of each adaptor is estimated, 18% of Mass Growth Allowance is added. Furthermore, the tool used to size the structure is the Launch Vehicle Analysis Tool (LVA). LVA has been in use at NASA MSFC since 1985 and has been used to develop every major NASA launch vehicle since that time. In addition, most major launch vehicle providers have a copy of the LVA tool; including Blue Origin, SpaceX, Boeing, and Northrup Grumman.
Description of manager’s reserve:
The manager’s reserve has been allocated to the EUS and the additional stages encapsulated in the fairing. The margin allocated as a percentage of wet mass of the stage relative to the summed mass of all upper stages. Furthermore, the manager’s reserve varies relative to the vehicle configuration being flown. For the initial configuration of the Block 1B, 1.4t of manager’s reserve is applied to the vehicle. After the block 1B is upgraded to accept the new enhanced performance boosters, the manager’s reserve is 2.1t.

## Slide 43: Embedded Data Files
Embedded Excel Spreadsheet
Embedded Word Document