## Slide 1: ACES Instrument
ACT- America Workshop- XCO2 Meeting
April 27th, 2020
Abigail Corbett1, Michael Obland2, Bing Lin2
SSAI, Inc.NASA LaRC

## Slide 2
ASCENDS CarbonHawk Experiment Simulator (ACES)
ACES is an intensity modulated continuous wave (IMCW) lidar developed to study column averaged CO2 mixing ratios (XCO2)
  Measures returns of multiple wavelengths (Pon/Poff) in three wavelengths at 1.57 m CO2 absorption band) in three bands to reduce noise and eliminate surface reflectance variation while targeting CO2
  Measurement techniques and instrument architecture similar to Multifunctional Fiber Laser Lidar (MFLL)
  Part of:
    Active Sensing of CO2 Emissions over Nights, Days, and Seasons (ASCENDS) Mission
  Piggybacked on:
    Atmospheric Carbon and Transport – America (ACT- America)

## Slide 3: ACES Differences from MFLL
ACES was built on the design pioneered by MFLL but was an attempt to shrink it into a smaller, UAV-capable instrument
ACES has more transmit power
  uses three ten-watt amplifiers instead of a single five-watt amplifier
  provides the opportunity to test for crosstalk by separating the wavelengths into separate amplifiers, which MFLL cannot do
Off the shelf unoptimized detector
No Zero Path measurement
  Difficult to measure with that much power output (6x more than MFLL)
  With no zero path measurement, one is estimated for each flight

## Slide 4: ACT – America Spring 2018 Data
17 flights between March 23rd and May 20th
Piggyback instrument
Experienced a data acquisition system issue that was fixed for the last 6 flights
Off the shelf unoptimized detector
Notes: amplifier was fixed and data acquisition was fixed for last 2 weeks of the campaign
some of the other days arent trash- just need to do some more intensive processing

## Slide 5: First Step: Filter Data
Take differential absorption optical depth from instrument and figure out what are full column, unobstructed measurements using 8 flags
  Filter out clouds, or other undesired scatterers
  Instrument errors
  Data recording errors
  Instrument attitude (pitch and roll <5o)
Notes: cloud- future work column from aircraft to cloud top
add cloud top arrow, surface arrows
This figure shows the ACES processing steps, comparing DAODACES, DOADin situ, and DOADMERRA
some of the noise" are cloud
single profile have multiple peaks, clouds, aerosols,
raw data time stamp
mention Joel's paper- "see Joel's paper"
mention why spirals arent continuous

## Slide 6
Spirals during the flight are used to create in situ profiles along the flight path.
Once in situ profiles have been created, DAODInSitu is derived using the profiles and the spectroscopy.
ACES DAOD points are matched to spirals based on aircraft attitude, location from the spiral, and time elapsed since spiral.
  < 25 kilometers from “spiral” center
  Within 1 hour of start and end of “spiral”
  No quality flags
Note:
DAODACESNadir – retrieval corrected to Nadir
DAODsmoothACES – filtered and smoothed
DAODInSitu - Only the relative in situ derived DADO points (where matched to ACES) are shown
Next STEP, comparisons

## Slide 7
** DAOD MERRA -
Assumes a constant CO2 profile throughout column (measured on airplane)
Uses GPS Altitude from aircraft as top column height
Only showing at this step to have more places to compare ACES than just in situ- really use it to scale DAOD to get XCO2
At higher altitudes, where CO2 concentrations are generally lower, we would expect the DAOD MERRA to be lower than DAOD ACES because we assumed CO2 remained at a low concentration through whole column
Next STEP, Analysis
Notes: say merra daod- uses merra profile and assumes a constant co2 concentration from picarro on aircraft
later on used to scaling OD to get xco2

## Slide 8
In order to derive MERRA DAOD of water vapor and carbon dioxide to compare with ACES 1:1,
Must use nadir range measured by the instrument, along with the GPS altitude
Notes: nadir range- use for merra altitude
5.8 high altitude clouds, not a lot of returns at 0
6 looks like flying in clouds

## Slide 9: XCO2 Retrievals
Process is similar to MFLL, where MERRA profiles are used to subtract DAOD from water vapor from the ACES total measured DAOD
ACES OD obs CO2 = ACES OD obs – modeled OD WV
Then, MERRA profiles assuming constant 400 ppm CO2 are used to scale the ACES DAOD
ACES XCO2 = (ACES OD obs CO2 / modeled ODCO2 =400ppm) * 400
Time (UTC seconds)
XCO2 (ppm)
* At this moment, we believe these large fluctuations are due to my MERRA modeled DAOD algorithm and are currently remedying this.

## Slide 10: Current work XCO2 Analysis
1 second and 10 second averages
Figure to show in situ XCO2 to show comparison