## Slide 1: Radio Occultation & Cloud-Free Land Surface Imagery
Liam Coulter & Joel McCorkel

## Slide 2: Radio Occultation
Remote sensing technique
Used to find atmospheric quantities:
  Temperature, pressure, water vapor content
Calculate bending of GPS signals through atmosphere
  Determine difference between theoretical distance wave travels vs actual distance
  Use integral transform to convert distance difference to angle of bending

## Slide 3
Data Processing Chain
GPS Data
Telemetry, PRNs, transmitted signals, clock information
GOES-R Data
Telemetry, received GPS signals, tracked PRNs, clock information
Convert ephemeris/almanac to ECEF
Precise Orbit Determination (POD) algorithm for GOES with MIT software
Correct for ionosphere delay (due to single frequency GOES receiver)
Compute pseudo-range from GPS & GOES-R timing, making more accurate by GOES phase observables
Compare GPS position with GOES-R to find times of possible occultations
End: Use RO in NWP
Compare pseudo-range computed w/ GOES & GPS clocks and phase to actual LOS distance
Sort received signals by tracked PRNS vs. used for navigation
Calculate bending angle α as a function of “impact parameter”
Calculate atmospheric profiles from bending angle
Determine PRNs from tracked GPS descending through atmospheric limb
Border Legend:
Blue: Done
Yellow: In Progress
Red: Not Attempted
Dashed: Not Essential
Get GPS and/or GOES clock errors

## Slide 4: Radio Occultation

## Slide 5: Cloud-Free Land Surface Imagery
Global Land Survey (GLS):
  Cloud-free land surface images generated every 10 years
  Image resolution: 30m (side of pixel)
MODIS-VIIRS:
  Cloud-free land surface images generated every 8 days
  Image resolution: ~1km
GOES-R:
  Could construct cloud-free images more quickly
  Image resolution: 2km (side of pixel)

## Slide 6: Cloud-Free Land Surface Imagery
Notes: Geometrically calculated distance from GOES to GPS 01

## Slide 7: Cloud-Free Land Surface Imagery
Notes: Geometrically calculated distance from GOES to GPS 01

## Slide 8: Future Work