## Slide 1: SPHERES/Astrobee Working Group (SAWG)
Meeting
April 29th, 2020

## Slide 2: Agenda

## Slide 3: Project Overview
Why Free Flyers on ISS? Provide a risk-tolerant testbed to:
Enhance & Enable Human Exploration (e.g. Gateway)
  Astrobee can potentially perform a range of Intra-Vehicluar Robotics (IVR) caretaking tasks to help maintain and protect the Gateway, particularly during uncrewed mission phases.
Perform Fundamental Research
Objectives
Based at Nasa Ames Research Center, the ISS Astrobee Facility provides a free-flying robotic system for ISS research and ISS STEM outreach. The Astrobee free-flying robotic system consists of three cubed-shaped robots, software, and a docking station used for recharging.
The project provides sustaining engineering tasks for ensuring the facility operational readiness on ISS.
The project provides payload support to users from academia, private industry, NASA, and other government agencies in the execution of ISS approved research and STEM objectives.
Current activities
Closing out SPHERES
Completing Astrobee commissioning activities
Maintaining & Operating Astrobee
Facilitating Free Flyer user community
  SPHERES/Astrobee Working Group (SAWG)
  International Partners: JAXA (Int-Ball) and DLR/Airbus (CIMON)
Notes: Tech dev, Tech matureing, Analog

## Slide 4: SAWG Community
SPHERES/Astrobee Working Group (SAWG) meeting
  Face-to-Face, twice a year
  Next will be in November 2020, location: Huntsville, AL
Purpose:
  Information sharing across the SPHERES/Astrobee community
  Astrobee Facility shares
    Status of resources (batteries, CO2 tanks, etc.),
    Overall Calendar (scheduled Test Sessions, upmass/return), and
    Updates on “new” PD, Investigations, and ISS infrastructure.
  Provide the SPHERES/Astrobee community (PD, investigators, etc.) with up-to-date information to determine opportunities to use the NL Facility
  Discuss proposed changes/updates to Astrobee Nat Lab which may be required to support a specific activity or research.

## Slide 5: Astrobee Users
10 Projects actively working towards ISS payloads
  Astrobatics (Naval Postgraduate School)
  SoundSee (Astrobotic/Bosch)
  Gecko (Stanford)
  RFID Recon (NASA AES/REALM-2)
  JAXA Kibo-RPC
  Astroporter (Tethers Unlimited)
  REGGAE (NanoRacks/Braunschweig)
  ISAAC
  R2AL (NASA AES)
  SVGS (FIT)
Ground Studies
  NMSU

## Slide 6: Highlights
SPHERES/Astrobee Working Group, Nov. 6th 2019
Hosted testing for JAXA, Columbia, Braunschweig, Naval Postgraduate School, RFID-Recon, and ISAAC
Last SPHERES session in December
Ramping up ISS Ops support capability from home during Covid-19 restrictions
Three-fingered Hand Integration, Columbia University
Astrobee SoundSee (Bosch) at CES 2020
IAC 2019

## Slide 7: Astrobee From Home

## Slide 8: Completed Commissioning
Crew Activity | Robot | Date
Checkout | Bumble | 4/30/19
Calibration & Mapping | Bumble | 5/13/19
Additional Mapping | Bumble | 5/23/19
Localization & Mobility 1 | Bumble | 6/14/19
Localization & Mobility 2 | Bumble | 7/12/19
Localization & Mobility 3a | Bumble | 7/24/19
Localization & Mobility 3b | Bumble | 8/28/19
Checkout & Calibration | Honey | 10/30/19
Localization & Mobility 4 | Bumble | 11/01/19

## Slide 9: What’s next
Extended Commissioning (Phase 1)
Crew Activity | Robot | Date
Battery Swap | Bumble and Honey | 04/29/20
Localization & Mobility 1 | Honey | 04/30/20
Payload Installation | TBD | TBD
Payload Demo | TBD | TBD
SPHERES/Astrobee Hand-off | TBD | TBD
Completion of Phase 1 enables support of initial Guest Scientists
RFID Recon, JSC
SoundSee, Astrobotic / Bosch
Gecko Gripper, Stanford
Kibo-RPC, JAXA
Notes: Update dates to be “Fall” “Spring 2020”

## Slide 10: Engineering

## Slide 11: Ground Lab Status
  Granite Lab: Online
  Flight Lab: Online
  Micro Gravity Test Facility (MGTF) Lab: Under Renovations
Under Renovations
  Engineering Evaluation Lab (EEL): Available upon request

## Slide 12: Hardware Status
Name | Status | Plans
Flat Sat A | Operational | Hardware checkout
Flight 1,2 | In Space, checked out | Honey LOMO
Flight 3 | In Space, still in box | None currently
Flight Spare | Complete | At JSC for integrated testing (EMI, Acoustic)
Cert (B#) | Operational | Available for testing
Ground (Wannabee) | Operational | Available for testing

## Slide 13: Port Tester
Astrobee Port Tester delivered for launch on SpX-19
Objectives:
  Facilitate diagnostics of the Astrobee Free Flyers’ internal USB ports
  Test safe electrical current and voltage operation limits
  Connect with Astrobee through the High Level Processor (HLP) using Guest Science APK
  Serves as a USB pass-through connection to the HLP
  Serve as an internal ARC based payload to learn and better improve the guest science payload development process
  Ground unit has been tested on FlatSat, Bsharp, and Wannabee
  Ground and Crew procedures submitted for review

## Slide 14: Mapping Trajectory Generation
To facilitate mapping process, a repeatable trajectory is being tested/developed
Simulation/GDS first, and then Astrobee in Lab
2 sets of trajectories are required:
  Initial operation (by human operator):
    Nav Camera used for collecting data for Image processing, i.e Features/Control points
    Robot has no pre-known information of coordinate system or environment
    Suggestion for Crew operation
  Updated operation (by unattended Astrobee):
    Nav Camera used for collecting images for map updates
    Known Features/Control points
    Plan for Autonomous motion
Future direction
  Tool for updating/expanding an existing Sparse Map

## Slide 15: Dock Shutdown anomaly
The dock switches to an unknown state every few weeks, causing the Astrobees connected to not charge their batteries and die.
I2C
I2C
I2C
1)EPS
1)EPS
2) DC
3) DP
AB1
AB2
Dock Controller
Dock Processor
Solution: Three Watchdog Timers
EPS Watchdog (~17 mins)
Dock Controller Watchdog (~17 mins)
Dock Processor Watchdog (Wandboard) (20 mins)

## Slide 16: GDS Guest Science Data View
Guest Science Commanding and Data View in the same place

## Slide 17: GDS Guest Science Data View
View data from multiple robots and APKS
View messages history
Advance to Data View

## Slide 18: GDS Guest Science Data View
Simple text based data display. More displays will be added
Return to Filters

## Slide 19: GDS Guest Science Data View
Simultaneous data display

## Slide 20: Flight Testing
Astrobee Robot Software release 0.10.4 is out on Github, it is being used for Honey LoMo
Today: Battery Swap
Tomorrow: Honey LoMo
  Verify Honey flight performance – have a second unit fully ready
  Validate current map prior to Kibo-RPC process checkout
  Gather mapping data
  Execute plans as time allows

## Slide 21: Lab Testing - Highlights
User Testing
  At Ames Visits
    JAXA visit to Ames developing testing strategy and evaluating game concept
    Astrobatics Lab test gathering trajectory data during tossing maneuver
    REGGAE lab test developing approach for operations and evaluating performance of various samples
    Columbia 3-finger gripper testing
  Remote Tests
    End-to-end test with JAXA controlling lab Astrobee from their lab
Imagery streaming to JSC Building 8 (a.k.a. VCC)
  Revalidated lab imagery streaming to Building 8
  Procedure for coordinating with Building 8 tested and finalized
  Observing Honey LoMo and viewing telemetry
SciCam Streaming
  End-to-end test successful.
  Will not be used until Building 8 Gateway-to-gateway VPN in place
  Building 8 Gateway-to-gateway VPN planned completion in June

## Slide 22: Ops

## Slide 23: Operations: Functions
Ensure Facility Readiness for ISS Test Sessions
  All crew training is handled via Onboard Training (OBT).
  Manage crew procedure and all planning products updates via OCR/ECR system
  Coordinate crew time with ISS Lead Increment Scientist and POIC Cadre
  Assist Astrobee team & PDs in acquiring proper access to ops systems as needed
  Coordinate with investigators for product development and delivery
  Help investigators set up remote communication capabilities as needed
Real-Time ISS Test Session support
  Coordinate with SpOC (Specialist OC) any deltas to real-time ops and products
  Support crew & POIC cadre real-time ops – conduct crew conferences as needed
  Coordinate Commanding Window requirements and planning
  Test session data and video management
Public Relations
  Maintain website, work with ARC PAO office to publish material on site

## Slide 24: Operations: Functions
Increment Planning
  2-pager development and submittal, updates as needed throughout increment
  Regular timeline planning with Lead PPM (Payload Planning Manager) and PPM planning team.
Safety and Verification Assessments
  Integrated Safety & Verification Assessments as needed (Guest Science etc.)
  Current SPHERES Safety & Verification focuses on return of hardware.
  Complete CoFR (Certification of Flight Readiness) for ground systems and on-orbit hardware and operations products.
Astrobee Ground Ops Development
  Coordinate ground Engineering and Operations Readiness Tests (ERTs/ORTs) in preparation for real-time ops.
  Work with Astrobee team and PDs to develop flight procedures, coordinate reviews with MSFC for final delivery and formal ECR review.

## Slide 25: Increments 60/61 & 62/63
Increments 60/61 (~Sept 2019 to April 2020)
SPHERES Test Sessions (since last SWG 11.6.19)
  ReSwarm Science 3 – December 31
Astrobee Commissioning Activities (since last SWG 11.6.19)
  Astrobee A Localization & Mobility 4 – October 30
  Astrobee B Checkout/Calibration – November 1
Increments 62/63 (April 2020 to April 2021)
Astrobee B Localization & Mobility 1 – April 30
JAXA Kibo-RPC Process Checkout – May 13
JAXA Kibo-RPC Rehearsal for Final Round – ~August 18
JAXA Kibo-RPC Final Round – ~September 17
SoundSee TBD [crew procedure initial draft in development]
RFID-Recon TBD [crew procedure final draft to be delivered to MSFC over next week]
Payload Install (Astrobee Arm) TBD [crew procedure in pre-ECR review at MSFC]
SPHERES/Astrobee Handoff TBD [no procedure]
Payload Demo (Astrobee Arm) TBD [procedures need to be developed]
Astrobee A/B LoMo as needed TBD [procedures already baselined]

## Slide 26: Increments 60/61 & 62/63
Increments 62/63 (April 2020 to April 2021)
Additional Guest Science
  Gecko TBD [final draft of crew procedure delivered to MSFC]
  Port Tester [final draft of crew procedure delivered to MSFC]
  Astrobatics [initial draft of crew procedure to be developed over next month+]
  REGGAE [initial draft of crew procedure to be developed over next month+]
Other ground and ISS activities
  Weekly Mondays commanding (Jonathan has been working his magic.)
  16 ERT/ORTs (Engineering/Operational Readiness Test)
  Astrobee Ops Planning for Increment 62/63 with MSFC ongoing
  59S Crew Debrief for Christina Hammock Koch & Luca Parmitano (3.25.20)
  A majority of the safety paperwork for return and trashing of SPHERES hardware has been complete.

## Slide 27: SPHERES & Astrobee Calendar

## Slide 28: Safety, Verification, Consumables
Safety
SPHERES (beacons, antenna, DP, 3D printed hooks) Return on SpX-20 – Approved: 2019/03/16
SPHERES (satellites) Return on SpX-21 – In work
Astrobee - JAXA Kibo-RPC software hazard exception – In Review
Consumables downmass
Empty SPHERES CO2 tanks have been returned to ARC. Remaining tanks on ISS have been trashed.
All SPHERES battery packs have been trashed.

## Slide 29: Astrobee and SPHERES on Social Media
Twitter
  https://twitter.com/NASA_SPHERES
Website
  http://www.nasa.gov/spheres
  http://www.nasa.gov/astrobee