## Slide 1
Luke D’Aquila*, Brian Helenbrook*, Alireza Mazaheri**
*Clarkson University, Department of Mechanical and Aeronautical Engineering
**NASA Langley Research Center, Aerothermodynamics Branch
AIAA Aviation Forum, June 15-19 2020
by Luke D’Aquila. Published by the American Institute of Aeronautics and Astronautics, Inc., with permission.
High-Order Shock Fitting With Finite Element Methods

## Slide 2
Shock Capturing
  Maintain monotonicity of flow solution around shock
  Capture shock within multiple mesh elements
  Easier to implement and generalize
Background – Shock Wave Simulations
Shock Tracking
  Align discontinuity with mesh interface
  Shock as a true discontinuity
  Difficult to generalize for multiple shocks

## Slide 3
Moving grid shock tracking
  Shock fitted mesh interface moves with shock
  Interior mesh deforms and adapts to maintain quality
Methodology
Finite element solver
  Euler equations
  Arbitrary Lagrangian-Eulerian (ALE) moving mesh
  Time advance flow solution and shock location consistently

## Slide 4
Three methods implemented:
  Zou (JCP 2017) Use a Riemann invariant with the Rankine-Hugoniot (RH) jump conditions to evaluate shock velocity [1]
  Henrick (JCP 2006) Use equation for momentum immediately downstream of shock with the RH jump conditions to evaluate shock acceleration [2]
  Zhong (JCP 1998) Use characteristic relation behind shock along with RH jump conditions to evaluate shock acceleration [3]
Shock Motion

## Slide 5
1D Method of Manufactured Solution (MMS)

## Slide 6
1D MMS – Grid Refinement Study
Mesh Spacing [m] | Method 1 | Method 2 | Method 3
0.1571 | 1.3854e-5 | N/A | 1.3969e-5
0.0785 | 8.6167e-7 | N/A | 8.6316e-7
0.0393 | 5.3834e-8 | N/A | 5.3856e-8
0.0196 | 3.3641e-9 | N/A | 3.3641e-9
Convergence Rate | 4.0024 | N/A | 4.0062

## Slide 7
Interface motion normal to shock:
Discrete form:
2D Interface Motion
Stabilization of interface motion
  U is interface wave speed
  𝜏 is stabilization parameter
No Stabilization
Stabilization

## Slide 8
Initialization
  1D isentropic nozzle
  Conserve mass in y-direction
  Initial shock at x = 7
2D Supersonic Nozzle
Evolution to steady state -- Mach number contours
Run simulation until steady state is reached

## Slide 9
2D Supersonic Nozzle
Steady state Mach number contours

## Slide 10
Richardson extrapolation
  Compare net wall force on 3 nested meshes
  Assume error ~ hα
Nozzle Solution Convergence

## Slide 11
Initialization
  Initial shock at x = 0.25y2 +1
  Initialize downstream properties based on incompressible flow over a cylinder
  Ramp up velocity near shock-outflow intersection
Blunt Body Problem
Mach 3 flow over cylinder at (2,0) with r = 0.5
Initial (left) and steady state (right) Mach number contours
Run simulation until steady state is reached

## Slide 12
Blunt Body Problem
Evolution from initial condition to steady state
  Contours of Mach number

## Slide 13
Blunt Body Problem – No Interface Stabilization
Solution does not converge
Left: Density (top) and temperature (bottom) along cylinder surface
Right: Contours of Mach number near the shock

## Slide 14
Nondimensional density (left) and temperature (right) along cylinder surface
Blunt Body Problem – With Interface Stabilization

## Slide 15
Blunt Body Problem
Nondimensional density (top) and temperature (bottom) along stagnation line

## Slide 16
Richardson extrapolation
  Compare net force on cylinder surface
Blunt Body Solution Convergence

## Slide 17
  Shock tracking can provide high-order solution accuracy
  Accurate evaluation of shock motion is critical
    Of the methods tested, Method 1 is preferred
  Initialization is a challenge when solving practical problems
  Stabilization must be introduced to the interface motion equation
Conclusions

## Slide 18
Dongyang Zou, Chunguang Xu, Haibo Dong, and Jun Liu. A shock-fitting technique for cell-centered finite volume methods on unstructured dynamic meshes. Journal of Computational Physics, 2017.
References
[1]
A. Henrick, T. Aslam, and J. Powers. Simulations of pulsating one-dimensional detonations with true fifth order accuracy. Journal of Computational Physics, 2006.
[2]
Xiaolin Zhong. High-order finite-difference schemes for numerical simulation of hypersonic boundary-layer transition. Journal of Computational Physics, 1998.
[3]