## Slide 1
Multidisciplinary Optimization of an Electric Quadrotor Urban Air Mobility Aircraft
Eliot Aretskin-Hariton, Eric Hendricks, Daniel Ingraham, Justin Gray, Sydney Schnulo, Jeffrey Chin, Robert Falck, Dustin Hall
NASA Glenn Research Center

## Slide 2: Goals Overview
Demonstrate ability of multidisciplinary analysis tools to perform coupled analysis in the preliminary design phase
Quadrotor and Mission
Optimization Environment
Coupling Subsystems
Subsystem Details
Results
Conclusions

## Slide 3: Quadrotor and Mission
Baseline Mission:
Single Passenger
All-electric
92.6 km
1.5km altitude ceiling
200m minimum cruise altitude
Subsystems: Propulsion, Thermal, Mass, Aero, Trajectory

## Slide 4: Optimization Environment:
OpenMDAO
  Gradient based optimization
  Analytical derivatives
  Open Source
Dymos
  Allows for time-varying optimal control optimization
  Pseudospectral methods
  Varying fidelity phases
  Open Source

## Slide 5: Tandem Flight Phases
Main Phase – Lower Fidelity
Thermal Phase – Higher Fidelity

## Slide 6: Coupling Subsystems – XDSM Main Phase

## Slide 7: Subsystems: Rotor
CCBlade.jl combines momentum theory and blade element theory (BEMT) library created by Andrew Ning
Breaks the blades up into sections or blade elements
Thrust input results in rotation rate output
Fixed pitch propeller
Optimizer Controls: Blade Twist

## Slide 8: Subsystems: Motor, Gearbox, Converter
Motor is a simple efficiency curve
  2000 rpm at max efficiency 97%
Gearbox has a fixed efficiency 99%
Converter has a fixed efficiency 98%
Heat load sent to thermal system
Optimizer Controls:
  Maximum Rotor Power,
  Optimal Rotor RPM (gearbox ratio)
Future Work:
Mid-Fidelity Motor Model

## Slide 9: Subsystems: Electrical Power
Zappy load flow model for electrical power distribution is typical of terrestrial power grids
Balances power output by the battery with power demand generated by the motor and line losses
Creates heat load on the thermal system

## Slide 10: Subsystems: Battery
Battery model uses battery temperature and state of charge to calculate voltage output.
State of Charge (SOC) starts at 95% charge and is allowed to sink to 20% but the end is just a lower constraint
Creates heat load for thermal system
Optimizer Controls: Total available power (kWh) , Maximum energy draw (amps)

## Slide 11: Subsystems: Thermal
Thermal system tracks battery, coolant, forward motor, and aft motor temperatures
Optimizer Controls: Heat Exchanger size, Throat Area

## Slide 12: Subsystems: Aerodynamics & Mass
Simple drag with spherical vehicle
Weights for all components
Calculates Masses for:
  Fuselage
  Landing gear
  instrumentation

## Slide 13: Subsystems: Trajectory
Equations of Motion (EOM) track vehicle translational position and velocity and rotational position and velocity
Uses thrust to calculate translational and angular acceleration based on axi-symmetric inertia matrix
Optimizer Controls: Thrust produced by forward and aft rotors

## Slide 14: Summary of Problem

## Slide 15: Results: Baseline Video

## Slide 16: Results: Baseline Video
* Altitude (ft)
* Battery Temp (C)

## Slide 17: Results: Battery Thermal Sweep

## Slide 18: Results: Design Sweeps
Sweeps of Range, Battery Temp, Energy Density, and Rotor Diameter

## Slide 19: Conclusions
Thermally constrained trajectory
Battery temp constraints have small effect on system weight
Changing trajectory can be more effective than increasing thermal management system weight
Demonstrated tightly coupled optimization
earetski@mail.nasa.gov
Questions?