## Slide 1: SpaceCubE OVERVIEW and Use of COTS Parts in Space
Dave Petrick, Gary Crum, Alessandro Geist, Christopher Wilson
Embedded Processing Group
2020 NEPP ETW
15 June 2020
Edited and Presented by: Dave Petrick, GSFC S&MA Assistant Director for Technical

## Slide 2: Outline
Background
SpaceCube Introduction
SpaceCube Design Approach
SpaceCube Flight History
Use of COTS Parts
Conclusion

## Slide 3: Embedded Processing Group (EPG)
EPG Group Specializes in Embedded Development
Hardware acceleration of algorithms and applications
Intelligence, autonomy, and novel architectures
Flight software integration for development platforms
Advanced architectures and research platforms
Advanced Platforms for Spaceflight
SpaceCube v1.0
SpaceCube v2.0 and v2.0 Mini
SpaceCube v3.0 and v3.0 Mini
SpaceCube Mini-Z and Mini-Z45
Key Tools and Skills
Flight Software: cFE/cFS, driver integration, flight algorithms
GSE: COSMOS, GMSEC, system testbeds
FPGA Design: Hardware acceleration, fault-tolerant structures
Mission Support: Supporting flight cards, algorithm development
On-board Autonomy and Analysis: deep-learning and machine- learning frameworks, unique architectures
SpaceCube v2.0

## Slide 4: Background
The next generation of NASA science and exploration missions will require “order of magnitude” improvements in on-board computing power …
Real-time Sensing and Control
On-Board Data Volume Reduction
Real-time Image Processing
Autonomous Operations
On-Board Product Generation
Real-time Event / Feature Detection
On-Board Classification
Real-time “Situational Awareness”
“Intelligent Instrument” Data Selection / Compression
Real-time Calibration / Correction
Inter-platform Collaboration
Mission Enabling Science Algorithms & Applications
Challenge

## Slide 5: Background (for context)
SpaceCube’s first mission use was for the HST Servicing Mission 4....which came with the strict HST design and mission assurance mindset of:
  Thou shalt fly only Level 1 parts  major screening/qual plan for Xilinx Virtex-4 FX60 FPGAs
  Thou shalt fly only IPC 6012B Class 3/A circuit boards  much time wasted
  Thou shalt mitigate ALL possibilities of SEUs  QMR was baseline mitigation....QMR!!!
What happened: we nearly didn’t make it due to unneeded requirements
  Schedule for screening started to slip and costs were sky-rocketing
     terminated the effort
  Cost/schedule growth for figuring out 6012 Class 3/A for a back-to-back 1mm-pitch FPGA
     went with Class 2/3
  Converging on a QMR voting structure for 4 PowerPC processors was more challenging than “sold”, risking not making the mission
    single-string, simple watchdog, internal TMR’d self scrubbing
Did I mention this was for an Autonomous docking tech demo that only had to operate for roughly 24 hours???

## Slide 6: The General Mentality in 2007....maybe still?
Unless you have 6012B Class 3/A circuit boards and Level 1 or 2 parts, it will never fly and never work
We want our mission to work, so we need Level 1 parts

## Slide 7: Introduction
Our Solution
SpaceCube
  A family of NASA developed space processors that established a hybrid-processing approach combining radiation-hardened and commercial components while emphasizing a novel architecture harmonizing the best capabilities of CPUs, DSPs, and FPGAs
High-performance reconfigurable science / mission data processor based on Xilinx FPGAs
  Hybrid processing - algorithm profiling and partitioning to CPU, DSP, and FPGA logic
  Integrated “radiation upset mitigation” techniques
  SpaceCube “core software” infrastructure (SCSDK) – Example (cFE/cFS and “SpaceCube Linux” with Xenomai)
  Small “critical function” manager/watchdog
  Standard high-speed (multi-Gbps) interfaces
SpaceCube is
Hybrid Processing…
SpaceCube v1.0

## Slide 8: Example SpaceCube Processing
Real-Time Image Tracking of Hubble
  Fire Classification
  Image Compression
Xilinx ISS Radiation Data
Spectrometer
Data Reduction
Gigabit Instrument Interfacing
Notes: SM4
Demonstration of data classification
Gigabit, flew on v1.5. 3 HD cameras, 2 SATA, GPS, IMU
Map: 4.5 years
Data reduction on ISS

## Slide 9: SpaceCube Approach
Our Approach
*Radiation tolerant – susceptible to radiation-induced upsets (bit flips) but not radiation-induced destructive failures
The traditional path of developing radiation-hardened flight processor will not work … they are always one or two generations behind
Accept that radiation-induced upsets may happen occasionally and just deal with them appropriately … any level of reliability can be achieved via smart system design!
Use latest radiation-tolerant* processing elements to achieve massive improvement in computing performance per Watt (for reduced size/weight/power)
01
02
03

## Slide 10: Device Comparisons
Chart: GOPS
| BAE Systems RAD750 | Cobham GR712RC | Cobham GR740 | BAE Systems RAD5545 | PowerPC 750FX (SCS750) | Freescale MPC8548E | Microsemi RTG4 | Xilinx Virtex-5QV FX130 | Virtex-5Q FX130T EF1738-1 | Zynq MPSoC 7EG* | Kintex UltraScale KU060*
8-Bit Integer | 0.266 | 0.08 | 1 | 3.728 | 12.8 | 16 | 418.32 | 503.72 | 870.4 | 2073.8659 | 3400.2121
16-Bit Integer | 0.266 | 0.08 | 1 | 3.728 | 6.4 | 8 | 252.18 | 214.57 | 422 | 796.5713 | 2512.7493
32-Bit Integer | 0.266 | 0.08 | 1 | 3.728 | 3.2 | 4 | 18.36 | 59.67 | 85.04 | 302.7467 | 563.887
Single-Precision Floating Point | 0.133 | 0.025 | 1 | 1.864 | 1.6 | 2 | 3.12 | 51.93 | 80.23 | 214.0443 | 332.317
Double-Precision Floating Point | 0.133 | 0.025 | 1 | 1.864 | 0.8 | 1 | 0.83 | 14.96 | 17.07 | 73.5485 | 136.2307
GOPS = Giga-Operations Per Second
T. M. Lovelly and A.D. George, “Comparative Analysis of Present and Future Space-Grade Processors with Device Metrics,” AIAA Journal of Aerospace Information Systems, vol. 14, no. 3, pp. 184-197, Mar. 2017.
SpaceCube Family provides more power efficient processing
*UltraScale results are an estimate based off of existing data, new metrics are in progress but not currently available

## Slide 11: Reconfigurability
    During mission development and testing
  Design changes without PCB changes
  “Late” fixes without breaking integration
Being Reconfigurable … … equals BIG SAVINGS (both time and money)
    During mission operations
  On-orbit hybrid algorithm updates
  Adaptive processing modes
    hi-reliability vs. high-performance
    intelligently adapt to current environment
    From mission to mission
  Same avionics reconfigured for new mission

## Slide 12: Reliability Analysis (SpaceCube v2.0)
Analysis | Status
Parts Stress and De-rating | Complete
Signal/Power Integrity | Complete
Reliability Block Diagram | Complete (specific to Restore-L use)
Worst Case Circuit Analysis | Complete
FMECA | Complete (specific to Restore-L use)
Radiation TID Analysis | Complete
Radiation SEE Rate Estimation | Complete for Polar, ISS, Mars
Back-to-Back CGA Solder Joint Fatigue | Complete
Test | Status
PWB Coupon Tests | Complete – All PASS IPC 6012B 3/A
Qual TVAC/Vibe per GEVS | Complete - PASS
RRM3/NavCube SpaceCube TVAC/Vibe/EMI | Complete - PASS
“Quick-Look” EMI/EMC | Complete - PASS
4x CGA Life Test Articles (-55/+100C) | Complete - 5x MoS factor achieved
SpaceCube is rooted on solid design, analysis and test practices

## Slide 13: Reliability Spectrum (It’s your choice)
Box redundancy
Card redundancy
Internal redundancy
Higher Part levels (COTS, 321)
Single string
Solid Robust Design Base
Full TMR/NMR
Selective mitigation
DDR ECC
Fault-Tolerant processor
Xilinx device type
BRAM Mitigation
Flash ECC
Configuration Scrubbing
SEL Monitors
No Mitigation
Reliability
Radiation Tolerance
The systems trades: Computing Performance vs. Radiation Performance
(adding levels of radiation tolerance requires some level of resources)
Mission Examples (low end to high end, in order of increasing cost):
Tech Demo (Do no harm): ISS, Single string, “EDU” parts, Config scrubbing, Flash ECC, Defense-grade Xilinx
Class D: COTs, Level 3 parts, selective mitigation and redundancy, FT processing
Class C: Level 3 parts, some redundancy, DDR ECC, FT processor for critical tasks, selective mitigation
Class A/B critical function: Level 1/2 parts, Box redundancy, FT processor, memory EDAC, possibly full TMR
Risk-based radiation assessment approach
COTS: Use-as-is from vendor, derated, most parts have “space” equivalent which gives some sense of radation performance, radiation assessment as needed. In some cases, DigiKey, Avnet, Mouser (as-is), “commercial” or “engineering model” versions of “flight” parts

## Slide 14: Flight History
SpaceCube is
Mission Enabling…
66+ Xilinx device-years on orbit
Closing the gap with commercial processors while retaining high reliability
26 Xilinx FPGAs in space to date (2020)
11 systems in space to date (2020)
SpaceCube v1.0
STS-125, MISSE-7, STP-H4, STP-H5, STP-H6
SpaceCube v1.5
SMART (ORS)
SpaceCube v2.0-EM
STP-H4, STP-H5
SpaceCube v2.0-FLT
RRM3, STP-H6 (NavCube), NEODAC, Restore-L (Lidar)
SpaceCube v2.0 Mini
STP-H5, UVSC-GEO
(all industry/commercial/defense grade, no additional screening)

## Slide 15: Flight Heritage

## Slide 16: SpaceCube Family Flight Mission Timeline
STP-H5
STP-H5
Today
2009
2010
2011
2012
2013
2014
2015
2016
2017
2018
2019
STS-125/HST/RNS
MISSE-7
SMART
STP-H4
STP-H4
STP-H5
RRM3
STP-H6
XCOM/NAVCUBE
UVSC
SpaceCube v1.0
SpaceCube v1.5
SpaceCube v2.0-EM
SpaceCube v2.0-FLT
SpaceCube v2.0 Mini

## Slide 17: SpaceCube v2.0 Processor Card
2x Xilinx Virtex-5 (QR) FX130T FPGAs (FX200T Compatible)
1x Aeroflex CCGA FPGA
  Xilinx Configuration, Watchdog, Timers
  Auxiliary Command/Telemetry port
4x 512 MB DDR SDRAM
2x 4GB NAND Flash
1x 128Mb PROM, contains initial Xilinx configuration files
1x 16MB SRAM, rad-hard with auto EDAC/scrub feature
16-channel Analog/Digital circuit for system health
Mechanical support for heat pipes and stiffener for Xilinx devices
Overview
External Interfaces
  Gigabit interfaces: 4x external, 2x on backplane
  12x Full-Duplex dedicated differential channels
  88 GPIO/LVDS channels directly to Xilinx FPGAs
Debug Interfaces
  Optional 10/100 Ethernet interface
Back-to-Back FPGA Design
Overview
Overview
TRL9 flight-proven processing system with unique Virtex back-to-back installed design methodology
3U cPCI (190 x 100mm) size
Typical power draw: 8-10W
22-layer, via-in-pad, board design
IPC 6012B Class 3/A PWB design
Key Features
US Patents:
9,705,320
9,549,467
9,851,763
10,667,398
10,681,837

## Slide 18: SpaceCube v1.0
STS-125 Shuttle Payload Bay
MISSE-7/8 ISS Payload
7 years of operation
4x Virtex-4 XC4VFX60: 0.1 SEU/FPGA/Week
2x on-orbit file uploads and reconfiguration
1% COTS Parts
2% COTS Parts

## Slide 19: On-Board Image Processing
Successfully tracked Hubble position and orientation in real-time operations
FPGA Algorithm Acceleration was required to meet 3Hz loop requirement
Rendezvous
Deploy (Docking Ring)
 Typical space flight processors are 25-100x too slow for this application
Notes:  RNS: Back of SM4 Shuttle
 Edge Detection  RED
Real-Time Processing: Compare to HST Model stored on SpaceCube
Objective: capture docking ring
Satellite Servicing  Upload new models

## Slide 20: STP-H4 ISS Payload
2 years of operation. 3x Virtex-5 XC5VFX130T: 1 SEU/FPGA/Week
Successful on-orbit file upload and reconfiguration
99% COTS Parts
COTS HD Cameras
COTS Ethernet Switch
1% COTS Parts
Notes:  STP-H5 has Mini, v1.0, v2.0EM

## Slide 21: STP-H5 ISS Payload
The Space Test Program-H5 (STP-H5) external payload, a complement of 13 unique experiments from seven government agencies, is integrated and flown under the management and direction of the Department of Defense’s Space Test Program.
Photo Credit: DoD STP
ISEM, SpaceCube Mini
SpaceCube v2.0 EM
SSCO Raven
SpaceCube v1.0 CIB
2/2017 - Current
98% COTS Parts
1% COTS Parts
99% COTS Parts

## Slide 22: Raven Payload
Objective:
To advance the state-of-the-art in rendezvous and proximity operations (RPO) hardware and software by:
Providing an orbital testbed for servicing-related relative navigation algorithms and software
Demonstrating relative navigation to several visiting vehicles:
  Progress
  Soyuz
  Cygnus
  HTV
  Dragon
Demonstrating that both cooperative and non-cooperative rendezvous can be accomplished with a single similar sensor suite
Visible Camera
Infrared
Camera
LIDAR
Raven
(Deployed Configuration)
Raven installed on STP-H5
(Stowed Configuration)
SpaceCube v2.0
$20M+ payload reliant on confidence in the SpaceCube computer, which in this case was pre-populated with 99% COTS Parts, and then thoroughly tested.

## Slide 23: Raven – Sample Data
Raven is currently generating valuable science that is setting the groundwork for future NASA missions that require rendezvous and proximity operations systems
Raven demonstrated successful on-board vehicle tracking of all vehicles docking with ISS
Dragon Tracking (VisCam)
CygnusTracking (VisCam)

## Slide 24: STP-H6 Payload
SpaceCube v1.0 CIB
SpaceCube v2.0 NavCube
1% COTS Parts
99% COTS Parts

## Slide 25: Infusion: NavCube on X-ray Communication Experiment (XCOM)
NavCube: Union of Navigator GPS and SpaceCube technology
  NavCube drives electronics for Modulated X-ray Source on Space Test Program-H6 (STP-H6) as part of X-ray Communications Experiment (XCOM)
  2016 Goddard Innovation of the Year
Flexible SpaceCube design enabled low-cost, rapid mission development
  Delivered Command and Data Handling FSW
  Supports inflight updates of FPGA and software
  Allowed significant software reuse leveraging key components from previous SpaceCube Missions
    RRM3: Core FSW component
    CeREs: AOS processing as part of cFS library
    STP-H: Packet processing for CCSDS and STP protocols
99% COTS Parts
Notes: https://www.nasa.gov/sites/default/files/atoms/files/cuttingedge_-_vol._13_issue_1_-_fall_2016.pdf
https://sites.google.com/site/cvgriffi/

## Slide 26: Accomplishments and Key Highlights: RRM3
1553/Ethernet/Digital Card
Analog Card
Robotic Refueling Mission 3 SpaceCube
Overview
Robotic Refueling Mission 3 (RRM3)
Technology demonstration experiment to highlight innovative methods to store and replenish cryogenic fluid in space
High Level Requirements
Interface with ISS and RRM3 instruments:
  Cameras, thermal imager, motors
Monitor/Control cryo-cooler and fuel transfer
Stream video data
Motor control of robotic tools
Host Wireless Access Point
95% COTS Parts
Notes: https://sspd.gsfc.nasa.gov/images/RRM3/RRM3_Factsheet_111318_final.pdf

## Slide 27: Accomplishments and Key Highlights: SpaceCube Mini-Z
Overview of SpaceCube Mini-Z
Collaborative development with NSF CHREC at University of Florida for Zynq-based 1U Board
  Selective population scheme between commercial and rad-hard components
  Rapid deployment prototyping
  Convenient pre-built software packages with cFS
Re-Envisioned to support quality-of-life upgrades and enable specific NASA mission needs
Missions and Heritage
Launched Feb 2017 to ISS on STP-H5/CSP featuring 2 CSPv1 cards performing image processing
Launched May 2019 to ISS on STP-H6/SSIVP featuring 5 CSPv1 for massive parallel computing
Featured on many more…
Original CSPv1
CSPv1 Development Board
STP-H5/CSP Flight Unit
NASA SpaceCube Mini-Z
98% COTS Parts

## Slide 28: Time-on-orbit
Project | Version | Part Req | BOM Count | COTS % | COTS Months
RNS | v1.0 | 2+ | 3700 | 1% | 12
MISSE-7 | v1.0 | N/A | 3100 | 2% | 22320
SMART | v1.5 | N/A | 1000 | 95% | 32
STP-H4 CIB | v1.0 | N/A | 1500 | 1% | 900
STP-H4 ISE2.0 | v2.0-EM | N/A | 1250 | 99% | 111375
STP-H5 CIB | v1.0 | N/A | 1500 | 1% | 1101
STP-H5 ISEM | v2.0 Mini | N/A | 1000 | 98% | 35966
STP-H5 Raven | v2.0-EM | N/A | 1500 | 99% | 136249
RRM3 | v2.0 | N/A | 1429 | 95% | 41498
STP-H6 CIB | v1.0 | N/A | 1500 | 1% | 295
STP-H6 GPS | v2.0 | N/A | 1157 | 99% | 22527
Restore-L Lidar | v2.0 | 3 | 2000 | 0% | N/A
STPSat6 | v2.0 Mini | N/A | 1500 | 98% | N/A
All Xilinxs flown have been unscreened
Failures:
Commercial Ethernet Hub on ISE2.0, 1-yr into mission
No known EEE part failures in orbit
Also to note: We flew many COTS components on some of these projects:
ISE2.0, SMART, and ISEM all flew COTS cameras that were ruggedized. SMART flew COTS SATA drives.
Raven flew a $5 USB interface card to an IR sensor
STP-H5 and -H6 have CHREC Space Processors (CSPs) that were 95% COTS components. See references for more info on CSP results (no failures to date)
RRM3 suffered a failure that may be related to a specific COTS part, but the part was used in a stressing condition that any grade part would eventually fail.
NavCube Commercial vendor populated PWBs

## Slide 29: Lessons
The likelihood of other issues is much greater than a part issue
  Workmanship, solder shorts, thermal design, cold solder joint, design deficiency, incompatible connectors, improper derating, worst case analysis deficiency, etc.
  Lots of “parts issues” that truly were not parts issues
Do not need to strictly satisfy long-standing practices or views
Robust design and test philosophy injects more confidence in end-product than what parts levels are inside the box. Part tolerance issues are flushed out of a good design and test program.
High number of EDUs increases the sample size, and the likelihood of finding a design/part issue

## Slide 30: Conclusion
SpaceCube is a MISSION ENABLING technology
Delivers exceptional computing power in number of form factors
Cross-cutting technology for Comm/Nav, Earth and Space Science, Planetary, and Exploration missions
Being reconfigurable equals BIG SAVINGS
Past research / missions have proven viability
Designs support AI applications for autonomy and analysis onboard
Successful technology transfer to industry through commercialization

## Slide 31: Contact Information
spacecube.nasa.gov
Principal Engineer Alessandro Geist alessandro.d.geist@nasa.gov
Special thanks to our sponsors: NASA/GSFC IR&D, NASA Satellite Servicing Programs Division (SSPD), NASA Earth Science Technology Office (ESTO), DoD Space Test Program (STP), DoD Operationally Responsive Space (ORS)

## Slide 32
Publications

## Slide 33: SpaceCube Publications
A. Geist, C. Brewer, M. Davis, N. Franconi, S. Heyward, T. Wise G. Crum, D. Petrick, R. Ripley, C. Wilson, and T. Flatley, “SpaceCube v3.0 NASA Next-Generation High-Performance Processor for Science Applications,” 33rd Annual AIAA/USU Conf. on Small Satellites, SSC19-XII-02, Logan, UT, August 3-8, 2019.
A. Schmidt, M. French, and T. Flatley, “Radiation hardening by software techniques on FPGAs: Flight experiment evaluation and results,” IEEE Aerospace Conference, Big Sky, MT, March 4-11, 2017.
A. Schmidt, G. Weisz, M. French, T. Flatley, C. Villalpando, “SpaceCubeX: A framework for evaluating hybrid multi-core CPU/FPGA/DSP architectures,” IEEE Aerospace Conference, Big Sky, MT, March 4-11, 2017.
D. Petrick, N. Gill, M. Hassouneh R. Stone, L. Winternitz, L. Thomas, M. Davis, P. Sparacino, and T. Flatley, “Adapting the SpaceCube v2.0 data processing system for mission-unique application requirements,” IEEE Aerospace Conference, Big Sky, MT, June 15-18, 2015.
T. Flatley, “Keynote 2 — SpaceCube — A family of reconfigurable hybrid on-board science data processors,” International Conference on ReConFigurable Computing and FPGAs (ReConFig14), Cancun, Mexico, Dec 8-10, 2014.
D. Petrick, A. Geist, D. Albaijes, M. Davis, P. Sparacino, G. Crum, R. Ripley, J. Boblitt, and T. Flatley, “SpaceCube v2.0 space flight hybrid reconfigurable data processing system,” IEEE Aerospace Conference, Big Sky, MT, March 1-8, 2014.
D. Petrick, D. Espinosa, R. Ripley, G. Crum, A. Geist, and T. Flatley, “Adapting the reconfigurable spacecube processing system for multiple mission applications,” IEEE Aerospace Conference, Big Sky, MT, March 1-8, 2014.
T. Flatley, “Keynote address I: SpaceCube: A family of reconfigurable hybrid on-board science data processors,” NASA/ESA Conference on Adaptive Hardware and Systems (AHS), June 25-28, 2012.
M. Lin, T. Flatley, A. Geist, and D. Petrick, “NASA GSFC Development of the SpaceCube Mini,” 25th Annual AIAA/USU Conf. on Small Satellites, SSC11-X-11, Logan, UT, August 8-11, 2011.
J. Esper, T. Flatley, and J. Bull, “Small Rocket/Spacecraft Technology (SMART) Platform,” ,” 25th Annual AIAA/USU Conf. on Small Satellites, SSC11-VII-6, Logan, UT, August 8-11, 2011.

## Slide 34: SmallSat / CubeSat Publications
S. G. Kanekal L. Blum E. R. Christian G. Crum M. Desai J. Dumonthier A. Evans A. D. Greeley S. Guerro S. Livi K. LLera J. Lucas J. MacKinnon J. Mukherjee K. Ogasawara N. Paschalidis D. Patel E. Pollack S. Riall Q. Schiller G. Suarez E. J. Summerlin, M. Desai, S. Livi, K. Llera, J. Mukherjee, and K. Ogasawara, “CeREs: The Compact Radiation belt Explorer,” 32nd Annual AIAA/USU Conference on Small Satellites, Logan, UT, Aug 4-9, 2018.
S. Sabogal, P. Gauvin, B. Shea, D. Sabogal, A. Gillette, C. Wilson, A. D. George, G. Crum, and T. Flatley, “Spacecraft Supercomputing Experiment for STP-H6,” 31st Annual AIAA/USU Conf. on Small Satellites, SSC17-XIII-02, Logan, UT, Aug 5-10, 2017.
C. Wilson, J. MacKinnon, P. Gauvin, S. Sabogal, A. D. George, G. Crum, T. Flatley, “µCSP: A Diminutive, Hybrid, Space Processor for Smart Modules and CubeSats,” 30th Annual AIAA/USU Conf. on Small Satellites, SSC16-X-4, Logan, UT, August 6-11, 2016.
C. Wilson, J. Stewart, P. Gauvin, J. MacKinnon, J. Coole, J. Urriste, A. D. George, G. Crum, A. Wilson, and M. Wirthlin, “CSP Hybrid Space Computing for STP-H5/ISEM on ISS,” 29th Annual AIAA/USU Conf. on Small Satellites, SSC15-III-10, Logan, UT, August 8-13, 2015.
B. LaMeres, S. Harkness, M. Handley, P. Moholt, C. Julien, T. Kaiser, D. Klumpar, K. Mashburn, L. Springer, G. Crum, “RadSat – Radiation Tolerant SmallSat Computer System, “29th Annual AIAA/USU Conf. on Small Satellites, SSC15-X-8, Logan, UT, August 8-13, 2015.
S. Altunc, O. Kegege, S. Bundick, H. Shaw, S. Schaire, G. Bussey, G. Crum, J. Burke, S. Palo, D. O’Conor, “X-band CubeSat Communication System Demonstration,” 29th Annual AIAA/USU Conf. on Small Satellites, SSC15-IV-8, Logan, UT, August 8-13, 2015
D. Rudolph, C. Wilson, J. Stewart, P. Gauvin, G. Crum, A. D. George, M. Wirthlin, H. Lam, “CSP: A Multifaceted Hybrid System for Space Computing,” Proc. of 28th Annual AIAA/USU Conference on Small Satellites, SSC14-III-3, Logan, UT, August 2-7, 2014.
S. Palo, D. O’Connor, E. DeVito, R. Kohnert, G. Crum, S. Altune, “Expanding CubeSat Capabilities with a Low Cost Transceiver,” Proc. of 28th Annual AIAA/USU Conference on Small Satellites, SSC14-IX-1, Logan, UT, August 2-7, 2014.