## Slide 1: SMD Class D standard MAR
Jesse Leitner, Chief SMA Engineer, GSFC
Agency-wide team including APL and SWRI
Notes: What do our colors really mean?
  Yellow (Warning)
    Management awareness/attention needed
    Items usually get discussed at Division/Directorate meetings
  Red (Critical)
    Impact is significant and management awareness/attention needed
    Items usually get discussed at Directorate/Center meetings

## Slide 2: Outline
Background
Agency Team
Class D principles
Significant departures from common practices
Other highlights
Summary

## Slide 3: Background
Numerous activities have taken place over the past several years to address the fact that Class D practices across the agency have differed little from those for Class A, B, or C missions
Most of these activities have not resulted in substantial efforts to tangibly change how we perform Class D developments
The result is that we have been limited in our ability to push the boundaries for moderate-risk/high-payoff missions
This development effort has taken a very detailed view of the practices that are in place to ensure safety and mission success, and tunes them into risk-driven activities that accept developers’ approaches in contrast to the current “do it the way we always have” approaches that have been difficult to depart from.
This approach emphasizes the processes that provide the most risk reduction payoff and avoids the “feel-good” types of requirements that are abundant for Class A and Class B missions, where there is significant tolerance for overrun.
This approach further emphasizes developer standard practices as opposed to prescriptive “do it our way” practices.
At this point, there will be no choice, no matter what the risk posture, but to implement a “true Class D” for most cubesat missions and a range of other highly resource-constrained missions that will soon be in development

## Slide 4: Agency Team
GSFC: Jesse Leitner (lead), Ron Perison
LaRC: Joey Patterson, Don Porter
JPL: Tom Ramsey, Sammy Kayali, Naomi Palmer
Glenn: Cynthia Calhoun
MSFC: Rodney Key, Kelly Bellamy, Michael Giuntini, James Kissell, Keith Dill
ARC: Steve Jara, Don Mendoza
APL: Steve Pereira, Rick Pfisterer
SWRI: Joerg Gerhardus, John Stone

## Slide 5: Class D Principles: Dos & Don’ts
Do:
  Streamline processes (less formal documentation, e.g., spreadsheet vs. formal software system for waivers, etc.)
  Focus on tall poles and critical items from a focused reliability analysis
  Tolerate more risk than A, B, or C (particularly schedule risk)
  Capture and communicate risks diligently
  Rely more on knowledge than indirect requirements
  Put more decisions into the hands of the engineers on the floor.
  Have significant margin on mass, volume, power (not always possible, but strongly desirable)*
  Have significant flexibility on performance (level 1/level 2) requirements (not always possible, but strongly* *desirable)
Don’t:
  Ignore risks!
  Reduce reliability efforts (but do be more focused and less formal)
  Assume nonconforming means unacceptable or risky
  Blindly eliminate processes
While the impression may be that a Class D is higher risk from the outside, if implemented correctly (and consistent with the intention), in reality the extra engineering thought about risk may actually reduce the practical risk of implementation.
*outside scope of MAR

## Slide 6: Significant departures from common practices (1/3)
GMIPs (consistent with NPR 8735.2B)
  No predefined set of GMIPs
  Based on upfront negotiation considering
    assessment of developer’s own inspection points
    developer identified risks
    project identified risks; and furthermore in response to events, such as failures, anomalies, and process shortfalls that prompt a need for further inspection.
  Will be coordinated with the project to maximize efficiency and minimize schedule impact
Inherited items process
  Allows a holistic, risk-based process based on
    Prior history
    Changes from previous (in H/W, S/W, operation, environment)
    Past anomalies
  Allows prior processes to be used without waivers
  Decisions to use or impose additional tests, etc., based on risk

## Slide 7: Significant departures from common practices (2/3)
Workmanship
  Workmanship standards (industry and NASA) provided as guidance, developer standard practices allowed
EEE parts
  Follows NASA-STD-8739.10 for Class D: Level 4 = COTS parts with no additional screening
  Guidance provided to consider:
    Prior usage of the part and qualification for the specific application
    Manufacturing variability within lots and from lot to lot for parts
    Traceability and pedigree of parts
    Reliability basis for parts.
    Parts stress/application conditions

## Slide 8: Significant departures from common practices (3/3)
Radiation
  Emphasis on radiation-tolerant design
  Part-by-part analysis and testing otherwise
Printed Wiring Boards
  Use own preferred standard
  Project retains coupons or spare boards until mission disposal

## Slide 9: Minor departures from common practices
ARB/MRB/FRB
  Government notified and invited to participate in type I (form, fit, function)
  Type II – Government given access to, but timely notification not required
Reliability
  Project completes reliability analysis (e.g., FTA, FMEA) for faults that may lead to injury to personnel or the public, or produce orbital debris, or that may affect host platforms
  Parts stress and derating analysis per EEE-INST-002 or comparable
Software assurance
  NASA-STD-8739.8 required
Software safety
  Safety critical elements determined from the hazard analysis and range requirements
GIDEP: project shall take action to mitigate the effects of alerts on the project

## Slide 10: Other elements
Lifting
  Vendor practices if command media exist
  NASA-STD-8719.9 for all others
ESD: ANSI/ESD S20.20-2007
Lead-free and whisker controls required
Assurance Plan for new digital electronic designs (FPGAs, ASICs, etc)
Planetary Protection for outside of earth orbit
Cybersecurity and Command Link Protection

## Slide 11: Review and Approval Process
Within MAR development team reviews
Team – Center/organization outreach
Program Office reviews
SMD technical area reviews
OSMA discipline review
  OSMA signoff
The MAR is now an Appendix in SMD’S Class D Implementation Plan
There is still debate in HQ about elements of the Implementation Plan, outside of the MAR that is holding up approval of the document

## Slide 12: Summary
A Standard Mission Assurance Requirements document has been produced to represent the general set of requirements to impose on SMD Class D missions
This is the first such document that truly addresses significant costs and programmatic risks that were not really addressed in the past.
The document has completed approval process in HQ/OSMA and is now baselined as part of a new SMD Class D Implementation Plan. We are waiting for unrelated issues with the Implementation Plan to be worked out.

## Slide 13: Backup materials