## Slide 1: SURF2ing from ground-based network towards space-borne orbit
SURF2: Strategies for UAS Resembled Formation-Flight
Si-Chee Tsay &
SMARTLabs team
FY21/IRAD GSFC/WFF/LaRC
To acquire PBL targeted observables (e.g., thermodynamics, kinematics, air quality, low-level cloud/precip) over densely-populated coastal region requires critical measuring strategies in dealing with heterogeneous surface conditions.
MODIS 30s (~1 km) Land Cover
60km30km
Evergreen Forest
Deciduous Forest
Mixed Forests
Closed Shrublands
Open Shrublands
Woody Savannas
Savannas
Grasslands
Wetlands
Croplands
Urban/Built-Up
Barren/Sparsely Vegetated
Water
: WFF
: UMD-ES
MD
VA
POPS: Printed Optical Particle Spectrometer for sizing range of 140 nm – 3 µm in radius
MA200: Micro-Aethalometer, absorption at wavelengths of 375, 470, 528, 625 and 880 nm
MHP: Multi-Hole Probe for 3D wind speeds and direction, including P, T & RH
Datalogger
GPS
1m inlet
P/T/RH
PM2.5 sensors
POPS,
MA200 sensors
Camera
Dryer
(a)
(b)
(c)
Nose cone modular payload
outside
inlets
inside
Fully automated launch & landing
PM2.5
Kite
MHP
P/T/RH & 3D-Winds
By mimicking space formation flights, sUAS probing over WFF supersite and strategically distributed network sites can characterize the PBL/TOs with reduced risk and improved cost efficiency for unprecedented sample size and statistics.
SURF2 observations will help (1) to shape the sampling criteria for future space-based PBL missions, and (2) to establish and serve as a calibration/validation baseline for future coastal PBL missions.