## Slide 1: Revealing TEMPO’s Capability for Observing Ozone Precursors
Presented by Laura Judd, NASA Langley Research Center

## Slide 3
Provides hourly daylight observations to capture rapidly varying emissions & chemistry important for air quality
  Key tropospheric pollutants measured
    Tropospheric ozone
    Ozone Precursors: nitrogen dioxide (NO2) and formaldehyde (HCHO)
    Aerosol optical depth
  Distinguishes boundary layer from free tropospheric ozone
Model-simulated NO2. Warmer colors indicate larger amounts.
Launching in 2022
TEMPO Mission Leads:
Principal Investigator:
Kelly Chance, Smithsonian Astrophysical Observatory
Instrument Development:
Ball Aerospace & Technologies Corporation
Project Management:
NASA/Langley Research Center
http://tempo.si.edu/

## Slide 4
NASA-Associated Air Quality Remote Sensing Campaigns 2011-Present
Tropospheric NO2 x 1015 molecules cm-2
Base Map: S5P TROPOMI Oversampled NO2 April 2018-March 2019
Data provided by Henk Eskes/KNMI
2
1,9
7
4
3, 13
6
10
8
1: DISCOVER-AQ Maryland 2011
2: DISCOVER-AQ California 2013
3: DISCOVER-AQ Texas 2013
4: DISCOVER-AQ Colorado 2014
5: Korea-US Air Quality (KORUS-AQ) Study 2016
6: Lake Michigan Ozone Study (LMOS) 2017
7: Student Airborne Research Program (SARP) 2017
8: Ozone Water-Land Environmental Transition Study (OWLETS)-1 2017
9: Ozone Water-Land Environmental Transition Study (OWLETS)-2 2018
10: Long Island Sound Tropospheric Ozone Study (LISTOS) 2018
11: Fire Influence on Regional to Global Environments and Air Quality (FIREX-AQ) 2019
12: GEMS Validation (2020)
13: TRACER-AQ (September 2021)
11
5, 12

## Slide 5: NASA GCAS/GeoTASO Airborne Spectrometers
~
Primarily been used for preparatory measurements for geostationary air quality observations as well as emissions mapping
Measures spectra in the UV-VIS-(NIR) at high spectral and spatial resolution from which trace gas columns can be remotely retrieved (NO2 and HCHO)
Observes from the bottom of an airplane (often the NASA LaRC B200) with a field of view of ~7 km at a nominal altitude of 28,000 feet executing gapless mapping over areas of interest
Heritage campaigns: DISCOVER-AQ 2013 & 2014, GOES-R Validation 2017, LMOS 2017, SARP 2017, LISTOS 2018, FIREX-AQ 2019, KORUS-AQ 2016, GEMS campaigns (fall 2020)
Trace gas data are publicly available on study archives, but also work toward the creating of a TEMPO-proxy dataset
Sampling strategy for the airborne spectrometers operating in a push-broom configuration
Instrument PI:
Scott Janz, GSFC
Kowalewski & Janz, 2014: doi:10.1117/12.2062058
Leitch et al., 2014: doi: 10.1117/12.2063763
Nowlan et al., 2016: doi:10.5194/amt-9-2647-2016
Nowlan et al., 2018: doi:10.5194/amt-2018-156
Judd et al., 2019: doi: 10.5194/amt-12-6091-2019
Judd et al., 2020: doi:10.5194/amt-2020-151
Some References:

## Slide 6
Revealing the capabilities to observe hi-res NO2
TROPOMI 06/25/2018 20:20 UTC
TROPOMI 07/19/2018 18:11 UTC
TROPOMI 07/08/2018 18:37 UTC
Los Angeles, California
New York City, New York
Chicago, Illinois
NO2 Column (molecules cm-2 x1015)
*not same date as TROPMI was not yet launched
*not same date as TROPMI was not yet launched

## Slide 7
Revealing the capabilities to observe hi-res NO2
TROPOMI 06/25/2018 20:20 UTC
TROPOMI 07/19/2018 18:11 UTC
TROPOMI 07/08/2018 18:37 UTC
*not same date as TROPMI was not yet launched
*not same date as TROPMI was not yet launched
Los Angeles, California
New York City, New York
Chicago, Illinois
NO2 Column (molecules cm-2 x1015)

## Slide 8
Revealing the capabilities to observe hi-res NO2
TROPOMI 06/25/2018 20:20 UTC
TROPOMI 07/19/2018 18:11 UTC
TROPOMI 07/08/2018 18:37 UTC
NO2 Column (molecules cm-2 x1015)
Los Angeles, California
New York City, New York
Chicago, Illinois
TEMPO FOR footprints courtesy of Xiong Liu, SAO
Pixel sizes here ~2.5 km x 5 km
*not same date as TROPMI was not yet launched
*not same date as TROPMI was not yet launched

## Slide 9: Developing applications with hi-res HCHO columns
Source: Airnow.gov
NO2 Column (molecules cm-2 x1015)
HCHO Column (molecules cm-2 x1015)
2018-06-25 Afternoon NO2
2018-06-30 Afternoon NO2
2018-06-25 Afternoon HCHO
2018-06-30 Afternoon HCHO
2018-06-25 O3 AQI
2018-06-30 O3 AQI
HCHO column relationship to surface ozone
(e.g., Schroeder et al., 2016
https://doi.org/10.1002/2016JD025419
NOx/VOC sensitivity for O3 production
(e.g., Souri et al., 2020
https://doi.org/10.1016/j.atmosenv.2020.117341)
Disclaimer: results of these ideas are not shown here but are being worked on
(1)
(2)

## Slide 10: Pandora Spectrometers
Developed at NASA GSFC and is primarily used for satellite validation activities, supporting science through NASA EV Missions and R&A Activities and EPA-PAMS Enhanced Monitoring upper air measurements.
Friday, July 20th, 2018
Bronx-Pfizer
  Ground-based UV-VIS spectrometer system collecting spectra in which trace-gas column densities can be retrieved continuously throughout the day.
  Operational products are NO2 and O3
  Research products include HCHO and others
Links: https://www.pandonia-global-network.org/ & https://pandora.gsfc.nasa.gov/

## Slide 11: EPA-NASA Pandora Network at U.S. Air Quality Sites
Contact: Jim Szykman (james.j.szykman@nasa.gov) and Luke Valin (valin.lukas@epa.gov )
Map of sites that currently or by the end of the summer (COVID-willing) include Pandora spectrometers colored by available co-located measurements.
First deployment in the NE Corridor region in 2018
Currently Operating Sites:
Rutgers, NJ
Bronx, NY
Queens College, NY
The number of sites will expand rapidly upon the lifting of restrictions related to COVID-19.
Current and future considerations for site placement are motivated by air quality management and TEMPO
Open to feedback on how you think Pandora + co-located measurements can address issues related to air quality and TEMPO
Flax Pond, NY
New Haven, CT
Chiwaukee Prairie, WI (May 2020)
Opportunity to add perspective to the understanding local/regional air quality by connecting to the satellite point of view.
Assists with satellite validation/evaluation studies (e.g., TROPOMI and TEMPO)

## Slide 12
Summer 2021
Finishing thoughts
GCAS will be used to do similar work for GEMS this fall in South Korea in collaboration with NIER.
First look at geostationary air quality data prior to the launch of TEMPO.
https://www-air.larc.nasa.gov/missions/tracer-aq/index.html
Doing a research study and you think these capabilities or TEMPO can help?
We want to hear about it!
Contact: laura.m.judd@nasa.gov
Airborne research campaign data can be found at
https://www-air.larc.nasa.gov/index.html
Questions about this presentation or data? feel free to contact me (laura.m.judd@nasa.gov)
Upcoming Activities