## Slide 1: Efficient Power Amplifiers for Radio Science, Remote Sensing, and Space Communications
Rainee N. Simons, Ph.D., Life Fellow, IEEE
NASA Glenn Research Center, MS 54-1
21000 Brookpark Road
Cleveland, OH 44135, USA
e-mail: Rainee.N.Simons@nasa.gov
Session WE-A4.2A: Remote Sensing, Wed, July 8, 2020, 11:20 am – 11:40 am

## Slide 2: Outline
Introduction and Problem
Challenges
Space Traveling-Wave Tube Amplifier
  Design, Modeling, and Manufacturing
Amplifier Performance Characteristics
  Model 9835H K-band Space TWT
  Model 999HA Ka-band Space TWT
  Model 9922H Q-band Space TWT
Applications to Radio Science, Remote sensing, and Space Communications
Conclusions

## Slide 3: Introduction and Problem
Signals transmitted from spacecraft have to travel astronomical distances
As the distance from the Sun increases the solar flux density available for conversion to electrical power on board the spacecraft decreases
Spacecraft travel time to reach their destination is several years
Long life and stable operation are essential for mission success

## Slide 4: Challenges
Hence, the need to develop reliable space amplifiers capable of
  enduring long duration space flights
  operating in extreme hot and cold environment
  radiation tolerant
  stable operation while delivering high output RF power with high efficiency, and
  long operating life

## Slide 5: Space Traveling-Wave Tube Amplifier
Vacuum electronics-based devices such as, the helical TWTA have demonstrated high on-orbit reliability, capability to operate in extreme environment, provide high output power with high efficiency, and longevity
In this paper we present the RF performance characteristics of helical TWTAs at K-Band, Ka-Band, and Q-band frequencies for space applications

## Slide 6: TWTA Design, Modeling, and Manufacturing
Modern electromagnetic simulation/optimization software tools enabled the first pass design success and include
  U.S. Naval Research Laboratory’s CHRISTINE 3-D Code for high efficiency slow-wave interaction circuit
  MICHELLE 3-D Code for multi-stage depressed collector design
  Thermal modeling/simulation tools enabled the design of an efficient conduction cooled package
Advances in materials technology resulted in lightweight, temperature stable, high B-H energy product samarium cobalt permanent magnets for focusing the electron beam

## Slide 7: NASA Applications of TWTAs
Space Radio Science
    Investigators examine small changes in the phase and/or amplitude of the radio signal propagating from a spacecraft to Earth to study the atmospheric and ionospheric structure of planets, planetary gravitational fields, shape, mass, etc.
    An example is NASA’s Cassini Mission to Saturn
  Spacecraft Based Remote Sensing
    The Remote sensing is the acquiring of information from a distance. NASA observes the Earth and other planetary bodies via remote sensors on spacecrafts that detect and record reflected or emitted energy. The sensors could be passive or active.
    Synthetic Aperture Radar (SAR) is a type of active data collection where a sensor produces its own energy and then records the amount of that energy reflected back after interacting with the Earth
    Example include NASA’s Global Precipitation Measurement (GPM) mission and Joint Polar Satellite System (JPSS)

## Slide 8: Applications of TWTAs (Continued)
Space or Satellite Communications
  The primary application here is for down linking the science data gathered by instruments onboard the spacecraft. Additionally, the communication link also enables commanding the spacecraft and; also downlinking the telemetry data that provides frequent update on the health and status of various systems onboard.
  Examples include NASA’s Lunar Reconnaissance Orbiter (LRO) and Kepler spacecrafts

## Slide 9: Conclusions
The design, modeling and manufacture of the space qualified high power and efficiency helical TWTAs are described
The RF performance of K-Band, Ka-Band, and Q-Band TWTAs are presented as examples
Application of TWTAs to space radio science, spacecraft based remote sensing, and satellite communications are also presented