## Slide 1: NASA Flight Opportunities – A Stepping Stone to Orbit Anh N. Nguyen NASA Ames Research Center anh.n.nguyen@nasa.gov SmallSat 2020

## Slide 2
Payload Accelerator for CubeSat Endeavors (PACE) goals are to mature Payloads from TRL 4 to TRL 7/9 utilizing a suborbital flight test supported by NASA Flight Opportunities and orbital flight supported by NASA CubeSat Launch Initiative through the NASA Small Spacecraft Technology Program

## Slide 3: NASA Suborbital Flight Opportunities
Suborbital reusable launch vehicles (sRLVs)
Minimum altitude of 80 km above Mean Sea Level (MSL)
Rocket-Powered Lander Vehicles
(RPLV)
Controlled descent and controlled vertical landing of a free-flying vehicle using a propulsion system of a class that can operate in a vacuum.
High-altitude balloons
Minimum altitude of 30 km above MSL
Parabolic aircraft
Aircraft Following Reduced-Gravity Flight Profiles
Minimum altitude of 30 km above MSL
Credit: Johnny MItchell

## Slide 4: Payload Maturation to Flight
Center Innovation Fund
Game Changing Development
Lunar Surface Innovation Initiative
NASA Innovative Advanced Concepts
NASA iTech
Prizes & Challenges
Small Business Innovation Research
Small Business Technology Transfer
TRL 4 Payload
Space Technology Research Grants
Technology Transfer
FO AI&T
Flight Opportunity
Integration onto SC Bus
Launch
Mission Ops
Close-out
SC-level
Env. test
Small Spacecraft Technology
(SSTP)
Flight Opportunities
(FOP)
CubeSat Launch Initiative (CSLI)
Other STMD Programs
Orbital Development
TRL 7 Payload

## Slide 5: PACE-1FO and PACE-1 Summary
Payload
Here
Payload
Here
Payload
Here
ADP
Core
ADP
Core
ADP
Core
CSLI
Launch
Orbital Development
TRL 9 Payload
Balloon Configuration
PACE-FO
Orbital Configuration
PACE-X
ADP Avionics Core
Payload
Development
ADP: Advanced Developments Projects group at NASA ARC
TRL: Technology Readiness Level
FO: Flight Opportunity
S/C: Spacecraft
CSLI: CubeSat Launch Initiative
NASA SUBORBITAL FLIGHT OPPORTUNITIES
Suborbital reusable launch vehicles
High Altitude
Balloon
Rocket-powered lander vehicles
Parabolic
Aircraft
FO Development
TRL4
Payload
ADP Spacecraft Platform
TRL7
Payload

## Slide 6: PACE-FO: PACE Flight Opportunities Unit
27 cm
37 cm
12 cm
≤12 kg
Notional Images
UHF UL/DL 900.0 MHz
S-band UL/DL 2.4 GHz
GlobalStar Simplex
Iridium Duplex
GPS
Sun
Sensors
Processing
Power
Communications
Sensors
Structure
TRL 4 Payload

## Slide 7: PACE-X:PACE Orbital Unit
Propulsion Unit
ADCS Unit
Solar Panels
Additional components integrated to balloon configuration to complete the ADP S/C Platform for orbital flight
Re-use where possible from Balloon
Processing
Power
Communications
Sensors
Structure
TRL 7 Payload
ADCS Unit
Solar Panels
Propulsion Unit (optional)
Orbital Additions
Notional Images

## Slide 8: Notional Initial ADP Platform Capabilities
C&DH
EPS
ADCS
Solar Array
Comm
RW, MT, Sensors
Star Trackers
Iridium, GlobalStar
S-band SDR,
UHF LoRa
GNC
SkyTraq, NovAtel
Payload Interface
TBD
SC Platform
Additions
FO Platform
Propulsion
ADP Platform
Payloads
C&DH: Command and Data Handling
EPS: Electrical Power System
ADCS: Attitude Determination and Control System
RW: Reaction Wheel
MT: Magnetorquer
GNC: Guidance Navigation and Control
Comm: Communications
SDR: Software Defined Radio
FO: Flight Opportunities
SC: Spacecraft
ADP: Advanced Developments Projects group at NASA ARC

## Slide 9: PACE
PACE-XFO
I&T
Flight
Opp.
Launch
Mission Ops
Close-out
Payload
TRL 4
FO
PACE
CSLI
ADP Core
Dev Kit
ADP Avionics Core Development
Payload
TRL 7
ADP S/C Platform
Development
PACE-X
I&T
5-7 mo.
5-7 mo.

## Slide 10: PACE Program Opportunities
PACE utilizes an Advanced Developments Projects (ADP) platform built for modularity that can be adapted to accommodate a variety of payload interfaces and requirements for both suborbital flight test supported by NASA Flight Opportunities and orbital launches supported by NASA CubeSat Launch Initiative
  ADP platform is developed at NASA ARC based on industrial electronics and hardware
  Can ‘up-scope’ ADP platform for payloads with demanding spacecraft requirements such as tight pointing needs, high data through-put needs, and challenging operational environments
  Can ‘de-scope’ ADP platform for payloads with less stringent spacecraft requirements for cost-effective and reliable quick-turn tech demos
A payload’s early-adoption of the PACE ADP FO platform for the FO-campaign provides a smooth and rapid transition to an orbital flight utilizing the PACE ADP SC platform
  Relieves the burden of payloads developing standard supporting subsystems (comm, power, processing)
  Focuses efforts (and funds) on the development of the payload itself

## Slide 11: Conclusion
The Payload Accelerator for CubeSat Endeavors (PACE) is a STMD Small Satellite Technology Program that focuses on maturing payloads from TRL 4 to TRL 9 utilizing a suborbital flight test supported by NASA Flight Opportunities
PACE is currently in its first pilot year
  First PACE Suborbital Flight Opportunities campaign Late 2020
  First PACE Orbital Launch targeted for Spring 2021
The PACE program will support flight demonstrations of new technologies, capabilities and applications for small spacecraft and reduces the cost, risk, complexity and/or time required to advance the state-of-the-art

## Slide 12
Adam Zufall
Attitude Determination and Control Lead,
Systems Engineer
Steve Battazzo
Embedded Systems Lead
Terry Stevenson
Propulsion Lead,
Lead Mechanical Engineer
Connor Nelson
Flight Software Lead
Anh Nguyen
Project Manager
Jan Stupl
Deputy Project Manager,
Systems Engineer
Dayne Kemp
Electrical Engineer Lead,
Systems Engineer
Cedric Priscal
Communications Lead,
Flight Software
Roger Hunter
SST Program Manager
Jackson Parker
Flight Software,
Electrical Engineer

## Slide 13: Payload Accelerator for CubeSat Endeavors (PACE) Anh N. Nguyen, NASA ARC anh.n.nguyen@nasa.gov