## Slide 1: Trajectory Optimization for OSIRIS-REx Earth Return
Noble Hatten, Jacob A. Englander, Donald H. Ellison, Ryo Nakamura, Brian Sutter, Kenneth E. Williams, Jeremy M. Knittel, James McAdams, Daniel Wibben, Peter Antreasian, Kenneth Getzandanner, Michael C. Moreau, Dante S. Lauretta
2020 AAS/AIAA Astrodynamics Specialist Conference
August 9 – 12, 2020

## Slide 2: OSIRIS-REx
Origins, Spectral Interpretation, Resource Identification, and Security-Regolith Explorer
New Frontiers mission to return sample from NEA Bennu
Launched 2016; arrived 2018; currently in orbit
  Smallest body ever orbited
  Lowest orbit ever achieved
Sample acquisition: Touch and Go (TAG)
  Currently scheduled for fall 2020
https://www.nasa.gov/press-release/nasa-s-newly-arrived-osiris-rex-spacecraft-already-discovers-water-on-asteroid

## Slide 3: Earth Return
Mission objective 1 is to return and analyze a sample
Post-TAG, spacecraft returns to Earth to deliver sample return capsule (SRC)
Nominally: Depart March 3, 2021, arrive Sept. 24, 2023

## Slide 4
But …

## Slide 5: Motivation for Current Work
TAG is a complex operation with many uncertainties
Multiple TAG attempts may be required
 Need Earth-return trajectories with a broad range of departure dates
We want to further explore the trade space
  Examine effect of (1) multiple DSMs and (2) tighter EDL interface velocity restriction on Δv
Establish Boundary Conditions
Develop Reference Trajectory
Perform Monte-Carlo Analysis
EMTG, GMAT
and/or STK
PIRATE or
MIRAGE
PIRATE or
MONSTER
Determine UTTR
Ground Ellipse
POST II
Iterate on Entry
Interface State
Possible Feedback
to Establish Walk-In Flyby Altitude
Final States and
Maneuvers
Prelim
States
And
Mnvrs
Verify UTTR
Ground Ellipse
POST II
Iterate on TCM
Placement and
Various Error
Assumptions

## Slide 6: Analysis and Optimization Tool: EMTG
Evolutionary Mission Trajectory Generator
Interplanetary trajectory optimization tool developed at NASA GSFC
Stochastic method to generate initial guesses combined with gradient-based optimizer
Finite burns and impulsive maneuvers
Scalable fidelity
100% analytical gradients
Recently released open-source
  https://github.com/nasa/emtg
EMTG Software Design Document

## Slide 7: Problem Setup
Bennu (massless)
Match point
Fwd prop
Bwd prop
Earth SOI
Earth
EDL Interface
Parachute
deployment
EDL constraints
Radius
Velocity
Flight path angle
Parachute constraints
Altitude
Latitude
Longitude

## Slide 8: Proof of Concept: Reproduction of Nav Plan Baseline
Stop propagation at EDL interface (“soft” constraints)
Low-fi  High-fi
Sun
Earth
OREx
Bennu

## Slide 9: Alternate Departure Dates
No exact EDL interface state to match  propagate to approximate parachute deployment (altitude boundary)
  Simple exponential atmosphere
  Eliminate “soft” constraints
Focus on most likely departure date range: March 3, 2021 – May 30, 2021
No post-departure DSM allowed

## Slide 10: Using “Seed-Sharing” to Find Solutions with EMTG
Use decision variables of converged solution as initial guess for a similar case
  Can be done with low-fi or high-fi dynamics
  Seed across departure dates
  Seed longitude-constrained problem with longitude-free solution
  Gradually step down Δv allowed at post-departure DSM until it disappears entirely
Allows a single EMTG solution to propagate to produce many more solutions
Seed-sharing also works backward: If a newly converged case finds a more optimal solution than a nearby, already-converged case, the new case seeds the old

## Slide 11: Alternate Departure Dates
Chart: Departure Date
| 44258 | 44268 | 44269 | 44270 | 44271 | 44272 | 44273 | 44274 | 44259 | 44260 | 44261 | 44306 | 44307 | 44262 | 44308 | 44309 | 44310 | 44311 | 44312 | 44313 | 44314 | 44315 | 44316 | 44317 | 44263 | 44318 | 44319 | 44320 | 44321 | 44322 | 44323 | 44324 | 44325 | 44326 | 44327 | 44264 | 44328 | 44329 | 44330 | 44331 | 44332 | 44333 | 44334 | 44335 | 44336 | 44337 | 44265 | 44338 | 44339 | 44340 | 44341 | 44342 | 44343 | 44344 | 44345 | 44346 | 44266 | 44267
 | 0.31649 | 0.33988 | 0.34603 | 0.35325 | 0.36171 | 0.37158 | 0.38308 | 0.3965 | 0.31667 | 0.31721 | 0.31814 | 0.41388 | 0.39369 | 0.3195 | 0.37613 | 0.3608 | 0.34735 | 0.33553 | 0.32512 | 0.31596 | 0.30789 | 0.3008 | 0.29457 | 0.28912 | 0.32134 | 0.28439 | 0.2803 | 0.27679 | 0.27382 | 0.27136 | 0.26934 | 0.26776 | 0.26656 | 0.26573 | 0.26524 | 0.32372 | 0.26508 | 0.26508 | 0.26456 | 0.26102 | 0.25796 | 0.25537 | 0.25323 | 0.25152 | 0.25021 | 0.24928 | 0.32668 | 0.24873 | 0.24852 | 0.24852 | 0.24866 | 0.24911 | 0.24986 | 0.25089 | 0.2522 | 0.25377 | 0.3303 | 0.33468
Arrive 9/24/2023
Arrive 9/25/2023
Minimum-Δv is 249 m/s on May 24
Dates between 3/20 and 4/19 require either large Δv or a post-departure DSM
Nav Plan Baseline

## Slide 12: EDL Interface Atmosphere-Relative Velocity
Chart: Departure Date
| 44258 | 44268 | 44269 | 44270 | 44271 | 44272 | 44273 | 44274 | 44259 | 44260 | 44261 | 44306 | 44307 | 44262 | 44308 | 44309 | 44310 | 44311 | 44312 | 44313 | 44314 | 44315 | 44316 | 44317 | 44263 | 44318 | 44319 | 44320 | 44321 | 44322 | 44323 | 44324 | 44325 | 44326 | 44327 | 44264 | 44328 | 44329 | 44330 | 44331 | 44332 | 44333 | 44334 | 44335 | 44336 | 44337 | 44265 | 44338 | 44339 | 44340 | 44341 | 44342 | 44343 | 44344 | 44345 | 44346 | 44266 | 44267
 | 12.1985 | 12.2016 | 12.2014 | 12.201 | 12.2005 | 12.1997 | 12.1987 | 12.1975 | 12.1992 | 12.1998 | 12.2003 | 12.3703 | 12.3673 | 12.2007 | 12.3649 | 12.3629 | 12.3613 | 12.36 | 12.359 | 12.3582 | 12.3577 | 12.3573 | 12.3571 | 12.3571 | 12.2011 | 12.3572 | 12.3574 | 12.3577 | 12.3581 | 12.3585 | 12.3591 | 12.3597 | 12.3604 | 12.3612 | 12.362 | 12.2014 | 12.3629 | 12.3629 | 12.394 | 12.3931 | 12.3924 | 12.3917 | 12.3912 | 12.3908 | 12.3905 | 12.3903 | 12.2016 | 12.3901 | 12.3901 | 12.39 | 12.3901 | 12.3901 | 12.3902 | 12.3904 | 12.3907 | 12.391 | 12.2018 | 12.2018
Arrival date change
Requirement: < 12.4 km/s

## Slide 13: EDL Interface Velocity Azimuth
Chart: Departure Date
| 44258 | 44268 | 44269 | 44270 | 44271 | 44272 | 44273 | 44274 | 44259 | 44260 | 44261 | 44306 | 44307 | 44262 | 44308 | 44309 | 44310 | 44311 | 44312 | 44313 | 44314 | 44315 | 44316 | 44317 | 44263 | 44318 | 44319 | 44320 | 44321 | 44322 | 44323 | 44324 | 44325 | 44326 | 44327 | 44264 | 44328 | 44329 | 44330 | 44331 | 44332 | 44333 | 44334 | 44335 | 44336 | 44337 | 44265 | 44338 | 44339 | 44340 | 44341 | 44342 | 44343 | 44344 | 44345 | 44346 | 44266 | 44267
 | 61.6716 | 61.1471 | 61.0573 | 60.9565 | 60.8433 | 60.7165 | 60.5731 | 60.4103 | 61.6404 | 61.6058 | 61.569 | 67.9753 | 67.7811 | 61.5246 | 67.6124 | 67.4635 | 67.3317 | 67.2141 | 67.1108 | 67.0147 | 66.9299 | 66.8532 | 66.7843 | 66.7216 | 61.477 | 66.665 | 66.6136 | 66.5676 | 66.5248 | 66.486 | 66.4511 | 66.4193 | 66.3905 | 66.3644 | 66.3407 | 61.4242 | 66.3204 | 66.3184 | 66.3795 | 66.3714 | 66.3647 | 66.3595 | 66.3556 | 66.3527 | 66.3514 | 66.3508 | 61.3655 | 66.3517 | 66.3534 | 66.3536 | 66.3558 | 66.3576 | 66.362 | 66.3671 | 66.373 | 66.3796 | 61.3006 | 61.2281
Arrival date change

## Slide 14: Additional Trade Studies
Examine departure dates through Sept. 2022
One post-departure DSM, 12.4 km/s max EDL velocity
Two post-departure DSMs, 12.4 km/s max EDL velocity
Two post-departure DSMs, 12.2 km/s max EDL velocity
  ~Same EDL velocity as Nav Plan baseline
EMTG + seed-sharing + server time = lots of solutions

## Slide 15: Δv vs. Scheduled Departure Date Summary
Leaving less efficient than waiting during loitering periods
Second DSM provides negligible benefit
Chart: Scheduled Departure Date
12.4 km/s loitering
All loitering

## Slide 16: Δv vs. Scheduled Departure Date Summary
12.4 km/s solutions in June 2021 do not use a post-departure DSM
 Continuation of the May 2021 family of solutions
Arrival date slips to Sept. 28, 2023 for June 30, 2021 departure
12.4 km/s loitering
All loitering
Chart: Scheduled Departure Date

## Slide 17: Δv vs. Scheduled Departure Date Summary
12.2 km/s 2023/2024 arrival switch: 07-05-2021
12.4 km/s 2023/2024 arrival switch: 07-31-2021
12.4 km/s loitering
All loitering
Starting in July 2021, the Δv-optimal arrival date moves from Sept. 2023 to Sept. 2024
Optimal solution results in arrival velocity < 12.2 km/s
Chart: Scheduled Departure Date

## Slide 18: Δv vs. Scheduled Departure Date Summary
DSM benefits 12.2 km/s arrival velocity case
DSM date moves forward in time with departure date:
  6/16/2021 for 3/3/2021 departure; 4/25/2022 for 7/5/2021 departure
12.2 km/s 2023/2024 arrival switch: 07-05-2021
12.4 km/s 2023/2024 arrival switch: 07-31-2021
12.4 km/s loitering
All loitering
Chart: Scheduled Departure Date

## Slide 19: EDL Interface Velocity Azimuth
Chart: Scheduled Departure Date
Constant azimuth during loitering periods (same solution)
Azimuth declines more steeply at end of analyzed window (as Δv increases)
12.2 km/s, 2 DSMs not shown for clarity (same as 1 DSM until Aug 2022)
12.4 km/s loitering
All loitering

## Slide 20: Conclusions and Future Work
EMTG used to optimize OSIRIS-REx Earth-return trajectories
  Recreated baseline
  Produced daily trajectories for two opportunities between March 2021 and June 2021
    Δv ranges from 249 m/s to 320 m/s
  Performed trade studies for departures through Sept. 2022
    Δv-optimal solution switches to Sept. 2024 arrival in July 2021
Next steps:
  Flight-fidelity retargeting of point solutions
  Monte Carlo analyses

## Slide 21: Acknowledgments
This material is based on work supported by NASA under Contracts NNM10AA11C, NNG12FD66C, and NNG13FC02C.
OSIRIS-REx is the third mission in NASA’s New Frontiers Program. Dante Lauretta of the University of Arizona, Tucson, is the mission’s Principal Investigator, and the University of Arizona leads the Science Team and the science observation planning and data processing.
Lockheed Martin Space Systems in Denver built the spacecraft and is providing flight operations.
NASA Goddard Space Flight Center and KinetX Aerospace are responsible for navigating the OSIRIS-REx spacecraft.
We are grateful to the entire OSIRIS-REx team for making the encounter with Bennu possible!

## Slide 23: Backup Slides

## Slide 24: DSM Date: 12.2 km/s-limited Case, Early Departures
Chart: Departure Date
177-day lag
85-day lag
294-day lag

## Slide 25: DSM Date: 12.2 km/s-limited Case, Early Departures
Chart: Departure Date

## Slide 26: Earth Return Concept of Operations

## Slide 27: Nav Plan Baseline Trajectory in Earth SOI
OREx