## Slide 1
Space Launch System
Flight Readiness Analysis Cycle Approach
Evan Anzalone
NASA/MSFC/EV42
2020 AIAA/AAS
Astrodynamics Specialist Conference
07/31/2020
Co-Authors: Ivan Bertaska, A. Scott Craig, Young Kim, Paul Von der Porten, Daniel Tyler, Ben Burger, Jimmy Compton, Ashley Hill, Thomas Park, John Wall, Adam Harden, Jayden Hauglie, Matthew Hawkins, Seth Thompson

## Slide 2: Outline
Introduction to SLS Flight Readiness Analysis Cycle
Approach to Integrated Analysis
Initial Results from FRAC-0
Lessons Learned and Next Steps

## Slide 3: Overview of FRAC Process
FRAC is used to provide expected mission performance and coordinate mission across partners
  Design of algorithms and implementation complete during DAC
  Verification Analysis Cycle (VAC) verified design can meet vehicle-level performance
  Focus on verifying dispersions across launch windows and flight day performance expectations
Needs:
  Analysis of planned flight days
  Verification of flight performances
  Development of flight day parameters
Feeds:
  Vehicle integration
  Launch window selection
  Certification of Flight Readiness
Captures:
  GNC and Flight Mechanics expectations

## Slide 4: VM FRAC-0 Process flow
1 deck for period
1
Traj. Review
Redo
TDDP
SLS-VDD-103 App A
2 Launch Periods
2 decks for period
Months each period?
Traj. Team
POST
Set throttle bucket based on mean monthly PMBT. Perform monthly PMBT sweep.
Input Models
GR&A
POST deck
Mean Monthly traj.
2
PMBT Sweep data and throttle bucket
Guid. Team
CHANGO
Update CHANGO VCFs to capture monthly variations. Submit into CM.
Traj. Team
Targets Gen.
Run POST Hypergrid. Use Copernicus to ascent & TLI targets for LWs.
6DOF Team
MAVERIC
Dev.
Setup MAVERIC for FRAC (1st time). Include mass properties (1st time). Port Mean Monthly.
SLS-VDD-103 App A
TDDP
POST deck
MM Traj.
CHANGO
Guid. Review
Redo
CHANGO tag
Traj. Review
EMPT Review
Redo
Redo
Upload TLI targets
Ascent targets & Launch Times
6DOF Review
Redo
POST
/MAV Compare
MAVERIC tag 1
SLS-VDD-103 App A
TDDP
Part 1
Part 2
Notes: Wrapping VM FRAC-0 process continuing on next slide. Schedule from left to right each row isn’t perfect depiction of start/stop of processes (e.g. CHANGO/MAV development and Target Generation). MAVERIC tag numbers are representative. Team reviews are within the purview of the technical team. EMPT review is as negotiated between SLS and Orion review teams. All reviews leading up to EV40 Mgmt review should be formally captured for mgmt. vetting before VM deliveries. AFSITT review will focus only on the approach to develop the products (Targets Generation, Launch Window polynomials, and 1-minute Check Cases).

## Slide 5: VM FRAC-0 Process flow (Continued)
Ascent Tgts
MAV tag 1
Guid. Team
Guid. Monthly
TDDs
Update monthly Time Dependent Data (TDD).
Guid. Review
Redo
MAVERIC tag 2
Guid. Team
LW Polynomial TDDs
RINU DUT1 and leapsec TDDs
Nav. Team
SLS-VDD-103 App A
Nav. Review
Redo
Fit inclination and RAAN targets to polynomial. Run MAVERIC throughout the window and fit change in Chi Table yaw to for optimal launch-to-orbit to a polynomial.
Guid. Review
Redo
MAVERIC tag 3
Update 3DOF launch time and Core Sep States
6DOF Team
1-minute Check Cases
Run nominal 6-DOF for every 1-minute for every launch day in the 2 launch periods.
MAV tag 3
Guid./6DOF Review
Redo
Upload check cases
EV40 Mgmt 1
Redo
AFSITT 1
Redo
Process and Products
Products
Start Monte Carlos
Deliver TLI targets and 1-min check
Part 3
Part 4
Notes: Wrapping VM FRAC-0 process continuing on next slide. Schedule from left to right each row isn’t perfect depiction of start/stop of processes (e.g. CHANGO/MAV development and Target Generation). MAVERIC tag numbers are representative. Team reviews are within the purview of the technical team. EMPT review is as negotiated between SLS and Orion review teams. All reviews leading up to EV40 Mgmt review should be formally captured for mgmt. vetting before VM deliveries. AFSITT review will focus only on the approach to develop the products (Targets Generation, Launch Window polynomials, and 1-minute Check Cases).

## Slide 6: VM FRAC-0 Process flow (Continued)
Data products include:
  Trajectory time histories
  Performance envelopes and re-entry conditions for core and boosters
After initial process complete several more steps:
  Continued analysis on stage separation and lift-off clearance
  Continued analysis on abort capability and performance
Data products delivered to ULA for their ICPS analysis:
  Generates upper stage trajectories
  Provides states at disposal and stage separation across launch windows
Upon data provided back to NASA:
  Verification of integrated SLS performance
  Data passed on to MPCV for vehicle analysis and mission design
Start MCs
6DOF Team
Fixed time MC
(first time)
Run a fixed time Monte Carlo for agreed upon epoch.
6DOF Team
Variable time MCs
Run a Monte Carlo throughout launch window for all launch days for 2 launch periods.
GN&C/6DOF Review
Redo
GN&C/6DOF Review
Redo
EV40 Mgmt 2
Redo
AFSITT 2
Redo
Process and Products
Products
Deliver Monte Carlos
Part 5
Notes: Wrapping VM FRAC-0 process continuing on next slide. Schedule from left to right each row isn’t perfect depiction of start/stop of processes (e.g. CHANGO/MAV development and Target Generation). MAVERIC tag numbers are representative. Team reviews are within the purview of the technical team. EMPT review is as negotiated between SLS and Orion review teams. All reviews leading up to EV40 Mgmt review should be formally captured for mgmt. vetting before VM deliveries. AFSITT review will focus only on the approach to develop the products (Targets Generation, Launch Window polynomials, and 1-minute Check Cases).

## Slide 7: Notional GNC Outputs – per Monte Carlo

## Slide 8: Notional GNC Outputs – Across Monte Carlos
Navigation Performance
Controller Performance

## Slide 9: Additional Results
Tower Clearance
Stage Disposal

## Slide 10: Lessons Learned and Next Steps
Automate tools as much as possible
  Generation of plots to track variation across launch vehicle
  Formalized/standard products to be able to integrate results as Monte Carlo complete
Practice makes perfect
  FRAC-0 useful in exercising process, understanding the schedule drivers
  Training important for team to know/understand tools for data processing and integration
  Due to long duration of analysis, need multiple backup levels to accommodate other activities and team schedules
Next Steps
  Implementation of FRAC-1 – This Fall
  Move to rolling targets, staying ahead of launch dates
  Certification of flight software parameters via Hardware in the Loop laboratories
  Flight-day processes for Day of Launch Activities