## Slide 1: Conjunction Assessment Risk Analysis
Lauri Newman
NASA CARA
Collision Avoidance “Short Course”
Part III: CA in Changing Space Flight Environment

## Slide 2: Changing Space Environment
Space environment has been changing, and will continue to evolve rapidly over the next few years due to the following drivers:
  Space Fence
  Large constellations
  Maneuver Plan Streamlining
  Increasing on-board autonomy
  New space actors
  SmallSat proliferation
CA practices will need to evolve to meet growing needs
  New methodologies
  Best practices
  Data sharing
  Orbital registry

## Slide 3: New Sensor: Space Fence (SF)
New Space Surveillance Network (SSN) sensor
  Equatorial phased-array S-Band sensor
  Can track to better than 5 cm (SSN capability 10 cm)
  Initial Operations Capability achieved
  Objects discovered by SF soon to be introduced into CA enterprise
Expected impact on CA
  Increased quantity of new objects
    Overall CA workload increase estimate: 25% at first; potentially as much as 100% after 1-2 years’ operation
  Quality of maintenance ODs
    Newly-discovered objects that can be tracked regularly should have reasonably good ODs
    Objects on edge of detection may have quality issues and create data actionability problems
  Workload increases will be felt both by CA practitioners and individual missions

## Slide 4: Increasing Workload-Space Fence and Large Constellations
Current CA workload is large and expected to grow
  Across the LEO fleet, NASA CARA sees about 700 unique conjunctions each month
  About one conjunction per month per LEO spacecraft requires further analysis and mitigation planning
    Requires ~1 staff week of work for the CARA team for risk assessment as well as support from the mission flight operations team for maneuver planning
    Only about 15% of analyzed events result in a maneuver
Unique Events within 0.5x5x5-km Volume by Object Type, LEO
Predicted Tracked Object Density
by Altitude in 2030
Chart: altitude (km)
*Prepared by The Aerospace Corporation

## Slide 5: Large Constellations
Planned large constellations will add thousands of objects to catalog
  Analysis of some proposed constellations has indicated a fresh conjunction event every 3 days vs 1-2 fresh events/month in current operations
Operations impact is large
  Effort to analyze the data will require more manpower
  Hopefully the development of robust automated risk assessment tools will follow to reduce operations impact
Current constellation information available at https://www.newspace.im/
Table excerpted from Shepperd, Ryan, “How Big is Big? Better Metrics for Defining Constellation Size regarding Space Sustainability,” International CA Workshop, Paris, France, June 2019.
Some Planned LEO Constellations
Name | Number | Altitude (km) | Inclination (deg)
ISS | 1 | 400 | 51.6
Starlink | 1584 | 550 | 53
OneWeb | 600 | 1200 | 88
Hongyan | 320 | 1094 | 50
Iridium | 75 | 780 | 86.4
GlobalStar Block 2 | 30 | 1410 | 52
Amazon Kuiper | 3236 | 630, 610, 590 | 51.9, 42, 33
Telesat Polar | 72 | 1000 | 99.5
O3B | 20 | 8063 | 0
Telesat Inclined | 45 | 1248 | 38
Envisat | 1 | 773 | 98.4
Hongyun | 156 | 1000 | 97.4
Synspective | 30 | 600 | 97.8
Orbcomm Block 2 | 18 | 750 | 47
Flock | 217 | ~489 | 97
Lemur | 76 | ~496 | 97

## Slide 6: Trending Concern: Maneuver Ephemerides Not Screened
Desire among satellite O/Os to streamline CA process
  Understandable, given additional expected CA loading
Use collected CDMs to screen maneuver plans in-house, instead of using pre-maneuver screenings by 18 SPCS to save time
  If screening volume large enough, all possible conjunctions, even with primary ephemeris altered due to a maneuver, should be represented by CDMs
  Can use state and covariance information in current CDM set to perform equivalent of maneuver screening
Issue: ignores potential maneuvers of other primary objects
  “Regular” screenings consider only the submitted primary ephemeris or DoD primary solution against remainder of catalogue
  “Ephemeris on ephemeris” screenings are conducted in order to consider potential maneuvers of secondary objects, but only if ephemeris submitted
  Not screening maneuver ephemerides thus leaves category of potential secondary objects (i.e., other primaries) unaddressed

## Slide 7: Trending Concern: Autonomous, On-Board CA
Some satellite operators have implemented autonomous, on-board CA
  Use 18 SPCS CDMs uploaded at regular intervals
  On-board algorithms identify and plan needed maneuvers autonomously
  No notifications to anyone about intended maneuvers in advance
Issue 1: Cannot know maneuver intentions of other spacecraft
  Maneuver plans often changed with little lead time
  Presently O/Os work together to address such situations; impossible here
Issue 2: “Kantian Universality” failure
  One must act only in a manner that can become a universal law
  Cannot have more than one constellation with insular, autonomous CA
    If two satellites autonomously reacting to avoid collision with each other, and neither knows how the other is planning to react, no way to know whether a collision is being avoided
    Result might be for both satellites to maneuver into each other

## Slide 8: New Space Actors
The space environment today is very different from a decade ago and continues to evolve very rapidly
  Historically, space operations were domain of large governmental entities.
  Commercial space operators are becoming commonplace and have different business models than government actors
  CubeSats are cost effective and accessible for everyone, even down to elementary schools
Challenge in educating new space actors on best practices and availability of data and tools
May require space “regionalization” rules
  E.g., altitude < 350km a “Wild West” region for cubesats with little flight dynamics experience or orbital control
  Allows inexperienced actors to access space without threatening high-value assets

## Slide 9: SmallSat Proliferation: Small Doesn’t Mean “Safe”
Small satellites can destroy large satellites and create large debris clouds as effectively as pieces of debris
Small satellites must be tracked in order to prevent collisions
  Small satellites harder to track, and some below regular tracking threshold
  Many small satellite operators do not compute their own ephemeris and rely on TLEs, making SSN tracking essential to their position determination
Maneuverable small satellites must have their maneuvers screened
  CA not effective if screenings cannot be performed against intended trajectories
In short, it is a fallacy that small, cheap satellites do not require CA
  In fact, in many respects more dangerous than traditional satellites

## Slide 10: New Methodologies
Potential new CA paradigms to handle workload
  CA remediation against “grouped” events using an aggregate Pc
  Station-keeping burn strategy to minimize conjunction risk, without actually remediating individual events unless an extremely high Pc
  Consideration of consequence in addition to risk to determine which events to remediate—already moving towards implementation at NASA
Automation/artificial intelligence
  Investigate methods to automate more of the process while retain key safety elements
  Determine usefulness of machine learning, neural nets, etc. in decision-making
  Enterprise difficult because CA lacks “truth” data—very few collisions actually take place
  NASA initial CA AI / machine learning studies show little improvement

## Slide 11: Best Practices
CA industry is evolving rapidly
Guidelines/standards are needed to enable healthy growth
  Safety of Flight best practices should be adapted universally
Sources of existing best practices:
    Best practices for 18 SPCS support are available on Space-Track.org website
    Secure World Foundation publishes “Handbook for New Actors in Space”
    Best practices for satellite operations at Spacesafety.org
    CONFERS publishes best practices for Proximity ops
    NASA to publish CA best practices Handbook in late October; contains analysis describing the technical/scientific foundations of best practices
  AIAA has a Space Traffic Management working-group to investigate various topics. One is best practices.
    For information contact Dan Oltrogge / AGI or Moriba Jah / UT Austin

## Slide 12: Importance of Data Sharing
Many spacecraft now using electric propulsion and/or automated onboard maneuver planning and execution
  Currently-maintained RSO catalog will lack up-to-date data on these satellites’ locations
Missions will need to share powered flight ephemerides to all for CA
  Without shared data, other operators have no way to tell where these assets are
  Users would have to change their practice to screen these ephemerides against their own instead of relying solely on 18 SPCS
  Sharing should be through a trusted/protected mechanism, like Space-Track.org or SDA
  Missions will have to have mechanism for screening these ephemerides
Issues
  How does an operator know that another operator exists, or know where to find ephemeris data for other assets?
  Many mission consider their ephemerides proprietary. This should never be the case, as this data is needed for flight safety and does not protect anything by being withheld.

## Slide 13: Orbital Registry
Propose an “Orbital Registry” service as part of STM that would:
  Deconflict orbital placement: provide evaluation of mission orbit selection during design phase to determine impact from close approach perspective and offer trade space of alternative orbits
    Similar to filing flight plans; during license evaluation is too late to change orbit selection – should be during design
      Tweaking orbits by a few km can make a big difference in reducing the number of close approaches with neighbors
    Allows for advance notice of potential co-locations so that they can be avoided or managed smartly.
  Maintain database of operator contact information
  Enable protected data sharing: Sharing ephemerides is critical for powered flight/low-thrust modelling. Operators need to be ensured that their sensitive data is protected.
    Centralized screening service would allow trusted agent to do this screening while keeping data secure
  Provide access to best practices/guidelines
    Links to multiple sources in one place for easy access

## Slide 14: Summary
Exciting growth offers opportunities that will change society, but needs to be done safely to ensure that we have continued use of the space environment for future generations
References:
  The Aerospace Corporation, “Space Traffic Management In The Age of New Space”
    https://aerospace.org/sites/default/files/2018-05/SpaceTrafficMgmt_0.pdf