## Slide 1
Chasing Volatiles,
Running From Shadows
NASA Ames Summer Series 2020
Ryan Vaughan, VIPER Mission Systems Engineer
August 13, 2020
Notes: STILL

## Slide 2
Humans Return by 2024
Notes: This is what we at HQ call the Swoosh chart.
It depicts all of the exploration elements that exist today, in development, or in the planning stages between now and 2024.
As you can see, VIPER is prominent in the human return strategy.
VIPER will perform the first lunar volatiles survey on the surface of the Moon.

## Slide 3
* Not including launch or lander
1 Volatiles Investigating Polar Exploration Rover
Lunar Prospector (Launched 1998, $63M*)
First global surface composition
Polar volatiles & global magnetic maps
VIPER1 (Launching FY23, ~$TBDM*)
Robotic rover at lunar pole
Resource mapping mission
Commercial Lunar Payload Services
LADEE (Launched 2013, $250M*)
Lunar atmosphere and dust
First deep space laser communication
NASA-ARC Low-cost Lunar Missions Portfolio
LCROSS (Launched 2009, $79M*)
Impacted lunar south pole
Evidence for water ice in cold, shadowed regions

## Slide 4: VIPER Science Objectives
The science objectives of the VIPER mission are to:
  • Characterize the distribution and physical state of lunar polar water and other volatiles in lunar cold traps and regolith to understand their origin
  • Provide the data necessary for NASA to evaluate the potential return of In-Situ Resource Utilization (ISRU) from the lunar polar regions

## Slide 5
Critical Observations Needed
Volatile Distribution (concentration, including lateral and vertical extent and variability)
Volatile Physical State (H2, OH, H2O, CO2, Ice vs bound, etc).
The Context and Correlation, including:
  Accessibility/Overburden: How much and type of material needing to be removed to get to ore?
  Environment: Sun/Shadow fraction, soil mechanics, trafficability, temperatures
  Distribution and Form vs Environment
  Extrapolates small scale distributions to global data sets, critical for developing “mineral/resource models”
From “Committee for Mineral Reserves and International Reporting Standards, 2013
Lunar Polar Exploration
Distribution. Physical State. Context. Correlation.
Lunar Polar Volatile Exploration: Science and Exploration

## Slide 6
LCROSS
LRO
Lunar Prospector
Clementine
V I P E R
Industry
VIPER bridges Government and Industry missions, addressing volatiles mapping, in support of the Economic opportunity of the Moon
Industry
Missions:
US Lunar Goals:
Orbital Observations
Orbital Prospecting
Ground Truthing
Ground Prospecting
Resource Mapping
Bulk Production
ISRU & Mining
Demonstrations
Chandrayaan-I
The Big Picture of Lunar Resources
(future science missions)

## Slide 7: VIPER Surface Segment (Rover + Instruments)
Subsurface excavation
TRIDENT Drill
Prospecting Neutron Spectrometer System (NSS) Instrument
Prospecting & Evaluation
Near Infrared Volatiles Spectrometer System (NIRVSS) Instrument
Rover Control Flight Avionics (internal)
Prospecting & Evaluation
Mass Spectrometer Observing Lunar Operations (MSolo) Instrument
Power
Solar Array (3-sides)
Vision & Comm Camera/Antenna Mast
Heat Rejection Radiator (on top)

## Slide 8: Historical Planetary Rovers & VIPER
http://historicspacecraft.com/Probes_Mars.html
*includes instruments
0.6m x0.5m x0.3m
11kg
Top Speed: 5cm/s
1.6m x2.3m x1.5m
180kg*
Top Speed: 5cm/s
3.0m x2.8m x2.1m
900kg
Top Speed: 4cm/s
1.3M x1.6m x1.5m, 840kg
Top Speed: 55cm/s
1.3M x1.6m x1.5m, 840kg
Top Speed: 500cm/s
Yutu (2013):
1.5m x1.1m, 140kg
5cm/s
Spirit & Opportunity
Curiosity
1.5m x1.5m x2.0m, 430kg
Top Speed: 20cm/s
(1970/1973):
(1996):
(2004):
(2011):
(1971/1972):
VIPER (2023):

## Slide 9: VIPER Performance Specs
Mass: ~430kg (950lbs) Power (peak): ~450W
Comms (DTE1): X-band (230kbps hi-gain / 2kbps omni)
Comms network: DSN 34m dishes
Canberra, Goldstone, Madrid
Dimensions: 1.5m x 1.5m x 2.5m (5ft x 5ft x 8ft)
Top Speed: 20cm/s (0.5 MPH)
Prospecting Speed: 10cm/s (4in/s)
Distance Travelled (goal): 20km (~12mi)
Lunar delivery: CLPS2 commercial contract
1 DTE = Direct-To-Earth
2 CLPS = Commercial Lunar Payload Services

## Slide 10: VIPER Science Specs
Mission Duration: 100+ earth days
Instruments: Neutron, Near-IR, and Mass Specs; 1m Drill
Detectable H2O Concentration: 0.5% (by weight)
Drill Depth: 1m (~3ft)
# of Surface Assays (drill sites): 30-40 sites (18 minimum)
Dark Survivability: 96hrs
PSR Working Duration: 6hrs
Surface Traverse Plan baselined: @CDR

## Slide 11: VIPER Instruments
MSolo (KSC, INFICON, NSF– SHREC Space Processor, & Blue Sun – Virtual Machine Language)
PI: Janine Captain (NASA KSC)
Instrument Type: Quadrupole mass spectrometer
Key Measurements: Identify low-molecular weight volatiles between 1-100 amu, unit mass resolution to measure isotopes including D/H and 018/016
TRIDENT (Honeybee Robotics)
PI: Kris Zacny (Honeybee Robotics)
Instrument Type: 1-meter percussive drill
Key Measurements: Excavation of subsurface material to 100 cm; Subsurface temperature vs depth; Strength of regolith vs depth (info on ice-cemented ground vs. ice-soil mixture)
NSS (NASA ARC/Lockheed Martin ATC)
PI: Rick Elphic (NASA ARC)
Instrument Type: Two channel neutron spectrometer
Key Measurements: NSS assesses hydrogen and bulk composition in the top meter of regolith, measuring down to 0.5% (wt) WEH to 3s while roving
NIRVSS (ARC, Brimrose Corporation)
PI: Anthony Colaprete (NASA ARC)
Instrument Type: NIR Spectrometer, 4Mpxl Imager with 7 banks of color LEDs, four channel thermal radiometer
Key Measurements: Volatiles including H2O, OH, and CO2 and, minerology, surface morphology and temperatures
NSS
NIRVSS
MSolo
TRIDENT

## Slide 12: Sampling: Demonstration
Multiple tests at GRC demonstrated the TRIDENT, MSolo and NIRVSS systems ability to capture samples at depth and identify water (at concentrations <0.25%) in real-time
DOC Composite
410, 740, 905nm
Chart: Wavelength (nm)
TRIDENT installed at VF13 TCAV facility
NIRVSS Spectra of cuttings piles
Water ice band depths calculated real time during VF13 testing

## Slide 13: Spatial Proxies for Resource Maps and Models
Primary environmental factor is temperature
At a minimum temperatures (surface or subsurface) must be low enough to retain water ice
Secondary environmental factors may include geophysical properties (e.g., association with craters of a certain size and age)
Also secondary is the ore extent, given regional data sets only extend to ~1 meter deep (i.e., neutron observations)
Using temperatures from the surface to 1 meter deep as primary surface proxy
Four environments defined based on the predicted thermal stability of ice with depth, the Ice Stability Regions (ISRs):
  Dry: Temperatures in the top meter expected to be too warm for ice to be stable
  Deep: Ice expected to be stable between 50-100 cm of the surface
  Shallow: Ice expected to be stable within 50cm of surface
  Surface: Ice expected to be stable at the surface (ie., within a Permanently Shadowed Region, PSR)
Ice Stability Depth Map
Ice Stability Region Map
Ice stable at surface (PSR)
Ice not stable at <1m
Ice stable at shallow depths

## Slide 14: Where to Land?
Surface/Subsurface volatiles
Sun illumination
Traversable terrain
Direct to Earth (DTE) comm
  Candidate polar landing sites meet these four criteria:
    Plausible surface/subsurface volatiles
    Reasonable terrain for landing and traverse
    Direct view to Earth for communication
    Maximize sunlight for power (including safe havens)
South Pole
To Earth
Notes: Level 1 and 2 requirements define the requirements that guide landing site selection. The overlap of (1) plausible surface/subsurface volatiles, (2) safe and traversable terrain, (3) maximum direct-to-Earth communications access, and (4) maximum solar illumination, determine the areas of interest for landing site selection.

## Slide 15: Shadows move at roughly the rover’s speed
Near the pole, sun against topography casts long shadows
Similar radio shadows are cast when using a line-of-site radio link to ground stations
Sun and radio shadows move on a timescale similar to the time needed to take the required measurements
  Shadows cast by a peak 3.9 km away move at 1 cm/s
Therefore, traverse plans must plan to avoid moving shadows
grayscale=amount of sunlight, 20 meter pixels, circles=drill sites;
green=candidate landing site; red square=the rover, Timespan = ~8 days
The movie shows a red square representing the rover moving as the shadows move. The rover starts at the center of the green circles. This example illustrates difficult sun and comm shadow constraints and meets all mission requirements, although it probably wouldn’t be selected given safer, multi-lunar day solutions

## Slide 16: Speed Made Good
Speed Made Good (SMG) :
Average speed
Accounts for all delays except recharging
  Downlink stereo images
  Images are processed to identify hazards
  Driver selects the next, safe waypoint
    Sometimes requests for more images
  Commands are uplinked
  The rover moves to the new waypoint
Includes margin to account for avoiding obstacles
Range used for traverse planning 0.7-1.0 cm/s
10 cm/s
Stationary
Rover Waypoints and Path Length

## Slide 17: Merging maps and operational constraints
Traverse planning efficiency is enabled by generating maps that have operational constraints integrated into them
Some examples
Sun Safety Margin (Time-dependent)
Color pixels that will have less than 80% sun within 48 hours yellow and within 24 hours, red
Landing Sites
(Time-dependent)
Green pixels lie at center of a 100 x 100 m landing error ellipse completely within slope limits of the lander that have sun and DSN access for at least 48 hours.
Red pixels are in permanent shadow and have DSN station access
Lander line-of-site (Varies with lander)
Given a landing site, color map pixels with line-of-site between given lander and rover antenna heights
Slope & Navigability
(Static)
Color map pixels within the slope limits of the lander (green) and of the rover (green and yellow).
LOLA roughness and Diviner blockiness products are also available
Earth Comm Blockage (Time-dependent)
Topographic maps generated from orbit have height errors, e.g., LOLA DEMs have a reported error of 1 m 1σ. These errors could result in planning to move the rover to a location where DSN stations are blocked by terrain. This map shows locations where the probability of the 2 deg horizon safety margin being exceeded is above a given risk threshold
ISRU Areas (Static)
Identify 60 x 60 meter areas that are predominantly one thermal environment and < 5 deg slope. Each is large enough to generate 1000 kg of O2 if 0.5% water and 10% extraction efficiency. These are candidate locations for doing the required measurements

## Slide 18: Rover Performance Model
Traverse planning tools contain rover performance models covering alternatives as the rover’s design has matured. Factors included are (not all in all models):
Model inputs Solar cell efficiency battery charge/discharge curve component and heater loads potential energy wheel slip driver decision delays orientation policy camera sun keepout zones rover pose on slope
Activity Dictionary Major modes the rover and payload can be in; each typically lasting 5-120 minutes Gives power used and data generated Determines the traverse planning level-of-detail
Model outputs (typical) battery state-of-charge, time-to-shadow, slope, sun-fraction, surface temperature
Early human-in-loop sims point toward 40-50% obstacle avoidance overhead
Activity Dictionary

## Slide 19: Planning Traverses
Type | Color
PSR, ice depth = 0 | 
Shallow, ice depth (0, 0.5] m | 
Deep, ice depth (0.5, 1] m | 
Dry, ice depth (1, ∞] m, drivable | 
Dry, ice depth (1, ∞] m, too steep | 
Type | Color |  | 
[0, 24] hours of shadow |  |  | 
(24, 96] hours of shadow |  |  | 
Thermal Environments
Lighting Environments

## Slide 20: Example Traverse Near Nobile

## Slide 21
Rover Driving Simulator Capability
NASA-ARC Lunar Operations Lab
Powerful, fully-synthetic, lunar terrain sim based on Digital Elevation Maps (DEM)
  Establishing driver decision-making times

## Slide 22: Notables
VIPER lunar-weight rover tested in lunar simulant soil bin
NASA-GRC, SLOPE laboratory

## Slide 23: Questions?