## Slide 1: Autonomous Freeflying Drones for Spacecraft Inspection
Sami Mian1, Tyler Garrett1, Alexander Glandon2, Christopher Manderino1, Swee Balachandran3, Cesar A. Muñoz4, and Chester V. Dolph4
1 NSF SHREC Center, University of Pittsburgh 2Old Dominion University 3National Institute of Aerospace 4NASA Langley Research Center 39th Digital Avionics Systems Conference (DASC 2020)
Virtual Conference
October 11-16, 2020

## Slide 2: Introduction
A major hazard for spacecraft is structural damage from collisions with orbital debris or ablations
  Can degrade performance or cause catastrophic failure
There is estimated to be nearly one million pieces of space debris greater than 1cm in length and over 128 million pieces less than 1cm [2]
Prior work has considered damage detection prior to orbit [3,4]
This project considers the novel problem of in-orbit damage detection
Our proposed solution simulates a swarm of autonomous free-flyer satellites surveying a larger spacecraft for possible damage

## Slide 3: Swarm UAVs for Inspection
We look to unmanned aerial vehicles (UAVs) for a simulation basis
UAVs have been used for visual inspections of roads, bridges, buildings, and other outdoor structures
  Includes a variety of sensors systems (IR, LIDAR, RGB, Acoustics, etc.)
Data streams from multiple UAVs can be combined for more accurate analysis and visual representations
Multi-agent approach allows for robustness against mission failure
Also allows for use of diverse, payload-specific platforms

## Slide 4: Project Overview & Goals
Proof-of-concept mission demonstrating a multi-agent system performing visual inspection of damage
Free-flying satellites simulated by unmanned aerial vehicles (UAVs)
Free-flyers are responsible for independently coordinating their flights while executing mission tasks
Damage analysis on the surface of the mock space module is performed in real-time using computer vision
Extend existing onboard software architecture ICAROUS to autonomous spaceflight for in-orbit systems

## Slide 5: ICAROUS Overview
ICAROUS: Independent Configurable Architecture for Reliable Operations of Unmanned Systems
  Onboard software architecture for distributed collaboration among free flying agents
  Enables modular development and accelerated incorporation of new applications and features
  Applications communicate via a publish/subscribe framework

## Slide 6: ICAROUS Overview
© NASA Langley, ICAROUS website

## Slide 7: System Design
New ICAROUS modules provide high-level mission management and multi-agent coordination
  Cognition determines various levels of mission tasks for each of the free-flyer
  Guidance issues low-level commands to each free-flyer based on their allocated tasks
  Coordination manages the multi-agent aspects of the mission
Developed a cFS Vicon™ interface for indoor localization
Inspection protocol uses computer vision (CV) techniques on video streams provided by each free-flyer to identify potential damage or anomalies

## Slide 8: System Design

## Slide 9: Main Software Apps
Coordination
  Manages multi-agent aspects of mission
  Accepts mission parameters from human operators
  Detects number of platforms available, splits up mission tasks for each platform
Cognition
  Determines high-level mission tasks for each platform
  Includes takeoff/land, assigning waypoints, modifying positions for data collection
Guidance
  Issues low-level commands to each UAV platform for local motion planning
  Changes in velocity/position/altitude

## Slide 10: Flight Software Architecture

## Slide 11: Support Apps
Hardware Interface
  In order to use COTS platforms with ICAROUS, we needed an application that can interface with existing drone APIs to send control + data commands
  Created a cFS application to interface with open source APIs for AT commands
Positioning System Interface
  Utilize a Vicon motion capture system for simulated GPS
  Created a cFS module to interface with system, spoof GPS data
Communication Bus
  Multiple instances of ICAROUS need to communicate and share data
  Created a cFS application built around Software Bus Network (SBN) to share telemetry data and waypoint mission lists

## Slide 12: Vicon System
Indoor Positioning and Localization System
Used to Simulate GPS
Captures 3D Frames Utilizing 15 Vicon Motion Capture Cameras
  Feeds messages to cFS applications over the software bus
    Position
    Rotation
    Velocity
  Vicon cFS Application converts END to GPS Coordinates required by ICAROUS

## Slide 13: Vicon System
Drones
Cameras

## Slide 14: Drone Platform: AR Parrot 2.0
ARM Cortex A8 1 GHz Processor
OS: Linux 2.6.32
RAM: DDR2 1 GB @ 200 MHz
WiFi b/g/n 2.4Ghz
3 Axis Gyro, 3 Axis Accelerometer, Magnetometer, Pressure Sensor
4 brushless motors, 14.5 W @ 28,500 rev/min
720p 30 FPS HD camera, Wide Angle lens 92°, H264 encoding
Vertical camera: QVGA 60 FPS to measure ground speed
Ultrasonic Sensor for height measurement

## Slide 15: Drone API
AR Drone Python API (PyARDrone)
Video Client (OpenCV support)
AT Command Library
Navigation Data Feedback
Provided Commands:
  Takeoff/Land
  Move(F/B,L/R,U/D,CW/CCW)
    Controls Roll, Pitch, Yaw, Gaz
  Hover
  Emergency
© Python.org, nugent.org
Notes: Connect over IP
Create a Drone Object

## Slide 16: Offboard Computing Proxy: Intel NUC
Intel NUC used for complex computing tasks
  Onboard drone CPU limited in capability
Running Ground Station, CFS, Drone API, and Computer Vision
Connects to drones using local network (TCP/IP)
Each drone has its own NUC, to simulate onboard computer
© Intel

## Slide 17: Drone Controller
Dynamics for UAV flight are different for various platforms
This system needs a way to normalize the flight characteristics for test platforms
Developed an in-house flight controller, works with most COTS systems

## Slide 18: Computer Vision Problem Specification
Segment Space Module (Cylinder) from Ambient Background in Flight Space
Detect Any Portion of Cylinder that is Damaged
Report Damage Assessment to System
3D Damage Reconstruction Solution

## Slide 19: Computer Vision Techniques Explored
Segmentation
  Otsu Thresholding
  Template Matching
  Grab Cut
  Color Based Segmentation
Damage Localization
  Sobel Edge Detection
  Convolution Neural Network Classification and Painting of Cylinders
  3D Navigable Reconstruction

## Slide 20: Damage Inspection cFS App Interface

## Slide 21: Computer Vision Offline 3D Damage Reconstruction
Photogrammetry based algorithm allowed offline 3D Reconstruction
Compliments the Real Time 2D Damage Localization
User in the loop can navigate 3D visualization of damage to modules

## Slide 22: 3D Reconstruction System Diagram

## Slide 23: Testing & Demonstration
Simulation of dynamic, multi-agent mission distribution
  Verify new localization data streams
  Assess optimal mission distribution and robustness
Conducted a set of flight experiments to tune and test the systems
Explored trade-off of performance vs accuracy of damage detection

## Slide 24: Final Demo Description
Free-flyer 1 enters flight space
Coordination module detects one freeflyer in swarm and distributes full flight plan from ground station
Free-flyer 1 begins orbit of top half of mock satellite
Free-flyer 2 is dispatched
Coordination module detects new free-flyer in swarm and dynamically updates mission into two subtask lists
  orbiting top-half
  orbiting bottom-half
Subtask lists are distributed between Free-flyer 1 and 2

## Slide 25: Final Demo Description
7. Free-flyer 1 and 2 begin executing mission subtasks
8. Free-flyer 2 abruptly departs
9. Coordination module detects Free-flyer 2 loss
10. Calculate new task list for Free-flyer 1 with remaining waypoints
11. Free-flyer 1 completes visual analysis of top-half
12. Free-flyer 1 enters downward helix pattern to complete analysis of bottom-half using inherited waypoints
13. Free-flyer 1 completes remainder of mission

## Slide 26: Results
Embedded video: 2_drones_demo.mp4

## Slide 27: Drone Controller Results
Drone physical position versus waypoints
  Based on MAVLink recorded odometry and post-flight analysis

## Slide 28: Drone Controller Results
Drone position error diagrams
Relative Error
Absolute Error

## Slide 29: Computer Vision Results
CNN damage localization
Sobel filter damage localization
Multi-cylinder segmentation and damage spotlighting
3D reconstruction

## Slide 30: Convolutional Neural Network Damage Localization
Window Based CNN Localized Damage Classification

## Slide 31: Sobel Filter Damage Localization
Tunable Threshold allows Reduction of False Negatives
Minimizes risk of overlooking mission critical damage

## Slide 32: Complete Multi Cylinder Segmentation and Damage Localization Solution
Realtime In Flight Module Localization and Damage Localization Output

## Slide 33: Offline 3D Reconstruction
Robust Human Navigable Damage Visualization
Given surface feature that do not represent damage, model comparison can detect discrepancies

## Slide 34: Discussion
Individual UAV Control
  Custom controller works extremely well, minimal position deviations
Multi-Agent Implementation
  Coordination app for dynamic mission distribution, robust performance
  Modular design allows for future extensibility
  UAVs cover 100% of object of interest guaranteeing full coverage inspection
Computer Vision System
  Comparative before and after models to detect damage
  3D models for visualizing damage offline in an interactive environment

## Slide 35: Future Work
Enhance the Coordination module to utilize more complex mission allocation algorithms
Extend support for other UAV hardware platforms
Incorporate the use of Data Distribution Service (DDS) into the cFS communication bus
  Allows for advanced networking and data sharing techniques
Implement the 3D reconstruction program in real-time

## Slide 36: Conclusions
Successful integration within ICAROUS framework
UAVs were successfully used to simulate free-flyer spacecraft
Localized damage was successfully detected on a uniform metallic surface
Efficient mission planning and completion based on a variable number of resources
Free-flyers are a viable platform for in-situ, real-time damage detection of spacecraft structures

## Slide 37: References
[1] D. McComas, “Nasa/gsfc’s flight software core flight system,” 2012.
[2] N. L. Johnson, “Orbital debris: the growing threat to space operations,” in 33rd Annual Guidance and Control Conference, 2010.
[3] D. Doyle, A. Zagrai, B. Arritt, and H. C¸ akan, “Damage detection in bolted space structures,” Journal of Intelligent Material Systems and Structures, vol. 21, no. 3, pp. 251–264, 2010.
[4] A. Zagrai, D. Doyle, and B. Arritt, “Embedded nonlinear ultrasonics for structural health monitoring of satellite joints,” in Health Monitoring of Structural and Biological Systems 2008, vol. 6935. International Society for Optics and Photonics, 2008, p. 693505.

## Slide 38: Questions?