## Slide 1
International Earth Science Constellation
Mission Operations Working Group (MOWG)
September 29 – October 2, 2020
Aura IAM Fall Series 2020 Updates
Nathaniel Johnson, a.i. solutions
EOS FDS, esmo-eos-fds@lists.nasa.gov, +1.301.416.5050

## Slide 2: Agenda
Recap Aura Fall 2020 Inclination Adjust Maneuver (IAM) Campaign
  Series Summary
  Maneuver Results
Aura’s IAM Performance Trends
2021 IAM Campaign Dates and Planning
Aura Latest Lifetime MLT Predictions

## Slide 3: Aura Fall 2020 Series Summary
Aura performed three inclination maneuvers, IAMs #68-70, on August 19th, September 9th, and September 16th.
As in the 2019 series, Aura’s Reaction Wheel Assembly (RWA) was successfully utilized to slew to the desired angle for the inclination maneuver.
For the Fall, results from the 2019 IAM Series were used as predictions.
The delta-inclination from IAM #68 was close to predictions and the maneuver was 0.788% cold.

## Slide 4: Results
Aura’s achieved delta-inclination for the series was 0.783% COLD, based on the Constellation Coordinated Plan
IAM # | Date | Burn Dur (sec) | Commanded Yaw (deg) | Achieved Yaw (deg) |  | Delta Inclination (deg) |  | Delta RAAN* (deg) | 
 |  |  |  | Predicted | Definitive | Predicted | Definitive | Predicted | Definitive
68 | Aug 19 | 200.0 | -77.6 | -75.7229 | -75.5958 | -0.00358 | -0.00355 | -0.00001 | 0.00001
69 | Sep 9 | 415.0 | -75.3 | -75.4048 | -75.4048 | -0.00745 | -0.00739 | -0.00001 | -0.00001
70 | Sep 16 | 415.0 | -75.3 | -75.4048 | -75.4048 | -0.00743 | -0.00737 | -0.00001 | -0.00001
*Right Ascension of the Ascending Node (RAAN) |  |  |  |  |  | Total: | -0.018314 | -0.00001 | 

## Slide 5: Aura Fall 2020 Performance Trends
The roll and pitch attitude errors during the burn have continued the trend of previous maneuvers
The yaw offset has once again flipped signs from previous maneuvers but is much lower in magnitude.
  More positive semi-major axis change was achieved than predicted
The delta-inclination efficiency of the Fall IAMs was in family with the Spring series

## Slide 6: Aura’s IAM Performance (1/2)
Chart: Average Roll, Pitch, and Yaw Error during INC
RWA slewed IAMs have two values for yaw offset, the yaw error from telemetry (grey) and calibrated yaw (red). The calibrated yaw is the angle necessary to achieve the delta-SMA observed.
2020 IAMs
INC #68’s yaw offset value has once again flipped signs.

## Slide 7: Aura’s IAM Performance (2/2)
Chart: Efficiency
2020 IAMs
The inclination efficiency has remained consistent with the previous RWA slewed IAMs

## Slide 8: Aura Spring 2021 IAM Campaign Planning
The Aura Spring 2021 IAM plan consists of 4 inclination maneuvers
Since burn can be centered on node with RWA slewed maneuvers, the ideal date is no longer a factor in efficiency
  Proposed plan –
    February 24 (IAM #71)
    March 3 (IAM #72)
    March 10 (IAM #73)
    March 17 (IAM #74)
Dates are set so Aura maneuvers a day before Aqua
Five maneuvers are planned for the Fall 2021 IAM campaign in addition to the Spring 2021 IAMs.

## Slide 9: Proposed Aqua/Aura 2021 Maneuver Schedule
*Spring Equinox on March 19
Sunday | Monday | Tuesday | Wednesday | Thursday | Friday | Saturday
February 21 | 22 | 23 | 24 Aura IAM #71 | 25 Aqua IAM#74 | 26 | 27
28 | March 1 | 2 | 3 Aura IAM#72 | 4 Aqua IAM#75 | 5 | 6
7 | 8 | 9 | 10 Aura IAM#73 | 11 Aqua IAM#76 | 12 | 13
14 | 15 | 16 | 17 Aura IAM#74 | 18 Aqua IAM#77 | 19 | 20*
21 | 22 | 23 | 24 Aura Back-up | 25 Aqua Back-up | 26 | 27
28 | 29 | 30 | 31 | April 1 | 2 | 3
4 | 5 | 6 | 7 | 8 | 9 | 10

## Slide 10: Predicted Maneuver Performance
Inc # | Date | Commanded Yaw* (deg) | Duration (sec) | Delta SMA** (m) | Delta Inc (deg) | Delta RAAN (deg)
71 | Feb 24 | -75.3 | 315 | 4.64771 | -0.00559 | -0.00001
72 | Mar 03 |  |  | 4.64281 | -0.00558 | -0.00001
73 | Mar 10 |  |  | 4.63728 | -0.00557 | -0.00001
74 | Mar 17 |  |  | 4.63204 | -0.00556 | -0.00001
 |  |  |  | Total: | -0.0223 | -0.00004
*Preliminary angles
**Semi-Major Axis (SMA)
The above predictions are based on maintaining phasing with the nominal Aqua plan until Aura performs the 2021 Fall IAM series.

## Slide 11
Upper Phase Limit
Phase Center
Target Range
The Aura MLT phasing is predicted to be maintained through the next series
Predicted Post- Fall 2020 IAM MLT

## Slide 12: Summary
Similar to the Spring series and previous Fall series, Aura used the RWA to slew to the necessary angle for IAMs #68-70
Aura’s maneuver performance for the 2020 Fall IAM Series was 0.783% cold.
The Spring 2021 IAM series will have 4 maneuvers and is predicted to keep Aura near the middle of the MLT phasing control box prior to the Fall 2021 series.