## Slide 1
Space Technology Mission Directorate
Game Changing Development Program
Karl Edquist, NASA LaRC | Ashley Korzun, NASA LaRC | FY20 Descent Systems Study Annual Review Presentation | 09.17.20

## Slide 2: Technology Overview
Using propulsive descent (PD) retro-rockets starting at supersonic conditions at Mars would enable landing human payloads (~4K-20K kg payloads) within 50 meters of a target – current capability is ~1K kg
Technology Goal: To inform STMD investments that will enable Mars human scale EDL
Descent Systems Study (DSS) is an extension and continuation of the Entry, Descent and Landing (EDL) Architecture Study (EDLAS) task that STMD started funding in FY16
Low-L/D Entry Concept
Mid-L/D Entry Concept

## Slide 3: Technology Overview
Low-L/D Flight Vehicle & CFD Calculation
Low-L/D Wind Tunnel Model & CFD Calculation
16 m
DSS (computational modeling) is partnering with ARMD’s Aerosciences Evaluation Test Capability (AETC) (wind tunnel testing) to advance the PD technology
The sole FY20 task is to complete a matrix of computational fluid dynamics (CFD) solutions at expected test conditions in the Langley Unitary Plan Wind Tunnel (UPWT) environment
The ability to test and computationally model PD aerodynamics must improve in order to reduce the risks of using the technology for future Mars missions

## Slide 4: Mission Infusion & Partnerships
Contributing partners and/or stakeholders
  ARMD’s Aerosciences Evaluation and Test Capabilities (AETC) is funding a PD test in the Langley Unitary Plan Wind Tunnel (UPWT) to provide aerodynamics data on Mars-relevant sub-scale models
  AETC is paying for the wind tunnel models and facility time and will provide all data to DSS
Infusion/transition plan
  STMD Earth sub-orbital flight testing to advance TRL
  HEOMD Mars precursor and human missions
  HLS testing may be impacted by what we learn, mostly in terms of GN&C and plume/surface interaction

## Slide 5: Descent Systems Study Technology Goals & Project Objectives
Technology Goals | 
Goal #1 | Improve methods for Earth-based testing of PD systems
Goal #2 | Develop best practices for calculating CFD-based PD aerodynamics at Mars conditions
Goal #3 | Establish baseline uncertainties for CFD-based PD aerodynamics models
Goal #4 | Reduce overall high-mass Mars EDL risks associated with PD
Project Objectives | 
Objective #1 | Complete CFD analysis to support AETC wind tunnel model and test matrix design
Objective #2 | Complete CFD solutions of Low-L/D and Mid-L/D propulsive descent wind tunnel models for a range of planned conditions in the Langley UPWT environment (model configurations, tunnel Mach number, model attitude, and model thrust)
Objective #3 | Quantify the differences between the CFD results and wind tunnel data

## Slide 6: Accomplishments - Overview
Presented 11 papers at 2020 AIAA SciTech conference
  Covered FY19 tasks and status of AETC PD test & DSS CFD
Supported AETC PD wind tunnel model design
  Ran CFD analysis to optimize wind tunnel model internal flow paths and instrumentation locations
  Supplied CFD-based wind tunnel model aerodynamics loads for model safety certification
Presented DSS overview at AETC “CFD as Surrogate for High Supersonic Mach Numbers” TIM
Completed ~105 CFD cases at the planned AETC PD wind tunnel test conditions
Numerous invited presentations for High Performance Computing (HPC) audiences, including High-End Computing Needs Assessment (HECNA) workshop

## Slide 7: AETC Wind Tunnel Models
1A | 1B | 1C | 1D | 1E | 1F | 2A
Low-L/D Model
Mid-L/D Model
HPA = high pressure air

## Slide 8: Model Design Support
Supported AETC wind tunnel model design
  Ran CFD analysis to optimize wind tunnel model internal flow paths and instrumentation locations
  Supplied CFD-based worst-case aerodynamics loads for model safety certification
Internal Flow Contour
Loads
High Pressure Air (HPA)
Star-CCM+ Solution (Veronica Hawke, NASA ARC STC
Instrument Placement

## Slide 9: Pre-Test CFD Case Matrix
9 models, 3 angles of attack, 4 thrust levels, 3 tunnel Mach numbers, 3 CFD codes = 168 primary cases and 303 bonus cases
Threshold: complete 50% of primary cases
Goal: complete 75% of primary cases and 25% of bonus cases
To date, have completed 41% of primary cases and 12% of bonus cases
 |  | Condition #5 (Mach = 2.386, Re = 1e6 / ft) |  |  |  |  |  |  |  |  |  |  |  | Condition #20 (Mach = 3.477, Re = 1e6 / ft) |  |  |  |  |  |  |  |  |  |  |  | Condition #35 (Mach = 4.568, Re = 1.5e6 / ft) |  |  |  |  |  |  |  |  |  |  | 
Model | a \ CT | 0.0 | 0.0 | 0.0 | 0.5 | 0.5 | 0.5 | 1.0 | 1.0 | 1.0 | 2.5 | 2.5 | 2.5 | 0.0 | 0.0 | 0.0 | 0.5 | 0.5 | 0.5 | 1.0 | 1.0 | 1.0 | 2.5 | 2.5 | 2.5 | 0.0 | 0.0 | 0.0 | 0.5 | 0.5 | 0.5 | 1.0 | 1.0 | 1.0 | 2.5 | 2.5 | 2.5
 |  | LC | F3D | OF | LC | F3D | OF | LC | F3D | OF | LC | F3D | OF | LC | F3D | OF | LC | F3D | OF | LC | F3D | OF | LC | F3D | OF | LC | F3D | OF | LC | F3D | OF | LC | F3D | OF | LC | F3D | OF
01 | 00 | 1 | 3 | 0 |  |  |  |  |  |  |  |  |  | 0 | 2 | 0 |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 |  |  |  |  |  |  |  |  | 
01 | 05 | 0 | 2 | 0 |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 |  |  |  |  |  |  |  |  | 
01 | 10 | 1 | 2 | 0 |  |  |  |  |  |  |  |  |  | 0 | 2 | 0 |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 |  |  |  |  |  |  |  |  | 
1A | 00 |  |  |  | 1 | 2 |  | 1 | 2 |  | 1 | 2 |  |  |  |  | 0 | 1 |  | 0 | 1 |  | 0 | 1 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 | 
1A | 05 |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 | 
1A | 10 |  |  |  | 1 | 2 |  | 1 | 2 |  | 1 | 2 |  |  |  |  | 0 | 1 |  | 0 | 1 |  | 0 | 1 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 | 
1B | 00 |  |  |  | 1 | 2 |  | 1 | 2 |  | 1 | 3 |  |  |  |  | 0 | 0 |  | 0 | 1 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 | 
1B | 05 |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 1 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 | 
1B | 10 |  |  |  | 1 | 2 |  | 1 | 2 |  | 1 | 1 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 | 
1C | 00 |  |  |  | 0 | 1 |  | 0 | 1 |  | 0 | 1 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 | 
1C | 05 |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 | 
1C | 10 |  |  |  | 0 | 1 |  | 0 | 1 |  | 0 | 1 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 | 
1D | 00 |  |  |  | 0 | 1 |  | 0 | 1 |  | 0 | 1 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 | 
1D | 05 |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 | 
1D | 10 |  |  |  | 0 | 1 |  | 0 | 1 |  | 0 | 1 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 | 
1E | 00 |  |  |  |  | 2 | 0 |  | 2 | 0 |  | 2 | 0 |  |  |  |  | 2 | 0 |  | 2 | 0 |  | 2 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0
1E | 05 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0
1E | 10 |  |  |  |  | 2 | 0 |  | 2 | 0 |  | 3 | 0 |  |  |  |  | 2 | 0 |  | 2 | 0 |  | 2 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0
1F | 00 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 1 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0
1F | 05 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0
1F | 10 |  |  |  |  | 1 | 0 |  | 0 | 0 |  | 1 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0 |  |  |  |  | 0 | 0 |  | 0 | 0 |  | 0 | 0
02 | 90 | 0 | 2 | 0 |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 |  |  |  |  |  |  |  |  | 
02 | 85 | 0 | 2 | 0 |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 |  |  |  |  |  |  |  |  | 
02 | 80 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 |  |  |  |  |  |  |  |  | 
2A | 90 |  |  |  | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 1 |  |  |  | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 |  |  |  | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1
2A | 85 |  |  |  | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 |  |  |  | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 |  |  |  | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1
2A | 80 |  |  |  | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 |  |  |  | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 |  |  |  | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1

## Slide 10: Computer Resources
Modeling PD using CFD is especially challenging
  Unsteady problem, sensitivity to grid and turbulence model settings, very large grids (disk space & memory), difficult to achieve numerical convergence, long run times
The UPWT environment adds complexity
  Non-uniform test section flow, tunnel walls, model support system
NASA Advanced Supercomputing (NAS) resources are needed to run most of the PD problems because of the resources required
  Unpredictably long queue wait times (sometimes days) if higher-priority (HEOMD) users are online
FY20 NAS resource request: 16M CPU hours, ~50% used to date
5 in
Schlieren
2010 UPWT Test
Journal of Spacecraft and Rockets, Vol. 51, No. 3
OVERFLOW CFD
Bil Kleb, NASA LaRC

## Slide 11: CFD Grids
Grids require 10s to 100s of millions of points to resolve all length scales
Generating a single grid can take days to complete
52M node FUN3D grid (no tunnel)
Justin Shafner, U. of Maryland
195M node Loci-CHEM grid (with tunnel)
Francisco Canabal, NASA MSFC

## Slide 12: CFD Results: Effect of Nozzle Thrust
How does nozzle thrust affect aerodynamics?
Aerodynamic axial force (drag) decreases non-linearly with increasing thrust and vanishes near CT,vac = 2.5
Increasing Thrust
Increasing Thrust
Model 1A
CT,vac = 0.5
CT,vac = 1
CT,vac = 2.5
Francisco Canabal, NASA MSFC
Increasing Drag
Notes: python aetc_report.py cfd_file=DSS_AETC_PD_Pre-Test_CFD_Logbook_MS_Teams_090220.csv cases=m01_c05,m1a_c05 omit=f3d,a05,a10 ct_axis=-0.5,3 cfx_axis=-0.5,2.5 cf_ct_axis=-0.5,3 pc_axis=0,500 title='Effect of Nozzle Thrust'

## Slide 13: CFD Results: Effect of Nozzle Cant Angle
How does nozzle cant angle (pointing direction) affect aerodynamics?
Pointing the nozzles outward 20-deg rather than forward increases aerodynamic axial force (drag) at all thrust levels
  Axial thrust decreases by 6%
Model 1A
Model 1B
Notes: python aetc_report.py cfd_file=DSS_AETC_PD_Pre-Test_CFD_Logbook_MS_Teams_090220.csv cases=m01,m1a_c05,m1b_c05 omit=f3d,a05,a10 ct_axis=-0.5,3 cfx_axis=-0.5,2.5 cf_ct_axis=-0.5,3 pc_axis=0,500 title='Effect of Nozzle Cant Angle'

## Slide 14: CFD Results: Effect of Nozzle Location
How does nozzle location affect aerodynamics?
Putting the nozzles farther outward on the heatshield increases aerodynamic axial force (drag), especially at higher thrust
Model 1F
Model 1B
Notes: python aetc_report.py cfd_file=DSS_AETC_PD_Pre-Test_CFD_Logbook_MS_Teams_090220.csv cases=m01_c05_g11_lc,m1b_c05_g11_lc,m1e_c05_g01_f3d omit=a05,a10,std ct_axis=-0.5,3 cfx_axis=-0.5,2.5 cf_ct_axis=-0.5,3 pc_axis=0,500 title='Effect of Nozzle Location'

## Slide 15: CFD Results: Effect of Nozzle Size
How does nozzle size affect aerodynamics?
Using larger nozzles causes small changes in aerodynamic drag, the direction of which depends on thrust
Model 1C
Model 1A
Notes: python aetc_report.py cfd_file=DSS_AETC_PD_Pre-Test_CFD_Logbook_MS_Teams_090220.csv cases=m01_c05_g11_lc,m1a_c05_g11_lc,m1c_c05 omit=a05,a10 ct_axis=-0.5,3 cfx_axis=-0.5,2.5 cf_ct_axis=-0.5,3 pc_axis=0,500 title='Effect of Nozzle Size'

## Slide 16: CFD Gallery
Bil Kleb, NASA LaRC
Tim Sandstrom, NASA ARC
Robert Childs, NASA ARC STC
Kristen Matsuno, NASA ARC
Notes: python aetc_report.py cfd_file=DSS_AETC_PD_Pre-Test_CFD_Logbook_MS_Teams_090220.csv cases=m01_c05_g11_lc,m1a_c05_g11_lc,m1c_c05 omit=a05,a10 ct_axis=-0.5,3 cfx_axis=-0.5,2.5 cf_ct_axis=-0.5,3 pc_axis=0,500 title='Effect of Nozzle Size'

## Slide 17: Project Assessment Summary
Project Name | Performance |  |  |  | Comments
 | C | S | T | P | 
Mid Year |  |  |  |  | C: No issues S: Partner project’s schedule had not yet been impacted by COVID-19 T: Often competing with higher-priority users for NAS supercomputer resources, not predictable but usually able to work around it P: No issues
Annual |  |  |  |  | C: Labor charges are at guideline S: Partner project’s wind tunnel test delayed by ~4 months due to COVID-19 and model fabrication delays. 2 AIAA SciTech 2021 papers were withdrawn. T: See above P: Delays in wind tunnel test will push FY21 milestones to the right by ~4 months

## Slide 18: EPO Update
Summary of Education and Public Outreach
AIAA SciTech 2020 conference
  Mars Human Entry, Descent and Landing Systems special session (6 presentations on FY19 tasks)
  SPLICE/other sessions (4 presentations on FY19 tasks)
  DSS FY20 task preview (1 presentations on FY20 results)
Mentored (A. Korzun) Langley summer graduate student (Justin Shafner)
Supporting Ames Pathways student (Kristen Matsuno)
Research Collaborator (A. Korzun) for new NSTGRO Fellow (Emily Jewell, Stanford)
Numerous presentations targeted at High Performance Computing (HPC) audiences

## Slide 19
  Mars Human Entry, Descent and Landing Systems Special Session
    Cianciolo, A. D., Korzun, A., Edquist, K., Samareh, J., Sostaric, R., Calderon, D., Garcia, J. A. “Human Mars Entry, Descent and Landing Architecture Study: Phase 3 Summary.”
    Korzun, A., Canabal, F., Tang, C., Childs, R., Van Norman, J., Tynis, J., Bibb, K. “Powered Descent Aerodynamics for Low and Mid Lift-to-Drag Human Mars Entry, Descent and Landing Vehicles.”
    Johnson, B., Sostaric, R., Lu, P. “Mid Lift-to-Drag Rigid Vehicle 6-DoF Performance for Human Mars Entry, Descent, and Landing.”
    Calderon, D., Sostaric, R., Garcia, J., Bowles, J., Gaytan, C., Newton, H., Amar, J., Wiens, Z. “Structural Mass Optimization with Manifest Packaging, and Outer Mold Line Updates of a Rigid Mid Lift-to-Drag Mars Entry Lander Vehicle.”
    Samareh, J. A., Behrend, M. P., Poteet, C. C., Komar, D. R., Theisinger, J. E., Lugo, R. A., Bowles, J. V. “Parametric Systems Analysis of a Mid-Lift/Drag Entry System for Human Mars Missions.”
    Friz, P. “Parametric cost estimates of three 20-ton payload Mars EDL vehicle concepts.”
  SPLICE Special Session
    Cianciolo, A. D., Lugo, R. A., Dutta, D., Williams, A., Chen, P. “A Simulation Framework for Precision Landing and Hazard Avoidance Technology Assessments.”
    Lugo, R. A., Powell, R. W., “Overview of a Generalized Numerical Predictor-Corrector Waypoint Guidance with Application to Human-Scale Mars Entry, Descent, and Landing.”
    Williams, J., Woffinden, D., Putnam, Z. “Mars Entry Guidance and Navigation Analysis Using Linear Covariance Analysis Techniques for the Safe and Precise Landing – Integrated Capabilities Evolution (SPLICE) Project.”
  Other
    Cianciolo, A. D., Korzun, A., Lugo, R. A., Slagel, A., Queen, E., Dillman, R., Powell, R. “Low Lift-to-Drag Morphing Shape Design.”
    Edquist, K. “Model Design and Pre-Test CFD Analysis for a Supersonic Retropropulsion Wind Tunnel Test.”
AIAA SciTech 2020 Papers
19

## Slide 20: High-Performance Computing (HPC) Presentations
Humans to Mars Summit 2020: Human EDL Panel (A. Korzun), 2 Sept 2020
Briefing to Jim Reuter (STMD) on Retropropulsion CFD and HPC Experience (A. Korzun and E. Nielsen), 20 Aug 2020
White House Office of Science and Technology Policy Convening (Panel – Future Advanced Computing Ecosystem) (A. Korzun), 17 Aug 2020
AFESB Summer Student Seminar Series: Propulsive Descent and Landing (A. Korzun), 27 July 2020
EDL SCLT F2F: EDL HPC – Summit Experience and Looking Ahead, SRP Use Case (A. Korzun), 23 July 2020
HECNA Use Case Presentation: Supersonic Retropropulsion CFD & Retropropulsion for Atmospheric Environments (K. Edquist and A. Korzun), 2 June 2020
Work featured in NVIDIA Keynote Address at SC19 (A. Korzun), Nov. 2019
SC19 Visualization Showcase Finalist (A. Korzun and Team), Nov. 2019
Briefing to Lori Glaze (Planetary Science Division) (A. Korzun), Nov. 2019)
NASA LaRC Center Leadership Council Presentation (A. Korzun and E. Nielsen): 23 Sept 2019

## Slide 21: Summary
Accomplishments for the Year
  Presented 11 papers at 2020 AIAA SciTech conference
  Supported AETC PD wind tunnel model design
  Presented at AETC “CFD as Surrogate for High Supersonic Mach Numbers” TIM
  Completed ~80 CFD cases at the planned AETC PD wind tunnel test conditions
  Numerous invited presentations to High Performance Computing (HPC) audiences, including High-End Computing Needs Assessment (HECNA) workshop
Plans Forward (FY21)
  Proposed budget was approved
  Complete the remaining primary CFD cases prior to the start of the AETC PD test (estimated to start in December)
  Make any needed adjustments to existing cases once the test data are collected and the conditions are known
  Complete an Uncertainty Quantification (UQ) of the CFD results compared to the test data
  Present test data and UQ results at the 2021 AIAA Aviation conference

## Slide 22: AETC/DSS FY20 Team
Karl Edquist, LaRC (PI)
Facility & Test Planning
  Bryan Falman, LaRC
  Matt Rhode, LaRC
Model Design
  Don Morr, ARC Millenium
CFD Pre-Processing, Analysis & Post-Processing
  Steve Alter, LaRC
  Francisco Canabal, MSFC
  Robert Childs, ARC STC
  Joseph Garcia, ARC
  Chris Glass, LaRC
  Veronica Hawke, ARC STC
  Bil Kleb, LaRC
  Ashley Korzun, LaRC
  Kristen Matsuno, ARC AA
  Justin Shafner, LaRC summer student
  Paul Stremel, ARC STC
  Bill Wood, LaRC

## Slide 23
BACKUP

## Slide 24: EPO Summary Chart
Conferences attended
Academic involvement
Conference | Papers/Posters/Panel Discussions
2020 AIAA SciTech | Cianciolo, A. D., Korzun, A., Edquist, K., Samareh, J., Sostaric, R., Calderon, D., Garcia, J. A. “Human Mars Entry, Descent and Landing Architecture Study: Phase 3 Summary.” Korzun, A., Canabal, F., Tang, C., Childs, R., Van Norman, J., Tynis, J., Bibb, K. “Powered Descent Aerodynamics for Low and Mid Lift-to-Drag Human Mars Entry, Descent and Landing Vehicles.” Johnson, B., Sostaric, R., Lu, P. “Mid Lift-to-Drag Rigid Vehicle 6-DoF Performance for Human Mars Entry, Descent, and Landing.” Calderon, D., Sostaric, R., Garcia, J., Bowles, J., Gaytan, C., Newton, H., Amar, J., Wiens, Z. “Structural Mass Optimization with Manifest Packaging, and Outer Mold Line Updates of a Rigid Mid Lift-to-Drag Mars Entry Lander Vehicle.” Samareh, J. A., Behrend, M. P., Poteet, C. C., Komar, D. R., Theisinger, J. E., Lugo, R. A., Bowles, J. V. “Parametric Systems Analysis of a Mid-Lift/Drag Entry System for Human Mars Missions.” Friz, P. “Parametric cost estimates of three 20-ton payload Mars EDL vehicle concepts.” Cianciolo, A. D., Lugo, R. A., Dutta, D., Williams, A., Chen, P. “A Simulation Framework for Precision Landing and Hazard Avoidance Technology Assessments.” Lugo, R. A., Powell, R. W., “Overview of a Generalized Numerical Predictor-Corrector Waypoint Guidance with Application to Human-Scale Mars Entry, Descent, and Landing.” Williams, J., Woffinden, D., Putnam, Z. “Mars Entry Guidance and Navigation Analysis Using Linear Covariance Analysis Techniques for the Safe and Precise Landing – Integrated Capabilities Evolution (SPLICE) Project.” Cianciolo, A. D., Korzun, A., Lugo, R. A., Slagel, A., Queen, E., Dillman, R., Powell, R. “Low Lift-to-Drag Morphing Shape Design.” Edquist, K. “Model Design and Pre-Test CFD Analysis for a Supersonic Retropropulsion Wind Tunnel Test.”
Student | Education Level | School Name
Justin Shafner (Langley summer) | Graduate Student | University of Maryland
Kristen Matsuno (Ames Pathways) | Graduate Student | Stanford University
Emily Jewell (NSTRGO) | Graduate Student | Stanford University

## Slide 25: Descent Systems Study – Annotated Cover Pictures
CFD calculation of Low-L/D powered
descent vehicle at Mars conditions
Artist depiction of Low-L/D powered
descent vehicle at Mars
AETC Low-L/D wind tunnel model heatshield
AETC Mid-L/D wind tunnel model heatshield
Artist depiction of Mid-L/D powered
descent vehicle at Mars
CFD calculation of Low-L/D powered
descent model at wind tunnel conditions

## Slide 26: GCD Project Performance Evaluation Criteria
Source: BPR Assessment Criteria for NASA R&T Projects, OCE/S. Hirshorn, 09/17/2015
 | Technical/Performance
Green | Project is demonstrably making progress on the Learning Trajectory (e.g. milestones met, knowledge advanced) or advancing TRL. Project is on track to meet L1 requirements.
Yellow | Project is making progress on the Learning Trajectory or advancing TRL with issues. Project is on track to meet L1 requirements but issues exist that may threaten achievement.
Red | Project has ceased to make progress on the Learning Trajectory or advance TRL. Project is unable to meet one or more L1 requirements.
 | Cost
Green | Project can meet its commitments with its planned/allocated budget.
Yellow | Project cannot meet its commitments within its planned/allocated budget but will not be requesting additional budget from Program. Mitigation plans have been developed.
Red | Project cannot meet its commitments within its planned/allocated budget and will be requesting additional budget from Program.
 | Schedule
Green | Project can meet its commitments within its planned/allocated schedule baseline for critical milestones.
Yellow | Project cannot meet its commitments within its planned/allocated schedule baseline but mitigation plans have been developed to pull it back in.
Red | Project cannot meet its commitments within its planned/allocated schedule baseline.
 | Programmatic (Institutional, Internal/External Dependencies **)
Green | Relevance of technology to stakeholders and/or technology infusion path is maintained. Mission sponsor still actively interested. No issues exist with workforce, test facilities, etc.
Yellow | Relevance of technology to stakeholders and/or technology infusion path are threatened. Mission sponsor backing off. Issues exist with workforce, test facilities, etc. but plans to mitigate are available.
Red | Relevance of technology to stakeholders and/or technology infusion path are not projected to be met, or has lost relevance to stakeholders. Mission sponsor cancelled interest. Issues pertaining to workforce, test facilities, etc. are preventing progress along the Learning Trajectory.