## Slide 1: Dr. Robin Hunt Research Aerospace Engineer Hypersonic Airbreathing Propulsion Branch NASA Langley Research Center
Wind Tunnel Testing of Next-Generation High-Speed Engines

## Slide 2: What is Supersonics? Hypersonics?
Mach number = speed of an object / speed of sound
Mach Number
1.0
5.0
0.3
Subsonic
(Pressure waves travel all directions)
Supersonic
(Pressure waves travel downstream)
1.2
0.8
Transonic
Nearly incompressible
(Air density is roughly constant)
Compressible
(Air density varies)
0
The flow physics depend on the Mach number
the transmission speed of a small disturbance through some medium
Hypersonic

## Slide 3: Supersonic Flow Physics: Shockwaves
For Mach numbers > 1, strong pressure waves (shock waves) form
Across a shock wave:
  Pressure and temperature increase
  Mach number decreases
NASA’s Air-to-Air Background Oriented Schlieren flights
Conceptual image of NASA’s X-59 QueSST Airplane (designed to reduce the loudness of a sonic boom to that of a gentle thump)
Shadowgraph of Gemini capsule model

## Slide 4
Hypersonic Flow Physics: High-Temperature Effects
High speed means high velocity (V) and high kinetic energy (1/2 V2)
As air flows around the vehicle, some kinetic energy is converted to internal energy = things get very hot
We melt metal!
  Vibrational energy states are excited
  Chemical reactions
  Dissociation (O2 -> 2O, N2 -> 2N)
  Ionization (+/- electrons)
One major challenge is dealing with the vehicle heating
  High temperature materials
  Active cooling
  Aerodynamic shapes/design
Other physics: low density flow, viscous interactions (friction), etc.

## Slide 5: Why are these speed regimes important? Access to space
Unpowered reentry to Earth or other planets for exploration
Rocket Launches
Ultimate goal: Air-Breathing propulsion systems
  Two-stage to orbit with airplane-like first stage for routine, affordable, safe access to space with increased launch flexibility
  Planetary atmospheric flight for exploration
Artist’s sketch of Apollo 11 reentry vehicle
NASA, SpaceX launched first astronauts to Space Station from U.S. since 2011

## Slide 6: Why are these speed regimes important? Military applications
Missiles
  Ballistic: High-altitude or sub-orbital flight with predictable trajectory
  Nonballistic: Sustained, maneuverable atmospheric flight
Reusable Vehicles for ISR (Intelligence, Surveillance, Reconnaissance)
SR-71 Blackbird - reconnaissance
Boeing X-51 waverider

## Slide 7: Why are these speed regimes important? Commercial transport
International day trips
Emerging market for a supersonic business jet?
  Boeing
  Lockheed Martin
  Boom Technology
  Aerion Supersonic
  Spike Aerospace
  The Spaceship Company
  Gulfstream Aerospace
Challenges:
  Costs
  Regulations
  Environmental impact
Concorde (1976-2003): Mach 2 British-French passenger airliner
Tu-144 (1970s): Mach 2 Soviet passenger airliner

## Slide 8: Air-Breathing Propulsion Options
ISP = Thrust force / fuel mass flow rate.
Higher ISP = larger range and payload capability
Turbojets
Scramjets
Ramjets
Turbojets
Ramjets
Scramjets
Hydrocarbon Fuels
Hydrogen Fuel
0
2000
4000
6000
8000
0
10
20
MACH NUMBER
I
sp
Rockets
2
Turbofans

## Slide 9: High-Speed Air-Breathing Engines: Ramjets & Scramjets
Ramjet (subsonic combustion)
Flow
Rely on shock waves created by the engine's forward motion to compress incoming air.
Cannot produce thrust at zero airspeed!
Dual mode ramjets capture both of these operating regimes to work over a wider range of Mach numbers.
Challenges: Extending the Mach number range, fuel mixing, ignition, flame holding, engine control, keeping structures cool
Inlet
Combustor
Nozzle
Isolator
Scramjet = Supersonic Combustion Ramjet

## Slide 10: Use a combined cycle engines for an even wider operating range
Combined-Cycle Engines
Flow
Flow
Runway to supersonic / hypersonic
Turbine-based combined cycle engine
Rocket-based combined cycle
Challenges: transitioning while maintaining thrust, integration with the airframe + all the other issues associated with the different engine components

## Slide 11: Designing a High-Speed Air-Breathing Engine
How do we design these engines?
  Engineering Design and Analysis
  Computational Fluid Dynamics
  Wind tunnel testing
  Rinse and repeat…
Converging-diverging nozzle delivers flow with desired Mach number to test section
(Supersonic: M>1)
Test section
Heated test gas
(Subsonic: Mach <1)
Colder test gas
Test model

## Slide 12: Why do we need wind tunnel tests?
Less risk and expense than flight tests
Test models of the entire vehicle or its specific components (e.g., propulsion system)
Computational code validation
Ability to study of complex flow phenomena that cannot be assessed in computational codes
Ground testing has historically, is currently, and will continue to be a critical part of the design of hypersonic vehicles, alongside computational techniques and flight testing.
Combined cycle engine tested @ NASA Glenn 10 x 10 ft. supersonic wind tunnel
Hypersonic Ground Demonstrator Engine No. 2 tested @ NASA Langley 8 ft. high-temperature tunnel

## Slide 13: Key hypersonic testing facilities @ NASA Langley

## Slide 14: 8-Ft. High-Temperature Tunnel: Free-jet testing
GROUND TEST
FLIGHT
Air flows through and around the model
Facility nozzle exit conditions match flight freestream or inlet entrance conditions
Complete “tip to tail”, propulsive flowpath when facility is large enough
Pre-flight verification of complete flowpath, engine subsystems

## Slide 15: 8-Ft. High-Temperature Tunnel: Free-jet testing
Heated by methane-air combustion
Total temperature: 1640 – 3560 R (1180 – 3100 deg. F)
Total pressure: 160 - 2000 psia (10.9 – 136 atm)
Multiple facility nozzles: Mach 4, 5, 7 (8’ diameter exit), Mach 3, 5 (4.5’ diameter exit)
Test section is 14 ft. long
Run duration up to 3 minutes (but only 2-3 runs per week)
March 1994
June 1999
Sept 2002

## Slide 16: Arc-Heated Scramjet Test Facility: Semi-free-jet
GROUND TEST
FLIGHT
Air flows through and around the model
Facility nozzle exit conditions simulate conditions near the inlet entrance
Model of the partial flowpath
Flowpath / engine component development and verification

## Slide 17: Arc-Heated Scramjet Test Facility: Semi-free-jet
Multiple facility nozzles: Mach 2.2, 3.5, 4.7, or 6.0
Heated by electric arc-jet discharge (total temperatures up to 4540 deg. F)
94’ long (37’ inside, 57’ outside) with 4’ x 11’ cylinder test section
Run times up to 5 minutes with 5 – 10 runs / day
Rectangular-to-Elliptical Shape Transition (REST) inlet installed
Hyper-X Engine Module: hypersonic technology development leading up to the X-43

## Slide 18: Direct-Connect Supersonic-Combustion Test Facility: Direct-connect testing
FLIGHT
Sub-component(s) of internal flowpath directly bolted to nozzle exit
Facility nozzle exit conditions simulate component entrance conditions
Component operability and performance verification
GROUND TEST

## Slide 19: Direct-Connect Supersonic-Combustion Test Facility: Direct-connect testing
Interchangable nozzle usually designed with the test article to match the cross-sectional shape and achieve the desired Mach number
Heated by hydrogen-air combustion (total temperatures up to 3340 deg. F)
Run times up to 15 minutes
5-20 runs / day
DCR in DCSCTF

## Slide 20: Isolator Dynamics Research Laboratory (IDRL)
Direct-connect facility for fundamental research on isolators
  Investigate shock wave structure and dynamics related to isolator stability / unstart
  Flow control methods to improve isolator performance
  Test-bed for laser diagnostics and advanced measurement techniques
  CFD code validation
Inlet
Combustor
Nozzle
Flow
Isolator
Scramjet = Supersonic Combustion Ramjet

## Slide 21: Instrumentation and Test Techniques
Pressure transducers
Oil flow
Laser diagnostics
Phosphor thermography
Schlieren /shadowgraph
Pressure and temperature sensitive paint

## Slide 22: My path to NASA Langley
Undergraduate @ U. Maryland (College Park, MD)
  Summer internships at Arnold Engineering Development Complex Tunnel 9 (White Oak, MD)
  AIAA Student conferences
Masters & PhD @ U. Michigan (Ann Arbor, MI)
  More AIAA conferences: Scitech, Aviation, Propulsion & Energy
  Summer fellowship at the Air Force Research Lab (Dayton, OH)
  NASA Pathways Program

## Slide 23
NASA Internships, Fellowships and Scholarships (NIFS) (https://www.nasa.gov/langley/education/internships)
  For high school to graduate school students
  Various sessions during the course of the year (summer, fall, spring)
  Program tries to match student and researchers interests
NASA Fellowships
  (https://www.nasa.gov/stem/fellowships-scholarships/index.html)
  For graduate students (Masters or PhD)
  Applications accepted once a year
  Fully funds tuition, stipend, health insurance, etc.
Pathways (https://www.nasa.gov/careers/pathways-program)
  For current students and recent graduates
  Sort of a co-op program with easy path to convert to full time civil servant position
  Exposure to NASA research during time at sponsoring org.
  Time at school can count towards service time
Student programs at NASA

## Slide 24: Dr. Robin Hunt Research Aerospace Engineer Hypersonic Airbreathing Propulsion Branch NASA Langley Research Center
Questions? Comments?