## Slide 1: Preliminary SnowSAR Results from SnowEx 2017
Edward Kim1, Jiyue Zhu2, Leung Tsang2, Do-Hyuk “DK” Kang1,3 and A. Coccia4
1NASA Goddard Space Flight Center, Greenbelt, MD 20771, USA
2 Radiation Laboratory, Department of Electrical Engineering and Computer Science, The University of Michigan, Ann Arbor, 48109-2122 MI USA
3ESSIC, University of Maryland, College Park, MD, 20740, USA
4MetaSensing, DKNoordwijk, 2201, The Netherlands
SnowEx 2017 central question:
How is SWE retrieval by volume scattering radar affected by forest?

## Slide 2
SNEX17_SnowSAR_20170221174335
Example 2017 data
SnowSAR observations from SnowEx 2017:
  X- (9.6 GHz) and Ku- (17.2GHz) bands
  full polarizations (VV, HH, VH, HV)
Flights: Feb. 16, Feb. 18, Feb. 21, and Feb. 22, 2017
  Most of the data from Feb. 21
pixel index
pixel index
Sigma0 in dB
SnowSAR Ku-band backscatterer (sigma-0) image. VV polarization. Feb 21 2017 at 20:23 UTC. White linear streaks on lake are snowmobile tracks.

## Slide 3
Backscatter of forest area larger than that of open land
Backscatter at open land close to the Gaussian distribution, while more complex at forest areas
Backscatter difference: forest and open areas
Check out SNEX17_SnowSAR data at NSIDC

## Slide 4
Most Ku band data located between -16 dB to -10 dB
Most of X band data -22 dB to -10 dB
Mean grain size:0.4 mm
X band simulations
Ku band simulations
Radar data
rms height= 0.5 cm,
OH for surface scattering,
snow depth 1.4m
For grain size of 0.4 mm
Ku band: total -10 dB, surface -14 dB, vol -12 dB
X band: total -14 dB, surface -14.5 dB, vol -22 dB
Ku band backscatter expected mainly from snow volume scattering
X band backscatter expected mainly from surface scattering
EM Simulation & SnowSAR Data are Consistent
Check out SNEX17_SnowSAR data at NSIDC