## Slide 1: Low NOx Fuel-Flex Combustor Summary Report
Brief Summary of Completion / Accomplishment:
Combustion and emissions testing of United Technologies Research Center’s (UTRC’s) small core combustor in NASA GRC’s CE-5 flametube test facility comprising of LTO and cruise conditions has been completed. Sufficient NOx emissions data was collected to formulate correlation equations for assessing reductions in NOx for LTO against CAEP/6 and cruise against 2005 best-in-class. Back-to-back testing of Jet-A fuel and a 50/50 blend of Jet-A with an alternative fuel demonstrated a measurable effect of fuel composition on non-volatile particulate matter emissions. Post-test analysis indicates LTO NOx emissions >80% below CAEP6 in UTRC single-sector tests of small-core N+3 combustor.
Documentation describing N+3 combustor concept selected, design approach, initial flametube test & analysis results; and preferred concept recommended for higher fidelity research has also been completed. This Lean Burn combustor concept shows potential to meet/exceed NASA’s Far Term LTO NOX reduction goals, but further investigation of dynamic characteristics of the combustor concept are required to ensure good operability over the entire flight regime conditions.
Beginning TRL 1, Final TRL 3

## Slide 2: Low NOx Fuel-Flex Combustor Publications
Publication Title / Description | Conference(s) Where presented
He, Z; Combustion Dynamics and Fuel Pressure Modulation with a Three-Cup Third-Generation Swirl-Venturi Lean Direct Injection Combustion Concept | 2019 SciTech Conf
Kumud et al; CFD Predictions of N+3 Cycle Emissions for a Three-Cup Gas-Turbine Combustor | AIAA Prop and Energy conf, Cinci
Hicks, Y.R et al; Flame Tube Testing of a GEA TAPS Injector: Effects of fuel staging on combustor fuel spray patterns, flow structure, and speciation | 6/18/2018 : JPC paper
Tacina, K.M et al; A Third-Generation Lean Direct Injection Combustor with a Pre-filming Pilot Injector | ASME Turbo Expo, June 2019, Phoenix, AZ
Tacina, K.M ; Lean Direct Injection Combustor Development at NASA Glenn Research Center | ASME Turbo Expo, June 2019, Phoenix, AZ
Tacina, H.M; A Third-Generation Swirl-Venturi Lean Direct Injection Combustor with a Prefilming Pilot Injector | ASME Turbo Expo, June 2019, Phoenix, AZ
Pilot Injector Redesign to reduce N+3 Cycle Emissions for a Gas-Turbine Combustor | AIAA, August 19-22, 2019, Indianapolis, IN
Podboy, Derek P., NASA GRC Particulate Emissions Sampling System Lessons Learns | AEC Aviation Roadmap Mtg - 5/21-24/19.
Zhuohui J. He and Derek Podboy, Emission Characteristics of an Axially Staged Sector Combustor - Abstract | AIAA Scitech Forum 2020, Jan 6-10, 2020
Tacina, K, Podboy, D., Dam, B., Lee, F., “A Third-Generation Swirl-Venturi Lean Direct Injection Combustor with a Prefilming Pilot Injector,” GT2019-90484, ASME Turbo Expo 2019, June 17-21, 2019, Phoenix AZ, USA. | ASME Turbo Expo, June 2019, Phoenix, AZ. June 17-21/19.
Ajmani, K., Lee, P., Chang, C., Tacina, K., “Pilot Injector Redesign to Reduce N+3 Cycle Emissions for a Gas-Turbine Combustor,” AIAA-2019-4371, AIAA Propulsion & Energy Forum & Exposition, August, 2019, Indianapolis, IN, USA. | AIAA Propulsion & Energy Forum & Exposition, August, 2019, Indianapolis, IN, USA.

## Slide 3
N+3 Low Emissions – Fuel Flexible Combustor Concept
Problem
Fuel flexible, Small Core, High OPR (50+) engines present greater challenges to combustor emissions and operability
Objective
Develop and demonstrate (to TRL 3) a low-emissions, fuel-flexible, small-core compatible combustor architecture that reduces LTO NOx 80% below CAEP/6 and cruise NOx 80% below 2005 best-in-class.
Results
Developed small-core lean-burn combustor technology for propulsion engines in efficient N+3 aircraft such as the D8 concept aircraft.
Completed emissions testing of small core combustor in CE-5 covering LTO and cruise conditions.
Completed testing using Jet-A and a 50/50 blend of Jet-A / Alternative fuel (Gevo Alcohol-to-Jet). Demonstrated equivalent combustor performance and the effect of fuel composition on non-volatile particulate matter emissions.
Demonstrated LTO NOx emissions >80% below CAEP6 in UTRC single-sector tests of small-core N+3 combustor.
Significance
Lean Burn combustor concept shows potential to meet/exceed NASA’s Far Term LTO NOX goal. But further investigation of dynamic characteristics of the combustor concept are required to ensure good operability over the flight conditions
Emissions goals achievable with small core compatible combustor
Summary of Emission Results