## Slide 1: SLS Evolution: Comparing Configurations Using System Exergy
16-November-2020
Terry Haws
Joshua Zimmerman
Michael Fuller
Dr. Michael Watson

## Slide 2: Introduction
Space Launch System (SLS) is the keystone of the NASA Moon/Mars campaign
SLS is evolving to improve performance
Compare the evolution using Exergy Analysis

## Slide 3: Approach to Moon and Mars Exploration
Image courtesy of NASA
SLS is a keystone of Moon and Mars Exploration plan
Notes: SLS enables science and human exploration of lunar surface and eventually mars
SLS is the keystone in a stepwise approach to get to mars

## Slide 4: SLS Evolutionary Path
RS-25 Engines
Core Stage
Interstage
Evolved
Boosters
Exploration Upper Stage
Orion
Launch Abort System
Launch Vehicle
Stage Adapter
Interim Cryogenic
Propulsion Stage
8.4m Fairing
Long (Up to 90’)
Solid
Rocket
Boosters
Core Stage
Interstage
Exploration Upper Stage
8.4m Fairing
Short (Up to 63’)
Universal
Stage Adapter
Core Stage
Interstage
Exploration Upper Stage
SLS Block 2 Cargo
SLS Block 1B Cargo
SLS Block 1B Crew
SLS Block 1 Cargo
SLS Block 2 Crew
RS-25 Engines
SLS Block 1
5m Class Fairing
(up to 63’)
Universal
Stage Adapter
Solid
Rocket
Boosters
RS-25 Engines
RS-25: 16 remaining from Shuttle program. After 4 flights, transition to new build RS-25.
Boosters: 8 flight sets of steel cases remaining from Shuttle program. After 8 flights, transition to BOLE.
EUS: Larger stage, more propellant, four engines
Sources: graphics courtesy NASA
New generation RS-25
Reduce costs
Certify to a higher thrust level
Simplify design
Utilize advanced manufacturing techniques – including 3-D printing
Booster Obsolescence and Life Extension (BOLE)
Composite cases
Updated insulation
Updated propellant
Optimized grain design
Optimized nozzle

## Slide 5: Exergy Explained
What is exergy? Let’s start with energy:
Example: Energy of a Rocket
Turn chemical energy into potential energy (altitude) and kinetic energy (velocity)
And that’s what orbit is – altitude and velocity
Sitting on the pad, full of fuel, the rocket has available chemical energy
If the rocket was perfectly efficient, all the chemical energy would be converted into potential or kinetic energy.
Potential Energy
Propulsion Exergy
Kinetic Energy
But of course it isn’t …

## Slide 6: Exergy Explained
What is exergy?
  Definition: The maximum useful work which can be extracted from a system as it reversibly comes into equilibrium with its environment.
Rocket experiences losses: gravity, atmosphere, pointing, etc.
The useful work turns into mass delivered to orbit
Rocket starts with maximum available work from propellant
Those losses do not turn into useful work.
This results in destroyed exergy.
)
Useful work (exergy)
Potential Energy
Propulsion Exergy
Kinetic Energy
Atmosphere
TVC/Pointing
Gravity

## Slide 7: Exergy Analysis Applied
How does it apply to launch vehicle design and analysis?
  Exergy analysis provides a way to measure the system efficiency of launch vehicles
Integrates all of the system’s thermodynamic properties
Combines all aspects of vehicle efficiency into one equation
Exergy efficiency can be plotted against time across the entire trajectory
Allows comparison of multiple vehicle configurations and determine where efficiency is being lost
More instructive to plot versus ideal velocity for better comparison
Timing of different rocket configurations can be very different, hard to compare versus time
Vehicles to similar orbits should have similar ideal velocities, making comparison easier
Allows comparison of solids and liquids, different number of stages
Rocket images courtesy NASA: https://www.nasa.gov/images/content/125306main_rocket%20chart.jpg
Provides a variable to compare very different vehicles

## Slide 8: SLS Block 1B Example
Sitting on pad
Max Q
Booster jettison
LAS jettison
Core jettison
Orbit
Departure burn
Sitting on pad
Max Q
Booster jettison
LAS jettison
Core jettison
Orbit
Departure burn
EUS jettison
Sitting on the pad:
Hasn’t burned any propellant, hasn’t done any work
η =1
Ascending:
Burning propellant, increasing kinetic and potential energy
Booster jettison:
Kinetic energy of the boosters is now wasted – causes drop in efficiency

## Slide 9: Comparing SLS Crew to TLI
Legend SLS Block 1
SLS Block 1B
Blk 1 booster generating more ΔV than Blk 1B
Core goes to orbit – results in much bigger loss
EUS is bigger  bigger loss
More efficient
Less efficient
Core providing much more velocity
Having an upper stage is more efficient than just an in-space stage
Orbit
Payload:
23.9 mT
36.0 mT
Efficiency shows core burns longer than optimal

## Slide 10: Comparing SLS Crew to TLI
Legend SLS Block 1B
SLS Block 2
BOLE booster provides more impulse  more efficient
Efficiency gain can be seen throughout trajectory
Overall more efficient
Booster burnout
Core burnout
Adding booster impulse increases system efficiency

## Slide 11: Comparing Block 1B Missions
Legend Lunar Mission
Jupiter/Europa
Saturn/Titan
Lighter payloads lead to greater efficiency at core burnout
Upper stage producing departure energy
Very similar through booster burn
Core inert is larger proportion of mass, leads to greater loss of efficiency
Outer planet missions use all the propellant to deliver a small payload  lower efficiency
Payload:
40.8 mT
6.8 mT
2.9 mT

## Slide 12: Comparing SLS Cargo to Europa
Legend SLS Block 1
SLS Block 1B
SLS Block 2
Payload:
2.8 mT
6.8 mT
8.3 mT
Slope of in-space curve shows ICPS is more efficient
Block 2 is most efficient, delivers the most payload
Block 1 is least efficient
Block 2 is the most efficient of the configurations

## Slide 13: SLS Block 1 to Europa – Add Kick Stage
Legend SLS Block 1
SLS Block 1 with STAR 48B
Payload:
2.8 mT
3.9 mT
STAR 48B is less efficient (slope) due to lower Isp
But staging the ICPS leads to better overall efficiency
Adding a kick stage is more efficient, delivers more payload

## Slide 14: Conclusions
SLS Evolution Analyzed Using Exergy Analysis
Conclusions
Having an upper stage (Block 1B) is more efficient than not (Block 1)
Having more impulse in the boosters (Block 2) is more efficient
Allows for an assessment of staging, bringing together the effects of the staged elements’ mass and Isp
Higher thrust engines are indicated for the EUS, shown by the slope in these plots
ICPS is more efficient as an in-space, having a much flatter exergy efficiency curve
Various configurations – crew and cargo; Block 1, Block 1B, Block 2; with and without a kick stage
Various destinations – TLI, Europa, Saturn
Staging, while causing a big drop in efficiency, helps overall system efficiency
Adding a kick stage is more efficient than doing the mission with the upper stage as departure stage
Indicates where the optimum cut off of a stage is, pointing to future improvements in vehicle configurations
Efficiency and payload appear to be correlated