## Slide 1
Aerospace Flutter & Dynamics Council - 2020 Fall Meeting
10/13/2020
Natalie Spivey, Samson Truong & Roger Truax
Structural Dynamics Group
NASA Armstrong Flight Research Center
X-57 Mod II Aircraft GVT

## Slide 2: Outline
2
X-57 Background
Mod II Wing Ground Vibration Test
  Objectives
  Test Setup
  Test Configurations
  Soft Support System
  Results
Other X-57 Aeroelastic Work
  Mod II FEM Correlation
  Mod II Flutter Analysis
  Mod II Flight Testing
  Mod III Wing Ground Vibration Test

## Slide 3: X-57 Background
Ultimate goal of the final X-57 modification is to demonstrate a 500% increase in high-speed cruise efficiency, zero in-flight carbon emissions, and 15 dB reduction in noise levels
3

## Slide 4: X-57 Mod II Background
4
X-57 Mod II Aircraft  2,780 lbs
X-57 Mod II aircraft is the Mod I baseline Tecnam P2006T aircraft redesigned with two electric motors powered by traction batteries
Mod II Modifications
  Added: Cruise Motors/Mounts (adapters, trusses), Propellers/Hubs, Cruise Motor Controllers (CMCs) Traction Batteries and Air Data Probe
  Electric motors mounted onto motor adapters and truss which has the new CMCs and then mounted onto the existing firewall
Motor Mount Truss
CAD of Motor Mount Truss, Adapter, Motor, Hub, Props & Spinner
Existing Firewall
Air Data Probe
Fwd Batteries
Traction Batteries
Aft Batteries

## Slide 5: X-57 Mod II Ground Vibration Test
5
X-57 Mod II Ground Vibration Test (GVT) conducted at NASA Armstrong from Nov – Dec 2019
  Goal: Gather modal data of a near flight ready configuration to correlate and validate the Mod II aircraft beam finite element model (FEM) to the GVT results
  Two boundary conditions were tested:
    Free-Free: Aircraft on soft support system to simulate free flight conditions
    On-Tires: Aircraft on-tires to characterize on-ground modes for future aircraft ground motor testing safety clearance and taxi tests
X-57 Mod II GVT, Conducted at NASA Armstrong Fall 2019
Right Electric Cruise Motor
https://www.youtube.com/watch?v=wsjdk790JlI

## Slide 6: X-57 Mod II GVT - Test Objectives
Primary Objective: Capture modes that are part of the aircraft predicted flutter & whirl flutter mechanism
Secondary Objective: Capture fuselage lateral bending & torsion modes, wing modes, and landing gear modes
Tertiary Objective: Capture higher order wing modes and control surface modes
Primary Objective | Reasoning
Stabilator Rotation Fuselage 1st Vertical Bending (F1VB) | Modes predicted in pre-test FEM that were part of Classical Flutter Mechanism
Motor Assembly Vertical Bending Motor Assembly Lateral Bending | Modes predicted in pre-test FEM that were part of Whirl Flutter Mechanism
Aircraft Rigid Body Modes | To characterize soft support system effectiveness
6

## Slide 7: X-57 Mod II GVT – Test Setup Overview
7
Nose Gear Bulkhead Soft Support
A-Frame for Nose Gear Soft Support
Lt MLG Soft Support
Lt Wing Shaker
X-57 Mod II GVT Test Setup on Soft Supports

## Slide 8: X-57 Mod II GVT – Traction Batteries
Traction batteries for electric motors compose nearly 1/3 of aircraft weight
Due to battery safety concerns, GVT used battery simulators mounted on fuselage floor with new battery mounts at a forward & aft location (previous backseat & cargo area, respectively) behind the pilot
  Battery simulators were designed to match weight & CG of actual hardware
  Battery power cables were connected to the simulators
Fore and aft traction battery vent covers and hoses to the aft cockpit roof exterior were installed for GVT
Two flight battery control modules (BCM) were not ready for GVT, so BCM mockup units were similarly mounted & ballasted
8
Fwd Batteries
Aft Battery Simulators
Aft Batteries
Fwd Battery Simulators
Fwd Batteries & Instrumentation Pallet
Battery Vent Covers & Hoses
Mockup BCM

## Slide 9: X-57 Mod II GVT – Locking Devices
Locking devices were used to constrain control surfaces which can dominate the desired structural modes, unless the control surfaces was the mode of interest
Stabilator (stab) counterweight block was used to simulate the stabilator as it would be for steady level flight to counteract the aerodynamic forces
  Majority of test runs had stab block removed, which caused stabilator to rotate down slightly
Yoke & pedal locks used to simulate pilot contact with the yoke & pedals for steady level flight as well as to prevent motion in the control surfaces
9
Rudder & Rudder Trim Tab Gust Locks
Aileron Gust Locks
Stab Counterweight Block
Stabilator Trim Tab Gust Lock
Cockpit Locks

## Slide 10: X-57 Mod II GVT – Finite Element Model (FEM)
X-57 Mod II FEM is a highly modified version of original Tecnam P2006T FEM provided by the manufacturer
  Due to proprietary nature of the original FEM, Mod II pre-test FEM comparisons to GVT results are not shown in this presentation
Aircraft primary structure, control surfaces and electric motors are modelled by elastically equivalent beams while retaining the same mode shapes and frequencies
Wing and fuselage are rigidly connected
Stiff beams and springs used for visualization
10
X-57 Mod II FEM

## Slide 11: X-57 Mod II GVT - Test Configurations
Free-Free: On Soft Supports
  To simulate free-free boundary condition flight and to separate the aircraft rigid body modes from its elastic modes
  Multiple tests were conducted on the aircraft at a variety of different shaker locations in order to excite the target modes
  Yoke & pedals were locked for the most part, except for one test case that when the yoke was free in order to excite the Stab Rotation mode
  Gust locks on the aileron and rudder, as well as the stab counterweight, were either installed or removed from time to time depending on the target mode to be excited
On-Tires
  To verify the taxi ground modes prior to flight and cross-check with the on soft support modes for any significant differences
  Also to obtain the baseline characterization of the motor assembly modes for safety clearance of near-term ground motor testing before flight
  Yoke & pedals were locked, all gust locks were removed, and stab counterweight was off
  For the motor test, aileron & rudder gust locks were installed as well as the stab counterweight
Additional last minute configuration was added during the GVT by exciting on the A-Frame lifting device directly in order to ensure there was no coupling to the aircraft modes of interest
11

## Slide 12: X-57 Mod II GVT - Test Matrix
12

## Slide 13: X-57 Mod II GVT - Soft Supports
To create the GVT Free-Free boundary condition, the Mod II aircraft was suspended around the nose bulkhead with the 2-ton A-Frame (via a single bungee, chain hoist, & lifting strap) and at each of the main landing gears (3 bungees on each MLG suspended on bungee support beams supported by two 5-ton jacks)
MIL-C-5651B, Type II bungees (1080HD loops) produced by SBC Industries (Huntsville, AL)
  Bungees were characterized prior to GVT  1 Hz
Aircraft modes did not couple with soft supports
Soft support system eliminated the need for overhead crane support and a critical lift
Soft supports easy & efficient to come on/off – took crew  10 minutes
Used same bungees throughout GVT with no need to swap out any bungees
13
1080HD Bungee Loop
X-57 Soft Support System

## Slide 14: X-57 Mod II GVT - Fuselage Nose Soft Support
Single bungee attached to chain hoist hook, and top of lifting strap, using two 6.5-ton shackles
Lifting strap wrapped around aircraft nose bulkhead
High-friction material placed in between lifting strap and fuselage surface to guard against slippage
A-frame wheels chocked using shot bags and mechanical wheels locked to prevent castoring
Nose wheel remained on and nose gear strut unlocked
14
X-57 Nose Soft Support

## Slide 15: X-57 Mod II GVT - Main Landing Gear Soft Support
15
X-57 Main Landing Gear (MLG) Soft Support
Two 5-ton Regent Model 985S jacks were positioned on each side of the aircraft around the axle and interfaced to the MLG soft support beam
Three bungee loops were linked between the jack soft support beam to MLG axle
MLG soft support setup was duplicated on both axles

## Slide 16: X-57 Mod II GVT - GVT Equipment
16
Accelerometers (100 mV/g)
  PCB T356A16 triaxial accels
  PCB T333B32 uniaxial accels
  PCB T333B uniaxial accels
Excitation System
  Shaker: MB Dynamics Electromagnetic Modal 110, 3 qty
Data Acquisition (DAQ) system: Brüel & Kjær LAN-XI DAQ
  Mainframes – Daisy chained together thru network switch
    LAN-XI 11-slot Main frame, 2 qty
    LAN-XI 5-slot Main frame, 2 qty
  Modules - Capable of recording 344 channels
    LAN-XI 4-ch Input + 2-ch Output 3160 Module, Qty 2
    LAN-XI 12-ch Input 3053 Modules, 27 qty
    LAN-XI 6-ch Input 3060 Modules, 2 qty
GVT Software
  BK Connect
    PCB T356A16
    Triaxial Accel
B&K LAN-XI Main Frame
LAN-XI Module
MB Modal 110 Shaker
    PCB T333B32
    Uniaxial Accel
    PCB T333B
    Uniaxial Accel

## Slide 17: X-57 Mod II GVT – LAN-XI DAQ Setup
17
LAN-XI DAQ Aft Aircraft Setup
For MLG soft support & aft aircraft accels
LAN-XI DAQ Fwd Aircraft Setup
For fwd aircraft accels & A-frame
LAN-XI DAQ frontend setup: Four mainframes (two 11-slot & two 5-slot) capable of driving 4 shakers & recording 344 channels with network switch daisy chaining modules
  Fwd aircraft setup
    MF#1: two source module (3160) & nine 12-channel input module (3053)
    MF#2: eleven 12-channel input module (3053)
  Aft aircraft setup
    MF#3: five 12-channel input modules (3053)
    MF#4: three 12-channel input modules (3053)
MF #3
MF #4
MF #2
MF #1
Network Switch

## Slide 18: X-57 Mod II GVT – Shaker Setup
18
Motor Prop Hub
Right Wingtip
Vertical Tail
Aft Fuselage
Main Landing Gear

## Slide 19: X-57 Mod II GVT – Accelerometer Locations
19
Left Side View
Front View
Top View
Free-Free
  127 accelerometer locations measuring 318 degrees of freedom (DOF)
On-Tires
  Soft support accelerometers removed
  113 accelerometer locations measuring 276 DOF
X-57 Mod II GVT Accel Locations

## Slide 20: X-57 Mod II GVT – Test Display Model
Test Display Model (TDM) was created in BK Connect using a combination of quad & triangular elements and trace lines for Nose Boom, MLG, Fwd/Aft Batteries & A-Frame
20
Additional elements added to motors during post-processing to better capture the behavior of the motor modes
Motor Model Modified Post-Test
X-57 Mod II Aircraft GVT Model
Rt MLG Soft Support
MLG Area (Looking Fwd)
MLG
Lt MLG Soft Support
Fwd Battery
Aft Battery
Nose Boom
Fuselage Nose
A-Frame Soft Support

## Slide 21: X-57 Mod II GVT – Aircraft Results
21
Aircraft results will focus on comparisons of the two main setups: Free-Free vs. On-Tires
  Stab counterweight block removed and cockpit locks (yoke & pedals) on
GVT results performed in BK Connect with different parameter estimation techniques
  Primarily used Polyreference Time method which helped in dictating how much time after the peak response to include in the curve fit calculation
Many modes were found during the GVT that were missing in the pre-test FEM
Asymmetries were seen between the left and right sides of the vehicle, particularly in the control surfaces, and was seen in all of the test configurations
GVT modes for On-Tires setup do not necessarily follow the order in the Free-Free setup, with several of them not observed or missing
Several modes from the Free-Free setup are coupled together in the On-Tire setup case

## Slide 22: X-57 Mod II GVT – Aircraft Results (cont.)
22
Mode names highlighted in blue were not predicted with pre-test FEM and frequency differences of over 5% are highlighted in red

## Slide 23: X-57 Mod II GVT – Free-Free Mode Shapes
23

## Slide 24: X-57 Mod II GVT – Free-Free Mode Shapes
24

## Slide 25: X-57 Mod II GVT – Free-Free Mode Shapes
25

## Slide 26: X-57 Mod II GVT – Motor Results
26
Motor results will focus on comparisons of the two main setups: Free-Free vs. On-Tires
  Stab counterweight block installed, all control surfaces locked and cockpit locks (yoke & pedals) on
Post-processing a bit tedious as motion from the wings and control surfaces tend to dominate over any motion from the motor assemblies
Motor modes fell between 29 – 35 Hz for both setups, with the anti-symmetric motor lateral mode being the most different between setups
Similar to the aircraft results, asymmetries were observed again between the left and right motor assemblies
Tight clearance around the motors prevented installation of additional accelerometers to capture any of higher-order lateral and vertical motor modes

## Slide 27: X-57 Mod II GVT – Motor Mode Shapes
27
Lateral Motor Modes
Vertical Motor Modes

## Slide 28: X-57 Mod II GVT – Rigid Body Results
28
Aircraft rigid body tests were performed while the aircraft was installed on soft supports in order to identify the approximate frequencies of the 6 different rigid body modes and to evaluate the frequency separation between the highest rigid body mode (1.06 Hz) and the first aircraft elastic mode (7.83 Hz)
Manual excitation was provided from test engineers and shakers were not used for rigid body tests

## Slide 29: X-57 Mod II GVT – Rigid Body Video
29

## Slide 30: X-57 Mod II GVT - Summary & Path Forward
GVT assisted in understanding Mod II vehicle’s modal characteristics
Pre-test FEM did not capture all modes that appeared in GVT
Asymmetries were present on both sides of the aircraft and were particularly visible in the control surfaces and motor assemblies
On-Tires config. showed some coupling of modes that were not seen in the Free-Free config.
Follow-on tasks include:
  Updating post-test Mod II FEM to match the GVT results
  Performing both Mod II classical and whirl flutter analyses to verify flight envelope flutter margins
  Prepping for Mod II flight testing next year  Spring/Summer 2021
30

## Slide 31: X-57 Other Aeroelastic Work
31
X-57 Mod II FEM Correlation
X-57 Mod II Flutter Analysis
X-57 Mod II Flight Testing
X-57 Mod III Wing Ground Vibration Test

## Slide 32: X-57 Mod II FEM Correlation
32
Mass and CG correlation/scrub, 90% complete
  Project CAD, weight and balance
  Flight configuration mass and CG correlation
    Individual primary structure (wing, fuselage, stab, vertical tail, winglets, ailerons, rudder)
    Non-structural mass and mass moment of inertias (secondary structure, batteries, electronics, wiring…)
  Remove/add mass for GVT configuration
    Remove tires, main gear doors, motor cowlings, nose cover…
    Add cockpit and control surface constraints
Modal frequency and shape correlation, following mass correlation
  Free-free FEM to soft support GVT results
  Adjust existing modes, introduce new modes (wing rock, stab roll/yaw)
  Create simple nose boom beam
  Modify beam element stiffnesses (bending, torsion, yaw)
  Modify point spring stiffnesses (control surface rotations)
  Start with primary large structure (W1B, F1B, F1T, W1T, Wing Rock)
  Proceed to control surfaces (stab roll/yaw, stab rotn, aileron and rudder rotations)
  Iterate to 5% frequency difference for primary modes, visual mode shape comparisons
X-57 Mod II FEM

## Slide 33: X-57 Mod II Flutter Analyses
33
Classical aircraft flutter analysis
  ZAERO Linear Panel Model using Matched Point Solution
  Mach 0.3
  ~25 Total Modes Used, Up to ~60 Hz
    Perfect Rigid Body Shapes, 0.0 Hz Each
    Cockpit controls “Fixed” FEM (Not Free)
    2% Structural damping crossing
  Expecting similar results outside of flight envelope
    Fuselage weight sensitivity, hump modes
  Not expecting results inside of flight envelope
    Flying fleet is aeroelastically incident-free
Whirl flutter analysis
  Using CAMRAD II as analysis tool
  No instabilities currently indicated for Mod II
  Analyzing isolated motor+motor mount system as well as coupled with full vehicle
  Preliminary analyses show large whirl flutter margins even with large parametric variations
  Updating motor FEM using GVT data to include 2nd pitch and 2nd yaw modes of motor mount systems
X-57 Mod II
ZAERO Aerodynamic Model
Flutter Mechanism
Stab Rotation & Fuselage 1st Vertical Bending

## Slide 34: X-57 Mod II Flight Testing
34
Mod II Flight Testing Objectives
  Clear flight envelope for later research flights
  Clear flight for potential emergency descent maneuver (high velocity, negative AOA)
Taxi Testing
  Low and high speeds
    Motor RPM buildup
    Blade pitch angle variations (automatic with airspeed & RPM)
    Up to just below Vr (aircraft rotation velocity)
Flight Testing  Spring/Summer 2021
  One flight altitude (4k or 6k ft MSL)
    Dynamic pressure and Mach variations are limited from top to bottom of envelope
  Dynamic discipline test points
    Two flights, repeat previous high test point - flight time limitation
      1st flt: 100, 120, 140, 150 KCAS
      2nd flt: 150, 160, 170 KCAS
        Note: Vne is 172 KCAS, Velocity never exceed (Vne)
    Control surface raps (sharp input): pitch, roll and yaw
    Real-time visual analysis of flutter stability (response decay time)
      Limited flight time
      Post-flight data analysis will be more extensive
  Atmospheric and local turbulence
    Excite higher frequencies above limitation of raps
    Aerodynamic discipline test points (211, POPU, beta sweep, wind turns, prop wind milling, decel/accel in higher turbulence, tower flyby)
    Loads discipline test points (wind up turns)
X-57 Mod II
Flight Accelerometers
17 Accel Locations with 23 DOFs

## Slide 35: X-57 Mod III Wing Ground Vibration Test
35
X-57 Mod III Wing GVT conducted at NASA Armstrong in June 2019
  Goal: Gather X-57 Mod III wing modal data to correlate the fundamental wing modes to the FEM without any complicated wing structure
  Objectives: Measure & characterize the target modes to understand the wing’s aeroelastic behavior
  Benefits
    Early characterization of basic Mod III Wing structure for FEM updates
    Early update to classical and whirl flutter analysis
    Reduces programmatic risk, otherwise would have been added to later GVTs, thus complicating future test efforts
  GVT Configurations
    Config. A: Clean Wing + Cruise Nacelle Simulators
      Conf. A: Flaps Stowed, Ailerons Locked
      Conf. A: Flaps Deployed, Ailerons Locked
      Conf. A: Flaps Slightly Deployed, Ailerons Locked
    Config. B: Clean Wing
      Conf. B: Flaps Stowed, Ailerons Locked
      Conf. B: Flaps Deployed, Ailerons Locked
NASA LaRC updated Mod III Wing FEM with GVT data
X-57 Mod III Wing GVT, June 2019
Config A
Clean Wing + Cruise Nacelle Simulators
Config B
Clean Wing

## Slide 36: Questions?
36
X-57 Mod II GVT
Test Team

## Slide 37
37
Backup Slides

## Slide 38: X-57 Mod III Wing GVT - Test Article
38
Wing Properties | 
AR | 15
MAC | 2.13 ft
Span (b) | 31.63 ft
Wing Area (S) | 67 ft2
λ | 0.7
ct | 1.74 ft
cr | 2.48 ft
WtClean Wing (includes H-Frame) | 313.5 lbs
WtClean Wing (H-Frame + Wingtip Plates) | 352.5 lbs
WtClean Wing + Cruise Nacelles (×2) | 581.5 lbs
WtCruise Nacelle (×1) | 134 lbs
Note: Based on April 2019 weights from ESAero
X-57 Mod III Wing
Wingtip Plate for Mounting Cruise Nacelle Mass Simulator
Note: Plate was removed for Conf. B – Clean Wing test runs

## Slide 39: X-57 Mod III Wing GVT - Test Configurations
39
Configuration A: Clean Wing + Cruise Nacelle Simulators
  At the time of the GVT, the cruise nacelle motors were not fabricated yet and as a result, mass simulators were used to simulate the mass & CG of those cruise motors.
Cruise Nacelle Mass Simulator with Wingtip Mounting Plate
FEM for Config A
Conf. A: Clean Wing + Cruise Nacelle Simulators

## Slide 40: X-57 Mod III Wing GVT - Test Configurations
40
Configuration B: Clean Wing
  Mod III wing without any nacelles, motors, nor internal wiring
  Cruise nacelle mass simulators & mounting plates were removed after Config A testing was complete
Cruise Nacelle Mass Simulator Removed
FEM for Config B
Conf. B: Clean Wing