## Slide 1
Mars Ascent Vehicle Hybrid Propulsion Effort
George Story - NASA Marshall Space Flight Center
Ashley Karp and Barry Nakazono - Jet Propulsion Laboratory
Greg Zilliac - NASA Ames Research Center
Brian Evans - Space Propulsion Group
George Whittinghill - Whittinghill Aerospace
August 24, 2020
2020 AIAA Propulsion and Energy Conference
Presented to HSV AIAA
Oct 27, 2020

## Slide 2: Mars Sample Return and MAV
MAV
Pre-decisional. For planning and discussion purposes only.

## Slide 3: FY 14 Comparison of Systems (Shotwell 2016)
6.65kg Payload, 20cm Reference OS
 | Case 1 | Case 2 | Case 3 | Case 4 | Case 5 | Case 6 | Case 7 | Case 8 | Case 9 | Case 10
 | Solid-Solid G-G | Solid-Solid G-U | Solid-Liquid G-G | SSTO Monoprop | SSTO Pump BiProp | SSTO Reg. BiProp | SSTO Hybrid | Hyb-Hyb G-G | Hyb-Solid G-G | BiProp-BiProp G-G
Score | 0.60 | 0.54 | 0.32 | 0.52 | 0.79 | 0.76 | 0.76 | 0.621 | 0.52 | 0.57
GLOM | 176 | 158 | 237 | 276 | 182 | 187 | 166 | 173 | 157 | 190
Length | 1.88 m | 1.98 m | 2.09 m | 2.76 m | 2.04m | 2.29 m | 2.16 m | 2.78 m | 2.21 m | 2.84 m
AFT | -40 C | -40 C | +17 C | +8 C | -37 C | -37 C | -66 C | -66 C | -40 C | -37 C
GLOM – Gross Lift Off Mass
AFT – Allowable Flight temperature

## Slide 4: [FY15]Current Options Under Consideration (Shotwell 2016)
14kg Payload, 30cm Reference OS
 | Case 1a | Case 1b | Case 2a | Case 2b | Case 5 | Case 6 | Case 7
 | Solid-Solid G-G | Fixed Solid-Solid G-G | Solid-Solid G-U | Fixed Solid-Solid G-U | SSTO Pump BiProp | SSTO Reg. BiProp | SSTO Hybrid
Max OS | OS can grow up to ~ 30 cm diameter without fairing (stay under max case diameter) |  |  |  |  |  | 
GLOM | 318.8 | 341.5 | 274.1 | 297.1 | 255.0 | 269.8 | 219.1
Length | 2.64 m | 2.96 m | 2.51 m | 2.87 m | 3.21 m | 3.39 m | 2.89 m
AFT | -58 C | -58 C | -58 C | -58 C | -90/-44 C | -90/-44 C | -90/-66 C
(Temp limit if frozen, temp limit if not frozen)
GLOM – Gross Lift Off Mass
AFT – Allowable Flight temperature

## Slide 5: Hybrid Motor Overview
Hybrid motor is based off of the 2016 Point of Departure Review
  Updated for system level design changes and to incorporate results of recent analyses and testing.
The fuel is a wax based, liquefying hybrid fuel, developed for this application. (SP7 and the reduced regression SP7A)
  Burn rate is dependent on oxidizer mass flux (very weak dependency on pressure and temperature)
  Shear force from oxidizer creates instability (roll waves and droplets) in the fuel liquid layer, essentially acting as fuel injection system and increases burn rate over conventional hybrid fuels.
2016 PODR

## Slide 6: SPG Fuel Formulation
  Space Propulsion Group, Inc. worked to developed new fuel (SP7) for operation in Mars-like temperatures
  Tested paraffin (SP1) and SP7 with N2O (non toxic analog to MON) to determine performance and behavior of new fuel.
  Tested SP7 with MON-3
  Determined material properties of SP7, Matured processing of SP7, Initiated study into fuel/casing thermal mismatch
N2O
MON3

## Slide 7: SPG Full Scale
Testing indicated heat addition needed at the head end of the motor for combustion stability.
  Testing with Gox injection confirmed heat addition necessary.
SPG pursued a composite overwrapped motor design.
  Composite curing lead to a condition where the grain may not have been supported at ambient and cold conditions.
  Flight weight motor case design to support grain in work at end of program.

## Slide 8: Thermal Cycling of Fuel Core Samples
MSFC Results: Some debonding (case/core), no radial cracking
EDL
Winter
Spring
Summer
Average Test Results [Test Objectives] | EDL | Winter | Spring | Summer
Max Temperature, °C | 40.3 [50] | -82.7 [-90] | -41.9 [-44] | -24.0 [-22]
Min Temperature, °C | -99.3 [-105] | -102.8 [-105] | -56.7 [-64] | -41.8 [-45]
Max Gradient, °C | 12.5 [7.0-17.5*] | 7.4 [0.9-17.5*] | 6.2 [1.8-17.5*] | 7.0 [2.3-17.5*]
Max Ramp Rate, °C/hr | 7.6 [7.3-10.8] | 7.5 [0.8-10.8] | 5.9 [1.6-10.8] | 6.0 [2.0-10.8]
* Max gradient and ramp rate objectives include the range from the predicted gradient to the highest successfully tested gradient or ramp rate.
10 in
5 in
2.5 in
Notes: Preliminary thermal testing completed at JPL to establish thermal rate limit using 2 samples.
Completed 201 cycles at MSFC: 1 EDL cycle, 50 winter cycles, 100 spring cycles, and 50 summer cycles
  100 day test plan
  8 samples: four neat SP7, four aluminized SP7
Gradient limits in ERD came out of thermal test failures
Issues:
  2.5 inch thick samples, have not completed full length tests
  b/a of tested samples was 2 instead of 3.
  Some debonding was observed between the case and the fuel, but no radial cracking under Mars- like conditions.

## Slide 9: Solid Hypergolic Additives
Purdue incorporated hypergolic additives by grinding the SP7, mixing the hypergolic materials in and pressing the mixture into fuel segments for a two inch motor.
Multiple materials were successfully tested at ambient conditions, with several restarts of the motor after holds.
A hybrid motor test stand was built inside a vacuum chamber and ignited at a near Mars vacuum condition.
  At a higher flux, it did not ignite.
Later investigation studied integration into a larger motor.
  Separating the ignition and sustain functions.
2” motor test at Purdue
2” motor test repeated in a vacuum at Purdue

## Slide 10: MSFC Casting Effort
Early casting efforts
Pancake grains
Thermal Mass and end cooler grain attempts
Multi-segment Fuel Grains

## Slide 11: MSFC Casting Effort
Wax Melter and Oven
Lathe processing
Freezer process
Relearning Thermal Shock

## Slide 12: Whittinghill Aerospace
Motors A, B and C were tests with MON-25 and -20C Mars conditions
Motors B and C had ignition by a series of gates to quicken the ignition
Motors A and B had efficiency increasing devices
Motor C was a lighter weight version without all the efficiency increasing devices
Grains were assembled into the motor case at -20C for motor A and -40C for B and C
Nozzle material changes between tests

## Slide 13: WASP Motor B Video

## Slide 14: Progress From Clean Sheet to…
 | Required | Achieved | Notes
New propellant combination demonstrated | MON-25 w/SP7 | MON-25 w/SP7 | 
Rapid ignition Mars ambient Hypergolic if possible | <750 ms 0.1 psi MMH or solid additive | 507 ms 0.1 psi GOX/TEA/TEB | 
Cold propellants (Operation/ Storage Qualification) | -20ºC/-50ºC | -20ºC/-50ºC | Limited by MON-25
Mission profile burns: long first burn with coast and restart | 121.5 s (93.3 s + +27.9 s) | 105 s (85 s + 20 s) | Achieved was full duration when motor case was manufactured. Limiting factor is nozzle erosion.
Stable combustion | Pc< 5% peak to peak | Pc< 5% peak to peak | 
High performance | C* > 95% | > 95% for almost 40 s | Strong dependence on chamber pressure– can be improved by lowering the nozzle erosion and potentially incorporating mixing devices
High fuel utilization | < 2% residual | ~0.4% residual | 
Liquid Injection Thrust Vector Control | MON-25 at vacuum | MON-3 at ambient | WSTF test descoped
A Technology Readiness Level of 5+ for the flight design

## Slide 15: Preliminary Architecture Assessment Hybrid Configuration
Single-Stage Hybrid Motor Vehicle
Designed to deliver 14kg payload to circular orbit of 343km @ 25o inclination
Storable, pressure-fed liquid oxidizer
Solid fuel
Liquid Injection Thrust Vector Control (LITVC)
Cold-gas Reaction Control System (RCS)
Hypergolic ignition
Note: Some systems have changed dramatically since the conclusion of the PAA.
MPA (20 samples)
Liquid Oxidizer Tank
Aft Deck
Motor Nozzle
Pressurant Tanks
Hybrid Motor
Forward Structure
Hypergolics Tank
Avionics Package
Aeroshell
Milkstool

## Slide 16: Decision Package for MAV
Hybrid configuration was found to successfully deliver 14kg payload of an expected 20 sample tubes to Martian orbit, meeting all size and mass constraints
This design featured versatility in ability to meet mission design constraints through hybrid propulsion technology; orbital accuracy can be attained
Largest downside to hybrid vehicle is lower TRL, presenting a significant risk in MSR campaign
Decision Package Review held at NASA MSFC in December 2019. Ultimately, the solid vehicle design was chosen going forward

## Slide 17: Questions? George Story NASA Marshall Space Flight Center George.Story@nasa.gov

## Slide 18: MAV Mission Objectives
Receive sample tubes inside Orbiting Sample (OS) on Mars surface.
Launch to predefined Martian orbit.
Eject OS into orbit for pickup by Earth Return Orbiter (ERO).

## Slide 19: Intro
Single Stage to Orbit (SSTO) hybrid propulsion system was being studied as an option for a conceptual Mars Ascent Vehicle (MAV).
Benefits of the hybrid option include its predicted low temperature behavior, high performance and ability to restart (enabling the SSTO).
  However, the hybrid technology remained at a relatively low Technology Readiness Level (TRL).

## Slide 20: Comparison of Systems (Shotwell 2016)
 | Case 1 | Case 2 | Case 3 | Case 4 | Case 5 | Case 6 | Case 7 | Case 8 | Case 9 | Case 10
 | Solid-Solid G-G | Solid-Solid G-U | Solid-Liquid G-G | SSTO Monoprop | SSTO Pump BiProp | SSTO Reg. BiProp | SSTO Hybrid | Hyb-Hyb G-G | Hyb-Solid G-G | BiProp-BiProp G-G
Score | 0.60 | 0.54 | 0.32 | 0.52 | 0.79 | 0.76 | 0.76 | 0.621 | 0.52 | 0.57
GLOM | 176 | 158 | 237 | 276 | 182 | 187 | 166 | 173 | 157 | 190
Length | 1.88 m | 1.98 m | 2.09 m | 2.76 m | 2.04m | 2.29 m | 2.16 m | 2.78 m | 2.21 m | 2.84 m
AFT | -40 C | -40 C | +17 C | +8 C | -37 C | -37 C | -66 C | -66 C | -40 C | -37 C
6.65kg Payload, 20cm Reference OS
GLOM – Gross Lift Off Mass
AFT – Allowable Flight temperature

## Slide 21: MAV Studies
MAV 2015 Study concluded that for a certain set of requirements, hybrids had advantages. However TRL was low and plan made to develop the technology to be ready to compete for > 2030 launch.

## Slide 22: Parabilis Effort
In 2016, Parabilis was contracted to do regression rate tests with full scale MON-3 and SP7 in a 10 inch diameter motor.
4 tests completed with problems keeping the motor ignited.
Last test auto-aborted do to instability induced low pressure oscillation, post test inspection revealed ~1lbm of melted SP7 outside the motor and cracks on the ID of the grain.
Issues found remained, how to sustain combustion and keep grains from cracking during tests.

## Slide 23: Hypergolic Ignition
Previous studies suggested that a hypergolic material added to the fuel ignition would be the lightest mass option for MAV
Two methods of hypergolic ignition were used during the program.
  Liquid: Triethyl Aluminum and Triethyl Borane (TEA/TEB) with the MON oxidizer.
    Commonly used (with oxygen) in rocket applications
    Purdue completed a drop test with N2O4 that indicated it is hypergolic with TEA
  Solid: Solid materials are added to the hybrid fuel grain that are hypergolic with MON.
    Testing and development work at Penn State and Purdue

## Slide 24: Liquid Ignition: TEA/TEB, MMH
TEA/TEB was used with a small amount of GOx to ignite the motor and maintain stable combustion throughout the burn (vaporize the MON)
Disadvantages:
  The TEA/TEB system accounts for nearly 20% of the total component count in the feed system.
  Safety considerations of carrying a hypergolic liquid
  Performance at low temperatures may not be sufficient
Ignition fluid tests were run, however unsuccessful.
Due to timing issues, the next candidate fluid, MMH, was not tested even though it was baselined for the MAV.
  MMH&MON-25 used in a hypergolic thruster.
Alternative ignition designs were analyzed.
  Small ignition cavity off MON injector.
Whittinghill

## Slide 25: Solid Hypergolic Additives
Solid hypergolic materials simplify the design by not requiring additional tanks/plumbing
Penn State and Purdue did drop tests to test for hypergolic ignition with various canidate materials.
Penn State found several neat compounds hypergolic with MON-3 in drop tests.
  However, when the materials were encapsulated with SP7, the wax inhibited further reaction.
Purdue University also found several compounds that were hypergolic with NTO and MON.
Penn State
Purdue University

## Slide 26: Hybrid Testing – Regression & Motor
SP7/
MON-3
Space Propulsion Group
Regression Rate
SP7/MON-25 at -20 C
LITVC
Restart
Whittinghill Aerospace

## Slide 27: RCS/TVC Design
Reaction Control System (RCS) provides roll control during motor burn and full control during coast. Liquid Injected Thrust Vector Control (LITVC) provides pitch and yaw control during burn.
RCS consists of a helium cold gas system.
  Helium already used as an oxidizer pressurant.
  Six independent thrusters to provide attitude control and two thrusters for settling
LITVC deflects flow at specific injection points within motor nozzle, allowing pitch and yaw control without the need for traditional external actuators.
  Shares oxidizer and pressurant tanks with main motor
  Eight valves, similar in design to RCS

## Slide 28: Preliminary Architecture Assessment
From January-July 2019, PAA was performed to mature the designs for two MAV concepts: MAV-Hybrid and MAV-Solid.
Analysis focused on discriminators between two designs
Hybrid Propulsion Overview
  Liquid oxidizer with solid fuel
  Capable of active shut down and throttling
  Higher Isp than solid counterparts, lower than liquid
  Flexibility with hypergolic ignition options
  Performance in cold environments
  Significant hazards avoided
  Added complexity
  Lower Technology Readiness Level (TRL) compared to solids/liquids

## Slide 29: Propulsion Design
Initial sizing driven by mass and physical size constraints
Hybrid propulsion offers versatility and performance at extremely low temperatures. Orbital quality met with ability to turn off motor when orbit reached.
MON-25 liquid oxidizer with SP7A wax-based solid fuel. SP7A has a high coefficient of thermal expansion.
Helium pressurant injects oxidizer and hypergolic MMH* into hybrid motor HTPB** forward dome for ignition.
Slosh analysis not included in PAA, however, slosh baffles were included in tank design to account for additional mass.
Fixed design motor nozzle that must survive two burns. Throat erosion a cause for concern, requiring more testing.
*MMH = Monomethylhydrazine
**HTPB = Hydroxyl-Terminated PolyButadiene

## Slide 30: Decision Package Remaining Challenges
1) Demonstration of selected flight ignition system
  Gox Tea/Teb tested
  MMH in the design
  Hypergolic addition to solid fuel requires more work
2) Further understanding of nozzle performance –
  Requirement of less than 0.5 mils/sec was not met over the length of the burn.
  Two Dimensional Kinetics indicated a lower Cf then expected from textbook
  Nozzle and fuel grain needed to survive a long boost firing, and heat soak back over ~10 minute coast time and a second circularization burn.
3) Demonstration of LITVC with MON-25 at vacuum
4) Improved understanding of grain processing and assembly including a repeatable process
5) Internal ballistics model – The need for additional energy for MON vaporization and stability coupled with the particulars of the injector design resulted in more complex regression behavior than typical hybrid motors leading to complex modeling.

## Slide 31: Conclusions
A wax-based fuel was developed
  Mars Summer, Spring/Fall and Winter temperature cycling turned out to be much more challenging than what would be required a potential MSR campaign as it is understood at this time.
  Process was developed and scaled up to produce grain sizes to support a full-scale motor design.
  Multiple segments are being used with the fuel grain under compression (assembled at lower temperature) to ensure it is fully supported during combustion.
  The wax-based fuel formulation can be re-proportioned to adjust the burn rate if desired, as was done during this program due to scaling effects on the regression rate.
All supporting analyses and efforts to enable the demonstration of a full duration burn of a SP7A/MON-25 hybrid motor at -20ºC with vacuum ignition were completed.
The final propulsion system was tested in a relevant environment, except for the LITVC. Unfortunately, the vacuum LITVC demonstration test, with a flight expansion nozzle, that was planned for 2019 at White Sands Test Facility was canceled due to funding issues.
Progress was made in the nozzle design, resulting in a low regression rate nozzle.
  Additional system level changes, like lowering the average O/F over the burn, may be required to get the nozzle throat regression rate where we need it to be.
  The throat erosion lowers the chamber pressure, which is believed to have contributed to the C* efficiency decrement over the burn.
  Decreased nozzle erosion is crucial to the adoption of hybrid rocket technology for long duration burns and future work in this area is recommended.
The ignition system tested in the full-scale motors didn’t implement a hypergolic system that could be used in the Martin conditions. However, MMH has been demonstrated hypergolic with MON-25 at temperatures under these conditions and was slated to be tested in the future. A simpler ignition system, with hypergolic additives to the fuel grain and no additional plumbing or valves, has been researched and developed and eventually demonstrated in a vacuum at subscale conditions.
While there are still several open items left to analyze or test, this technology development effort resulted in a dramatic step forward in hybrid rocket development. A wax/MON based motor could be moved to qualification with a little more effort. Alternatives such as HTPB fuel or different methods of energy addition to stabilize the combustion could be considered.
Clean sheet to TRL 5+ in 5 years.