## Slide 1
Wireless Systems Applications and Opportunities from the ISS
Name of Forum: CCSDS WWG
Date: 10/28/2020
Presenter: Declan McCloskey and Chatwin Lansdowne
Disclaimer: Trade names and trademarks are used in this report for identification only. Their usage does not constitute an official endorsement, either expressed or implied, by the National Aeronautics and Space Administration

## Slide 2: Introduction
Feedback from the ISS crew has helped inform decisions as technology is added to the space station
Feedback from EWC operators and engineers
Positive and negative feedback can help inform decisions for future programs
  While Wi-Fi did not exist when the ISS was first being constructed, the standard has been integrated into the station over time
  With decades of experience in implementing wireless technology on the ISS, lessons can be learned for a more functional implementation in the future
Areas of Focus
  Wireless Architecture
  Tablets
  Wireless Laptops
  Opportunities

## Slide 3: Wireless Architecture
ISS is tight on equipment and wireless capacity with 5-6 crewmembers
  Crew describes wireless laptops as a “limited resource” on ISS
At some point in the near future 11 individuals may be on-board at once
Two factors lead to additional strain on ISS wireless architecture
  Additional crew members using devices simultaneously
  More wireless applications being installed as technology develops and as crew requests additional conveniences
These factors create a trend of more devices > more simultaneous clients > more data flows > more strain on network
  Expanding or upgrading to accommodate many more devices than originally planned is important to avoid frequent service interruptions as more technology is brought into the network, e.g. Additional WAPs have been added over time in response to frequent network complaints aboard ISS
WAPs
  Coverage provided by WAPs was often worse than predicted, even with LOS
  WAPs are not reaching into adjacent modules
  Performance degradation the longer WAPs operate, suggest scheduling a power cycle. Unit performance stability varies.

## Slide 4: Tablets
40 of 300 individual ISS crew comments explicitly mentioned tablet integration as a problem
The crew appreciates wireless devices, iPads especially
Tablets promise convenience but still posed many problems
  Using iOS to interface with anything else can be cumbersome
  iPad remote desktop is clunky; it would be easier to just use a wireless SSC
  Some common applications like OPTIMIS IPV Vsee and AirDrop are difficult or impossible to use on tablets
Benefits of well-integrated tablets
  Slim profile for easy maneuverability
  Reduced ethernet cable cluttering
  No reliance on peripherals like a USB mouse and keyboard
  General convenience of a tablet with the work efficiency almost equivalent to a laptop
Focus on integrating tablets and allowing them to interface with other crew applications to benefit crew productivity
Disclaimer: Trade names and trademarks are used in this report for identification only. Their usage does not constitute an official endorsement, either expressed or implied, by the National Aeronautics and Space Administration

## Slide 5: Wireless Laptops (1 of 2)
The crew is extremely positive about wireless laptops for almost every task
A glut of wires and peripherals is hard to manage
  For most tasks it is preferable to have a wireless laptop that can be removed from its power supply and relocated
  Wired peripherals like radiation monitor tether laptops
Station Support Computers (SSCs) dedicated to single tasks are usually inconvenient for the crew, who would prefer the flexibility of general purpose machines.
Crew members want to take their work with them so they can multitask
Even with extensive praise, there are complaints
  Described as a “limited resource” among 5-6 crewmembers
  The ISS does not have enough to comfortably serve a maximum capacity crew
  Want fewer wires for computers

## Slide 6: Wireless Laptops (2 of 2)
The only drawback to wireless laptops is that there is a less reliable connection than if they were wired
  In some cases (ex: video conferencing; ex: ultrasound telemedicine), a wired connection is preferred
The process for switching SSCs on the ISS between wired and wireless is not intuitive and not emphasized in training
An architecture focused on general purpose computers that can freely switch between wired and wireless is the most user-friendly approach for the crew
An architecture with SSCs not tethered by wire to stationary peripherals is the most user-friendly approach for the crew

## Slide 7: Other Applications to Look Into
Crew members have recommended various applications of wireless technology
Wearable Technology
  Vitals monitors for exercise
  Hands-free peripherals for laptops/tablets
  Smart watches
Wireless Communications
  Bluetooth headsets paired to iPads for intra-vehicular communications
  Bluetooth speakers for use as an intercom system
  Slave wireless speakers to forward warnings/alerts
    Based on a missed alarm event by an exercising crew member
  Greater reliability to make wired applications, portable
Other
  Wireless multimedia library
  Medical equipment that transmits data wirelessly to any paired device
  A way for wireless devices to cache data in the event of an outage so that the information isn’t lost (ARED example)

## Slide 8: External Wireless Existing Application Areas
Fixed payload locations need only power, structural interface, and wireless: astronomy, earth observation, materials exposure, physics, etc.
Mobile Video: pan/tilt camera upgrades, body cameras, SSRMS inspection tool camera, borescope camera, worksite camera, visiting vehicle docking camera, viewfinder stream for VR movie camera
Best-effort telemetry and control: suit telemetry, experiment telemetry and control