## Slide 1: Coherent Digital Signal Processing Algorithms for 10Gbps and Above Optical Communications Modems IRAD End of Year Status Report
Rick Butler
Electronics Engineer / Code 566
October, 2020
Starting TRL: 2
Current TRL: 3
Ending TRL: N/A

## Slide 2: Motivation & Project Summary
Motivation/Problem Statement:
  Develop optical communications modems that increase performance while reducing size, weight and power (SWaP) and build complexity
  Leverage industry investment in Photonic Integrated Circuits (PICs)
  Targets innovations two IRAD topics prioritized for FY20:
    Optical Communications Systems for all space regimes (Near Earth, GEO, Deep Space)
    Processes for integrating leading edge COTS products into space communications systems
Project Summary:
  Develop digital signal processing (DSP) algorithms for 10 Gbps and above optical communications modems using coherent detection
  Targeting near-Earth/near-Lunar satellite networks
  Port algorithms to VHDL code
    Targeting Rad-hard Field Programmable Gate Arrays (FPGAs)
  Assess performance

## Slide 3: Project Objectives
Goals for FY20
  Develop digital signal processing (DSP) algorithms for 10 Gbps and above optical communications modems using coherent detection for near-Earth/near-Lunar satellite networks
  Port Matlab algorithms to hardware (VHDL) optimized for rad-hard FPGAs
  Create a hardware breadboard based on commercial evaluation boards, with parts that have flight equivalents
    Include a clock network disciplined by common receiver—useful for ranging applications
  Assess performance on hardware breadboard
    Quantization noise is important parameter
Status
  Modified Decision Directed – Least Mean Square (MDD-LMS) Algorithm Development: Complete
  Porting of Matlab code to VHDL: Complete
  Optimization of VHDL for Rad-hard FPGAs: Ongoing
  Create hardware breadboard: Complete
  Sample data run through breadboard in loopback and processed offline to show recovery of original signal

## Slide 4: Process/Materials/Methodology
Development process
  MDD-LMS Algorithm was developed and validated in Matlab using floating point operations
  Hardware breadboard was assembled using commercially available evaluation boards
    Run in loopback
    Based on path to flight FPGAs, ADCs and clock synthesis hardware
  PRBS dataset was developed using Matlab model and run on breadboard in loopback mode
    Captured data was post-processed and original signal was recovered
  Floating point Matlab algorithm was ported to fixed-point VHDL code
  VHDL was then synthesized targeting breadboard FPGAs and simulated
  VHDL code was then iterated with optimization as the primary parameter
    Goal is to fit inside realistic number of FPGAs for a flight system

## Slide 5: Results & Conclusions
Results:
  Completed MDD-LMS algorithm
  Ported algorithm VHDL
  Optimizing of algorithm is ongoing
  Data run through breadboard and post-processed
Conclusions:
  Developed optical modem architecture using path to flight hardware that can communicate at 10Gbps
  Algorithm & architecture is extensible, so as faster hardware becomes available, performance can increase

## Slide 6: Challenges Encountered / Lessons Learned
Challenges
  Remote work due to Covid did decrease pace of work, but we were able to continue making meaningful progress
  The optimization of the VHDL to fit into reasonable number of FPGAs is a larger challenge than anticipated
Lessons Learned
  When developing hardware breadboards, ensure that they are remote controllable
    Can significantly increase productivity
  Engaging with toolset developer Mathworks on optimization issues helped the team make progress
    The earlier in the design cycle, the better

## Slide 7: Future Plans/Next Steps
This technology is targeted for science and communications missions with large data requirements, but limited available size, weight and power (SWaP)
Path Forward
  Complete porting of algorithm to VHDL and complete synthesis and optimization of VHDL code targeting rad-hard FPGAs
  Partner with industry to create software defined radio (SDR) utilizing rad-hard microelectronics, FPGAs and photonic-integrated circuits (PICs)
  Complete waveform design, including framing, command/telemetry definition and runtime software
  Integrate SDR into TRL6 protype modem; Complete performance tests in optical communications test bed
NTRs Filed
  Channel Deskew Algorithm, e-NTR Number: 1585841383
  Digital signal processing algorithm for coherent laser communication modems tolerant to self-phase modulation induced by high-power optical amplifier used for boosting transmitter power, e-NTR Number 1585851491
  Computationally efficient feedback iteration algorithm for tap weights calculation in adaptive digital FIR filtering using decision-directed least-mean-square technique, e-NTR Number 1585931943