## Slide 1: Linear System Assembly on GPU for an Inviscid Flux Miniapp
Daniel Steinberg – University of Illinois at Urbana-Champaign
Jeffrey Hill – NASA
Joey Schulz – AMA
NASA ARC-TS Intern Presentations, August 28, 2020

## Slide 2
Trends in Computing
More high- power computing (HPC) devices built, more computing power demanded
Allows for larger and more complex problems
  Refinements made to existing CFD codes
  More advanced physical models
Top 500 computers of various architecture:
  Top computer (Fugaku, RIKEN, Japan) still runs on CPU (central processor)
  Increasing number of GPU-based cores (graphics processor)
  Heterogeneous architecture: CPU and GPU working in tandem within a system
To allow for use in more HPC systems, code necessary to be implementable on GPU
Performance of HPCs over time (nextplatform.com)

## Slide 3
More adept at serial processing
Lower latency
Few complex cores
Why GPU?
CPU (Central Processing Unit)
GPU (Graphics Processing Unit)
More adept at massive-parallel processing
Higher throughput
Multiple simple compute elements
Lower power and cost requirements
High temperature, multi-species gas physics codes are one such massively-parallel routine
  Typically run on large domains
  Requires flux computation across multiple faces simultaneously
Single Summit node
Modern HPC machines are evolving rapidly; how can we write code to also leverage the GPU?

## Slide 4
DPLR: Current implementation of high-temperature, reacting Navier-Stokes gas physics routine
Inviscid routine represents greatest bottleneck
Can we turn that implementation into a performant GPU miniapp?
  Miniapp (mini-application): tool to simulate section of larger code
  Represents area of significant time consumption
Is the GPU more performant for these flow routines than CPU, by how much?
Project Goals
Chart: DPLR Performance Profile
| Inviscid Assembly | Viscous Assembly | Source Assembly | Linear Solve | Update
DPLR Earth 11sp | 0.43 | 0.23 | 0.11 | 0.16 | 0.02
DPLR Mars 8sp | 0.37 | 0.25 | 0.11 | 0.21 | 0.02

## Slide 5
Motivation for creating multi-dimensional flow solver:
  Reacting gases can contain multiple species (e.g. N2, NO+)
  Exist at multiple spatial temperatures (translational, vibro-electronic)
  Reentry flow structures like conical shocks need multiple spatial dimensions to be described
Start with simple, 1D, perfect gas code
Goal: take shock tube code, implement in C++, modified Steger-Warming
Modified Steger-Warming used in DPLR
Algorithm:
Verified with standard shock tube problem; shock and rarefaction structures behave as expected
Inviscid Flow Solver: 1D
Toro test 1:
Fan
Contact
Shock

## Slide 6
Analytical form of flux Jacobian (two temperature model):
Jacobian computed directly from eigenvalues and eigenvectors, flux using modified Steger-Warming
Algorithm for computing inviscid flux kernel:
  Septadiagonal (3D), block-banded linear system
  Compute flux between cell and each of its six spatial neighbors in parallel (Kokkos)
  Sum all fluxes for total flux, store to residual vector
Inviscid Flow Solver: 3D
2D representation of block-banded system

## Slide 7: Results: CUDA vs OpenMP
Ran miniapp on Pleiades, CPU/GPU tests
Ran range of grid resolutions
  Varied from 4 to 64
The CPU line slows down as problem size increases, while GPU increases in throughput
  GPU has more cores with higher bandwidth, so larger problem sizes allow it to fully saturate and speed up
For smaller problem sizes, CPU outperforms GPU
Saturation
Throughput vs spatial resolution for CPU and GPU

## Slide 8
Conclusions:
  GPU implementation is viable, can perform better than CPU for large problems
  CPU can dominate for smaller problem sizes
  Only naïve implementation, room for refinement and sizeable margin of error
Future work:
  Investigate different CPU and GPU implementations
    Can they be further optimized?
    Does this result hold up as we optimize CPU?
Conclusions and Future Work

## Slide 9
QUESTIONS?

## Slide 10
Eigenvalues and Eigenvectors

## Slide 11
Given :
  Smoothing: for hypersonic blunt bodies
First-order accurate flux:
Steger-Warming Algorithm

## Slide 12
Evaluate split Jacobians at the same index (first-order accurate):
  Half-indices indicate average of states
For second-order accuracy, improve with projections:
  MUSCL for improved accuracy:
Modified Steger-Warming Algorithm

## Slide 13
Miniapp outputs:
  Domain size ()
  Density residual
  Elapsed time ()
  Throughput
  Backup:
    Working theory: for , CPU memory saturates