## Slide 1: Earth Global Reference Atmospheric Model (GRAM) Overview and Future Improvements
Patrick White
NASA, Marshall Space Flight Center, Huntsville, AL Natural Environments
Earth-GRAM Lead

## Slide 2: Earth-GRAM Overview
Earth Global Reference Atmospheric Model (Earth-GRAM) provides monthly mean and standard deviation for any point in the atmosphere
  Includes Monthly, Geographic, and Altitude Variation
Atmospheric variables output included: pressure, density, temperature, horizontal and vertical winds, speed of sound, and atmospheric constituents
Used by engineering community because of ability to create dispersions in the atmosphere at a rapid runtime
  Often embedded in trajectory simulation software
Earth-GRAM is not a forecast model
Does not readily capture localized atmospheric effects

## Slide 3: Earth-GRAM Status
Currently Releasing Earth-GRAM 2016 Version 2.0
  C++ object oriented software
  Ability to incorporate code in multi-body trajectory simulations
  Includes ability to produce hourly atmosphere dispersions
  Software Request Link: https://software.nasa.gov/software/MFS-32780-2
Featured in NASA SPINOFF 2018 for use in Commercial Crew Program
Conducted comparison of Earth-GRAM hourly wind dispersions to hourly wind pairs databases
Conducted comparisons of Earth-GRAM to Modern-Era Retrospective Analysis for Research and Applications, Version 2 (MERRA-2)
  Conducted comparison of wind and thermodynamic monthly statistics
  Conducted comparison of boundary layer variables

## Slide 4: Earth-GRAM Upgrade Plans
Plan to implement Earth-GRAM in GRAM Suite Software
  Common C++ framework of GRAM Planetary Models
  GRAM Suite is available through NASA Software Catalog https://software.nasa.gov
Improve boundary layer capabilities in Earth-GRAM
Incorporate MERRA-2 as global atmosphere option in Earth-GRAM
  Have developed global monthly wind statistics on 42 pressure levels
  Next step develop global monthly thermodynamic statistics

## Slide 5: Coming to COSPAR2021
Benefits to using Earth-GRAM!
Provide overview of features in Earth-GRAM
Plan to work with COSPAR community to identify available data sources to implement and compare to Earth-GRAM
Details and benefits of MERRA-2 implementation
Options to improve boundary layer capabilities