## Slide 1: EVAA RTA Research Update Expandable Variable Autonomy Architecture (EVAA) & HQ-90 Reference Implementation
Mark Skoog
Principal Investigator for Autonomy
NASA / Armstrong Flight Research Center

## Slide 2: Resilient Autonomy Technology & Airworthiness Development & Transition
USAF
F-16 & F-35
Army
Future Vertical-Lift & UAS
USAF
Future Attack UAS
Drone Package Delivery
UAM
Performance Based Certification
F-16 Auto GCAS & ACAS
AvSP
Resilient Autonomy
NASA
Industry
DoD
Autonomy
Safety
Standards
Reference Implementation Development
1st Industry Standard
2018 Collier
UTM & SASO
Joint Capability Technology Demonstration
ASTM International
Notes: Resilient Autonomy research has two primary thrusts:
Performance Based Certification
Reference Implementation Development
Performance based certification is focused on the aggregate safety of the system as opposed to the more common prescriptive certification which looks at each individual component for safety. Performance base certification is a relatively new approach to certification being used for Part 23 aircraft. Resilient Autonomy is expanding on its former standards development with the FAA and ASTM International that culminated in the publishing of the first industry standard for safely bounding complex behavior in UAVs. This standard is based on a software architecture that leverages run-time assurance (RTA). This work is being done through a tight collaboration with the FAA.
A reference implementation of the software architecture is being developed that highly leverages RTA. This architecture is being integrated onto a UAV and evaluated for airworthiness as a means of validating the use of RTA as a means of compliance to the above certification approach being developed. This reference implementation leverages decades of work that went into the development of the F-16 automatic ground collision avoidance system (Auto GCAS).

## Slide 3: The Challenge of Autonomy
Complex or Untrusted
System
Deterministic
Safety Net
Verification & Certification of a Complex System
A Possible Solution – Run-Time Assurance (RTA)
Notes: Certification of autonomy is considered very challenging, if not impossible, using conventional methods such as DO-178. The problem being with such a complex system, you can’t guarantee that the system can’t get to a state from which there are possible bad outcomes.
Our project posed the question,
“What if you could stretch a safety net across just the bad outcomes? And, you only certified that safety net, not trying to certify the complex system? That safety net could be made less complex (or more deterministic) and thus much easier to certify.”
This concept is part of an approach called run-time assurance or RTA.

## Slide 4: Ground Collision Avoidance System (GCAS)
Notes: Auto GCAS basically stretches this safety net across the ground, preventing the aircraft from crossing to the bad outcome of ground impact. Our previous research has shown that one basic architecture can be easily adapted to a wide variety of aircraft.

## Slide 5: Multi-Monitor RTA (MM-RTA) with Risk-Based Decision Making
EVAA
Expandable Variable-Autonomy Architecture
Notes: What if you developed a software framework of multiple safety nets, each protecting the aircraft from the various hazards it may encounter in flight? In the RTA vernacular these safety nets are called monitors.. Although not previously considered in RTA research, this sort of framework would contain multiple monitors, each focused on a separate category of flight hazard.
Our reference implementation is a multi-monitor RTA (MM-RTA) framework and the monitor control/switching is controlled with risk-based decision making. We call this reference implementation of an MM-RTA, the expandable variable-autonomy architecture or EVAA (pronounced Eva) for short.

## Slide 6
Recovery
Controllers
Recovery
Controllers
Recovery
Controllers
RTA Input Manager
Vehicle Management System
Safety Monitor
Sensors
Sensors
Sensors
Sensors
RTA
Switch
Untrusted System
Traditional RTA Framework
Baseline Aircraft
RTA Trusted Functions
Untrusted Controllers
Legend
Sensors
https://www.astm.org/Standards/F3269.htm
This illustration represents what is in the published industry standard
Publish Oct 2017
Notes: Shown is the RTA framework covered in the ASTM standard. The orange boxes are the certified safety net wrapping around the untrusted or complex system. The switch is controlled by the monitor. Under normal circumstances, the untrusted system is allowed to send commands to the flight controls of the aircraft. If the monitor determines that the boundary is about to breeched, control is switched from the untrusted system and gives it to a trusted controller. When breech of the boundary is no longer imminent, control is returned to the untrusted controller.
For Auto GCAS, the pilot is the untrusted system and Auto GCAS is the monitor, evaluating if the aircraft is in imminent breech of the safety boundary (hitting the ground).

## Slide 7
Recovery Controller
Autopilot
RTA Integrity Manager
Vehicle Management System
Sensors
Sensors
Sensors
Sensors
RTA
Switch
Multi-Monitor RTA (MM-RTA) Framework
Safety/Behavioral
Monitor
Safety/Behavioral
Monitor
Safety/Behavioral
Monitor
Maneuver Request
Consequence
Untrusted System
Moral Compass
One monitor to protect against all hazards is similarly a complex system
We partition the monitors into separate functions & govern their selection through a risk-based switch (the Moral Compass)
EVAA Phase 1 : 2017
Notes: Shown is the RTA framework covered in the ASTM standard. The orange boxes are the certified safety net wrapping around the untrusted or complex system. The switch is controlled by the monitor. Under normal circumstances, the untrusted system is allowed to send commands to the flight controls of the aircraft. If the monitor determines that the boundary is about to breeched, control is switched from the untrusted system and gives it to a trusted controller. When breech of the boundary is no longer imminent, control is returned to the untrusted controller.
For Auto GCAS, the pilot is the untrusted system and Auto GCAS is the monitor, evaluating if the aircraft is in imminent breech of the safety boundary (hitting the ground).

## Slide 8
Vehicle Management System
Sensors
Sensors
Sensors
Sensors
RTA
Switch
RTA Network
Safety/Behavioral
Monitor
Safety/Behavioral
Monitor
Safety/Behavioral
Monitor
Maneuver Request
Consequence
RTA
Switch
Emergency Functions
Emergency Mode
Consequence
RTA Integrity Manager
Untrusted System
EVAA Phase 2 : Current Work
Expandable Variable-Autonomy Architecture
Moral Compass
In-flight emergencies are coordinated through an additional RTA switch
This switch feeds into the Moral Compass so safety monitors can still protect
Recovery Controller
Autopilot
EVAA Phase 2 : 2020-21
Resilient Autonomy JCTD
Notes: Shown is the RTA framework covered in the ASTM standard. The orange boxes are the certified safety net wrapping around the untrusted or complex system. The switch is controlled by the monitor. Under normal circumstances, the untrusted system is allowed to send commands to the flight controls of the aircraft. If the monitor determines that the boundary is about to breeched, control is switched from the untrusted system and gives it to a trusted controller. When breech of the boundary is no longer imminent, control is returned to the untrusted controller.
For Auto GCAS, the pilot is the untrusted system and Auto GCAS is the monitor, evaluating if the aircraft is in imminent breech of the safety boundary (hitting the ground).

## Slide 9: Functional Deconstruction of Piloting
Observe Airmanship Rules
Contingency Management
A/C Control
Plan Mission
Follow Mission Plan
Coordinate Mission with other Agents
Aircraft Controlling Entity
Agents in Near Vicinity
Airspace Control Authority
Piloting
Navigate
Communicate
Aviate
Interpret mission
objectives
AI
Path finding
Pilot commands
Waypoint following
Etc.
Intelligent routing
Formation flying
Interactive re-routing
Etc.
Surveillance/tracking
ATM
UTM
Etc.
Pilot in control
Company operations center
Etc.
Nearby aircraft
Launch & recovery operator
Others?
Stability
Stall
Structural limits
Flightpath control
Etc.
Well clear
Minimum flight levels
Etc.
Air Traffic
Ground
Obstacles
Birds
Tactical
Strategic
Onboard failures
Weather
Airspace boundaries
Action in one category can initiate other functional processes
EVAA
A/C Safety
Notes: With EVAA (an MM-RTA), we determine what monitors are needed by deconstructing the responsibilities of piloting. We begin with the three commonly known categories: aviate, navigate and communicate. We further break these down until we reach the fundamental functional categories that we can develop specific monitors for. EVAA addresses the piloting responsibilities under aviate that do not fall under aircraft control. The Resilient Autonomy project is developing monitors for most, though not all of these responsibilities.

## Slide 10: Resilient Autonomy
Project Goals & Status

## Slide 11: RA JCTD Proposal
What is the need?
  Effectively & affordably counter threat networks (CTN)
    Extend current capability which is limited to 35nm & 5k for Due Regard
What is it?
  Airworthy, Safe, Scalable Autonomy Framework for an Airborne Agent that can react to unanticipated events and situations
What will the project do? - The Reference Implementations
  Develop a Government Owned System that can be Adapted to any Vehicle and allow Link-less & Multi-Aircraft to One Operator Capability DoD-wide
  Develop and Evaluate an Airworthy System for the HQ-90 UAS that will allow beyond line-of-sight (BLOS) operations in Domestic and International Airspace
Operational value to the warfighter:
  Greatly increased mission capability, flexibility and reactivity
  Significant support cost reductions of UAS performing DoD ISR missions
    Eliminate need for AWACS mission support
    Eliminate need for continuous operator oversight of vehicle, can continue mission with lost link
    Greatly reduce crew support & training needs
    Enables multi-vehicle to single operator
    System can be easily be tailored to evolving mission requirements
Notes: Resilient Autonomy is developing two things:
A software architecture that can be adapted to any vehicle
That architecture adapted to an HQ-90
The software architecture is envisioned to be used by many users wishing to adapt it to a vehicle other than an HQ-90 UAV. The HQ-90 adaptation can be used for a wide array of missions/ConOps. US SOUTHERN COMMAND is looking to use it for drug interdiction missions over the Gulf of Mexico and Eastern Pacific.

## Slide 12: The EVAA Reference Implementation (Expandable Variable-Autonomy Architecture) v2
RTA Network
Moral Compass
Maneuver
Selection
Select Highest Consequence
Switch Controller
Geo-Fence
Integrity Manager
Dynamic Consistency Checks
Outer Loop Integrity Verifier
Self-Health Checks
In-Flight Re-Planner
Re-Route
Selection
Switch
Controller
iACAS
AI/Guidance/Pilot
Command Coupler
Sensors
Sensors
Sensors
Sensors
Flight Management System
Autopilot
Maneuver type & Consequence
Maneuver type
Capture values
Mission Guidance and Consequence
iGCAS
Input data & associated uncertainty
FLS
Geo-Recovery
Well Clear
Obstacle Spacing
Intent Manager
Voice
Sound
Lighting
GCS
VComm
FltMngmnt
Map Manager
Trajectory Manager
Consequence Calculator
Helper Functions
Sensor Coupler
Untrusted Guidance Commands
& Priority
…
Derived Data
Emergency Re-Plan & Consequence
…
Autopilot engagement & capture values
Contingency Functions
Strategic Contingencies
System Health
Vehicle Unique Elements
Safety Monitors
Airmanship & Tactical Contingencies

## Slide 13: The HQ-90/EVAA Reference Implementation
Aircraft
Aircraft Control
Autopilot
Navigation
GPS
INS
Image Referenced Navigation
Visual Inertial
Odometry
Ground/Obstacle/Risk Detection
Digital Maps
Air Traffic Detection
SARA Acoustic
ADS-B
Echodyne Radar
Cooperative & Non-Cooperative Targets
HQ-90C
117 Lbs. Max Gross Takeoff Weight
14’ 8” Wingspan
11 pounds of Payload
Up to 15 Hours Endurance
Terrain
Obstacles
Risk
Landing
EVAA Autonomy
Notes: EVAA is hosted on an Up2 processor. A wide variety of sensors feed the monitors within EVAA and the EVAA commands are sent to a Piccolo 2 autopilot used by the HQ-90. Although a wide variety and spectrum of sensors are used, the Resilient Autonomy project is really about the software that makes up EVAA.

## Slide 14
Whitney Portal
X-Plane Cessna 172SP

## Slide 15: iACAS/GA

## Slide 16: EVAA Tech Transition Early Out-of-Cycle Beta Release
Who
  160th SOAR
    MQ-1ER Integration
    Noel Khan is the transition Lead
      Has been imbedded in the RA software team since before JCTD start
  Skyborg
    Brian Krumheuer is the transition Lead
      Has been imbedded in the RA software team for a number of months
  FAA
    General aviation flight test project
  US Army PM UAS
    Evaluation in consideration for inclusion upcoming platform development
    Future Vertical Lift
    Future UAS Programs
  A-10 Program
    Evaluation to replace current GPWS
What
  Full hardware and software list for a working simulation
  EVAA Software
  Simulation Interface Software
  Analysis Software
How
  NASA Software Release
  Interagency Software Use Agreement
When
  This fall
  Status:
    Basic software documentation completed
    Additional software design documentation completed
    Software V&V completed
    Software Use Agreements in Work

## Slide 17: HQ-90 Ref. Imp. Status
Ship 1 – Lewis
  Built with JCTD unique hardware installed & integrated
    Does not include Amazon Prime Air vision sensor
  Baseline acceptance & acoustic characterization flights flown
  Arrived at Armstrong 30 Sep
  Aircraft personnel on site prepping for functional check flights
Ship 2 – Clark
  Aircraft build beginning
    Will include Amazon Prime Air sensor if project collaboration is successful
    Lewis to be retrofitted at Armstrong following Clark readiness to begin flight test
  Arrives at Armstrong in November

## Slide 18: Airworthiness Status
Project Specific Certification Plan for EVAA/General Aviation
  First critical step in certification
  Addresses multiple levels of automation
    Pilot cuing only
    Various level of automated maneuvering
  Shows how accepted certification practices can be used to certify autonomy
  Completed on time
Project Specific Certification Plan for EVAA/HQ-90
  Builds on GA approach
  Will address multiple ConOps
    US SOUTHCOM ISR mission
    Long-range low-altitude rural mission within national airspace
    Long-range medium-altitude rural mission within national airspace
  Currently under development
    Scheduled completion at end of project

## Slide 19: Questions

## Slide 20: The Algorithms
Monitors & Emergency Re-planners

## Slide 21: Algorithms
4 Categories of EVAA Algorithms
  Tactical monitors for stationary collision threats
  Tactical monitors for moving collision threats
  Strategic algorithms for re-planning some portion of the mission
  Integrity Monitors for triggering mission re-planning
General Description of Tactical Monitors
  Sense
    Sensor Coupler
    Own State
      Nav Data
      Air Data
    Collision Threat
      Terrain
      Obstacles
      Aircraft
      Etc.
  Evaluate
    Predict Escape Trajectories
      Trajectory Manager
      Any number of maneuvers
    Predict Future Collision Threat
    Determine Need to Avoid
  Act
    Execute Avoidance
      Command Coupler
      Autopilot
Tactical Monitor Common Algorithm Framework

## Slide 22: iGCAS
Improved Ground Collision Avoidance System
Trajectory Manager
Map Manager

## Slide 23: iGCAS Design
Software Structure
  Easily adjusts to new aircraft performance
  Easily adjusts to evolving requirements
Higher Fidelity Terrain Maps
  NASA-unique terrain encoding with ~2,000:1 file size reduction
  81x finer resolution than F-16/F-35 1/3rd AS (10m)
  Obstacle map 1/9th AS (3m)
  In-flight switchable acceptable landing map
More Accurate Aircraft Performance Modeling
  Easily tuned to specific aircraft/autopilot flight dynamics
  Performance can switch in-flight with aircraft configuration changes
Multiple Avoidance Options Evaluated
  Normal = left, straight & right climbs at max climb rate of aircraft
  No-Climb = Bush pilot mode for scud-running under weather
New Advanced Features
  Activation suppression on landing
  Leeward ridgeline downdraft protection
Avoidance Director Cuing
System Status
Fully mechanized
Included in latest release
ICD, Documentation included with release
Computational Agility enabling beneficial emergent behavior during hard landings

## Slide 24: Map Manager Design
Purpose
  Provide common interface method for data bases
Basic Concepts
  Manage any number of data base products
  Access data in non-volatile memory
  Store subset of data in RAM
    Update this Local Map with data surrounding the aircraft position as the aircraft moves
  Provide a standard set of interface calls for monitors to access data for their use
Capability
  Supports a wide variety of resolutions
  Supports a multiple formats
System Status
Multi-Resolution & Multi-Format terrain data supported
Raster Obstacle data supported at resolution as low as 1/9th arc-sec
Multiple landing data bases supported
Can switch landing data base in-flight
Risk data base will be added as part of Spiral 2 to support FLS and Rules of Behavior

## Slide 25: Trajectory Manager Design
Purpose
  Prefict the future flight path trajectory of various maneuvers
Basic Concepts
  Kinematic modeling: F = Ma
  3 control loops modeled
    Climb rate
    Roll rate
    Speed
Capability
  Models an extremely wide variety of potential escape maneuvers
  Supports low-speed, climb-limited aircraft
    <300 KCAS
    <3,000 FPM climb rate
System Status
Fully functional in current release
Developing tuning guide for users
Developing generic PID auto-tuning mechanization

## Slide 26: iGCAS/GA

## Slide 27: iACAS
Improved Air Collision Avoidance System
Trajectory Manager

## Slide 28: iACAS Design
Purpose
  Avoid midair collisions and request an aggressive escape maneuver
    “Don’t scrape paint”

## Slide 29: iACAS Design
Purpose
  Avoid midair collisions and request an aggressive escape maneuver
    “Don’t scrape paint”
Basic Concepts
  Generates multiple Escape Trajectory Options
  Evaluates Separation of Each
  Waits Until Last Maneuver can Barely Avoid to Request that Maneuver
    Do nearly everything you can with the maneuverability of the aircraft to avoid collision
Uncertainty

## Slide 30: iACAS Design
Purpose
  Avoid midair collisions and request an aggressive escape maneuver
Basic Concepts
  Generates multiple Escape Trajectory Options
  Evaluates Separation of Each
  Waits Until Last Maneuver can Barely Avoid to Request that Maneuver
Capability
  Any Number of Intruder Aircraft
  Any Type and Number of Avoidance Options
    We are currently using 7 avoidance options
    Maneuvers are aggressive & the same or similar to those used by iGCAS
    Maneuver profiles are generated by the Trajectory Manager
  Easily Tailors to Aircraft Dynamics
  Additional DAA Sensors Easily Added
    ADS-B
    Echodyne Radar 1 to 2 km (only detects aircraft @±60oAz
    Sara Acoustic Sensor 2 to 10 km (only detects propeller aircraft to include helicopters)
Uncertainty
System Status
Initial mechanization completed & running within EVAA
The current focus of our software development

## Slide 31: iACAS/GA

## Slide 32: Well Clear
Observing Airmanship Rules
Trajectory Manager

## Slide 33: Well Clear Design
Purpose
  Observe appropriate airmanship behavior
Basic Concepts
  Detune iACAS
    Larger separation
    Less aggressive maneuvers
      Less bank angle used
      Will increase bank angle used if still not maintaining appropriate separation
    Favor horizontal maneuvers over vertical
      Will coordinate appropriate maneuvers with FAA
Capability
  Acts before iACAS if intruder is sensed early enough
Larger
Separation
Bubbles
Larger
Separation
Bubbles
Less Aggressive Maneuvers
System Status
Spiral 2 work
Beginning coordination of maneuvers with FAA
Low Bank
Medium Bank
Higher Bank

## Slide 34: Obstacle Spacing

## Slide 35: Obstacle Spacing Design
Purpose
  Observe appropriate airmanship behavior near structures
Basic Concepts
  Detune iGCAS
    Larger horizontal separation distances
    Less aggressive maneuvers
      Less bank angle used
      Will increase bank angle used if still not maintaining appropriate separation
    Favor horizontal maneuvers over vertical
      Will coordinate appropriate maneuvers with FAA
Capability
  Acts before iGCAS if obstacle is sensed early enough
Larger
Separation
Bubbles
Larger
Separation
Bubbles
Less Aggressive Maneuvers
System Status
Spiral 2 work
Beginning coordination of maneuvers with FAA

## Slide 36: Geo-Fence
Airspace & Other Restricted Boundaries
Map Manager
Trajectory Manager

## Slide 37: Geo-Fence Design
Purpose
  Observe appropriate airmanship behavior by staying out of restricted airspace
Basic Concepts
  Repurpose iGCAS by substituting airspace boundaries for terrain and obstacles
    MSL & AGL floor values
    MSL & AGL ceiling values
    Airspace boundaries equivalent to obstacle walls
  Boundaries will be stored as separate data base
    Loaded as part of pre-flight
Capability
  Pulls up to avoid floor penetration
  Pushes over to avoid ceiling breech
  Maneuvers horizontally to avoid wall boundaries
System Status
An extremely similar version of this flew on our previous program
Ready to add a modified instance of iGCAS as part of Spiral 2 work

## Slide 38: FLS
Forced Landing System
Integrity Manager
Map Manager

## Slide 39: FLS Design
Purpose
  Generate a flight plan for an emergency landing when contingencies arise that compromise safely continuing the remaining mission
Basic Concepts
  Integrity Management
    Identifies the need for an emergency landing
    Identifies constraints for and how soon the aircraft must land
  FLS
    Computes the reachable landing areas
    Requests risk data from the Map Manager
      Provides the lowest risk location for each reachable area
    Sends the landing location to the flight control system and requests landing initiation
Capability
  Risk map allows significant flexibility
    Currently configured to generate landing risk from LiDAR data
      Terrain slope & small obstructions
      Road/highway data from available vector maps
      Population data
  FLS leverages the inherent landing capability of the Piccolo
System Status
FLS has been developed over previous programs & flown on a similar UAV
We have initial software to automatically generate risk maps
We currently expanding this auto-generate software capability
X sec ahead
Land in X sec
Search area
Lowest risk landing location
Current Flight Path
Emergency Flight Path
Current Flight Path
Lowest risk landing location
Search areas
Land here
Emergency Flight Path
Command Location
Risk map of New York city

## Slide 40: Example of Landing Risk Generation
Area on Edwards AFB
Landing risk map
Road vector data