## Slide 1: IV&V Finalized Challenge Problems from NASA
Nathaniel Hildebrand and Matthew O'Connell
Computational AeroSciences Branch
David Wagner, Nelson Carvalho, Vesselin Yamakov, and Edward Glaessgen
Durability, Damage Tolerance, and Reliability Branch
NASA Langley Research Center
Hampton, Virginia
DARPA Computable Models Phase II Kickoff
December 3-4, 2020
Computational AeroSciences Branch

## Slide 2
2/22
Outline
Modeling flow instabilities in hypersonic boundary layers with finite-rate chemistry using machine learning
  Performer: Brown University
  Monitor: Nathaniel Hildebrand
Computational conjugate heat transfer simulation of wind tunnel model of Aerobraking for planetary (re)entry
  Performer: Galois
  Monitor: Matthew O’Connell
Laminated composites challenge problem
  Performer: MIT
  Monitors: Nelson V. De Carvalho & Vesselin Yamakov
Modeling Ti-6Al-4V anisotropy, hysteresis, and fracture with an inferred particle system
  Performer: MIT
  Monitor: Vesselin Yamakov
Integrating applications to solve multiscale multiphysics problems
  Performer: U.S. Naval Research Laboratory
  Monitor: David Wagner

## Slide 3
3/22
Modeling flow instabilities in hypersonic boundary layers with finite-rate chemistry using machine learning
Relevance to NASA’s Mission
  High-speed boundary-layer transition increases skin-friction drag and heat flux, and hence, it is critically important for the design of hypersonic vehicles
  Modeling laminar-turbulent transition is a pacing item for the foreseeable future according to the NASA CFD Vision 2030 Study (Slotnick et al. 2014)
  Research in transition modeling (Paredes et al. 2020) is currently supported by the NASA Tools, Technologies, and Techniques Project
Background Information
  Planar second-mode waves (Mack 1984) initiate transition to turbulence in hypersonic axisymmetric and 2D boundary layers
  Logarithmic amplification ratio (N-factor) of the most amplified instability mode is frequently used to estimate the transition location
  N-factor methods require significant user expertise, relatively-high computational cost, and accurate basic states
  Machine learning could dramatically simplify transition modeling in practical applications and reduce the time required for transition prediction
Brown University: George Karniadakis, Tamer Zaki, & Zhongqiang Zhang
Monitor: Nathaniel Hildebrand

## Slide 4
4/22
Modeling flow instabilities in hypersonic boundary layers with finite-rate chemistry using machine learning
Scope of the Challenge Problem
  Verify DeepM&Mnet and CPINNs can accurately model canonical boundary-layer solutions with finite-rate chemistry
  Apply DeepM&Mnet and CPINNs to model spatial linear and nonlinear instability waves (e.g., second mode)
  Use DeepM&Mnet and CPINNs to study receptivity of transitional boundary layers due to freestream disturbances
Benchmarks
  Reproduce hypersonic boundary-layer profiles from a well-established code with finite-rate chemistry (Marxen et al. 2011) using DeepM&Mnet and CPINNs
  Use machine-learning codes to reproduce a few selected results based on linear stability theory for both nonreacting hypersonic flows with shocks (Paredes et al. 2020) and boundary layers with finite-rate chemistry
  Extend the DeepM&Mnet and CPINNs tools to study nonlinear development of Mack-mode instability waves at finite amplitudes and the receptivity of transitional boundary layers (Li et al. 2012)
Brown University: George Karniadakis, Tamer Zaki, & Zhongqiang Zhang
Monitor: Nathaniel Hildebrand

## Slide 5
5/22
Modeling flow instabilities in hypersonic boundary layers with finite-rate chemistry using machine learning
Metrics
  Computability – The level of effort with using DeepM&Mnet and CPINNs is closely tied to the amount of training that is needed for an accurate solution. A comparison with results from machine-learning efforts at NASA will be made in terms of research hours, computing time, and ease of use.
  Conservation & Accuracy –Brown has shown that DeepM&Mnet and CPINNs can successfully model flat-plate boundary-layer solutions with finite-rate chemistry. The performers need to show that these tools can also model the linear and nonlinear growth of instability waves. These results will be verified by the monitor.
  Composability & Scale Range – The problems encapsulate multiple aspects of hypersonic aerothermodynamics including shocks, nonequilibrium flow, finite-rate chemistry, interactions between acoustic, vorticity, and entropy modes, and viscous/inviscid flow phenomena across a broad range of length scales from boundary-layer thickness to instability wavelength to the overall vehicle dimensions. The time and effort to integrate new multiphysics will be provided by the performer.
  Computational Speed – DeepM&Mnet and CPINNs could dramatically speed up the overall time to perform transition modeling. A benchmark will be provided by the performer and verified by the monitor.
Brown University: George Karniadakis, Tamer Zaki, & Zhongqiang Zhang
Monitor: Nathaniel Hildebrand

## Slide 6
6/22
Modeling flow instabilities in hypersonic boundary layers with finite-rate chemistry using machine learning
Tech Transfer
  Allow the monitor and other NASA researchers access to the machine-learning tools DeepM&Mnet and CPINNs
  The monitor will run DeepM&Mnet and CPINNs with help from the performers to duplicate results from the challenge problems
  The performers can help the monitor and other NASA researchers setup DeepM&Mnet and CPINNs on NASA supercomputers (including the local K cluster and Pleiades)
  NASA researchers and the monitor will apply DeepM&Mnet and CPINNs to other problems of interest to gain a fuller understanding of how their capability would could impact current and future NASA projects
  The performers and monitor will determine if any other pre- or post-processing scripts apart from DeepM&Mnet and CPINNs are needed for NASA to effectively perform a transition analysis with machine learning
  NASA researchers and the monitor will provide Navier-Stokes solutions and basic states from in-house codes if they are needed by the performers
Brown University: George Karniadakis, Tamer Zaki, & Zhongqiang Zhang
Monitor: Nathaniel Hildebrand

## Slide 7
7/22
Computational conjugate heat transfer simulation of wind tunnel model of aerobraking for planetary (re)entry
Relevance to NASA’s Mission
  Non-thermally conductive materials used in thermal protection systems can be difficult to rapidly fabricate and instrument for wind tunnel experiments; while materials easier to use for experiments, such as steel, are thermally conductive
  Quantifying body heat transfer can help validate experiments using metals instead of ceramics or help put temporal and spatial bounds on confidence of these tests.
  Model fabrication from metals may help reduce fabrication lead time or allow more complex instrumentation at a lower cost
Background Information
  Historical aerobraking wind tunnel experiments were conducted with models built out of chromel, nickel and chromium (Horvath et al. 1996, 1997, & 1998)
  Short duration experiments used to measure heating rates observed temperature increased near the vehicle payload (behind the thermal protection system)
  If heat was conducted from the thermal protection system to the payload region the experiment would have under-predicted surface heating rates near the payload
  Simulation has been performed for fluid only region but has not included both fluid simulation and body heat transfer
Galois: Charisee Chiw & Eric Davis
Monitor: Matthew O’Connell

## Slide 8
8/22
Scope of the Challenge Problem
  Simulate fluid flow and body heat transfer for an axisymmetric aerobraking wind tunnel model assuming an ideal gas at Mach 10 in laminar flow over a 7 second duration
  Use an automatically generated simulator with a low level of development effort
Benchmarks
  Reproduce surface heating rates obtained from fluid-only simulations that were performed with a fixed surface temperature
  Quantify any discrepancy in surface heating rates with and without body heat transfer.
  Compare with experimental results from wind tunnel test performed at NASA for a model made of chromel (Horvath et al. 1996, 1997, & 1998)
Computational conjugate heat transfer simulation of wind tunnel model of Aerobraking for planetary (re)entry
Galois: Charisee Chiw & Eric Davis
Monitor: Matthew O’Connell

## Slide 9
9/22
Metrics
  Computability – Creating a simulator capable of such coupled simulations would likely take months to years of full-time equivalent development. The manual nature of this kind of coupling may be error prone due to the challenges in coupling two legacy simulation tools not intended to work together.
  Conservation & Accuracy –The simulator is expected to be fully conservative in mass momentum and energy for in each respective physics zone – by construction. The simulator will be relying on proven numerical techniques. These results will be verified by the monitor.
  Composability & Scale Range – Two physical regions will be included; modeling the heat conduction within the wind tunnel model and modeling the fluid flow around the model. The interface between the two regions must be included. There is expected to be 4 orders of magnitude of separation between the time and spatial scales of the fluid and structural domain.
  Computational Speed – Due to increased physics; computational cost is expected to increase compared to baseline fluids only simulation.
Computational conjugate heat transfer simulation of wind tunnel model of Aerobraking for planetary (re)entry
Galois: Charisee Chiw & Eric Davis
Monitor: Matthew O’Connell

## Slide 10
10/22
Tech Transfer
  Allow the monitor and other NASA researchers access to the developed multiphysics simulator
  The monitor will run the simulator with help from the performers to duplicate results from the challenge problems
  The performers can help the monitor, and other NASA researchers, setup the simulator on NASA supercomputers (including the local K cluster and Pleiades)
  NASA researchers and the monitor will apply the simulator to other problems of interest to gain a fuller understanding of how their capability would could impact current and future NASA projects
  The performers and monitor will determine if any other pre- or post-processing scripts apart from the simulator are needed for NASA to effectively perform conjugate heat transfer analysis
  NASA researchers and the monitor will provide application specific grids (unstructured or multi-block structured) as needed to the performers
Galois: Charisee Chiw & Eric Davis
Computational conjugate heat transfer simulation of wind tunnel model of Aerobraking for planetary (re)entry
Monitor: Matthew O’Connell

## Slide 11
11/22
Laminated composites challenge problem
MIT: Neil Gershenfeld
Relevance to NASA’s Mission
  Advanced composite materials are applied across the range of NASA missions, from aeronautics to space
  Damage tolerance assessments are gaining increased relevance, e.g.:
    Simulate micro-meteor impacts in lower earth orbit
    Develop durable urban mobility concepts
  Effective tools are needed that:
    Simulate complex loading conditions (thermal + mechanical + …)
    Predict complex interacting failure modes in various composite topologies
    Are scalable
Background Information
  Matrix failure modes, (e.g. delamination, matrix cracks) and their interaction are typically the first failure modes observed in a composite structures
  High-fidelity models that can capture these mechanisms are:
    Computationally expensive and require judicious use of global/local strategies
    Accuracy tends decreases beyond the first stages of growth
    Non-trivial to assemble and cannot easily be extended to material topologies other than Uni-Directional Laminates (e.g. 2D/3D woven) while preserving accuracy/generality
Monitors: Nelson V. De Carvalho & Vesselin Yamakov

## Slide 12
12/22
Scope of the Challenge Problem
  Verify the approach can simulate Mixed-Mode fracture with application to delamination and matrix crack growth
  Apply the approach to validation exercise(s) involving delamination, matrix crack growth and their interaction
Benchmarks
  Elasticity: Following [1] consider different ply orientations and laminates. Use FE results as benchmark. Establish that the approach can accurately predict the deformation of anisotropic layered materials.
  Fracture, Plate-like benchmarks: Using the benchmarks and analytical solutions summarized in [2] determine whether the approach can predict growth onset for Mode I, Mixed Mode I/II and Mode II loadings
  Fracture, Beam-like benchmarks: Using the benchmarks summarized in [3] determine whether the approach is capable of reproducing mixed-mode fracture and understand eventual discrepancies
  Reproduce the experimental results obtained in [4, 5] which provide validation data for delamination growth and delamination/matrix crack interaction, namely delamination migration
Monitors: Nelson V. De Carvalho & Vesselin Yamakov
Laminated composites challenge problem
MIT: Neil Gershenfeld

## Slide 13
13/22
Metrics
  Computability – Time and effort from design to simulation to be provided by the performer. Estimate of time/effort to perform similar analysis with SOA tools to be provided by the IV&V team.
  Conservation & Accuracy – Level of accuracy assessed by comparing the results obtained by the performer to published data as described in the challenge problem definition.
  Composability & Scale Range – Fracture in composites is inherently multi-scale (fiber/matrix – layer – laminate - component). The scale range considered will depend on the idealization chosen by the performer and can span from micron to meter.
  Computational Speed: – Computational speed will be compared to estimates (extrapolations) based on the performance of similar (spanning the same scale range) SOA tools available.
Monitors: Nelson V. De Carvalho & Vesselin Yamakov
Laminated composites challenge problem
MIT: Neil Gershenfeld

## Slide 14
14/22
Monitors: Nelson V. De Carvalho & Vesselin Yamakov
Tech Transfer
  NASA IV&V team will access the code and run it internally
  Select challenge problem benchmarks will be re-run by the IV&V team under the performer’s guidance
  Performance of the code will be further evaluated via application to additional problems of interest and comparison to experimental results in the NASA Advanced Composites Project validation database
  Follow on publications and dissemination of capability will be pursued as deemed fit
  Integration with existent tools and in current and future projects will be assessed
References:
[1] Madenci, Erdogan, Cagan Diyaroglu, and Nam D. Phan. "ANSYS implementation of peridynamics for deformation of orthotropic materials." 2018 AIAA/ASCE/AHS/ASC Structures, Structural Dynamics, and Materials Conference (2018)
[2] Leone, Frank, et al. "Benchmarking Mixed Mode Failure in Progressive Damage and Failure Analysis Methods.", Proceedings of the American Society for Composites (2018).
[3] Krueger, Ronald. "A summary of benchmark examples to assess the performance of quasi-static delamination propagation prediction capabilities in finite element codes." Journal of Composite Materials 49.26 (2015): 3297-3316.
[4] Ratcliffe, James G., Michael W. Czabaj, and Thomas K. O'Brien. "A test for characterizing delamination migration in carbon/epoxy tape laminates." NASA/TM–2013-218028 (2013).
[5] De Carvalho, N. V., et al. "Modeling delamination migration in cross-ply tape laminates." Composites Part A: Applied Science and Manufacturing 71 (2015): 192-203.
Laminated composites challenge problem
MIT: Neil Gershenfeld

## Slide 15
15/22
Relevance to NASA’s Mission
  Ti-6Al-4V aerospace alloy, known for short as Ti64, has been identified by NASA LaRC as key material produced through additive manufacturing (AM) in aerospace industry
  A central issue for introduction of AM process in aerospace industry is the lack of suitable certification and validation procedures for AM materials as requested by FAA
  NASA has helped develop such procedures based on detailed investigation of Ti64 mechanical properties, which include fatigue resistance and fracture toughness
Background Information
  Ti64 is a light-weight alloy, characterized with superior strength,
  thermal and corrosion stability. Still, its processing remains
  challenging and expensive
  AM is a promising method for decreasing the cost and improving
  reliability of the components made of Ti64
  Structurally, Ti64 is a Ti-based alloy, which typically exists as a
  mixture of two phases - alpha, and beta phase. Their relative content and mixing
  depends strongly on the processing history of the material and affects significantly the
  mechanical and other physical properties of the alloy
Monitor: Vesselin Yamakov
Modeling Ti-6Al-4V anisotropy, hysteresis, and fracture with an inferred particle system
MIT: Neil Gershenfeld

## Slide 16
16/22
Scope of the Challenge Problem
  Verify that the Discrete Inverse Methods approach, developed by MIT, can reproduce the elastic and plastic anisotropy, and the tension–compression asymmetry behavior of Ti–6Al–4V alloy
  Verify the effect of microstructure on the elasto-viscoplastic deformation of dual phase titanium structures of Ti–6Al–4V
  Verify the ductile fracture in tension and torsion of Ti–6Al–4V titanium alloy
Benchmarks
  Reproducing anisotropy and tension–compression asymmetry of the room temperature plastic response of Ti–6Al-4V as given in (Tuninetti et al. 2015)
  Reproducing the effect of microstructure on the elasto-viscoplastic deformation of dual phase titanium structures as given in (Ozturk et al. 2018)
  Reproducing fracture mechanisms in ductile fracture in tension and torsion of Ti–6Al-4V as given in (Giglio et al. 2012)
Monitor: Vesselin Yamakov
Modeling Ti-6Al-4V anisotropy, hysteresis, and fracture with an inferred particle system
MIT: Neil Gershenfeld

## Slide 17
17/22
Metrics
  Computability –
    Time and effort from design to simulation
    Time and effort to integrate multiphysics
    Time and effort to develop new force laws
    Simulation speed and scaling
  Conservation & Accuracy –
    Level of satisfying the appropriate for each system conservation laws, such as conservation of energy and/or momentum where relevant.
    Level of accuracy in reproducing the published data as listed as Benchmarks.
  Composability & Scale Range – The problems encapsulate multiple aspects of the mechanical properties and behavior of Ti64 alloy, including elasto-plastic anisotropic rfesponse, tension-compression asymmetry, ductile fracture in tension and torsion. The scale range varies from submicron microscale to millimeter part scale range.
  Computational Speed – A benchmark will be provided by the performer on SOA supercomputer centers, such as Summit at Oak Ridge Nat. Lab.
Monitor: Vesselin Yamakov
Modeling Ti-6Al-4V anisotropy, hysteresis, and fracture with an inferred particle system
MIT: Neil Gershenfeld

## Slide 18
18/22
Tech Transfer
  Allow the monitor and other NASA researchers access to the software tools developed by the performer
  The monitor will run the developed software tools on NASA computing clusters, K-cluster at LaRC, and Pleiades at NAS - AMES
  NASA researchers and the monitor will apply the developed methodology and tools to the AM program at NASA LaRC.
References:
Giglio, M., Manes, A., Vigano, F., “Ductile fracture locus of Ti-6Al-4V titanium alloy”, International Journal of Mechanical Sciences, 54 (2012) 121-135.
Ozturk, T., Rollett, D., “Effect of microstructure on the elasto-viscoplastic deformation of dual phase titanium structures”, Comput Mech 61 (2018) 55–70.
Tuninetti, V., Gilles, G., Milis, O., Pardoen, T., Habraken, A.M., “Anisotropy and tension–compression asymmetry modeling of the room temperature plastic response of Ti–6Al-4V” International Journal of Plasticity, 67 (2015) 53-68.
Monitor: Vesselin Yamakov
Modeling Ti-6Al-4V anisotropy, hysteresis, and fracture with an inferred particle system
MIT: Neil Gershenfeld

## Slide 19
19/22
Integrating applications to solve multiscale multiphysics problems
Relevance to NASA Missions
  The need to integrate numerical solution applications, each chosen by a different subject mater expert as appropriate to solve a specific part of a multiscale/multiphysics problem, is common to many NASA projects
  Multiphysics integration is currently supported by many projects, including the NASA Tools, Technologies, and Techniques project, and NASA Project Innovation Concepts
Background Information
  Lower-level (low TRL) NASA research is typically done by independent team experts, each using or creating a tool specific to one domain, but only part of a larger multiscale/multiphysics problem
  Integrating individual applications into a larger framework at the current SoA is cumbersome and time-consuming, often relegated to a higher-TRL follow-on project
  An efficient, robust, and reliable framework to integrate applications prior to project close could reduce time to mission deployment by an entire budget cycle
U.S. Naval Research Laboratory: John Michopoulos
Monitor: David Wagner

## Slide 20
20/22
Scope of the Challenge Problem
  Problem selected from among large-scale multicscale multiphysics problems previously solved by manual composition of components
Benchmarks
  Set up framework-component linkages
  Verify that the framework composes two models correctly
  Verify that the framework composes several models with a lower level-of-effort compared to manual composition
  Verify that the framework reproduces the accuracy of the manually-composed effort
  Verify that the framework reproduces computational speed of the manually-composed effort
Monitor: David Wagner
U.S. Naval Research Laboratory: John Michopoulos
Integrating applications to solve multiscale multiphysics problems

## Slide 21
21/22
Metrics
  Computability – Assess the level of effort necessary to integrate commercial and NASA applications into the NRL framework to solve current NASA problems in additive manufacturing.
  Composability & Scale Range – Assess the level of effort to increase the scale range, the number of interacting physics, and the number and type (FEM, FD, MD) of different applications necessary for anticipated NASA problems of interest.
  Conservation & Accuracy and Computational Speed – Verify that composed solutions maintain SoA for NRL’s selected challenge problem(s). If the level of effort assessed above is sufficiently low, such that it can be completed before project close, also verify these for a current NASA application to additive manufacturing analysis.
Monitor: David Wagner
U.S. Naval Research Laboratory: John Michopoulos
Integrating applications to solve multiscale multiphysics problems

## Slide 22
22/22
Tech Transfer
  If successful, integrate some or all of the modular framework developed for this project with NASA applications
  Apply or adapt framework modules, alone or in combination, to NASA applications
  Explore extending NRL’s hypercomplex algebraic simplification technique to direct numerical analysis by integration with a NASA hypercomplex solver in development
Monitor: David Wagner
U.S. Naval Research Laboratory: John Michopoulos
Integrating applications to solve multiscale multiphysics problems