## Slide 1: Monitoring
From Requirements to Autonomous Flight
Swee Balachandran3, Esther Conrad1, Aaron Dutle1, Dimitra Giannakopoulou2, Alwyn Goodloe1, Anastasia Mavridou2,4, César Muñoz1, Ivan Perez3, Laura Titlolo3
1NASA Langley Research Center
2NASA Ames Research Center
3National Institute of Aerospace
4KBR, Inc.

## Slide 2: Why Runtime Monitors?
Verification is hard
  Large, complex system built of diverse components.
  Components may not be designed with formal verification in mind.
Runtime Monitors are flexible
  Monitor and alert for unexpected events, instead of verify they don’t happen.
  Easier to add new monitors than verify new properties.
Can allow for integration of untrusted components (when Simplexed)
The project is a research demonstration of monitors as an alternate/additional means to assure safety.

## Slide 3: Goal: Simple, accurate, integrated monitors
Write or select requirements in a natural(ish) language.
Create (automatically!) safe monitors in software.
Integrate them into an autonomous flight system.

## Slide 4: Goal: Simple, accurate, integrated monitors
Write or select requirements in a natural(ish) language.
Create (automatically!) safe monitors in software.
Integrate them into an autonomous flight system.

## Slide 5: Project Workflow
ICAROUS-specific requirements
FRET translation to Copilot
Monitor integration
ICAROUS

## Slide 6: Tool Descriptions
ICAROUS-specific requirements
FRET translation to Copilot
Monitor integration
ICAROUS

## Slide 7
For more details, see the FRET website: https://github.com/NASA-SW-VnV/fret

## Slide 8: Copilot
Runtime verification language & framework that produces hard real time C99 code.
For details, see the Copilot website: https://copilot-language.github.io/ and the NASA Technical Manual 2020–220587 "Copilot 3".
Copilot Specification
(eDSL)
C99 implementation
Object file
C compiler
Copilot Compiler

## Slide 9: Copilot ICAROUS Monitor Example
elevation :: Stream Double elevation = extern ”elevation” Nothing
−− Estimate derivative by delaying the elevation
climbrate :: Stream Double climbrate = elevation − ([0] ++ elevation)
falling :: Stream Bool
falling = climbrate < (−6)
−− Specification that defines triggers based on streams
spec :: Spec spec = do
trigger ”falling” falling [arg counter, arg climbrate]
trigger ”not fallen” (alwaysBeen (not falling)) [] -- PTLTL
Defined as a function in a CFS application in C
Defined as a global variable in a CFS application in C

## Slide 10
Architecturally:
Separate software modules, with extensibility
Some included modules have formal verification
Publish -- Subscribe communication
Built on NASA-pedigreed core Flight System platform
Detector A
Functionally:
Mission applications maintain and achieve goals
Detectors anticipate upcoming problems
Resolvers avoid problems discovered by detectors
Decision making layer negotiates and communicates
For more details, see the ICAROUS website: https://github.com/nasa/icarous

## Slide 11: Integration
ICAROUS-specific requirements
FRET translation to Copilot
Monitor integration
ICAROUS

## Slide 12: ICAROUS-specific requirements
Current ICAROUS interface to set waypoints, geofences, change parameters
Monitors:
Collision Avoidance
250 ft
Horiz
50 ft
Vert
Enabled
Geofence Standoff
25 ft
Enabled
Path Deviation
100 ft
Disabled
Custom Monitor
Generate Monitors
Cancel Changes
“Monitors” pane concept

## Slide 13: ICAROUS-specific requirements: Current Issues
FRET allows arbitrary variable names in specification
  Restrict the interface to only see or allow systems/signals available
  Requires cataloging of available ICAROUS-published signals
Tablet interface is used post-installation of ICAROUS
  Generating, compiling, and installing C on-board sUAS is tricky
  Custom requirements require full FRET and Copilot
  Parametric template monitors from the interface?
    Current Copilot doesn’t support parametric C code
Properties concerning all traffic, all geofences
  "Spawning” monitors is a bad idea with limited resources.

## Slide 14: FRET translation to Copilot
OGMA is a tool that translates temporal expressions into Copilot monitors.
FRET
Copilot
Monitor
OGMA
Lustre
C99 implementation
Object file
C compiler
Copilot

## Slide 15: FRET translation to Copilot
OGMA is a tool that translates temporal expressions into Copilot monitors.
FRET
Copilot
Monitor
OGMA
Lustre
C99 implementation
Object file
C compiler
Copilot

## Slide 16: Monitor Integration
Developing a “Runtime Verification” module for ICAROUS
  Receives data requirements for monitors at start, subscribes accordingly
  Provides data to the Copilot generated monitors
  Monitors have no feed-back into ICAROUS functions (no side-effects)
  Violation alerts are raised to the operator/logged
Monitors
Module
Copilot Generated Monitors
Firewall
Violation Alert

## Slide 17: Current Project status
ICAROUS requirements/interface:
  Catalog ICAROUS signals
  Develop user interface for templates and custom requirements
  Overcome generating monitors post-installation
FRET to Copilot translation:
  Fret output accepted by Ogma
  Ogma creates Copilot monitor
Monitor Integration:
  Prototype monitors module created

## Slide 18: Tangents, Future work
PVS Specification of the syntax and semantics of FRETish.
  Proving equivalence of FRET evaluation on traces with LTL translations.
Future: Check conformance of the generated monitor with the original requirement?
  By construction? (Likely very difficult)
  Verify on a per-monitor basis after generation? (Easier perhaps)
Future: Use RV in a Simplex architecture for ICAROUS.
  Use modular architecture to cut off ICAROUS interaction when untrusted component causes violation.