## Slide 1: NearField Summary and Analysis of the Third AIAA Sonic Boom Workshop Shock-Plume Interaction Case
Melissa Carter &
Michael Park
NASA Langley Research Center
Copyright 2021 United States Government as represented by the Administrator of the National Aeronautics and Space Administration. No copyright is claimed in the United States under Title 17, U.S. Code. All Other Rights Reserved. Published by the American Institute of Aeronautics and Astronautics, Inc. with permission.

## Slide 2: Workshop Objective
The objective of the Third Sonic Boom Prediction Workshop was to assess the state of the art for predicting nearfield signatures with Computational Fluid Dynamics (CFD) and propagation codes used to propagate nearfield signatures to the ground.

## Slide 3: 3rd Workshop: 23 participants
ANSYS
Boeing
Boom Aero
DASSAV
DLR
FAA
INRIA
JAXA
Lockheed Martin
Metacomp
NASA
Northwestern Polytech
ONERA
Penn State
Siemens
Texas A&M
Volpe

## Slide 4: Workshop Culture
Adjectives such as good, bad, right, and wrong oversimplify issues and should be avoided
Focus on describing observed differences and communicate why things are different

## Slide 5: Models and Cases
Ames 9’x7’ UPWT Biconvex Plume-Shock Interaction Case
C608, an early X-59 Prototype
IGES and STEP geometry files along with workshop generated grids provided
Biconvex
C608

## Slide 6: Biconvex computational model
Biconvex
Nozzle lip

## Slide 7: Simulation Conditions
1.6 Mach
0.0 angle of attack
0.0° angle of attack
Geometry and grid provided in correct orientation
374 degrees Rankine temperature
376,850 Reynolds number per inch
8.0 Engine plenum pressure ratio, PT/P∞
1.768 Engine plenum temperature ratio, TT/T∞
Data extracted at Z~15 inches, at 3 Phi angles
Phi angles of approx. 0, 15 and 30
Phi angles of approx. 0°, 15° and 30°
1.6 Mach
Geometry and grid provided in correct orientation
374 degrees Rankine temperature
376,850 Reynolds number per inch
8.0 Engine plenum pressure ratio, PT/P∞
1.768 Engine plenum temperature ratio, TT/T∞
Data extracted at Z~15 inches, at 3 Phi angles
7

## Slide 8: Grid Details
Scale | Nodes | Tetrahedral
1.57 | 846,227 | 4,785,786
1.28 | 1,576,352 | 8,977,516
1.00 | 3,286,221 | 18,815,990
Scale | Nodes | Tetrahedral | Prisms | Pyramids
1.57 | 846,227 | 2,825,421 | 650,469 | 4479
1.28 | 1,576,352 | 5,984,989 | 993,489 | 6030
1.00 | 3,286,221 | 14,627,534 | 1,388,470 | 11523
Tetrahedral Grids
Mixed-Element Grids

## Slide 9
Grid 100 (fine grid) Tetrahedral
Signature is ~15” below the model

## Slide 10: BiConvex Submissions

## Slide 11: BiConvex
Grid 100
Tetrahedral
USM3D
Production
code
dp/p∞ which is the pressure disturbance normalized by freestream pressure
~15"
Nose
shock
Nozzle
lip shock
Biconvex
shock
Strut
shock

## Slide 12: BiConvex density gradient
Grid 100
Tetrahedral
USM3D
Production
code
Density gradient

## Slide 13
PHI=0°
N=31
BiConvex Fine-Grid
dp/p∞

## Slide 14
BiConvex Fine-Grid
PHI=15°
N=31
dp/p∞

## Slide 15
BiConvex Fine-Grid
dp/p∞
PHI=30°
N=31

## Slide 16: Biconvex Fine-Grid Ensemble With Standard Deviation
dp/p∞
PHI=0°
N=31

## Slide 17: Identification of Outliers
Goal is to use an objective tool to identify and learn from differences in submissions
Previous workshop used box and whisker plots with an effective coverage factor of 2 (exceed 95% likelihood)
Coverage factor of 1 (exceed 68% likelihood) used here

## Slide 18: SBPW2 C25P Context
PHI=0°
1 Body Length
dp/p∞

## Slide 19: Biconvex Fine-Grid Ensemble With Standard Deviation
dp/p∞
PHI=0°
N=31

## Slide 20: Nozzle Lip Shock
PHI=0°
dp/p∞
dp/p∞

## Slide 21: Nozzle Lip Shock Integral Outliers
dp/p∞
PHI=0°
dp/p∞

## Slide 22: BiConvex Shock
dp/p∞
PHI=0°
dp/p∞

## Slide 23: BiConvex Shock Outliers
dp/p∞
dp/p∞
PHI=0°

## Slide 24: Biconvex Summary
Participant submissions tightly grouped and strict criteria required to identify outliners
Outliers were identified in multiple regions:
  Majority of outliers from the nozzle lip shock were from participant created grids
  Three outliers from the biconvex shock solutions provide an opportunity to further investigate the cause of the slight differences

## Slide 25: Conclusions
Sincere thank you to all the participants!
These cases included propulsion boundary conditions and realistic geometry making them the hardest attempted in the workshop series
The variation is lowest of SBPW, requiring a stricter criterion to identify outliers
  A coverage factor of one was used (outliers exceed 68% likelihood) via sample mean and standard deviation
  SBPW-2 coverage factor of two (outliers exceed 95% likelihood) via box and whisker plots