## Slide 1
James Ecker, Benjamin Kelley, Danette Allen
AIAA SciTech, January 2021
Synthetic Data Generation for 3D Mesh Prediction and Spatial Reasoning During Multi-Agent Robotic Missions
Notes: Shorten examples

## Slide 2: Computer Vision During In-Space Assembly
Difficulties
  Illumination
  Angle
  Orientation
  Movement
Constraints
  Energy
  Mass

## Slide 3: Computer Vision During In-Space Assembly
Difficulties
  Illumination
  Angle
  Orientation
  Movement
Constraints
  Energy
  Mass
High Degree of Variation Requires More Information

## Slide 4: Computer Vision During In-Space Assembly
Difficulties
  Illumination
  Angle
  Orientation
  Movement
Constraints
  Energy
  Mass
High Degree of Variation Requires More Information
More Sensors = More Information = More Energy Use & More Mass

## Slide 5: Mitigating the Constraints
High Degree of Variation Requires More Information
More Sensors =
More Information =
More Energy Use & More Mass

## Slide 6: Mitigating the Constraints
High Degree of Variation Requires More Information
More Sensors =
More Information =
More Energy Use & More Mass
Maximize

## Slide 7: Mitigating the Constraints
High Degree of Variation Requires More Information
More Sensors =
More Information =
More Energy Use & More Mass
Maximize
Minimize

## Slide 8: Mitigating the Constraints
High Degree of Variation Requires More Information
More Sensors =
More Information =
More Energy Use & More Mass
Maximize
Minimize
Predict 3D Mesh from Single View

## Slide 9: Mitigating the Constraints
High Degree of Variation Requires More Information
More Sensors =
More Information =
More Energy Use & More Mass
Maximize
Minimize
Single Camera
Predict 3D Mesh from Single View

## Slide 10: Related Work
[1] He et al – Mask R-CNN
[2] Gkioxari et al – Mesh R-CNN
[3] Sonawani et al - Assistive Relative Pose Estimation for On-orbit Assembly using Convolutional Neural Networks
[4] Pal et al - 3D Point Cloud Generation from 2D Depth Camera Images using Successive Triangulation
[5] Valsesia et al - Learning Localized Representations of Point Clouds with Graph-Convolutional Generative Adversarial Networks
[6] Ramasinghe et al - Spectral-GANS for High Resolution 3D Point Cloud Generation

## Slide 11: Synthesizing Data
3D model of objects projected over 3D background in Blender
  Can be extended to full simulation environments
    ROS, Gazebo, Mujoco, etc
Variations in observations
  Orientation of camera and light source
  Relative orientation between objects
  Number of objects in scene
  Background
Sim to Reality Problem
  Domain Randomization

## Slide 12: Metadata for Training Mask R-CNN

## Slide 13: Metadata for Training Mesh R-CNN

## Slide 14: Building the Dataset
Generate a parent pool of data
  20,000 image/metadata pairs
For each sample generated
  Extract/Calculate ground truth to build metadata
  Configure metadata to conform to model
Sample training set from parent pool
  Sample –n (default: 1500) instances from parent pool randomly
  Split into training and validation sets
    --training-split (default:0.75) / 1 - --training-split (default: 1 – 0.75 = 0.25)
Merge all training/validation set metadata into one JSON, respectively

## Slide 15: Mask Prediction – Mask R-CNN
Backbone
  Resnet-50-FPN
Region Proposal Network
  Applies a sliding window over a convolutional feature map to generate proposed bounding boxes for likely objects
  Proposed regions are aligned to the feature map and sent to fully connected layer to classify a bounding box (regressor) and the object itself (soft max)
Mask Prediction
  Generate a binary mask for pixels in proposed region using the aligned features
The Mask R-CNN Architecture [1]

## Slide 16: Mask Prediction – Mask R-CNN Advantages
Transfer Learning
  Use a pretrained network (Resnet) to initialize weights instead of training from scratch (random initial weights)
  Lowers training time and generalization error
Region of Interest Alignment
  Each region of interest is fed into a fixed-size input fully connected (FC) layer
  Need to account for all pixels in ROI while conforming to fixed input size of FC
  Bilinear Interpolation instead of Quantization
The Mask R-CNN Architecture [1]

## Slide 17: Mask Prediction – Mask R-CNN Advantages
Transfer Learning
  Use a pretrained network (Resnet) to initialize weights instead of training from scratch (random initial weights)
  Lowers training time and generalization error
Region of Interest Alignment
  Each region of interest is fed into a fixed-size input fully connected (FC) layer
  Need to account for all pixels in ROI while conforming to fixed input size of FC
  Bilinear Interpolation instead of Quantization
Masks provide a measure of visual explainability
The Mask R-CNN Architecture [1]

## Slide 18: Mask Prediction – Mask R-CNN Performance
98% instance segmentation accuracy
  object
  bounding box
  mask

## Slide 19: Mesh Prediction
Extends Mask R-CNN
  Mesh Predictor
    Voxel Prediction
    Mesh Refinement
The Mesh R-CNN Architecture [2]

## Slide 20: Mesh Prediction
Extends Mask R-CNN
  Mesh Predictor
    Voxel Prediction
      Predicts a voxel occupancy grid
      Cubify function binarizes voxel occupancy probabilities according to a threshold and generates a cuboid triangular mesh for each likely voxel
    Mesh Refinement
The Mesh R-CNN Architecture Voxel Branch[2]

## Slide 21: Mesh Prediction
Extends Mask R-CNN
  Mesh Predictor
    Voxel Prediction
      Predicts a voxel occupancy grid
      Cubify function binarizes voxel occupancy probabilities according to a threshold and generates a cuboid triangular mesh for each likely voxel
    Mesh Refinement
      2 passes
        Vertex alignment
        Graph convolution
        Vertex refinement
The Mesh R-CNN Architecture Mesh Refinement Branch[2]

## Slide 22: Metrics
Chamfer distance
  Where point is the closest neighbor to in point cloud
Normal distance
  Where is the unit normal to point in point cloud
Edge loss
Where⊆×are the edges between each vertex ∈ in the predicted mesh

## Slide 23: Results
Ours (Custom Synthetic Data)
  Chamfer (lower is better)
    0.621
  F1 (higher is better)
    47.51
Theirs (Mesh R-CNN trained on Pix3D)
  Chamfer (lower is better)
    0.306
  F1 (higher is better)
    74.84

## Slide 24: Results
Ours (Custom Synthetic Data)
  Chamfer (lower is better)
    0.621
  F1 (higher is better)
    47.51
Theirs (Pix3D)
  Chamfer (lower is better)
    0.306
  F1 (higher is better)
    74.84
2 Quadro 6000 RTX GPUs
8 Tesla V100 GPUS
Requires hyperparameter tuning specific to hardware configuration

## Slide 25: Conclusion
Generated a synthetic dataset capable of training state of the art 2D mask and 3D mesh prediction models
Can train each model end-to-end from no data to trained model
Future work
  Hyperparameter tuning
  Further domain randomization
    Randomize object’s rendered skin
  Extending Mesh R-CNN to use a Generative Adversarial Network to generate point clouds instead of voxel model
    Higher resolution 3D mesh prediction

## Slide 26: References
He, K., Gkioxari, G., Dollár, P., and Girshick, R., “Mask R-CNN,”2017 IEEE International Conference on Computer Vision(ICCV), 2017, pp. 2980–2988. https://doi.org/10.1109/ICCV.2017.322.
Gkioxari, G., Johnson, J., and Malik, J., “Mesh R-CNN,”2019 IEEE/CVF International Conference on Computer Vision(ICCV), 2019, pp. 9784–9794. https://doi.org/10.1109/ICCV.2019.00988.
Sonawani, S. D., Alimo, R., Detry, R., Jeong, D., Hess, A., and Amor, H. B., “Assistive Relative Pose Estimation for On-orbitAssembly using Convolutional Neural Networks,”ArXiv, Vol. abs/2001.10673, 2020.
Pal, B., Khaiyum, S., and Kumaraswamy, Y. S., “3D point cloud generation from 2D depth camera images using successivetriangulation,”2017 International Conference on Innovative Mechanisms for Industry Applications (ICIMIA), 2017, pp. 129–133.https://doi.org/10.1109/ICIMIA.2017.7975586.
Valsesia, D., Fracastoro, G., and Magli, E., “Learning Localized Representations of Point Clouds with Graph-ConvolutionalGenerative Adversarial Networks,”IEEE Transactions on Multimedia, 2019.
Ramasinghe, S., Khan, S. H., Barnes, N., and Gould, S., “Spectral-GANs for High-Resolution 3D Point-cloud Generation,”CoRR, Vol. abs/1912.01800, 2019. URL http://arxiv.org/abs/1912.01800.
Tobin, J., Fong, R., Ray, A., Schneider, J., Zaremba, W., and Abbeel, P., “Domain Randomization for Transferring Deep NeuralNetworks from Simulation to the Real World,”CoRR, Vol. abs/1703.06907, 2017. URL http://arxiv.org/abs/1703.06907.
He, K., Zhang, X., Ren, S., and Sun, J., “Deep Residual Learning for Image Recognition,”CoRR, Vol. abs/1512.03385, 2015.URL http://arxiv.org/abs/1512.03385.