## Slide 1: Clinical Decision Support – ConOps
B. Russell, M. Krihak, S. Shetye, K. Martin and T. Shaw
2021 NASA Human Research Program Investigators' Workshop
February 2021

## Slide 2: Outline
Clinical Decision Support (CDS) background
Defining a Clinical Decision Support System (CDSS) for exploration
Technology Development Plan – how Concept of Operations (ConOps) are used in the process
Example ConOp
Investigate the questions of operation, implementation and validation of CDS in long duration exploration missions
Research
  clinical workflow and user interaction for different scenarios
  models and datasets required
  architecture required to incorporate third party models and apps
  inter-dependency of CHP domains
Notes: BACK GROUND:
The CDS project address the need for crew to operate independently during long duration space exploration missions investigating level of care and increased crew autonomy in the domains of crew clinical, health and performance.
The project investigates the various implementation challenges for select scenarios associated with LevCare IV and V, requiring long duration autonomous missions.
The project uses software prototypes to generate requirements and identify impacts to CHP architecture and systems.
The goal of the CDS project is to recommend requirements for an in vehicle system addressing mass, volume, power, crew time and medical capabilities.
CDS FOR EXPLORATION:
The role of a CDS is to augment KSA for all crew in various scenarios related to CHP.

## Slide 3: Need for Crew Self-Reliance
NASA-STD-3001 presents the need for crew members to operate independently during long duration space exploration missions that require medical Level of Care V
  Interpretation of NASA-STD-3001 Levels of Care for Exploration Medical System Development (NASA/TM-2017-219290):
    Maintains ‘autonomous’ in the description of capabilities and definitions that pertain to medical Level of Care V.
Computational and data resources will play an important role in maintaining crew health, wellness and performance where the crew will need to be more self-reliant.
  Communication lags (~20min each way on a Mars mission)
  Communication blackouts, planned and unplanned

## Slide 4: Clinical Decision Support Background
ExMC Element Risk:
Risk of Adverse Health Outcomes & Decrements in Performance due to Inflight Medical Conditions
Clinical Decision Support (CDS) Project Need:
ExMC Gap Medical-701: Enhance medical capabilities within an exploration medical system.
CDS Project Goal:
The aim of the CDS project is to develop and provide recommended requirements for an in-vehicle CDS System (CDSS) that acts as an assistant for delivering optimal health and performance and medical care during exploration missions.
Notes: The CDS project addresses medical risk and identified gaps.
Clinical care includes clinical scenarios and prevention to maintain crew health and performance.

## Slide 5: CDS Technology Development Plan
Requirements
Demonstrations
SysML Model
Deliverables
Evidence
Reference Documents
Liaison - Industry and Agency’s
Liaison - HRP Projects
Liaison - R&D Funding
Datasets
Autonomy approaches
Additional evidence types…
Tech Risks
Datasets
Models
Architecture (library)
Interoperability
Clinical
Work flow
Model validity
Scientific
Gap
Tasks
Testbed
Documentation
Start with Evidence
  Risk based gaps
    Tasks to close gaps
      Deliver requirements
Process to be implemented starting FY21
Source:
ExMC Clinical Decision Support Project Exploration Medical Capability Clinical Decision Support Technology Development Plan Doc. No. 7868
Notes: The TDP starts by collecting evidence including AMCL, HRP Risks, medical knowledge, datasets and similar approaches in the diff fields.
Con Ops are developed and gaps are identified that are defined as use Cases with implementation guidance to the SW team to maximise coverage of various categories, maximising the utilisation of various categories including, work flow, user interface, instruments to fly and models.
EXAMPLE:
The example Con Op toady will be for Kidney Stone, which is an identified medical risk.

## Slide 6: FUNCTIONALITY OF CLINICAL DECISION SUPPORT
DATA
DERIVED DATA
CLASSIFICATION/
REGRESSION
DIAGNOSTICS
PROBABILISTIC CDSS
HEURISTIC - PERSON
TREATMENT
KNOWLEDGE BASED
CARE GIVER/
CONTEXT BASED
SENSORS
INSTRUMENTS
LAB TEST
RESOURCES
Pharmacy, Consumables
MISSION TIME
Predicted remaining conditions
CLINICAL ALGORITHM
VITAL SIGNS
ALERTS
IMAGE ANALYSIS
INSTRUMENT GUIDANCE
DIAGNOSIS
GUIDANCE
High Acuity
Low Acuity
CONTEXT AWARE SYSTEM
CLINICAL AND PERFORMANCE MANAGEMENT
MEDICAL HISTORY
Existing conditions
PREVENTION
PERFORMANCE OPTI
KNOWLEDGE BASED
SCHEDULING
Emergency
Symptom
Scheduled
Alert
Inquiry
Scenarios
Training
Notes: A CDS system
is used in difference scenarios
must be context aware to change how it interacts with the user to maximum their cognition and performance
is made up of an architecture of data and algorithms to perform diagnosis, treatment and prevention

## Slide 7: Datasets, Models and UI/UX
CLINICAL
User Interface
Medical Data
Architecture
Model
Decision
Model
2. Kidney Model
calculates probability
3. Graphical interface takes CMO through diagnosis
with automated suggestions
Drag and drop patient history, daily data, blood and urine
Database
Data Bus
Database
Model
Clinical Decision Support System
Kidney
Model
Notes: A CONOP scenario is broken down into three main groups, user interface, models and data.
Firstly the workflow is developed, then datasets and models identified to enable the scenario.
The development process works through a user workflow, then addresses the datasets required, which models can be used, any API updates and external models from collaborators.

## Slide 8: Kidney Stone from Symptom ConOp
CLINICAL
LOGIN
Nutrition
Plan
Kidney Diagnosis Probability
Medical
History
Symptoms
Sensors
Lab
Tests
HOME
Exercise
Plan
Kidney Model
1
LOGIN.
2
SELECTION.
3
CLINICAL
Decision
Engine
Enter Symptoms
Request Info
Enter Dara
4
EXTRA INFO
1
Before mission
DATASETS
0
1
During mission
DATASETS
1
MDA Infrastructure Bus
Reference Model
5
Precipitation model
PROBABILISTIC ANALYSIS
6
USER
INTERFACE
LAYER
MEDICAL
DATA
ARCH
DECISION
SUPPORT
LAYER
7
UPDATE EHR
SCHEDULE
SCHED EXAM
8
Data
Ingestion
Engine
0111001
time trigger
user trigger
event trigger
Notes: The ConOps to diagnose kidney stones requires a clinical diagnostic.
The diagnosis implementation starts with a chief complaint, diagnosis using interactive probabilistic model based decision making supported by physics based models determining risk
When a crew member presents with a symptom of ‘lower flank pain’, the inference engine determines possible diagnosis by referring to the models and determining the ‘next best question’ to determine the probability of each condition.

## Slide 9
Chief complaint
GUI
Screen, mouse, keyboard
Instruments
Ask related symptoms
Blood report
Urine report
Diagnosis
Treatment
Find related diseases
Ask related history
Measure vital signs
Request blood data
Vital signs
Kidney model data
Lab Equipment
Model
Inference engine + knowledge base
Data
Medical Resources
EHR
History QnA
Symptom QnA
vitals
needed?
Y
N
Diagnosis is updated and displayed after each step. Some steps and GUI operations are omitted for simplicity.
Exam
needed?
Y
N
Blood lab
needed?
N
Y
Urine lab
needed?
N
Y
Request urine data
Final Diagnostic
Request prediction data
prediction data
available?
N
Y
perform physical exam
Procedural Guides
and
Diagnostic updates
Disease
probability,
severity,
prediction confidence
Diagnostic Flow Chart
Lab Equipment
Notes: Here is a swim lane diagram for the clinical algorithm in the context of the CDS system interacting with the crew via the GUI and referring to available and relevant data in the data base, while the inference engine determines the best questions to ask to increase the confidence of its diagnostic prediction.

## Slide 10: Sequence Diagram
Update Prediction
Chief complaint
Find related diseases
Inference Engine
GUI
Knowledge Base
Instruments
Ask related history
Find related history
Ask related symptoms
Predictions
Kidney Model
Request related prediction data
Diagnosis
Treatment
system actors
CDS
Diagnosis
Find related symptoms
Update Prediction
Find related prediction data
Update Prediction
Request vital signs
Instrument Data
Find related vital signs
Request blood report
Blood Report
Find related blood data
Request urine report
Blood Report
Find related urine data
Update Prediction
Update Prediction
Update Prediction
Notes: A sequence diagram enables us to understand how different parts of the system communicate. This is important to develop API interfaces and processes ti enable modellers to supply their models in a way that the CDS architecture can utilise them.

## Slide 11: ConOps and Use Cases – Coverage of Architecture
Heart Rate
Sensor
Store data
Calculate
Calories
Historical
CMO vs CM view of data
Kidney Stone Diagnosis
Exercise from Epic 2
Cognitive
Patient History
Blood Labs
Urine Labs
Daily Data
Store data
CMO vs CM view of data
Kidney Model
Kidney clinical algorithm
Kidney Diagnosis
Diagnosis
Workflow
Cognition Test
VOLT config + images
Cognition Test Protocol
VOLT Test
VOLT Test
Response Times
Process Lab Reports
Key: Color is used to show each Use Case
Clinical
Exercise
Neuroscience
Domain
Schedule
Exercise
Event
Perform
Live
Exercise
Analyse
Historical
Data
Notes: This slide shows the systematic approach to use case scenarios to cover broad functionality based on ConOps scenarios. This an important aspect of the CDS project researching implementation approaches.
The AMCL has 140 conditions so any approach we take must scale to cover at least this many conditions.

## Slide 12: CDS Screenshot – Kidney Stone Diagnostic
Diagnosis screen
Blood report
Questions
Log
Vital Signs
Lab Reports
# | DISEASE | P R O B | S E V | CON
1 | Kidney Stones | 75 | 50 | 80
2 | Pyelonephritis | 22 | 50 | 70
3 | ACS | 11 | 90 | 40
4 | Anxiety | 15 | 20 | 55
5 | Atrial Fib | 05 | 80 | 43
6 | Heedache CO2 | 10 | 30 | 80
7 | Space Motion Sickness | 13 | 10 | 40
1. 2. 3. 4. 5. 6. 7.
Diagnostic Report
Notes: CDS is a research project to explore HOW to do this work as there is no standard approach at present data, decision tools and workflow can assist the clinician in their decision making.
Here is an example screenshot from the kidney stone ConOps for the GUI during the diagnostic process.

## Slide 13: Summary
CDS development in ExMC develops test beds and requirements
Focus is LevCareV for exploration missions to increase crew autonomy
HRP gaps and evidence are used to determine ConOps. Use Cases develop further detail to answer implementation questions including:
  Context aware user interfaces
  API based architecture for to incorporate models from different groups
  Validation on model approach and accuracy
  Determine what datasets are required
  Determine a validation strategy
  Uncover and address process challenges