## Slide 1: Conjunction Assessment Risk Analysis for Smallsats
Lauri K. Newman
NASA CARA Manager
Jan 12, 2021

## Slide 2: Agenda
NASA CARA Process
Changing Space Environment
Risk Assessment
NASA CA Best Practices

## Slide 3: NASA CARA Process
  The NASA Conjunction Assessment Risk Analysis (CARA) program has provided CA services to the Agency’s unmanned missions since 2004
    Largest single governmental organization that performs CA risk assessment
    Includes CA ops, SME support, and internationally-recognized R&D
    Well-honed relationship with DoD data providers, international partners, and commercial entities
  CARA provides CA support, risk analysis, and mitigation for all NASA non-human spaceflight (HSF) missions (~70 spacecraft)
  NASA requires CA for all operational missions regardless of orbit, maneuver capability, or size
CARA Orbital Safety Analysts at 18th Space Control Squadron (18 SPCS)
NASA CARA
Missions
Conjunction Assessment
Risk Analysis
Risk Mitigation
Close approach predictions
-State and state uncertainty data
-Force model information
-Orbit Determination quality and tracking
Conjunction risk assessment & mitigation recommendations

## Slide 4: Changing Space Environment
Dramatic increase in owner/operators (O/O), orbital objects, and associated launches
  More independent operators with varying expertise and capabilities, some with invalid assumptions (including about Government-provided services)
  Large constellations in progress (e.g., OneWeb, Starlink, Kuiper) using novel techniques
    Ex. 1500 Starlink spacecraft in ~550 km (circular) orbit
Challenge areas include:
  Launch injections of 60-100 payloads at once, without enough separation to be easily trackable
    Can take 7-14 days to catalogue
  Onboard autonomous maneuvering, including on-board Conjunction Assessment
  Maneuvering without CA screening of maneuver ephemeris, which can prevent other operators from having position knowledge
  No established community best practices
Challenge in educating new space actors on best practices and availability of data and tools

## Slide 5: “Small” Doesn’t Mean “Safe”
Small satellites can destroy large satellites and create large debris clouds as effectively as orbital debris
Small satellites must be tracked in order to prevent collisions
  Small satellites are harder to track, and some have been smaller than US Space Force’s (USSF) regular tracking threshold
  Many small satellite operators do not compute ephemerides and rely on Two-Line Elements (TLEs), making Space Surveillance Network (SSN) tracking essential to their position determination
Maneuverable satellites, even if small, must have maneuvers screened
  CA is not effective if screenings cannot be performed against intended trajectories
In short, small, less expensive satellites require the same CA as large satellites

## Slide 6: Risk Assessment
CA screenings determine which space objects will have close approaches with a protected asset, several days in advance
  Often many close approaches, few result in safety of flight concerns
Risk assessment is the practice of determining which close approaches present a serious collision risk
  Precision state and covariance data are required
  Advanced probabilistic calculations and data analysis are performed
  Enables mitigation action decision
Risk assessment is thus an essential component to CA
  Necessary for operational application
  Conjunction Data Messages (CDMs) are screening data to be analyzed for risk – they are not warnings that indicate an action is necessary
  Meaningful risk assessment is not possible with TLEs, as there is no associated covariance
Risk assessment is not performed by US Space Force (USSF) 18th Space Control Squadron — they provide screenings only

## Slide 7: Protecting the Space Environment
A robust Conjunction Assessment process is necessary because
  Risk is not just to the protected spacecraft but also to the space environment
  Loss of one cubesat may be tolerable to the owner of a large constellation from a mission performance standpoint, but could put hundreds of pieces of debris in the environment used by other spacecraft
  Even if a smallsat is non-maneuverable, the other object may be maneuverable and coordination with the other operator is thus warranted
Be a responsible operator via best practices for space safety
Sources of existing best practices:
    Best practices for 18 SPCS support are available on Space-Track.org website
    Secure World Foundation publishes “Handbook for New Actors in Space”
    Best practices for satellite operations at Spacesafety.org
    CONFERS publishes best practices for Proximity ops
    NASA published CA best practices Handbook in December; contains analysis describing the technical/scientific foundations of best practices

## Slide 8: Best Practice: Don’t Use Two-Line Elements (TLE) for CA
Available only for objects in public catalog, so screening against TLEs misses a large portion of the full catalogue
No covariance information (crucial for Probability of Collision calculation)
Accuracy is only on the order of 1-2km within a few days of the epoch of the element set – not sufficient for CA per 18 SPCS https://www.space-track.org/documentation#/user_agree
Uses for TLEs:
  Can provide the state (position and velocity) predictions with enough accuracy to allow reaquisition
  Can be mined for maneuver information about other objects

## Slide 9: Best Practice: Robust Risk Assessment
The Probability of Collision (Pc) or equivalent metric must be computed, requiring:
  Accurate owner/operator (O/O) ephemeris with realistic covariance
  Defined size of protected asset (to allow calculation of hard-body radius)
Ephemerides should be sent to 18 SPCS for screening
  Maneuverable payloads need to provide statement of predicted position that includes planned maneuvers—only way to perform useful CA screenings
  Providing of ephemerides is the only reliable way to communicate future positions to users of autonomous flight control and navigation (e.g., Starlink)

## Slide 10: Best Practice: Trackability
Technology advances make possible spacecraft that are too small to be tracked by the SSN
  SSN is the DOD USSF resource assigned to track all on-orbit objects
  Objects must be ~10 cm to be tracked reliably by more than one sensor
  CA can be performed only against objects in the catalog
Un-trackable objects on orbit pose threat to flight safety
Basic actions to advance safety of flight:
  Ensure objects be large enough to be tracked passively on-orbit
  At injection, make sure object placed far enough away from other deployed sats and on-orbit objects to allow unique, unambiguous tracking
Potential workarounds include:
  Active tracking (e.g. beacon), though may not be sufficient after mission end (e.g., beacon becomes inactive)
  Laser reflectors, so long as tracking service operative and funded
  Providing O/O ephemerides of sufficient accuracy and realism to 18 SPCS

## Slide 11: Best Practice: Safe Autonomous Maneuvering
Large constellations are achieving economy of scale through increased automation and autonomy of flight dynamics
Automated on-board maneuvering and CA practices may prevent CA screening of maneuvers and hence add flight safety risk
  Maneuvers planned/executed only a few hours in advance—no time or mechanism for CA screenings
  Satellites cannot know maneuver intentions of non-constellation spacecraft
  Without coordination, there is no way to ensure safety
    Ex. If two satellites autonomously plan mitigations to avoid collisions with each other, result might be for both satellites to maneuver into each other
NASA missions employing autonomy required to ensure flight safety
  Ability to notify ground controllers of any autonomous maneuvers planned or taken, including characteristics of the maneuver
  Ability for the ground controllers to pause or abort planned autonomous maneuvers
  Accurate on-ground emulation capability that can reasonably predict the autonomous behavior and give advance notice of maneuver plans

## Slide 12: NASA Points of Contact
Feedback on general technical and handbook topics:
ca-handbook-feedback@nasa.onmicrosoft.com
Support to specific space flight missions:
  Human spaceflight (HSF) missions: JSC Flight Operations Directorate (FOD) jsc-dl-topo-iwg@mail.nasa.gov
  Non-HSF missions: Conjunction Assessment Risk Analysis (CARA) program cara-management@lists.nasa.gov
NID 7120.132: Collision Avoidance for Space Environment Protection https://nodis3.gsfc.nasa.gov/OPD_docs/NID_7120_132_.pdf
NASA Spacecraft Conjunction Assessment and Collision Avoidance Best Practices Handbook https://nodis3.gsfc.nasa.gov/OCE_docs/OCE_50.pdf
NASA OCE web site with FAQs and future content: https://www.nasa.gov/oce