## Slide 1: Quantifying Performance Requirements for Next-Generation Spaceborne Aerosol Lidars
AMS Annual Meeting, 10-14 Jan 2021
Dave Winker1, Mark Vaughan1, Stuart Young2, Travis Toth1,
Kathy Powell1 and Anne Garnier3
NASA Langley Research Center, Hampton, VA
CISIRO, Aspendale, Australia (retired)
NASA LaRC/SAIC, Hampton, VA

## Slide 2: Motivation
A question before the ACCP study team:
How can we improve on CALIOP performance?
  Better SNR  better spatial resolution than CALIOP
    PBL height
  More accurate AOD
    Climate forcing from aerosol radiative effects at TOA and surface
  More accurate near-surface aerosol extinction
    Air Quality
    Model evaluation (surface is an aerosol source)
A few issues
  How to flow science requirements defined for ACCP down to instrument design requirements?
  What are the best performance metrics?
  Better quantify CALIOP performance as a baseline

## Slide 3: Current state of global AOD datasets
CALIOP biased low due to undetected aerosol
MODIS likely biased high, due to cloud masking biases, 3D scattering
Kim et al (JGR 2017):
Estimate CALIOP daytime global mean AOD bias of 0.036 due to undetected aerosol (25%)
See also:
  Thorsen et al (GRL 2017)
  Toth et al. (AMT 2018)
(Sayer et al., JGR, 2018).
Global-mean over-ocean AOD

## Slide 4: Power-Aperture Product as a Simple Metric
Power aperture product: PxA = J x pps x D2
  Is proportional to signal and is related to SNR
  Useful for a relative ranking of performance, if everything else is the same:
    Orbit altitude, detectors, receiver FOV, pulse rate, solar rejection etc.
LITE CALIOP CATS ATLID
J 0.530 0.110 0.002 0.035
l(nm) 532 532 532 355
pps 10 20 4000 51
P (W) 5.3 2.2 8.0 1.8
D 1 1 0.60 0.62
PxA 5.3 2.2 2.9 0.69

## Slide 5: Power-Aperture Product as a Simple Metric
Power aperture product: PxA = J x pps x D2
  Is proportional to signal and is related to SNR
  Useful for a relative ranking of performance, if everything else is the same:
    Orbit altitude, detectors, receiver FOV, pulse rate, solar rejection etc.
LITE CALIOP CATS ATLID
J 0.530 0.110 0.002 0.035
l(nm) 532 532 532 355
pps 10 20 4000 51
P (W) 5.3 2.2 8.0 1.8
D 1 1 0.60 0.62
PxA 5.3 2.2 2.9 0.69
R (km) 250 705 550 400
PxAxH2 42.2 2.2 4.8 2.1 range-normalized, H = 705 km/orbit altitude

## Slide 6
Minimum detectable scattering ratio
- more meaningful than SNR as a simple BSL metric
St
Pd
Pfa
In the limiting case where background light, detector noise, and dark current are all negligible:
For reference:
CALIOP dynamic range
Notional scattering strengths for various targets
Usefulness of this relation validated starting with McGill et al. (2007)

## Slide 7: bmin vs. SNR (CALIOP, 532 nm)
Performance improves with SNR, but SNR does not define “performance”
SNR requirements depend on:
allowable averaging
magnitude of target scattering
required retrieval accuracy
Can always trade resolution for SNR
LITE aerosol
bmin = minimum particulate backscatter detectable against the molecular background

## Slide 8: bmin for CALIOP and Two Variants
CALIOP 532 nm at 705 km
CALIOP at 450 km vs 705 km
Lidar-04 = hi rep rate backscatter lidar

## Slide 9: bmin for constant average laser power as a function of pulse rate
One design choice: high energy/low rep rate vs low energy/high rep rate
At night – if detectors/electronics are signal-limited there is no penalty to high rep rates
During day – each time a profile is acquired, solar background is integrated into the signal
SNR µ
((J + BG) x pps )½
J x pps

## Slide 10: bmin is relevant to detection of layer top
Detection of layer base is a separate issue
An important part of the ‘missing AOD’ issue
  CALIOP only retrieves between detected layer top and estimated layer base
  Layer base is ‘extended’ in some cases, but imperfectly

## Slide 11: Analysis of BSL Retrieval Uncertainties
Examine error sources one at a time
Consider idealized case of a single, homogeneous aerosol layer
  lidar ratio and scattering ratio are constant with range
Goal:
  Quantify impact of calibration errors
  Quantify impact of lidar ratio uncertainties
  Quantify impact of errors in retrieval of overlying cirrus

## Slide 12: Retrieval errors scale non-linearly with AOD
Contour plots of the relative error in retrieved optical depth as a function of optical depth and error in lidar ratio, for scattering ratio = 1.5.
Magnitude of optical depth error is indicated by the color bar and contour lines.
Young et al. (JTech 2013)

## Slide 13: Lidar Ratios retrieved by airborne HSRL as a function of CALIOP type classification
Figure 11. Daytime histograms of lidar ratio. The numbers in the top row are the means and SDs of the lidar ratios measured by the HSRL.
Rogers et al. (AMT 2014)
Daytime
flights
Lidar ratio selected by CALIOP typing algorithm vs measured by HSRL
  Uncertainty in Sa used by CALIOP: 20% at best, more typically 30% - 40%
CALIOP-HSRL discrepancy is also an indicator of limited type information
  HSRL retrievals of Sa provide additional information on aerosol type

## Slide 14: Relative uncertainty in AOD (single layer)
Accurate AOD is important for:
Aerosol climate forcing
An important performance metric for model evaluation
Uncertainty due to lidar ratio uncertainty only
Uncertainty due to calibration error only

## Slide 15: Uncertainty in near-surface aerosol extinction (BSL)
Uncertainty due to lidar ratio uncertainty only
Uncertainty due to calibration error only
Accurate near-surface extinction (to 20-30%) is important for:
  Air Quality
  Evaluation of models

## Slide 16: Quantification of CALIOP Cirrus OD Errors
DAY
unconstrained
constrained

rms CALIOP-IIR COD

mean CALIOP-IIR COD
CALIOP cirrus OD errors from co-located 5-km IIR OD retrievals
Ocean only, single-layer ROI
These results suggest daytime unconstrained retrievals are more accurate than constrained for OD < 0.5
Mostly interested in thinner cirrus
Most cirrus has OD < 1
retrieval errors under dense cirrus are large

(analysis by Anne Garnier)

## Slide 17: Uncertainty from error in correction of overlying cirrus attenuation Assumes unconstrained retrievals with perfect lidar calibration and lidar ratio
Relative uncertainty in PBL AOD Relative uncertainty in near-surface aerosol extinction
Solid lines: 2 km PBL height
Dashed lines: 500 m PBL height
Using results from Young et al. (2013), the cirrus attenuation correction error is converted into a relative calibration error:

## Slide 18: Uncertainty from correction of overlying cirrus attenuation Assumes perfect calibration and lidar ratio
Solid lines: error from correction of overlying attenuation
Dashed lines: error from CALIOP calibration (1.5%) in cloud-free skies
Relative uncertainty in PBL AOD, 2 km PBL height Relative uncertainty in near-surface aerosol extinction, 500 m PBL height
Plotting previous results as a function of AOD or extinction:

## Slide 19: How is HSRL different from backscatter lidar?
A backscatter lidar measures the total attenuated
backscatter signal:
b’ = (bp + bm) e-2t
and retrieves particulate backscatter:
bp = b’ e+2t – bm
extinction is then estimated:
sp = Sp bp
Uncertainties propagate downward, largest near the surface
HSRL measures aerosol scattering ratio from attenuated
particulate and molecular backscatter signals:
R = 1 + (bp e-2t ) / ( bm e-2t ) = 1 + bp / bmol
HSRL particulate backscatter is computed :
bp = bm,mod (R – 1)
Aerosol extinction is estimated independently from the slope of the (attenuated) molecular channel signal:
Aerosol scattering ratio measured directly, overlying extinction errors do not propagate downward
ln -

## Slide 20: Uncertainty in aerosol backscatter coefficient: BSL vs HSRL
R = particulate scattering ratio
N = photoelectron count in range bin i
Dbp/bp
An ideal HSRL measures aerosol and molecular backscatter independently
For a given number of signal photons:
uncertainty in retrieved aerosol backscatter coefficient varies with scattering ratio
HSRL is more sensitive to tenuous aerosol:
- Important for Objective 5
- Important for Objective 8
- Important for evaluation of Aerocom models
in free troposphere

## Slide 21: Conclusion: Comprehensive Retrieval Simulations for ACCP
Simulated 532 nm lidar extinction retrieval uncertainties including SNR and systematic calibration and lidar ratio errors
Figures courtesy of Travis
Toth and Kathy Powell (ACCP SIT)
Method developed by Mark Vaughan
Night
smoke
pollution
Day
(AOD = 0.43)
Lidar09 – advanced
backscatter lidar
Lidar05 – HSRL
Lidar06 – HSRL