## Slide 1: Case Studies in Verifying Spacecraft Autonomy
Lorraine E. Prokop & Daniel J. Dorney: NASA – Langley Research Center
Martin S. Feather: Jet Propulsion Laboratory, California Institute of Technology
Stephen B. Johnson: NASA Marshall Space Flight Center, Jacobs Space Exploration Group

## Slide 2: The Authors
This research was carried out at NASA - Langley Research Center, Jacobs Space Exploration, and the Jet Propulsion Laboratory, California Institute of Technology under a contract with the National Aeronautics and Space Administration.
Transit Phase –
Orion Optical Navigation (OpNav)
Ascent Phase –
Space Launch System (SLS) Fault Management
Ascent Phase –
SpaceX Autonomous Flight Termination System (AFTS)
Descent/Landing Phase – MER-DIMES
Science Phase –
Curiosity/Opportunity AEGIS
lorraine.e.prokop@nasa.gov
martin.s.feather@jpl.nasa.gov
stephen.b.johnson@nasa.gov
daniel.j.dorney@nasa.gov
Dr. Stephen Johnson
Dr. Daniel Dorney
Dr. Lorraine Prokop
Dr. Martin Feather

## Slide 3: Ascent - Human-Rated Launcher Fault Management (FM): NASA Space Launch System (SLS)

## Slide 4: SLS – Key Autonomy and FM Requirements
NASA’s next-generation human-rated deep space launch vehicle
  Intended to boost humans and cargo beyond Earth orbit
SLS autonomy needed for nominal flight sequencing and control, and for FM due to very fast times-to-criticality
  Rapid failure propagation - engine combustion, thrust vector control, propellant mixing
Key Autonomy & Fault Management requirements derived from NASA NPR 8705.2C Human Rating Requirements for Space Systems
  Autonomous operation for functions, which if lost, would result in a catastrophic event
  Isolate and recover from faults … that would result in a catastrophic event
  Failure tolerance to catastrophic events, with levels of failure tolerance and implementation (similar or dissimilar redundancy) derived from integration of the design and safety analysis
  Abort capability from the launch pad to Earth-orbit insertion to protect for the following ascent failure scenarios (minimum list): a. Complete loss of ascent thrust propulsion; b. Loss of attitude or flight path control

## Slide 5: Autonomy Verification Strategy
Fault Management Architecture is “monitor-respond”
NASA process uses “Detailed Verification Objectives” (DVOs) for top-level requirements
Nominal autonomy verified by Systems Integration Laboratory (SIL) test for nominal flight operations.
Fault Management verification is much harder due to the large number of algorithms (>200) and very large number of failure scenarios (>1,600) and modes (> 30,000)
  Each algorithm is executed for risk reduction via State Analysis Model (SAM) execution (state machine) and physics-based simulation in Vehicle Management End-to-End Testbed (VMET), and formally tested in the Software Development Facility (SDF) and SIL.
  The need for algorithms (which ones are valuable and needed), and their performance is verified by analysis. Analysis performed via failure scenarios.
    Quantitative estimates of the value of abort algorithms against the metric of “Loss of Crew Benefit” (Loss of Crew avoided due to existence of the algorithm), compared to the risks of those algorithms activating when they should not (false positives, causes Loss of Mission). Estimated per scenario and then results “slice and diced” to get the total estimates per algorithm.
    Qualitative judgments of algorithm need & value via task teams that include SLS engineering, Systems Engineering & Integration, Mission Operations and Crew Office (both part of Flight Operations Directorate).

## Slide 6: Ascent - Launch Termination : SpaceX Falcon 9

## Slide 7: Automated Flight Termination System (AFTS)
The launching of flight vehicles is a complex and energetic process necessitating many safety precautions and protocols
The time-to-criticality can be below human reaction time, necessitating the need for increased flight system autonomy
Active monitoring , historically provided by range-safety personnel, is becoming more automated
The Falcon 9 originally used a traditional flight termination system but transitioned to an AFTS to enable the simultaneous return of multiple boosters and to support crewed launches

## Slide 8: AFTS Development
The AFTS system uses a core software package developed by NASA, the Air Force and DARPA  with a customized software wrapper added by SpaceX
AFTS design features include (not limited to):
  Complete functional independence from the launch vehicle
  Reliability of 99.9% with a 95% confidence level
  Single fault tolerance with regard to performance degradation during flight and inadvertent initiation of the termination command
  Capability to issue telemetry throughout all mission phases by land-based connections or by interfacing with a space based telemetry system
AFTS can use multiple sensor types to provide position, velocity, attitude, and other state vector data  inertial navigation system (INS), global positioning system (GPS), inertial measurement units (IMUs), accelerometers, etc.
Configurable rule-based algorithms make the flight termination decisions
Mission rules are developed using the inventory of rule types from current human-in-the-loop operational flight safety practices

## Slide 9: AFTS Hardware and Applications
The AFTS uses redundant chassis (each with redundant sensor inputs), the Core Autonomous Safety Software (CASS), and a launch vehicle specific software wrapper  either chassis can initiate flight termination
AFTS built and tested to NASA design and construction standards
  Hazard report process to identify catastrophic failure modes for crewed flights
  Tested on sounding rockets and operated in shadow mode on the Falcon 9 for thirteen flights
AFTS first flown as primary flight termination system for the Falcon 9 on 2/19/17 and used on all Falcon 9/Falcon Heavy launches since
SpaceX estimates that AFTS provides a 50% reduction in range-related expenses
https://ses.gsfc.nasa.gov/ses_data_2011/110913_Esper.pdf
Early Test Hardware on SpaceX Falcon 1

## Slide 10: Transit – Orion Optical Navigation

## Slide 11: Orion Optical Navigation (OpNav)
Shield
Optical Images processed for autonomous navigation under communications loss – safety critical
Similar role as Apollo Space Sextant
Star Tracker 2
Star Tracker 1 with RCS plume shield
OpNav Camera

## Slide 12: OpNav Software Basics
Images processed onboard in real time during “opnav passes”
Still images of Moon or Earth -> apparent angular diameter/centroid -> range/bearing
  Artemis 1 – range/bearing with star tracker attitude
  Artemis 2 – self attitude determination from star centroiding
Calibrates and undistorts images in real-time based on star centroids
Class A Safety-Critical Software, developed according to the following process standards:
  NPR 7150.2B
  CMMI Level 3

## Slide 13: OpNav Software Test Campaign
Item | Quantification
Flight Software Size (SLOC) | 8,800
Test Software Size (SLOC) | 35,400
Individual Pass/Fail Test Cases (Total) | 21,322
Unit Test Cases | 2,769
Verification Test Cases (Nominal) | 16,618
Verification Test Cases (Off Nominal) | 1,935
Nominal Synthetic Test Images | 3,382
Off Nominal Test Images | 2,299
Review Type / Product | Major Issues | Minor Issues
Software Development Plan (SDP) | 1 | 6
Software Requirements Specification (SRS) | 4 | 21
Critical Design Review (CDR) | 7 | 11
Verification Test Review (VTR) | 0 | 7
Test Readiness Review (TRR) | 0 | 0
Code Inspections | 49 | 305
Key performance requirements on accuracy of calibration, undistortion, range/bearing, and attitude drove test success criteria
  No output data allowed out of spec
Test campaign consisted of the following
  Lifecycle reviews
  Unit testing (100% Multiple Condition Coverage – MCC)
  Code inspections & static code analysis
  Verification testing – synthetic imagery
    Verification test peer reviews
    Extensive test cases
  Off-nominal and robustness testing
  Continuous integration & regression
  Integration testing – higher fidelity labs
  Validation – final validation with actual imagery in-flight during outbound leg of Artemis I

## Slide 14: Sample OpNav Synthetic Test Imagery
Multiple phases and exposures
Nominal Images expected during mission timeline
Off Nominal Images

## Slide 15: Entry, Descent and Landing - Mars Exploration Rovers (MERs) DIMES

## Slide 16: Successful Entry, Descent & Landing of both Mars Exploration Rovers in 2004
https://mars.nasa.gov/mer/mission/timeline/edl/steps/
Airbags
Airbags cushion final drop
Rockets
Rockets cancel velocity
Rover
Parachute
Lander
Parachute slows descent

## Slide 17: DIMES (Descent Image Motion Estimation System)
https://mars.nasa.gov/mer/mission/timeline/edl/steps/
Vertical velocity predicted
UNKNOWN horizontal velocity due to unpredictable cross-winds in Martian atmosphere
DANGER Addition of horizontal velocity may exceed capacity of airbags
DIMES estimates horizontal velocity
Rockets fired to compensate if need be
Estimation:
During descent, take photos of ground
Pick a feature in first photo
Identify that feature in second photo
Deduce horizontal velocity from motion of feature between photos

## Slide 18: DIMES requirements
Perform within 20 seconds using 40% allocation of flight processor
Probability of reporting an incorrect velocity estimate < 0.1%
Probability of not reporting a velocity estimate ≤ 10%
“Do no harm” - avoid an incorrect estimate causing failure when the landing might have succeeded anyway
DIMES had to be autonomous – control from Earth would be too slow
The challenge: how to have confidence in DIMES?
Design: predict hazards & avoid by design if possible, otherwise recognize when an estimate is not to be trusted; provide multiple (4) chances to produce a trusted velocity estimate
Test: simulations and field tests made as representative as possible

## Slide 19: Science - (Opportunity & Curiosity)

## Slide 20: “Laser-targeting A.I. Yields More Mars Science” https://www.jpl.nasa.gov/news/news.php?feature=6879
https://mars.nasa.gov/resources/4845/high-resolution-self-portrait-by-curiosity-rover-arm-camera/
At the end of Curiosity's day’s drive
Take a panoramic picture
Identify the most scientifically interesting target
Point the laser & spectrometer at it
“Zap” it with the laser to yield measurements
At the end of Opportunity’s day’s drive
Take a panoramic picture
Identify the most scientifically interesting target
Point the narrow field-of-view camera at it
Take a photograph to then send back to Earth
https://mars.nasa.gov/resources/5852/opportunity-self-portrait/

## Slide 21: AEGIS (Autonomous Exploration for Gathering Increased Science)
DANGER
Do NOT point the camera at the sun
Do NOT “Zap” the rover with the laser (!)
Stop gracefully if interrupted or anything odd happens
https://www.jpl.nasa.gov/news/news.php?feature=6879
1. Identify targets (rocks) outlines by image processing
2. Rank targets by scientific interest
(winner shown here colored in green)
3. Plan and execute trajectory to point camera/laser at selected target
4. Take science measurement (photo or laser zap)

## Slide 22: AEGIS (Autonomous Exploration for Gathering Increased Science)
Design: • heritage algorithm for identifying rocks
• criteria & formulae for ranking rocks defined by scientists
• perform its own safety checks (don’t rely on rover to do so)
Testing: • using images of a variety of Martian terrains
• in avionics simulators
• on hardware rover in large Mars-like terrain sandbox
• nominal & off-nominal (e.g., image with no rocks)
Deployment: • progressive checkout – incrementally do more steps
• success on Opportunity paved way for use on Curiosity
Benefit clear: • additional science measurement not otherwise obtained
• much better than purely random targeting
Note: AEGIS only enhanced, it was not essential → crucial it be low risk

## Slide 23: Conclusions
Autonomous systems have been successfully employed and verified in launch vehicles and spacecraft
Automation is especially necessary with the presence of the following:
  Time criticality
  Communications delay or absence
These case studies provide examples of successful verification strategies across a broad range of domains:
  Multiple mission phases (ascent, transit, decent/landing, science operations)
  Multiple launch vehicles and spacecraft
  Differing criticality levels
Some Common Themes
  Lots of testing (!) - analysis / tests in environments with increasing fidelities
  Concerted team effort and much time devoted not only to duplicate nominal, but also identify extensive off-nominal conditions to minimize “false positives”

## Slide 24
Thank you for your attention