## Slide 1: Orion Optical Navigation
2021 Flight Software Workshop
Lorraine E. Prokop, Ph.D. / NASA-LaRC
February 9, 2021

## Slide 2: OpNav Contacts
Orion Optical Navigation (OpNav)
Software Lead (former)
Langley Research Center
Orion Optical Navigation (OpNav)
Project Lead
Johnson Space Center
Orion Optical Navigation (OpNav)
Software Lead (current)
Johnson Space Center
lorraine.e.prokop@nasa.gov
michael.buttacoli@nasa.gov
greg.n.holt@nasa.gov
Dr. Greg Holt
Dr. Lore Prokop
Mike Buttacoli

## Slide 3: Orion Optical Navigation (OpNav) Software
Shield
Optical still images are processed for autonomous spacecraft navigation
  Completes the mission if Earth communication is lost
  Onboard computed navigation data substitutes for nominally provided ground trajectory course maneuver updates
Star Tracker 2
Star Tracker 1 with RCS plume shield
OpNav Camera
Fixed mounted commercial optical camera

## Slide 4: Loss of Comm Navigation

## Slide 5: Orion EM-1 OpNav Pass Visualization
Images taken every 30 seconds during dedicated “OpNav Passes”
  Vehicle slewed to take measurements

## Slide 6: Orion Optical Navigation (OpNav) System Architecture
OpNav Software Runs on a Camera Control Computer, external from the primary flight computers
  64-bit Linux running Core Flight System (CFS)
  Images taken when commanded by GNC
Bi-directional communication with GNC software in primary flight computers
  Star tracker data, closed loop exposure adjustments
  Range, bearing, attitude provided in real time

## Slide 7: OpNav Software Basics
Still images of Moon or Earth are processed to find apparent angular diameter and centroid in camera focal plane
  This raw data is transformed into range and bearing angle measurements using planetary data and precise star tracker inertial attitude
Artemis Mission Progression
  Artemis 1 – range/bearing with star tracker attitude
  Artemis 2 – self attitude determination from star centroiding
  Artemis 3 – rendezvous targeting for Gateway
The measurements are sent to the main flight computer’s Kalman filter to update the onboard state vector.
Calibrates and undistorts images in real-time based on star centroids
Class A Safety-Critical Software, developed according to the following process standards:
  NPR 7150.2B
  CMMI Level 3
18 month development time for Artemis I

## Slide 8: Orion Optical Navigation (OpNav) Software Architecture
OpNav is Single CFS App at 1 Hz
  Reads images from file system
Camera Drivers running in “non CFS” environment communicate with CFS Camera Controller Apps to take and store images as instructed by GNC
Data Sent to/from Orion onboard network with Custom Orion CI/TO functioning Applications

## Slide 9: Opnav Software Decomposition
CSCI Number | CSCI Name | Description
1 | OpNav_ImgProc | ImgProc Performs calculations necessary to produce range and bearing information to a target planetary body from optical image data.
2 | OpNav_ImgCal | ImgCal analyzes star field image data to produce data that characterizes image distortions and camera alignment adjustments. It also includes object centroiding.
3 | OpNav_Common | Common provides utility functions and math libraries needed as service routines to the other CSCI’s. It also provides image processing utilities, interpolation functions, sorting, and ephemeris calculations.
4 | OpNav_CFS_App | CFS_App is the outermost application running part of the CFS framework, serves as the overall driver for optical navigation and calibration functionality, implements external interfaces, manages global data, and provides real-time control.
5 | OpNav_FileData | FileData consists of files and/or tables of data both needed as well as produced by CSCIs which are delivered along with the flight software. This CSCI excludes files and data used for verification. Data used for verification will be outlined in the OpNav software Verification Plan, Procedures, and Report document.
6 | OpNav_ImgAtt | ImgAtt performs on-demand attitude determination and star identification based on images exposed to show stars. The images may contain extended objects in the field of view such as the Earth or Moon, or other non-stellar objects.

## Slide 10: OpNav Test Types & Framework

## Slide 11: OpNav Software Test Campaign
Item | Quantification
Flight Software Size (SLOC) | 8,800
Test Software Size (SLOC) | 35,400
Individual Pass/Fail Test Cases (Total) | 21,322
Unit Test Cases | 2,769
Verification Test Cases (Nominal) | 16,618
Verification Test Cases (Off Nominal) | 1,935
Nominal Synthetic Test Images | 3,382
Off Nominal Test Images | 2,299
Review Type / Product | Major Issues | Minor Issues
Software Development Plan (SDP) | 1 | 6
Software Requirements Specification (SRS) | 4 | 21
Critical Design Review (CDR) | 7 | 11
Verification Test Review (VTR) | 0 | 7
Test Readiness Review (TRR) | 0 | 0
Code Inspections | 49 | 305
Key performance requirements on accuracy of calibration, undistortion, range/bearing, and attitude drove test success criteria
  No output data allowed out of spec
  Better to NOT provide output, than provide output out of tolerance
Test campaign consisted of the following
  Lifecycle reviews (SDP, SRS, PDR/CDR, VTR, TRR)
  Unit testing
    100% Multiple Condition Coverage – Utassert / gcov
  Code inspections & static code analysis
  Verification testing – synthetic imagery
    Generated with EDGE tool
    Verification test peer reviews
    Extensive nominal and off nominal test cases
  Robustness testing
  Continuous integration & regression
  Integration testing – higher fidelity labs
  Validation – final validation with actual imagery in-flight during outbound leg of Artemis I

## Slide 12: Expected Test Results (Run from opnav_gui)

## Slide 13: Verification Test Review Portfolio

## Slide 14: Sample OpNav Synthetic Test Imagery
Multiple phases and exposures
Nominal Images expected during mission timeline
Sample Off Nominal Images

## Slide 15: Lessons Learned - Observations
Team started with Matlab/Simulink Autocode and quickly chose to hand code for tighter control, optimization, readability / maintainability, and better control of testing for off-nominal conditions
  Learning to code in “C” with engineers experienced only on Matlab was *not* a big schedule or learning curve hit, team adapted quickly and easily
Should have initially used Doxygen to link code to SDD, and generate certain SDD sections – corrected in next release
Should have used CCDD tool so Requirements & Test Matrix for Commands/Telemetry maintained synchronization with code rather than maintaining by hand – initially thought project “too small”
Began notion of “Incremental Verification Test Reviews (VTR)” - was a very valuable process addition, peer reviewed each individual verification test with entire group/stakeholders as each test was completed -- spanned over 8 months of time
  Added an additional useful formal review prior to TRR called “VTR”, Verification Test Review at end to recap all prior “Incremental Verification Test Reviews”
Code inspections were very value added on this project - if *right people* involved with devoted time
  Static analysis tools unable to find what was *missing* from code
Schedule should allow for slack/risk introduced with Class A flight certifying first-time/new technology (crossed many TRL levels rapidly on this project 38)
Testing, yet again, was underscoped. This time took 4x SLOC that of flight code, planned for 2x
  Should have standard CFS test framework rather than re-invent every time (believe in work at JSC)

## Slide 16: Conclusions
OpNav will be the first autonomous safety-critical onboard navigation system
OpNav was developed for the Orion Artemis Missions
  Artemis I – Range/bearing
  Artemins II - self attitude determination added
  Artemis III – automated rendezvous targeting for Gateway
OpNav was developed as Government Furnished Equipment (GFE), and is available US Release
  https://software.nasa.gov/software/MSC-26456-1

## Slide 17
Thank you for your attention