## Slide 1: LunaNet: NASA’s Communications and Navigation Architectural Framework for the Moon
Dave Israel, ESC Architect
January 25, 2020

## Slide 3: Introduction to the Lunar Network, LunaNet
LunaNet is envisioned as a framework of standards, protocols, and interfaces to support a scalable, interoperable communications and navigation network-of-networks with nodes provided by NASA, commercial, and international partners.
LunaNet is open and scalable similar to the terrestrial internet
  It can be introduced with early robotic missions and expanded as new spacecraft and missions come online.
Its service-oriented architecture provides data transmission, sharing of position, navigation and timing (PNT), and situational awareness information.
The LunaNet concept is applicable to any planetary body and offers even greater advantages as the distance from Earth increases. LunaNet will demonstrate many capabilities needed for Mars exploration and mirrors the architecture of the future MarsNet.
There is broad interest in developing and implementing lunar communications relay services among industry (US and foreign), international partners, and NASA Centers.

## Slide 4: LunaNet Services
PNT Services
Precise position, velocity and time for autonomous nav and collision avoidance
Fusion of multiple data types including radiometrics, optimetrics, celestial nav, optical nav, terrain relative nav, & GNSS
Broadcast service supplies time transfer and metric tracking to synchronize users
Detection and Information Services
Alerts for events such as space weather, collision avoidance, & surface impact predictions sent to all LunaNet subscribers
Mission sensors for space weather and other measurements distribute information services to other users via LunaNet information services
Networked Communication Services
Critical data transmitted in real time.
Data aggregated and transmitted in store-and-forward mode from orbiting and surface relays.
Data exchanged among lunar users with no need for transfer to and from Earth
Data sent on demand by user or scheduled to better manage Earth stations loading & spectrum use
Science Services
Use RF & optical assets (part of) as scientific instruments
Supports Radio & Radar Sciences, Radio Astronomy / Very Long Baseline Interferometry (VLBI) & other space sciences

## Slide 5: Abstract Lunar Comm & Nav Architecture
5
Lunar Surface Assets
Human landers
Robotic landers
Rovers
EVA crews
Science payloads
Comm relays & nav aids
Surface to surface links
Gateway
Orbit to
orbit links
Direct to Earth links
Visiting Vehicles
Surface
to orbit links
Lunar orbit relays
Other orbiting spacecraft
Earth Stations
• US, international and commercial networks
• Ground and space-based
LunaNet - a framework of standards and protocols for a scalable, interoperable network with multiple users and providers
Types of Links
Direct to Earth
Lunar surface to orbit
Orbit to orbit
Surface to surface
Bands
RF and Optical
Communication Services
Real-Time and Store-and-Forward
Scheduled and Unscheduled Access
PNT Services
Radio- & optimetric range/range-rate
Broadcast ephemeris, time, PNT status
Space systems can be Service Providers, Service Users, or both
Lunar Orbiting Assets
Providers: Dedicated LunaNet relays or spacecraft with secondary LunaNet capability
Users: Human and robotic spacecraft using LunaNet services

## Slide 6: Relationship between Service Providers and Service Users
Any LunaNet Service Provider (LNSP) operates a LunaNet System (LNS) that provides Communications and PNT (CPNT) services to Service Users
Only two interfaces must be public and standardized:
  User Services Interface defines services that may be offered by an LNS and service characteristics required for interoperability
  Internetwork Interface defines the network management and network data exchange between two LNSs required for interoperability
Choice of services offered by an LNS is up to the LNSP owner/operator
Internal design of an LNS is the responsibility of the LNSP owner/operator

## Slide 7: Any Link Provides LunaNet Access – Lunar Surface Direct with Earth
A lunar surface mission connects to the LunaNet through links directly with Earth
Data may still be routed to and from Earth destinations or back to lunar destinations
7

## Slide 8: Any Link Provides LunaNet Access – Gateway as Access Point
The Gateway provides relay between lunar surface and Earth or other lunar users, either real-time or store-and-forward.
Data is still formatted the same and routed to final destinations as in the DTE case.
8

## Slide 9: Any Link Provides LunaNet Access – Store and Forward Relay
Lunar surface user exchanges data with other LunaNet users through relay, even when other users are not connected to relay.
Lunar surface user may also receive position, navigation, and timing services and situational alerts when out of contact with Earth.
9

## Slide 10: Any Link Provides LunaNet Access – Store and Forward Relay
10
Relay forwards data to the network when Earth is in view
Relay receives data for other lunar users not in view of Earth

## Slide 11: Networked Communication Services
Link Type A
Link Type B
Link Type C
Real-time and store-and-forward services available
Data services may be provided at different layers:
  Fundamental communications capabilities will be provided by DTN Bundle Protocol-based networking services.
  Some portions of LunaNet may route by IP packets, but IP is not guaranteed to provide full end-to-end data delivery to all nodes in the larger network.
  Some intermediate nodes may switch or forward data at the link or lower layer to enable speed or interoperability.
Interoperability between immediate neighbors with a standardized network layer allows the LunaNet architecture to be assembled through multiple infrastructure systems independent of frequency band, type of spacecraft, or provider.
The security objectives of confidentiality, integrity, and availability will be applied to all data carried across LunaNet.

## Slide 12: Position, Navigation, and Timing
Courtesy of SCaN
Notes: Defined standard messages and info content

## Slide 13: Autonomous Navigation for Future NASA Missions
Optical
Navigation:
CelNav, Bright
Body, TRN
AMA-SS / DPS
SM - MIST
Timing
OCXO
mini-RAFS
DSAC
Ground validation and support
NavCube
Receiver
Weak Signal
GNSS
X-ray Pulsar
Navigation
and Timing
Galactic Positioning System
Mars Forward
Test it at the Moon
Repeat it at Mars
CAPSTONE
Broadcast
Surface Beacons
Optical & RF
Crosslink
Lunar Node-1
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
Broadcast Service
Ephemeris, Rendered Imagery,
Signal design similar to GPS
Autonomy and graceful degradation through use of multiple sensors.
Master Oscillator
Central reference for time and frequency
C&DH
autoNGC
A
n
a
l
y
s
e
s
,
U
s
e
C
a
s
e
s
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
core Flight System (cFS)
Executive
autoNGC Flight SW
Apps under cFS
Autonomous Navigation, Guidance, and Control
Orbit/Attitude Determination
Control & Actuation
Guidance:
Trajectory Planning
Maneuver Planning
Sensing
LiDAR
Accelerometer
Radio- & Optimetrics
MAScOT
Multi-channel Receiver
Notes: Central Master oscillator and autoNGC to unify the system (on one asset) and synchronize across multiple assets
Take advantage of existing required components and incorporate provisions that assist nav to reduce SWaP.

## Slide 14: Detection & Information Services
Time
2000 Min Event Over
Solar Eruption
8 Min
X-Ray
Arrival
200 Min SEP Arrival
ENA Arrival / SEP Predictions
SEPf ux (>10MeV)
Solar Event Warning Example:
  Early warning of solar event onset
  Utilization of soft X-ray and Solar Energetic Particle (SEP) monitoring via a heterogeneous configuration
    X-rays arrive in 8 minutes after event starts
    Arrival of Solar Energetic Particles (SEP) in 200 minutes after event starts

## Slide 15: Science Services
LN
LN
M
E
LunaNet is comprised of two types of nodes: Users and C&N Service Providers.
LunaNet nodes (LN) carry comm and nav payloads that are connected by electromagnetic (EM) signals which propagate through different free-space regimes (direct-Earth, space-space, surface-to-surface, etc.)
These EM signals have attributes (i.e., frequency, power, etc.) that encode comm and nav information and “noise” that can be exploited for scientific purposes directly (e.g., C&N payload measurements of range, doppler etc.) or indirectly (environmental-induced perturbations are comm and nav noise but science signal)
Type 1 science opportunities exploit the the inherent functions, performance capabilities, and nominal operations and services of the comm and nav payloads carried by user and service provider nodes to perform scientific measurements.
Examples include radio occultation, gravity field mapping, exosphere dynamics, etc.
LN
Direct-Earth Signals
Cross-Link Signals
Reflected Signals
LN
Occulted Signals
Surface-Space Signals
Broadcast Signals
LN
Surface-Surface
Precise Location

## Slide 16: LunaNet Infrastructure Disaggregation
16
The LunaNet infrastructure may be comprised of nodes with varying degrees of service provision capabilities
  Allows the LunaNet flight elements to range from satellites to larger spacecraft
  For example, some orbiting elements may provide PNT services only, while others may primarily provide high rate communications links
The overall LunaNet infrastructure performance is the aggregation of all of the nodes.
Network Services
PNT Services
Detection Services
Science Services

## Slide 17: Flexible and Extensible
LunaNet is both flexible and extensible and will be continue to evolve after NASA develops the first instantiation of the architecture.
Lunar missions may be part of the LunaNet infrastructure, a LunaNet user, or even both.
A lunar mission can conduct its mission objectives while also acting as a LunaNet node or simply be a user of the architecture.
There is limited direct-to-Earth link availability once multiple assets are established within the lunar region, some operations will need to be:
  More autonomous
  Act as data aggregation points
NASA Goddard Space Flight Center

## Slide 18: LunaNet Service Architecture
Moon to/from trunk link: Between relay orbiter and Earth station
Moon to/from trunk link: Between lunar orbiter/landed vehicle and Earth station
Proximity link:
Between relay orbiter and landed vehicle/orbital vehicle
Cross link:
Between two relay orbiters
Proximity link:
Between relay orbiter and landed vehicle/orbital vehicle
Lunar surface-to-surface link:
Wireless link between surface elements
Lunar Relay Network; Lunar Surface Network; Earth Network

## Slide 19: Provider Payload Types
Payload types include:
A networking services payload:
  Radio Frequency and/or Optical Communications Terminals
  Disruption Tolerant Networking Bundle Protocol network layer routing
  Data switch
A position, navigation, and timing payload:
  ranging devices, autonomous navigation processors, broadcast beacons, and time reference source / distribution modules.
  Broadcast beacons on many satellites can provide multiple signals that surface assets can use for surface location determination, etc.
Detection and information services:
  satellites can carry science instruments or operational detectors that can contribute to the larger mission and provide situational alerts.

## Slide 20: User Systems
LunaNet will enable lunar missions and allow them to dedicate more of their resources to their science payloads and overall objectives.
With LunaNet, satellites will not need to carry the capability to return all of their science data solely through long links back to Earth.
Each mission would be able to use the PNT services for autonomous guidance, navigation, and control.
Detection & Information Services could provide alerts that may allow placing sensitive instruments into safe mode or, perhaps, turning on science instruments designed to capture specific science events.
LunaNet User System Requirements
  Communications and PNT systems compatible with LunaNet signals and standards
  Flight software and data systems leveraging available DTN and other data services

## Slide 21: Summary
LunaNet is proposed as the open, international architecture to provide standardized interoperable communications, PNT, and other services to cislunar-orbiting and surface missions
Participation is open to all – No one owns the entire LunaNet
NASA released a Request For Information on October 1, 2020 soliciting interest in Lunar Communications Relay and Navigation Services
  Services are needed to support Science and Exploration missions beginning in 2024
  Responses are open to all, domestic & foreign, by 30 Oct
  RFI and detailed description of the LunaNet architecture and concept of operations can be found at: https://beta.sam.gov/opp/8116f285e8d841a6a5e030c00fb7fa76/view

## Slide 22: Conclusion
Development of LunaNet is currently in progress and is being led by the Space Communications and Navigation (SCaN) program.
LunaNet is a flexible and scalable architecture for the provision of Network, PNT, and Detection & Information Services at the Moon.
The infrastructure can be built up over time as mission requirements and operations concepts evolve.
Satellites can be providers or users of the LunaNet architecture.
Infrastructure nodes can be provided by any combination of NASA, commercial, or other partner systems.
The LunaNet architectural approach is applicable to any planetary body to establish the solar system internet, such as MarsNet.

## Slide 23
Questions?