## Slide 1
UTM Technical Interchange Meeting
February 23rd, 2021
Unmanned Aircraft Systems (UAS) Traffic Management (UTM) Project
Advanced Airborne Autonomy
for Urban Flight Operations
Dr. Corey A. Ippolito
Lead, UTM Task 10 - Urban Autonomy

## Slide 2: Intelligent Flight Control and Autonomy For Urban Flight
Unmanned Aircraft Systems (UAS) Traffic Management (UTM) project seeks to advance concepts towards higher-density operations over densely-populated areas
UAM and UTM industry partners are actively seeking access to this space
Anticipated high-demand market with significant economic growth potential
Non-trivial challenges for routine high-density urban UAS operations
Seeking to Safely Enable Routine High-Density Low-Altitude UAS Operations over Densely-Populated Urban Environments

## Slide 3: Challenges for High-Density Urban Flight Operations in UTM
Flight over people, property, and critical urban infrastructure
Highly constrained spaces within urban canyons
Operations almost entirely beyond visual and communication line-of-site
Concurrent operations in high-density air traffic
Mission designs drive towards larger more-capable vehicles in higher risk categories
Cluttered and challenging RF environment and GPS degraded/denied
Urban environment is unpredictable and dynamic
Complex hazardous atmospheric conditions that are poorly understood
Many stakeholders with competing needs and desires
Image courtesy of Pixabay.com

## Slide 4: Enabling Safe Autonomous UAS Urban Operations
Gaps
Approach
Technical Objectives (Vehicle Autonomy Focus)
Technology Gap
Identify gaps and advance the state of the art in fundamental understanding.
Develop high-fidelity environment models. Develop validated flight dynamics models from wind-tunnel experimental data.
Knowledge Gap
Concepts and Standards Gap
Perform systems-wide studies to show path towards urban access for UTM through onboard autonomy.
Develop feasible validated reference architectures for advanced vehicles.
Conduct system-wide/systems-level reference design study.
Develop and validate SAFE50 reference design vehicle and autonomy architectures.
Enabling Autonomous High-Density Urban UAS Operations.

## Slide 5: SAFE50 Design Process
Concept of Operations (Con-Ops)
Requirements Architecture
Stakeholder Needs and Desires
Functional Decomposition Architecture
Physical Decomposition Architecture
KPPs & MPPs
Reference Design Study
Flight Phases
Autonomy Architecture
H/W Arch.
S/W Arch.
Reference Autonomy Flight S/W Architecture
Reference Avionics Architecture
Reference Vehicle
Architecture
Reference Design Architectures
FFBD
Risks/Hazards Analysis
Functional Requirements
Performance Requirements
Equipage Requirements
Simulation
Standalone
HILS
Batch
AOL Intgrn.
UTM Arch.
Validated Deliverables
Scenarios and Use Cases:
Nominal, Off-Nominal, Contingency Requirements
Research Focus
Vehicle/Avionics Design
Flight H/W Prototypes
Flight Software
Analysis & Publications
Experiment Data
Functional Requirements
Verification and Validation

## Slide 6: SAFE50 Autonomous Operations Example
Use case 1: point-to-point
Take-Off Point
Theater (customer)
Overlapping Operations
Airspace overlap
Emergency
Landing
1
2
3
Take-off
Climb out
Cruise
Approach
Descent
Landing
4
Off-nominal cases
Emergency Landing Point
Emergency Landing Point

## Slide 7: SAFE50 Autonomous Operations Example
Known (A Priori) Ground Object
Unknown Ground Object
Adverse Area (e.g., Wind or Traffic)
‘Approved’ UTM Volumes
‘Approved’ UTM Contingency Volumes
Nominal Trajectory
Energy-Optimized or Wind-Adverse Trajectory
Failure Trajectories

## Slide 8: SAFE50 Autonomous Operations Example
Known (A Priori) Ground Object
Unknown Ground Object
Adverse Area (e.g., Wind or Traffic)
‘Approved’ UTM Volumes
‘Approved’ UTM Contingency Volumes
Nominal Trajectory
Energy-Optimized or Wind-Adverse Trajectory
Failure Trajectories

## Slide 9: SAFE50 Autonomous Operations Example
Known (A Priori) Ground Object
Unknown Ground Object
Adverse Area (e.g., Wind or Traffic)
‘Approved’ UTM Volumes
‘Approved’ UTM Contingency Volumes
Nominal Trajectory
Energy-Optimized or Wind-Adverse Trajectory
Failure Trajectories

## Slide 10: SAFE50 Autonomous Operations Example
Known (A Priori) Ground Object
Unknown Ground Object
Adverse Area (e.g., Wind or Traffic)
‘Approved’ UTM Volumes
‘Approved’ UTM Contingency Volumes
Nominal Trajectory
Energy-Optimized or Wind-Adverse Trajectory
Failure Trajectories
Overlapping Operations

## Slide 11: Vehicle Autonomy Requirements
Dynamic Ground Objects (DGO)
Static Ground Objects (SGO)
Other Aircraft
Detect, Operate-Near, and Avoid-Endangering SGOs
Detect, Operate-Near, and Avoid-Endangering DGOs
Hazard Footprint Awareness, Risk Minimization/Avoidance,
Health Monitoring
Detect, Operate-Near, Avoid-Endangering Other Aircraft
UAS
Environment Challenges
Atmospheric Uncertainty
Failures and Contingencies
Degraded RF and GNSS, BV/RF-LOS
Winds and microbursts
Avoid endangering objects in environment.
Ground Operators and UTM System
C3 and Surveillance Requirements
Manned Aircraft
Do not interfere

## Slide 12: Autonomous Ground-Risk Mitigation
Dynamic Ground Objects (DGO)
Detect, Operate-Near, and Avoid-Endangering DGOs
Hazard Footprint Awareness, Risk Minimization/Avoidance,
Health Monitoring
UAS
Vehicles must be able to:
(1) Detect dynamic ground objects (DGO)
(2) Autonomously avoid putting DGO at risk
2a. Evaluate the probabilistic cost model for DGO risk
2b. Autonomously avoid flying into areas of high DGO risk
(3) Understand their own nominal and off-nominal behavior (suggested manufacturer certification requirement)
X Bouyssounouse and C Ippolito. “Urban Area Unmanned Aerial Systems Sensor Capabilities for Ensuring Ground Hazards Safety”. 38th AIAA/IEEE Digital Avionics Systems Conference (DASC), 2019.
C Ippolito, K. Krishnakumar. “Dynamic Ground Risk Mitigation for Autonomous Small UAS in Urban Environments”. AIAA InfoTech@Aerospace, 2019.

## Slide 13: Autonomous Ground-Risk Mitigation
UAS
h
v
Sensor Range
DGO Identified
Classification: Person
Range and Position Known
Confidence Rate
False-Positive Rate
Miss-Rate
Slant Range
Vehicles must be able to:
(1) Detect dynamic ground objects (DGO)
(2) Autonomously avoid putting DGO at risk
2a. Evaluate the probabilistic cost model for DGO risk
2b. Autonomously avoid flying into areas of high DGO risk
(3) Understand their own nominal and off-nominal behavior (suggested manufacturer certification requirement)
X Bouyssounouse and C Ippolito. “Urban Area Unmanned Aerial Systems Sensor Capabilities for Ensuring Ground Hazards Safety”. 38th AIAA/IEEE Digital Avionics Systems Conference (DASC), 2019.
C Ippolito, K. Krishnakumar. “Dynamic Ground Risk Mitigation for Autonomous Small UAS in Urban Environments”. AIAA InfoTech@Aerospace, 2019.

## Slide 14: Autonomous Ground-Risk Mitigation
Nominal trajectory with safety bounds
Tracking of ground objects and hazard mitigation
Ground Hazard Footprint
UAS
Set of Off-Nominal and Failure Trajectories
Dynamically Calculated No-Fly Area (Risk Probability Too High)
X Bouyssounouse and C Ippolito. “Urban Area Unmanned Aerial Systems Sensor Capabilities for Ensuring Ground Hazards Safety”. 38th AIAA/IEEE Digital Avionics Systems Conference (DASC), 2019.
C Ippolito, K. Krishnakumar. “Dynamic Ground Risk Mitigation for Autonomous Small UAS in Urban Environments”. AIAA InfoTech@Aerospace, 2019.
Vehicles must be able to:
(1) Detect dynamic ground objects (DGO)
(2) Autonomously avoid putting DGO at risk
2a. Evaluate the probabilistic cost model for DGO risk
2b. Autonomously avoid flying into areas of high DGO risk
(3) Understand their own nominal and off-nominal behavior (suggested manufacturer certification requirement)

## Slide 15: SAFE50 Autonomy Reference Architecture
C Ippolito, K. Krishnakumar. “An Autonomy Architecture for Autonomous Urban Environment Operations”. In 2019 AIAA Modeling and Simulation Technologies Conference. San Diego, CA. Jan. 2109.

## Slide 16: SAFE50 Autonomy Reference Architecture
Input: High-Level Mission Goal and Constraints
C Ippolito, K. Krishnakumar. “An Autonomy Architecture for Autonomous Urban Environment Operations”. In 2019 AIAA Modeling and Simulation Technologies Conference. San Diego, CA. Jan. 2109.

## Slide 17: SAFE50 Reference Avionics Prototypes and Flight Platforms
Experimental Multicopter Flight Management and Flight Control System
Real-Time Embedded Software Architecture
Systems Analysis, CAD and Hardware Design

## Slide 18: GPS-Denied Navigation – IMU-Integration of Vision and LIDAR based SLAM
Hening, S., Ippolito, C. A., Krishnakumar, K. S., Stepanyan, V., & Teodorescu, M. “3D LiDAR SLAM integration with GPS/INS for UAVs in urban GPS-degraded environments”. In AIAA Information Systems-AIAA Infotech@ Aerospace (p. 0448). 2017.

## Slide 19: Modeling, Simulation and Real-Time Environment Hazard Mapping
Ippolito, Corey A., S Hening, S Sankararaman, and V Stepanyan. “A modeling, simulation and control framework for small unmanned multicopter platforms in urban environments”. In 2018 AIAA SciTech Modeling and Simulation Technologies Conference, p. 1915. 2018.

## Slide 20: Intelligent Cable and Power Line Detection
Power Line Identification and Reconstruction using Artificial Intelligence and Machine Learning (AI/ML) Techniques
Raw LiDAR point clouds at 75% of LIDAR range (left), voxel processing (middle), reconstructed powerlines at 75% of LIDAR range (right).
Ippolito, Corey, Kalmanje Krishnakumar, and Sebastian Hening. "Preliminary results of powerline reconstruction from airborne LiDAR for safe autonomous low-altitude urban operations of small UAS." 2016 IEEE SENSORS. IEEE, 2016.

## Slide 21: High-Level Path Planner
Chakrabarty, A, Vahram S, Kalmanje S. K, and C A. Ippolito. "Real-time path planning for multi-copters flying in UTM-TCL4." In AIAA Scitech 2019 Forum, p. 0958. 2019.

## Slide 22: Real-Time Trajectory Optimization and Obstacle Avoidance
Chakrabarty, A, Vahram S, Kalmanje S. K, and C A. Ippolito. "Real-time path planning for multi-copters flying in UTM-TCL4." In AIAA Scitech 2019 Forum, p. 0958. 2019.
Stepanyan, Vahram, Anjan Chakrabarty, and Corey A. Ippolito. "Pursuit-Evasion Game approach to Tree-Based Path Planning for Airborne Dynamic Obstacle Avoidance." AIAA Scitech 2021 Forum, p. 1575. 2021.

## Slide 23: Collaborative Sense and Avoid through V2V-V2X Communication
A Chakrabarty, S Hening, J Baculi, C Ippolito, K Krishnakumar. “Real Time Collision avoidance for UAVs and Vehicle to vehicle (V2V) and Vehicle to Infrastructure (V2X) Communications Requirements”. AIAA InfoTech@Aerospace 2019.
V Stepanyan, C Ippolito, and K Krishnakumar. “Non-cooperative Airborne Dynamic Obstacle Avoidance Using Differential Games and Adaptive Control”, AIAA Science and Technology Forum and Exposition, 6–10 January 2020, Orlando, FL.

## Slide 24: Select Publications
Full publication list available at http://utm.arc.nasa.gov
Baculi, Joshua E., and Corey A. Ippolito. “Towards An Autonomous sUAS Operating in UTM TCL4+ and STEReO Fire Scenario”. AIAA Scitech 2021 Forum, p. 1471. 2021.
Stepanyan, Vahram, Anjan Chakrabarty, and Corey A. Ippolito. "Pursuit-Evasion Game approach to Tree-Based Path Planning for Airborne Dynamic Obstacle Avoidance." In AIAA Scitech 2021 Forum, p. 1575. 2021.
C Ippolito, K. Krishnakumar. “Concept of Operations Towards Fully Autonomous UAS Operations over Urban Environments”. AIAA InfoTech@Aerospace, 2019.
C Ippolito, K. Krishnakumar. “An Autonomy Architecture for Autonomous Urban Environment Operations”. AIAA InfoTech@Aerospace, 2019.
A Chakrabarty, S Hening, J Baculi, C Ippolito, K Krishnakumar. “Real Time Collision avoidance for UAVs and Vehicle to vehicle (V2V) and Vehicle to Infrastructure (V2X) Communications Requirements”. AIAA InfoTech@Aerospace, 2019.
V Stepanyan, C Ippolito, and K Krishnakumar. “Non-cooperative Airborne Dynamic Obstacle Avoidance Using Differential Games and Adaptive Control”. AIAA Science and Technology Forum and Exposition, 6–10 January 2020, Orlando, FL.
V Stepanyan, K Krishnakumar, C Ippolito. “Coordinated turn trajectory generation and tracking for multirotors”. AIAA InfoTech@Aerospace, 2019.
A Chakrabarty, V Stepanyan, C Ippolito, Kalmanje Krishnakumar., “Recursive Tree based Local Planner for Multi-copters flying in UTM -TCL4”. AIAA InfoTech@Aerospace, 2019.
Chakrabarty, Anjan, Vahram Stepanyan, Kalmanje S. Krishnakumar, and Corey A. Ippolito. "Real-time path planning for multi-copters flying in UTM-TCL4." In AIAA Scitech 2019 Forum, p. 0958. 2019.
C Ippolito, K. Krishnakumar. “Dynamic Ground Risk Mitigation for Autonomous Small UAS in Urban Environments”. AIAA InfoTech@Aerospace, 2019.
(Best of Session Award, AIAA/IEEE DASC 2019)- X Bouyssounouse and C Ippolito. “Urban Area Unmanned Aerial Systems Sensor Capabilities for Ensuring Ground Hazards Safety”. 38th AIAA/IEEE Digital Avionics Systems Conference (DASC), 2019.
V Stepanyan and K Krishnakumar. “Input constrained M-MRAC for uncertain multirotors”. AIAA InfoTech@Aerospace, 2019.
J Baculi, C Ippolito, K Krishnakumar, S Hening. “Onboard Decision-Making for Nominal and Contingency UAV Flight”. AIAA InfoTech@Aerospace, 2019.
C Ippolito, K. Krishnakumar. “An Interface-based Cybersecurity Analysis Methodology for Untrusted Sub-Systems”. AIAA InfoTech@Aerospace, 2019.
(Best Paper Award, AIAA SciTech 2018) - Ippolito, Corey A., Sebastian Hening, Shankar Sankararaman, and Vahram Stepanyan. A modeling, simulation and control framework for small unmanned multicopter platforms in urban environments. In 2018 AIAA SciTech Modeling and Simulation Technologies Conference, p. 1915. 2018.
Hening, S., Ippolito, C. A., Krishnakumar, K. S., Stepanyan, V., & Teodorescu, M. (2017). “3D LiDAR SLAM integration with GPS/INS for UAVs in urban GPS-degraded environments”. In AIAA Information Systems-AIAA Infotech@ Aerospace (p. 0448).
M Konstantin, Rafael D. Apaza, Alan N. Downey, R J. Kerczewski, J Jung, C Ippolito, and H Modi. “Analysis of at-Altitude LTE Power Spectra for Small Unmanned Aircraft System C2 Communications”. In 2019 Integrated Communications, Navigation and Surveillance Conference (ICNS), pp. 1-12. IEEE, 2019.
Ippolito, Corey, Kalmanje Krishnakumar, and Sebastian Hening. "Preliminary results of powerline reconstruction from airborne LiDAR for safe autonomous low-altitude urban operations of small UAS." 2016 IEEE SENSORS. IEEE, 2016.

## Slide 25
UTM Technical Interchange Meeting
February 23rd, 2021
Unmanned Aircraft Systems (UAS) Traffic Management (UTM) Project
Advanced Airborne Autonomy
for Urban Flight Operations
Dr. Corey A. Ippolito
Lead, UTM Task 10 - Urban Autonomy