## Slide 1: DAIDALUS, ICAROUS, SIRIUS, and Their Batch Simulation Capabilities
Presented by César Muñoz
February 22, 2021
ICAROUS Team: María Consiglio (NASA), César Muñoz (NASA), Swee Balachandran (NIA), Brendan Duffy (NIA), Andrew Peters (NIA), Marco Feliu (NIA), Víctor Carreño (NIA)

## Slide 2: DAA Research at LaRC
2007-2013: RTCA SC-203 SG3 (Unmanned Aircraft System – UAS Airspace Integration)
2012: First NASA publication described the concept later adopted by RTCA SC228 and the UAS community*
2013-2015: SARP (Science and Research Panel) for DAA convened by DOD and MIT-LL on the development and evaluation of DAA WC models
2013-…: RTCA SC-228, Minimum Performance Standards (MOPS) for UAS Detect and Avoid (DAA)
2017: RTCA DO 365 MOPS (Phase 1: En-route). NASA’s DAIDALUS (Detect and Avoid Alerting Logic for Unmanned Systems) included as the reference implementation for DAA in MOPS**
2020: DO 365A MOPS (Phase 2: Terminal Area): DAIDALUS v2.0.1
2021: DO 365B MOPS (Phase 3: Non-cooperative aircraft): DAIDALUS v2.0.2
* Concept of integration for UAS operations in the NAS, M. Consiglio, J. Chamberlain, C. Muñoz, and K. Hoffler, Proceedings of the 28th International Congress of the Aeronautical Sciences (ICAS 2012), 2012.
** https://shemesh.larc.nasa.gov/fm/DAIDALUS/

## Slide 3: From Separation Assurance to DAA
(1x1 State-Based CD&R Algorithms)
(1x1 State-Based CD&R Library)
(1xN State-Based CD&R )
(1xN Intent-Based CD&R)
(DAIDALUS v0)

## Slide 4: DAIDALUS: DAA Software Library (https://github.com/nasa/daidalus)
Detect and Avoid Alerting Logic for Unmanned Systems (DAIDALUS) is an open-source software library (available in Java and C++) that implements a configurable detect and avoid (DAA) concept
Formally verified, ownship-centric, state-less core algorithms:
  Detection Logic: Determines the current pairwise well-clear status
  Maneuver Guidance Logic: Computes maneuver guidance to maintain or regain well-clear status:
    suggestive guidance: kinematic and instantaneous bands
    directive guidance: track, ground speed, vertical speed, altitude
  Alerting Logic: Determines alert level

## Slide 5: DAIDALUS High Level Architecture

## Slide 6: DAIDALUS Outputs
Alert Level
Suggestive Guidance
Directive Guidance

## Slide 7: DAIDALUS Features to Explore in UAM
Support for dynamic alerters depending on type of aircraft, sensor source, participant vs. non-participant, phase of flight, etc. Each alerter defines well-clear volume and alert levels.
Intruder-centric alerting logic
Sensor Uncertainty Mitigation (SUM) logic
Hysteresis and persistence logic
DAA Terminal Areal (DTA) logic
Beyond DO-365:
  Directive guidance
  Ground speed maneuvers
  Implicit coordination and priority rules

## Slide 8: DAIDALUS Directive Guidance is (Mostly) Implicitly Coordinated
From Ownship’s Point of View
From Intruder’s Point of View

## Slide 9: DAIDALUS Directive Guidance Doesn’t Necessarily Follow Right of Way Rules (14 CFR 91.113)
From Ownship’s Point of View
From Intruder’s Point of View

## Slide 10: Right of Way (14 CFR 91.113)
“(d) When aircraft of the same category are converging at approximately the same altitude (except head-on, or nearly so), the aircraft to the other’s right has the right-of-way.
(e) When aircraft are approaching each other head-on, or nearly so, each pilot of each aircraft shall alter course to the right.
(f) Each aircraft that is being overtaken has the right-of-way.”
Which aircraft has the right-of-way?
AC0
AC1
A. Narkawicz, C. Muñoz, and J. Maddalon, A Mathematical Analysis of Air Traffic Priority Rules, Proceedings of the 12th AIAA Aviation Technology, Integration, and Operations (ATIO) Conference, AIAA-2012-5544, Indianapolis, Indiana, 2012.

## Slide 11: DAA-Displays: DAA Visualization and Analysis Tool (http://github.com/nasa/daa-displays)*
Encounter
(.daa)
Configuration
(.conf)
v1
v2
ACAS Xu
DAA-Displays
Replay encounters (list of aircraft states at a series of times)
Different configurations and DAA logics, e.g., DAIDALUS v1, DAIDALUS v2, and, future, ACAS Xu
Visualize maneuver guidance, alerts, compliance to functional requirements, etc.
Time-step by time step computation of DAA metrics, e.g., tcpa, dcpa, etc.
* Joint work with P. Masci (NIA)

## Slide 12: ICAROUS: DAA On-Board System (https://github.com/nasa/icarous)
ICAROUS is an on-board software system of distributed services for autonomous UAS
Provide modules that monitor and autonomously enforce containment constraints such as detect and avoid (DAA), geofencing, path planning, path conformance, distributed merging and spacing, etc.
Use formally verified algorithms such as DAIDALUS (DAA) and PolyCARP (Geofencing)
Support for ACAS sXu (collaboration with JHU/APL)
C++ software available under NASA Open Source Agreement
Over 400 flight tests under the UTM project.

## Slide 13: ICAROUS High Level Architecture
DAIDALUS provides DAA functionality.
ICAROUS autonomously implements avoidance maneuver and returns to mission.

## Slide 14: ICAROUS/DAIDALUS Evolution
ACCORD/Stratway
2001-2012
Formally developed and verified models and algorithms
for DAA.
Provides maneuver guidance and conflict alerting for the pilot in command to maintain “well clear” separation.
Formally developed and verified models and algorithms for
conflict detection and resolution for airborne separation assurance. Predicts potential conflicts and computes resolution routes.
DAIDALUS
2013-2017
Manned aviation
Large UAS (IFR)
RTCA SC228 DAA Requirements for TCAS interoperability and Alerting
Small UAS, very Low altitude operations, sUAS (<55 lbs)
Airspace segregation (time/space) constraints (geofencing)
ICAROUS
2016-2020
Small UAS (<55lbs))
UTM
Small UAS-Very Low Altitude Operations.
Airspace Segregation. Performance Based Authorization.
ICAROUS
2019-…
4D trajectories.
DAA and airspace constraints (path conformance, corridors)
Varying levels of autonomy
Merging and crossing corridors
UAM
4D trajectories.
DAA and airspace constraints (path conformance, corridors)
Varying levels of autonomy
Merging and crossing corridors
UAM VTOL

## Slide 15: UAM Separation: From Pre-Flight to Collision Avoidance*
DAA/On board systems
UAM Operator
PSU
ATC
Airspace and Operations Authorization, Emergencies/Off-Nominal Conditions
Pre-flight, Strategic Deconfliction
Operations Planning and runtime monitoring
Tactical Separation, DAA/CA
ICAROUS
*Min Xue, Generalized Conflict Management Model

## Slide 16: DAA Encounters Type in UAM
Merging UAM Traffic
VFR Traffic
(Non-equipped)
Aircraft complies with a 4D trajectory comprised of time- controlled segments.
Conflict 3: UAM Merging Coordination: A coordinated merge is executed as the two UAM vehicles communicate to agree on a merging order. Both aircraft proceed safely to their destination maintaining safe in-trail spacing.
Conflict 1: Non-UAM Traffic
UAM vehicle flying a 4D trajectory as provided by the UAM scheduler. A conflict is predicted with a non-participating GA aircraft entering the UAM corridor. An ownship avoidance maneuver is computed that makes best effort to maintain separation and ownship time constraints.
Conflict 2: UAM Crossing Coordination: A coordinated resolution maneuver is executed and both aircraft proceed safely to their destination
Crossing UAM Traffic

## Slide 17: ICAROUS Features in Support of UAM Research
4D kinematic trajectories
  Linear 4-D trajectories
  Kinematic 4-D trajectories (LaRC’s EUTL)
Aircraft dynamic models
  Simple point-mass
  6-DOF High Fidelity Rotorcraft UAS
  6-PAX Quad EVT
Real- and fast-time simulation
✓
✓
✓

## Slide 18: ICAROUS Integration with External Systems
ICAROUS Vehicle 2
Langley
TestBed
Standalone Bridges
Ames
TestBed
ACAS sXu
ZeroMQ
DDS
ActiveMQ
…
…
Langley’s UAM Software
UAMSim
ATS TIGAR
Flight Kiosk
Telemetry
Commands
ICAROUS Vehicle 1
ZMQ IFACE
Software Bus Network
…
cFS
DAIDALUS
Merging &
Spacing
PolyCARP
ICAROUS
Gateway
ACAS sXu
Server
ZeroMQ
cFS
cFS
cFS

## Slide 19: ICAROUS Testbed Software Integration
UAM SIM
WebGS
Vertiport Scheduler
ATS TIGAR
LaRC Testbed
4D Trajectories
Bands, 4D Trajectory
Resolutions
Ownship State
Traffic and Ownship
State Information
Bands, 4D Trajectory
Resolutions
Configuration
Interface
Information
(MS Windows)
(MS Windows)
(Mac OSX)
(Linux)
ICAROUS
ICAROUS Gateway
Implemented bi-directional communication between ICAROUS, ATS TIGAR, and UAM Sim through LaRC Test Bed.
ATS TIGAR uses the Vertiport Scheduler to provide deconflicted trajectories for a fleet of UAM vehicles.
The ownship is simulated in the UAM Sim and is running ICAROUS.
ICAROUS detects potential ownship conflicts and provides maneuver guidance.
UAM Sim automatically implements maneuver guidance.
WebGS (a web-based research ground station) displays ICAROUS information.

## Slide 20: ICAROUS Testbed Software Integration (Demo)
Maneuver
Guidance
Maneuver
Guidance
New 4D Trajectory
New 4D Trajectory

## Slide 21: SIRIUS: Fast Time Simulation of DAA for UAM (https://gitlab.larc.nasa.gov/larc-nia-fm/Sirius)
Simulation Infrastructure for Research on Interconnected Unmanned System (SIRIUS)
Graphical research environment for fast-time simulation and analysis of Urban Air Mobility (UAM) airspace operations.
SIRIUS provides a seamless integration of
  detect and avoid (DAIDALUS), merging and spacing, path planning, and geofencing capabilities (PolyCARP),
  an autonomous decision-making on-board architecture (ICAROUS),
  a fast-time batch simulation environment, and
  graphical analysis tools
  for evaluating alerting and guidance performance of separation provisions for UAM

## Slide 22: SIRIUS High Level Architecture
Python
Simulation Environment
for ICAROUS
Encounter
Builder
Configuration
DAA Parameters
ICAROUS Parameters
Encounter
Parameters
Communication
and
Environment
Parameters
Pairwise Encounter
Builder
Network
Builder
Surveillance
Uncertainty
Simulation
Parameters
Pycarous
Logs and Data
Analyzer
Python
Simulation Environment
for ICAROUS
Pycarous
Python
Simulation Environment
for ICAROUS
Pycarous

## Slide 23: Batch Parallelization
Python Simulation Environment
Decision
Making
DAIDALUS
PolyCARP
Planning
Merging
Aircraft simulator
Decision
Making
DAIDALUS
PolyCARP
Planning
Merging
Aircraft simulator
Decision
Making
DAIDALUS
PolyCARP
Planning
Merging
Aircraft simulator
Decision
Making
DAIDALUS
PolyCARP
Planning
Merging
Aircraft simulator
Aircraft Cn
Aircraft 1
Aircraft 2
Aircraft C3
Python Simulation Environment
Decision
Making
DAIDALUS
PolyCARP
Planning
Merging
Aircraft simulator
Decision
Making
DAIDALUS
PolyCARP
Planning
Merging
Aircraft simulator
Decision
Making
DAIDALUS
PolyCARP
Planning
Merging
Aircraft simulator
Decision
Making
DAIDALUS
PolyCARP
Planning
Merging
Aircraft simulator
Aircraft Bn
Aircraft A1
Aircraft A2
Aircraft A3
Computer 3
Python Simulation Environment
Decision
Making
DAIDALUS
PolyCARP
Planning
Merging
Aircraft simulator
Decision
Making
DAIDALUS
PolyCARP
Planning
Merging
Aircraft simulator
Decision
Making
DAIDALUS
PolyCARP
Planning
Merging
Aircraft simulator
Decision
Making
DAIDALUS
PolyCARP
Planning
Merging
Aircraft simulator
Aircraft An
Aircraft A1
Aircraft A2
Aircraft A3
Computer 1
Scenario 1 Controller
Computer 2
Scenario 2 Controller

## Slide 24: Pairwise Encounter Configuration
Type of Encounter:
  DAA
  Merging
Type of Simulation:
  Exhaustive
  Monte Carlo (Uniform, Normal, Gamma, Exponential)
Type of Geometry:
  Based on Miss Distance
  Based on Convergence Angle

## Slide 25: Communication and Surveillance Configuration*
Propagation Model*:
  Constant, No Loss, Free Space, Two Ray Ground
Reception Model*:
  Perfect, Deterministic, Constant, Rayleigh, Nakagami
Communication Delay
Wind
Ownship and intruder covariances and z-score for position and velocity
*https://gitlab.larc.nasa.gov/larc-nia-fm/icarous/-/blob/master/Python/pycarous/communicationmodels/modelinformation.md

## Slide 27: Head-on Encounter

## Slide 28: Network Builder
Ports have an output rate and output variance
Support for merging waypoints
Waypoints have multiple inputs and outputs.
Random generation of scenarios

## Slide 30: Dallas-Fort-Worth (DFW) Area in SIRIUS

## Slide 31: SIRIUS Main Features
Highly Configurable:
  DAA: Well-clear definition, alerting logic, maneuver guidance, support for intruder-centric DAA logic
  Uncertainties: Surveillance, communication delays, winds
  Equipped and non-Equipped aircraft
  Aircraft models: point mass, 6-DOF High Fidelity Rotorcraft UAS, 6-PAX Quad EVTOL aircraft models
Support for 4-D Kinematic Trajectories (LaRC’s EUTL)
Batch Parallelization:
  Scenarios can be run in parallel on different computers
  Aircraft from the same scenario can be run on different computers
Modular:
  Support for alternative DAA logic, e.g., Xu, noise models, metrics, etc.
Deterministic and Monte-Carlo based generation of scenarios

## Slide 32: On-Going and Future Work
Network builder
  Integration with TIGAR/Vertiport Scheduler
  Integration of concepts such as ”routes”, “tracks”, ”corridors” as defined for the UAM project
Design of case studies and specific metrics, e.g.,
  Implicit coordination and priority
  Recapture strategy (next way point, to segment)
  Airspace complexity metrics