## Slide 1: Modeling Spacecraft Separation Dynamics in Julia
Jonnie Diegelman
Guidance, Navigation, and Control Engineer
a.i. solutions / NASA Launch Services Program
SIAM 2021 Conference on Computational Science and Engineering
Symposium on High Performance Simulation and Estimation with Julia’s SciML
March 5, 2021

## Slide 2: Intro
NASA Launch Services Program

## Slide 3: Intro NASA Launch Services Program
NASA LSP: “Earth’s Bridge to Space”

## Slide 4: Intro NASA Launch Services Program
NASA LSP: “Earth’s Bridge to Space”
Kennedy Space Center, FL

## Slide 5: Intro NASA Launch Services Program
NASA LSP: “Earth’s Bridge to Space”
Kennedy Space Center, FL
Connecting NASA scientific missions to commercial launch vehicle providers

## Slide 6: Intro LSP Mission Analysis
Mission planning

## Slide 7: Intro LSP Mission Analysis
Mission planning
Analysis and simulation
  Loads
  Thermal
  Fluids
  Space environments/radiation
  Flight controls
  Trajectory analysis
  etc.

## Slide 8: Intro LSP Mission Analysis
Mission planning
Analysis and simulation
Special studies

## Slide 9
Spacecraft Separation

## Slide 10: Spacecraft Separation Sentinel 6 Michael Freilich

## Slide 11: Spacecraft Separation Modeling
Rigid body dynamics

## Slide 12: Spacecraft Separation Modeling
Rigid body dynamics
  Velocity, position, and rotation rate equations about center of mass

## Slide 13: Spacecraft Separation Modeling
Rigid body dynamics
  Velocity, position, and rotation rate equations about center of mass
  Quaternion attitude update

## Slide 14: Spacecraft Separation Modeling
Rigid body dynamics
  Velocity, position, and rotation rate equations about center of mass
  Quaternion attitude update
Forcing functions

## Slide 15: Spacecraft Separation Modeling
Rigid body dynamics
  Velocity, position, and rotation rate equations about center of mass
  Quaternion attitude update
Forcing functions
  Clampband release

## Slide 16: Spacecraft Separation Modeling
Rigid body dynamics
  Velocity, position, and rotation rate equations about center of mass
  Quaternion attitude update
Forcing functions
  Clampband release
  Pusher springs

## Slide 17: Spacecraft Separation Modeling
Rigid body dynamics
  Velocity, position, and rotation rate equations about center of mass
  Quaternion attitude update
Forcing functions
  Clampband release
  Pusher springs
  Various connectors (not pictured)

## Slide 18
Current Separation Analysis Tool

## Slide 19: Current Separation Analysis Tool Overview
Written in block-diagram-based causal modeling language (Simulink)
User-facing input deck – MATLAB script

## Slide 20: Current Separation Analysis Tool Problems
Problem: Not very flexible
  Can only handle a single spacecraft/launch vehicle separation
    There is a growing demand for CubeSats and other rideshares on NASA launches
  Difficult to handle derived dispersed parameters
    Monte Carlo dispersion draws happen after input deck is read in
    New intermediate parameters must be hard-coded into simulation setup and input deck
    Example: Vehicle dry mass: Vehicle propellant mass: Total (wet) mass: The simulation itself only needs to know the wet mass, but now we need to add entries into our input deck and input parsing function to handle separate dispersions for dry and propellant masses. Leads to explosion of input deck size and complexity.

## Slide 21: Current Separation Analysis Tool Problems
Problem: Complicated
  Input deck --> “explosion of complexity”
  Current input script is over 1000 lines of MATLAB code
  Error-prone
    Did you remember to set all the parameters you needed?
    Did you remember to unset all the parameters you didn’t need?
  Prohibits quick turn-around analyses
  High learning curve

## Slide 22: Current Separation Analysis Tool Problems
Problem: Slow
  ~15 minutes for 514 Monte Carlo runs
  “Engineer time vs. compute time”
    Engineer time is expensive, compute is cheap… … until it takes engineering hours to iterate with slow tools
    When computation takes minutes, debugging takes hours
  Cannot interactively explore design trade-offs or parameter sensitivities
  Too slow for robust design parameter optimization

## Slide 23
Alternative Frameworks

## Slide 24: Alternative Frameworks Acausal Modeling
Pros
Simple initial set up – no hand-deriving equations of motion
Easier to add new features or do custom mission-unique work
Modular
Cons
Can be even slower
  Prohibitive for Monte Carlo analysis
Limited by features of framework
DAEs: Overkill for spacecraft separation simulation?
Examples: Simscape, Modelica

## Slide 25: Alternative Frameworks Standard ODE Solver
Pros
Fast
Cons
Difficult to set up
Not modular: flat state vector
  Q: How do you handle an arbitrary number of spacecraft with a flat state vector? A: Lots of index juggling
  Q: What about nested spacecraft separations (spacecraft with child spacecraft)? A: ??
Examples: ODEPACK, MATLAB, Sundials

## Slide 26: Alternative Frameworks ODE Solver+ (SciML and Julia Ecosystem)
Pros
Fast
Composable with Julia ecosystem
  Modularity: ComponentArrays.jl
  Derived uncertain parameters: MonteCarloMeasurements.jl
  Physical unit checking: Unitful.jl
  Sensitivity analysis: DiffEqSensitivity.jl
  Interactive exploration: Pluto.jl
  3D visualization: Meshcat.jl
  etc.
Cons
Users must learn new language

## Slide 27
RECURSAT

## Slide 28: RECURSAT Requirements
RECURSAT requirements

## Slide 29: RECURSAT Requirements
RECURSAT requirements
Efficient – Be able to run hundreds of Monte Carlo runs in under a second for interactive exploration

## Slide 30: RECURSAT Requirements
RECURSAT requirements
Efficient
Composable – Must work together with external tools, such as optimizers

## Slide 31: RECURSAT Requirements
RECURSAT requirements
Efficient
Composable
Universal – Handle every type of mission, including multiple spacecraft or even nested spacecraft

## Slide 32: RECURSAT Requirements
RECURSAT requirements
Efficient
Composable
Universal
Reasonably simple – Easy to learn with no “explosion of complexity” when adding new features

## Slide 33: RECURSAT Requirements
RECURSAT, the
Efficient
Composable
Universal
Reasonably simple
Separation
Analysis
Tool

## Slide 34: RECURSAT Design
Recursive Design

## Slide 35: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
(it doesn’t)

## Slide 36: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
The function is called on all children

## Slide 37: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
The function is called on all children

## Slide 38: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
The function is called on all children

## Slide 39: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
The function is called on all children

## Slide 40: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
The function is called on all children

## Slide 41: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
The function is called on all children
The net force and moment goes into the vehicle’s equations of motion

## Slide 42: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
The function is called on all children
The net force and moment goes into the vehicle’s equations of motion
The function returns equal and opposite force points to parent

## Slide 43: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
The function is called on all children
The net force and moment goes into the vehicle’s equations of motion
The function returns equal and opposite force points to parent

## Slide 44: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
The function is called on all children
The net force and moment goes into the vehicle’s equations of motion
The function returns equal and opposite force points to parent

## Slide 45: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
The function is called on all children
The net force and moment goes into the vehicle’s equations of motion
The function returns equal and opposite force points to parent

## Slide 46: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
The function is called on all children
The net force and moment goes into the vehicle’s equations of motion
The function returns equal and opposite force points to parent

## Slide 47: RECURSAT Design
Recursive Design
Forces and points of application are calculated from a vehicle’s parent separation system (if it has one)
The function is called on all children
The net force and moment goes into the vehicle’s equations of motion
The function returns equal and opposite force points to parent
Update state

## Slide 48: RECURSAT Requirements Met
Efficient
514 Monte Carlo runs in < 60 ms
15,000x faster* than the baseline model
*Some features of the baseline model are not implemented yet, expect this number to drop a small amount

## Slide 49: RECURSAT Requirements Met
Composable
MonteCarloMeasurements.jl: random variables that propagate through arithmetic operations
Unitful.jl: physical unit checking
DiffEqSensitivity.jl: global or local sensitivity analysis
ForwardDiff.jl or Zygote.jl: automatic differentiation
DiffEqUncertainty.jl + Optim.jl: robust design optimization under uncertainty
dry_mass = (25 ± 2)kg
prop_mass = (300..350)kg
mass = dry_mass + prop_mass

## Slide 50: RECURSAT Requirements Met
Universal
Recursive structure allows for completely arbitrary configuration
ComponentArrays.jl lets complex, nested structures pass through differential equation solver as a flat vector

## Slide 51: RECURSAT Requirements Met
Reasonably Simple
New models can be set up in minutes with few lines of code
Import types and functions from library rather filling out input deck
  Specify only what you need
  No more “exploding complexity”
  View docstrings of exported functions in REPL

## Slide 52
RECURSAT Example

## Slide 53: RECURSAT Example Intro
Requirements
Tip-off Rates
< 1°/sec rotation rate in all spacecraft axes for all runs
Separation Velocity
> 0.55 m/sec relative velocity (between launch vehicle and spacecraft) for all runs
Assumptions
Launch vehicle and one spacecraft
514 Monte Carlo runs
Stacked vehicle starts with dispersed body rates about the combined center of mass.

## Slide 54: RECURSAT Example Input Specification
The .. and ± operators are imported from MonteCarloMeasurements.jl to describe uniform and normal random variables, respectively
kg, m, and mm are imported from Unitful.jl to enforce correct units
spacecraft = Vehicle(
sim_name = :SC,
mass = (1000..1200)kg,
inertia = inertia_tensor(
xx = (500..600)kg*m^2,
yy = (1500..2500)kg*m^2,
zz = (1600..2600)kg*m^2,
xy = (5 ± 20)kg*m^2,
xz = (5 ± 20)kg*m^2,
yz = (-20..20)kg*m^2,
),
cg = Vector3(
x = (1.4..1.6)m,
y = -(20..40)mm,
z = -(40..60)mm,
),
sep_plane = Plane(
normal = Vector3(x=-1)
),
)

## Slide 55: RECURSAT Example Results
Not meeting tip-off requirement about the spacecraft y-axis.
High center of mass offset along -z direction

## Slide 56: RECURSAT Example Mitigation Strategy
Mitigation strategy: Add a ballast mass inside the spacecraft
Free variables and constraints:
  Ballast mass: 200 kg
  Ballast position from spacecraft separation plane:
    1m x 2m
    -0.1m y 0.1m
    -0.15m z 0.15m
Must be careful not to violate minimum separation velocity requirement

## Slide 57: RECURSAT Example Mitigation Strategy

## Slide 58: RECURSAT Example 3D Visualization

## Slide 59
Backup