## Slide 1
National Aeronautics and Space Administration
ATTAM/EOA Steering Committee Update
Jimmy Kenyon
Director, Advanced Air Vehicles Program
March 24, 2021

## Slide 2: NASA Aeronautics – Vision for Aviation in the 21st Century
U.S. leadership for a new era of flight
ARMD continues to evolve and execute the Aeronautics Strategy
https://www.nasa.gov/ aeroresearch/strategy

## Slide 3: Research Programs Align with Strategic Thrusts
AIRSPACE OPERATIONS & SAFETY
AOSP
PROJECTS
ATM Tech Demonstrations*
UTM*
ATM-X
System-Wide Safety
ADVANCED AIR VEHICLES
AAVP
PROJECTS
Advanced Air
Transport Technology
Hybrid Thermally Efficient Core**
Hi-Rate Composite Aircraft Manufacturing**
Commercial Supersonic Technology
Revolutionary Vertical Lift Technology
Advanced Composites*
Hypersonic Technology
INTEGRATED AVIATION SYSTEMS
IASP
PROJECTS
UAS in
the NAS*
Flight Demonstrations
and Capabilities
Low Boom Flight Demonstrator
Electrified Powertrain Flight Demonstration**
Advanced Air Mobility
TRANSFORMATIVE AERONAUTICS CONCEPTS
TACP
PROJECTS
Convergent Aeronautics Solutions
Transformational Tools and Technologies
University Innovation
MISSION PROGRAMS
SEEDLING PROGRAM
Integration and Flight
AEROSCIENCES EVALUATION & TEST CAPABILITIES
AETC
Subsonic
Transonic
Supersonic
Hypersonic
Propulsion
Test Technology
PORTFOLIO OFFICE
GROUND FACILITIES
* Projects end in FY 2020/21
** Projects start in FY 2021

## Slide 4: Thrust 2: Innovation in Commercial Supersonic Aircraft

## Slide 5: Overcoming the Barrier to Overland Flight
New Environmental Standards are needed to open the market to supersonic flight
An En Route Noise Standard is the biggest challenge
  Requires proof of new design approaches, test procedures and response metrics
  No relevant data exists to define limits - community data from large, diverse population is a requirement
  Standard must be accepted internationally
  Standards to Replace Current Prohibitions

## Slide 6: Low Boom Flight Demonstration Mission
Phase 2 – Acoustic Validation (FY22 - 24)
  Aircraft operations & support, range ops, support aircraft
  Ground and in-flight measurement capabilities
  Validation of X-59 boom signature and prediction tools
  Development of acoustic prediction tools
Phase 3 – Community Response (FY24 - 26)
Initial community response overflight study
Multiple campaigns (4 to 6) over representative communities and weather across the U.S.
Noise exposure measurements and community response surveys
Phase 1 – X-59 Aircraft Development (FY18 - 22)
  Detailed design
  Fabrication, integration, ground test
  Checkout flights
  Subsonic and supersonic envelope expansion

## Slide 7: Low Boom Flight Demonstration Progress
X-59 Aircraft Development
Design and drawings complete
Assembly and systems testing underway
Acoustic Measurement
Awarded contract for Ground Recording System development
Continuing progress on airborne acoustic measurement systems
Community Test Planning
Test airfield selection process underway
Test support team contract solicitation in progress
Conducted Community Test International Workshop
International Standards Development
On-going engagement with ICAO CAEP and international research community
Image Credit: Lockheed Martin
  Significant progress despite COVID-19 pandemic impacts
Potential Community Test Airfield Locations Combined with Regions of Noise-Sensitive Considerations
Notes: FAA engagement: TO BE VERIFIED BY LORI
FAA Office of Environment & Energy:
Coordination with ASCENT COE on Over the Top Boom (with PSU), High Altitude Emissions (Projects 47 and 48)
Guidance/input on community response planning
Support for and engagement with ICAO; specifically STCA modeling and LTO noise predictions
Support for the Notice of Proposed Rulemaking for supersonic aircraft

## Slide 8: LTO Noise Prediction Uncertainty Reduction
LTO Noise prediction uncertainty is a key problem for emerging supersonic market
FAA’s NPRM based on NASA predictions for ICAO, despite large uncertainty
Launched new Technical Challenge to reduce uncertainty in prediction of noise for supersonic aircraft
  Physics-based simulations of supersonic-relevant inlet, fan, and nozzle designs with OEM input
  Input to system-level tools and Monte Carlo simulations
  Data releasable for impact on international regulators
  Potential validation approaches being assessed
Conventional Product Development
Test
Design
Prediction
Prediction
Cumulative
EPNL
2019 ICAO Study Supersonic
Noise Uncertainties
Fan
Jet
  New effort reduce uncertainty in LTO noise predictions
Notes: Although there have been budget cuts to our airport noise work, we are still committed to kicking off a new technical challenge. We have descoped it to be focused on reducing the uncertainty in LTO predictions. As shown the uncertainty in the predictions for LTO noise are currently much larger than that for subsonic vehicles.
We had a contract with GE to design and test a releasable flow-path and fan which we re-negotiated to include just the design aspect. The budget profile shown highlights that we were able to fully fund that renegotiated contract to offset our inability to get the CTPE contract awarded. This allowed us to obligate most of our FY20 funding and that contract should complete in FY21. The TC will be planned with the ability for on ramps for testing if budgets allow.
But we feel even with this reduced scope, this work is so critical that it needs to be raised to the level of a technical challenge.
Develop a releasable flow-path and fan design for a commercial supersonic transport relevant geometry to enable Landing/Take-Off noise predictions and testing.

## Slide 9: Thrust 3: Ultra-Efficient Subsonic Transports

## Slide 10: 3 Pillars to a More Sustainable Future
USE
LESS ENERGY by aircraft design
USE LESS ENERGY by how you fly
USE CLEANER ENERGY full lifecycle

## Slide 11: Carbon Impact Across the Global Commercial Fleet - 2018
289 million metric tons (912 Mt carbon)
  65% International / 35% Domestic
Industry Carbon Goal 2050 (ATAG Waypoint 2050)
  Carbon neutral growth from 2020
  Reduce fleet carbon emission by 50% from 2005 (from 650 Mt to 325 Mt with fleet growth)
Single Aisle Aircraft Families emit the most carbon (38%), 92% of which is flying ≤ 2000 nm (2302 miles)
Chart: Total Fuel BURN - GLOBAL
| TP 1-85 | RJ 20-125 | SA 126-210 | STA 211-300 | LTA 301-400 | VLA 400+ | Freighter | BizJet
TOTAL | 3.1613 | 16.1407 | 110.2429 | 68.9582 | 43.1383 | 18.3207 | 24.8244 | 4.0302
Chart: 
| < 500 | 0.5-1k | 1-1.5k | 1.5-2k | 2-4k | 4-6k | 6-11k
 | 0.085489 | 0.14133 | 0.078103 | 0.045233 | 0.028795 | 0.0025347 | 0.00022497
SA Fuel Burn by Range
Volpe Preliminary Data - used with permission final data to be published in Chapter 1 of 2022 ICAO Environmental Report)
Notes: More precisely US Gov Internal, not just NASA per Volpe. Permission to use with the NAC received from Volpe on 3/9/21
288.82 million metric tons of Jet A is 95.46 billion gallons
US TOTAL is 69.64 MMT or ~ 24% of global total …. 23.02 billion gallons, 9 international departing, 14.02 domestic
NOTE: the SA 126- 210 seat class captures the 737 and A320 families + the A220-300 (A220-100 is < 125 pax)
NOTE: 912 Mt (million metric tonnes) in 2018. from ATAG, 2005 was 650 Mt so the -50% goal at fleet level for 2050 is 325 Mt. 912 is 39% higher than 650, and the fleet needs to get to 325 Mt or better

## Slide 12: Subsonic Transport Strategy
Electrified Aircraft Propulsion
~5% fuel burn and maintenance benefit
High-Rate Composite Manufacturing
4x-6x manufacturing rate increase
Small Core Gas Turbine
5-10% fuel burn benefit
Transonic Truss-Braced Wing
5-10% fuel burn benefit
Ensure U.S. industry is the first to establish the new “S Curve” for the next 50 years of transports

## Slide 13: Next Gen Transports: Integrated Technology Development
Leverage the Asset –
Future Spirals
Planned
Notional
Sustainable Flight Demonstrator (SFD)
Model Based Systems Analysis & Engineering
AATT - Transonic Truss Braced Wing
Hi-Rate Composite Aircraft Manufacturing
(HiCAM)
Hybrid Thermally Efficient Core (HyTEC)
AATT - Electrified Aircraft Propulsion
Technology Readiness Target
Electrified Powertrain Flight Demonstration (EPFD)
Achieve TRL 6 in time for Industry Product Decision-Making
Flight Test
Mfg Demo & Structural Test
Core Demonstration & Test
Flight Test
Notes: 1 slide

## Slide 14: AATT – TTBW Technology Maturation
Further maturation and risk reduction of TTBW technology
Focus on edge-of-envelope performance, safety, and environmental concerns.
  Buffet Boundary Prediction
  Stall Characteristics
  High-Lift System Integration
  Acoustic Assessment
  Icing Impact
  Thin Wing Design/Unique Joints
Approach:
  Identify key barriers at critical flight points that will impact performance of the TTBW technology
  Perform high-fidelity prediction, testing and validation to increase confidence in fuel burn benefit
increase confidence in TTBW technology integrated in the aircraft system
New Technology Challenge launched
Wing Section Fab

## Slide 15: New Projects in Formulation
Hybrid Thermally Efficient Core (HyTEC)
Goal: 5-10% Fuel Burn Improvement
  Reduce engine core size, increase thermal efficiency
  Enable up to 20% electrical power extraction
Core/Engine Ground Test (TRL 6) by 2026
High-rate Composite Aircraft Manufacturing (HiCAM)
Goal: 4-6x Manufacturing Rate Increase
  High-rate manufacturing and assembly technologies
  Model-based engineering tools
Large Structure Ground Test (TRL/MRL 6) by 2027
  Accelerating development and demonstration of key technologies
NRA for technology development to be released soon
Meeting of Experts on partnership strategy being planned for this spring

## Slide 16: Thrust 4: Safe, Quiet, and Affordable Vertical Lift Air Vehicles

## Slide 17: Strategic Thrust 4 Safe, Quiet, and Affordable Vertical Lift Air Vehicles
Airspace System Design & Implementation
Airspace & Fleet Operations Management
Vehicle Development & Production
Individual Vehicle Management & Operations
Community Integration
Community Integration
Vehicle Development & Operations
Airspace Design & Operations
AAM Community Outcome
  Deliver a validated
    1) system concept and
    2) corresponding set of requirements
  for a safe and scalable AAM transportation system.
Advanced Air Mobility (AAM) Vision
Revolutionize mobility in and around metropolitan areas by enabling a safe, efficient, convenient, affordable, and accessible air transportation system for passengers and cargo

## Slide 18: Revolutionary Vertical Lift Technology Project
Noise & Performance of Multi-Rotor Vehicles
Fleet Noise
Reliable & Efficient Propulsion Components
National Campaign

## Slide 19: Hypersonics

## Slide 20: Hypersonic Technology Project
Industry Engagement on Future Commercial Hypersonic Vision
Fundamental Research on Dual-Use Applications
Strong DoD Partnership

## Slide 21: Hypersonic Strategy Assessment
Industry announcements reveal interest in commercial applications
Workshop held to understand interest and identify needs
  Independent market study
  Regulatory and data protection concerns
  Hypersonic ground and flight test capability
  Technology development
Assessing strategy in light of growing industry interest
  Enabling routine, reusable, airbreathing hypersonic flight
Emerging industry vision for potential future commercial hypersonic market

## Slide 22: Independent Market Studies
Key Findings
  SAIC: Commercial and private segments are most viable. Cargo demand not strong for civil use.
  Deloitte: Commercial, private, and cargo are all viable segments. Top routes vary by segment.
  Barriers largely similar to commercial supersonic flight, e.g., certification, LTO noise, emissions, field length, airspace integration
  Concern with export controls and market impacts
Industry Feedback on Results
  Favorable markets in a speed regime between NASA’s current supersonic and hypersonic portfolios
  Desire to extend market study to explore additional areas (e.g., including transpacific routes and alternative aircraft fuels)
  Interest in potential synergy between civil and defense applications for lowering required investment
  Role for NASA in facilitating working group with FAA, Department of State, Department of Defense, airport authorities, and industry to address certification, regulatory, and environmental barriers
 | SAIC (with Bryce Space and Technology) | Deloitte (with SpaceWorks & NIA)
Mach | 3 | 2 - 4
Range | 4500 nmi | 4000 nmi – 4500 nmi
Number of routes(1) | 300 | 90
Aircraft Size (# PAX) | 10 GA or 50 Commercial | 20 to 50
Aircraft Cost | $200M - $300M | $131M - $228M(2)
(1) Deloitte only considers over water routes
(2) Mach 3 at 4500 nmi
Favorable High-Speed Market Characteristics
  Potentially viable markets for high-speed air transportation

## Slide 23: Wrap-up

## Slide 24: A New Era of Flight Is Emerging
Next Generation Subsonic Transports
Making commercial air travel more sustainable
Advanced Air Mobility
Allowing people to move about more easily
Commercial Supersonic Flight
Addressing environmental barriers to connect people faster
Hypersonic Flight
Enabling a future vision for hypersonic transport
  Breaking down barriers to open new markets, advance U.S. competitiveness, and make air travel better for all Americans and for people around the world
Creating new “S” curves for the next 50 years of aviation