## Slide 1: Assessing Next-Gen Spacesuit Reliability: A Probabilistic Analysis Case Study at NASA
Jim Warner1, Patrick Leser1, Paul Leser1, Geoffrey Bomarito1, Austin Cole2
NASA Langley Research Center
Virginia Tech
DATAWorks 2021
April 13th, 2021

## Slide 2: Motivation
Probability of fall
Probability of impact location
Mission-related probabilities
Impact velocity uncertainty
Material Uncertainties
Probability of rock size
Impact Damage Simulation
Designing the Exploration Extravehicular Mobility Unit (xEMU) spacesuit
Variability in lunar regolith
Traditional approach of considering worst-case type loading and applying conservative factors of safety for certification was likely to be infeasible
Instead: introduce & verify a probabilistic requirement based on the probability of no impact failure (PnIF)
https://www.nasa.gov/specials/artemis/

## Slide 3: Case Study Overview
Motivated by the xEMU, a case study was conducted to demonstrate the application of uncertainty quantification (UQ) to estimate spacesuit reliability
  A previous generation of spacesuit (Z-2) was considered for demonstration
Case study demonstrated approaches for overcoming two common challenges in reliability analysis:
  Computational expense associated with using high-fidelity models
  Quantifying uncertainty in model input parameters
Research focus of the project: leveraging & developing multifidelity UQ methods for efficient and accurate reliability estimation

## Slide 4: Assessing Design Reliability with UQ
Output
Probability
Output
Inputs
Load parameters
Strength parameters
Computational Model
Spacesuit Design
Max. Stress
Damage Index
...
Param1
Prob
Param2
Prob
Prob
Param3
Structures & Materials
Param2
Prob
Prob
Param3
Param1
Prob
Loads
Reliability
Failure Threshold
Input Parameters
1) A validated computational model for the spacesuit is available
2) Reliable estimates for uncertainty in all input parameters are available
3) Computation time is not an issue
The reliability of a spacesuit design could be straightforwardly assessed with Monte Carlo simulation if:
Notes: Point out

## Slide 5: UQ Workflow for Assessing Design Reliability
  Sensitivity analysis identifies the most influential system parameters to properly focus effort/resources in a probabilistic analysis
Output
Inputs
Load parameters
Strength parameters
Computational Model
Max. Stress
Damage Index
...
Param1
Prob
Param2
Prob
Prob
Param3
Structures & Materials
Param2
Prob
Prob
Param3
Param1
Prob
Loads
Output
Reliability
Failure Threshold
Probability
Param A
Prob
Param E
Prob
Param C
Prob
Param D
Prob
Param F
Prob
Param B
Prob
Param A
Prob
Param E
Prob
Param C
Prob
Param D
Prob
Param F
Prob
Param B
Prob
Sensitivity Analysis
Input Parameters
Spacesuit Design
In this work: sensitivities computed using delta moment-independent measures [1]
[1] Plischke et al. Global sensitivity measures from given data. 2013.

## Slide 6: UQ Workflow for Assessing Design Reliability
  Model calibration explicitly quantifies model input uncertainties using experimental data (can be used to improve or update initial assumptions)
Output
Inputs
Load parameters
Strength parameters
Computational Model
Max. Stress
Damage Index
...
Param1
Prob
Param2
Prob
Prob
Param3
Structures & Materials
Param2
Prob
Prob
Param3
Param1
Prob
Loads
Input Parameters
Output
Reliability
Failure Threshold
Probability
Laboratory Testing
Model Calibration
Experimental Data
Spacesuit Design
In this work: calibration performed using Bayesian inference and Markov Chain Monte Carlo sampling [2]
[2] Kennedy & O’Hagan. Bayesian calibration of computer models. 2001.

## Slide 7: UQ Workflow for Assessing Design Reliability
Output
Inputs
Load parameters
Strength parameters
Computational Model
Max. Stress
Damage Index
...
Param1
Prob
Param2
Prob
Prob
Param3
Structures & Materials
Param2
Prob
Prob
Param3
Param1
Prob
Loads
Output
Reliability
Failure Threshold
Probability
  Uncertainty propagation produces probabilistic predictions of quantities of interest (QoIs) and determines system reliability given quantified model input uncertainties
Uncertainty Propagation
Input Parameters
Spacesuit Design
In this work: reliability estimated using multifidelity importance sampling [3]
[3] Peherstorfer et al. Multifidelity importance sampling. 2015.

## Slide 8: Multifidelity UQ Methods
Inputs
Physics Simulation
Outputs
Machine Learning
Data
Inputs
Outputs
Surrogate Modeling
Multifidelity Methods
Machine Learning
Data
Inputs
Physics Simulation
Outputs
Replace expensive high-fidelity model with fast low-fidelity model for more efficient (but biased) UQ
Combine high-fidelity and low-fidelity model predictions for accurate & efficient UQ
Multifidelity methods vs. other advanced UQ methods
Relatively straightforward extension of a commonly used approach (surrogate modeling)
Generally perform well for high dimensional problems
Lend themselves to a hierarchical UQ analysis:
  Surrogate model based-analysis
  Multifidelity analysis
  High-fidelity analysis
Increasing rigor & analysis time

## Slide 9: Multifidelity Importance Sampling (MFIS)
Output
Failure Threshold
Probability
Monte Carlo (MC) simulation can require a huge number of samples to estimate reliability since the probability of failure is generally a rare event
  Rule of thumb: 10 failed samples for accurate estimate (e.g., 10M total for prob. of failure = 10-6)
Importance sampling (IS) leverages an alternate (“biasing”) input distribution designed to produce more failures; then reweights the samples to maintain unbiased estimator
  But it can be challenging to construct an effective biasing distribution, especially in high dimensions
Multifidelity IS (MFIS) constructs a bias distribution using a surrogate model for efficiency then estimates reliability using the high-fidelity model for unbiasedness
  As long as the surrogate model is accurate at/near the failure region, significant performance gains are possible versus MC
Strength
Probability
Load
Probability
Computational Model
Reliability
Biasing distribution

## Slide 10: Case Study: Z2 Spacesuit Reliability
Given: existing test data & models for the Z2 spacesuit:
LVI Test Data
Dyna Coupon Model
Dyna Assembly model
Goal: estimate the probability of no impact failure (PnIF) in the Z2 suit due to impact
  Sensitivity analysis to identify the most/least important material model parameters
  Model calibration to quantify uncertainty in the material model parameters
  Uncertainty propagation to predict PnIF
Assumptions/simplifications:
  Impact load uncertainty is the result of specified variability in impact velocity only
  Failure criteria based on max contact force in lieu of a TBD leak rate formula for xEMU
  Parameter uncertainty only considered for one of two composite laminate materials; other parameters fixed at nominal values
Notes: *coupon model – 2 hours on 4 CPU cores
*assembly model - 16 hours on 10 CPU cores

## Slide 11: Step 0: Computational Efficiency
Useful models are often expensive
  Coupon model: 2 hr on 4 CPU cores; Assembly model: 16 hr on 10 CPU cores
  Training a surrogate model still requires a lot of computational resources
Developed SimTools for easy, parallel execution of finite element simulations
  Interfaces with common FEA codes (Abaqus, LS-Dyna, Marc)
  Automated job submission/monitoring using NASA’s Portable Batch System (PBS)
Example: Needed full suit simulations for 200 different inputs; Ran 15 simulations at a time on 10 processors each
  Performed 1+ years of serial computation time in around 1 week of wall time, minimal user effort
x | y | x | k | d | e | 3
1 | 2 | 3 | 5 | 2 | 5 | 3
3 | 3 | 3 | 2 | 2 | 2 | 3
3 | 2 | 2 | 2 | 2 | 2 | 2
0 | 9 | 8 | 6 | 5 | 4 | 3
AM1 | … | VEL
12.4 | … | 1.0
14.3 | … | 1.4
… | … | …
13.1 | … | 1.1
Param1
Prob
Prob
Param3
Impact Velocity
Prob
Input Distributions or bounds
Inputs
…
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
Inputs and Outputs
Parallel execution of models
Notes: Point out

## Slide 12: Step 1: Sensitivity Analysis
Assembly Model
Output
Inputs
Impact Load
Material Model
Max. Force
Leak Rate
...
Param1
Prob
Param2
Prob
Prob
Param3
Material Parameters
Param2
Prob
Prob
Param3
Param1
Prob
Load Parameters
Output
Reliability/PnIF
Failure Threshold
Probability
Z2
Design
Param A
Prob
Param E
Prob
Param C
Prob
Param D
Prob
Param F
Prob
Param B
Prob
Input Parameters
  Goal: Identify most/least important material model parameters to identify a subset that can be fixed at nominal values for the remaining UQ process
Loads Analysis
Suit fall probability
Suit impact mapping
Impact analysis
Notes: Point out

## Slide 13: Sensitivity Analysis
Global Sensitivity Analysis was used to rank the material parameters based on how much effect each has on the predicted force vs time using the FEM coupon model
Selected Parameters
1. MAT162 User Manual Version 17A-2017.
Material Model Parameters1
AM1-AM4: Strain softening coefficients for different damage modes
ELIMIT: Element eroding axial strain
Note: Additional parameters OMGMX & EEXPN fixed at nominal values provided by SMEs

## Slide 14: Step 2: Material Parameter Calibration
Assembly Model
Output
Inputs
Impact Load
Material Model
Max. Force
Leak Rate
...
Param1
Prob
Param2
Prob
Prob
Param3
Material Parameters
Param2
Prob
Prob
Param3
Param1
Prob
Load Parameters
Input Parameters
Output
Reliability/PnIF
Failure Threshold
Probability
Impact Test Data
Model Calibration
Coupon Model
Loads Analysis
Suit fall probability
Suit impact mapping
Impact analysis
Z2
Design
  Goal: Estimate uncertainty in material parameters based on given impact test data using Bayesian inference and Markov chain MC sampling
Notes: Point out

## Slide 15: Material Calibration Results
Coupon Surrogate Model
3 Random Samples
Different material parameter values result in comparable agreement with experimental data; probabilistic model calibration considers a range of plausible values
Calibrated Material Uncertainty
Notes: “assumed” is a best guess without data; adding on estimated error with Gaussian

## Slide 16: Material Calibration Results
Coupon Surrogate Model
Credible intervals contain 95% of simulations
Prediction intervals contain a future data point with 95% probability
Propagating material uncertainty with MC simulation
Calibrated Material Uncertainty
Notes: “assumed” is a best guess without data; adding on estimated error with Gaussian

## Slide 17: Step 3: Uncertainty Propagation
Output
Inputs
Impact Load
Material Model
Max. Force
Leak Rate
...
Param1
Prob
Param2
Prob
Prob
Param3
Material Parameters
Param2
Prob
Prob
Param3
Param1
Prob
Load Parameters
Input Parameters
Output
Reliability/PnIF
Failure Threshold
Probability
Impact Test Data
Model Calibration
Coupon Model
Loads Analysis
Suit fall probability
Suit impact mapping
Impact analysis
Z2 Design
Uncertainty Propagation
  Goal: Estimate the probability of no impact failure in the Z2 spacesuit under materials/load uncertainties using MFIS
Assembly Model
Notes: Point out

## Slide 18: Uncertainty Propagation Results
Input Distributions
Material Parameters
Estimating Z2 reliability using high-fidelity MC simulation
Load Parameters
Z2 Suit Model
Nominal
Nominal
Nominal
Nominal
 | High-fidelity MC
Reliability (PnIF) | 0.9932
# FEM evals | 2500
 | High-fidelity MC | Multifidelity IS | Low-fidelity MC
Reliability (PnIF) | 0.9915 | 0.9930 | 0.9852
# FEM evals | 2500 | 450 | 200
Failure Threshold
Output Distribution
Reliability Estimate

## Slide 19: Uncertainty Propagation Results
Input Distributions
Material Parameters
Failure Threshold
Load Parameters
Z2 Suit Model
Failure Threshold
Nominal
Nominal
Nominal
Nominal
Estimating Z2 reliability using MFIS
Output Distribution
 | High-fidelity MC | MFIS | Low-fidelity MC
Reliability (PnIF) | 0.9932 | 0.9930 | 0.9852
# FEM evals | 2500 | 450 | 200
Reliability Estimates
Biasing failure rate: 6.4%; MC failure rate: 0.68%

## Slide 20: Summary
Demonstrated UQ workflow for assessing reliability of Z-2 spacesuit:
  1) Sensitivity analysis, 2) model calibration, 3) uncertainty propagation
  Overcame computational burden using high performance computing (with the help of SimTools), surrogate modeling, and multifidelity methods
  Showed that ignoring materials/loads uncertainties can overestimate reliability
MFIS was demonstrated to be an efficient alternative to MC simulation for estimating reliability
  A biasing distribution constructed using a surrogate model resulted in a 9.5X higher failure rate
  Motivated research on surrogate models designed for superior accuracy near failure region (focus of next presentation)

## Slide 21: Future Work – xEMU Certification
The capabilities developed and lesson learned under the presented case study are currently being applied under the xEMU certification effort
E.g., soil model calibration for simulating impact on lunar regolith
Sensitivity Analysis
Model Calibration
LS-Dyna Penetrometer Model
Calibrated Soil Model
Penetrometer Measurement Data
Apollo mission lunar data
Most Influential Soil Model Parameters
Calibrated soil model vs data

## Slide 22: Questions
References:
  [1] Plischke et al. Global sensitivity measures from given data. 2013.
  [2] Kennedy & O’Hagan. Bayesian calibration of computer models. 2001.
  [3] Peherstorfer et al. Multifidelity importance sampling. 2015.
  [4] Warner et al. Assessing next-gen spacesuit reliability: A probabilistic analysis case study. In review.
Email: james.e.warner@nasa.gov