## Slide 1: In-Situ Resource Utilization For “OSAM” Logistics and Space Development
Dennis M. Bushnell [NAE]
Chief Scientist
NASA Langley Research Center

## Slide 2: Space Assembly – Instruments, Spacecraft, Equipage, Etc., i.e. ISS Space Service – Refueling, Batteries, Sensors, Repairs, Enhancement, Etc. Space Manufacturing – of “everything”, increasingly via printing

## Slide 3: Major Benefits
Reuse, repurposing of space debris
ISRU, Earth Independence, “living off the land”….
Increased instrument capability, aperture
Greater capabilities than could be shrouded for launch [i.e. telescopes, artificial gravity systems]
Major Cost Savings, especially with respect to ISRU and life extension/ capability improvements

## Slide 4: Applicable Technologies
AI/ Robotics/Autonomy
Nuclear batteries, up to 22 KWs/Kg of isotope, 1% the weight of a nuclear reactor, scalable from sensors to tens of MWs, Can power everything space – propulsion, habitats in space and on body, ISRU, manufacturing, on body transportation…….
Sensors, navigation, communications
Joining, magnetics, electrostatics
Printing manufacture
Tethers for fuel-less transport in Earth environs, cleaning up space debris, orbit raising
Structural engineering, trusses, etc.

## Slide 5: Resources in Space
Vacuum
Low temperatures
Solar energy
Solar and galactic radiation
Micro gravity
Minerals, volatiles, oxides, etc., on planets, moons, asteroids, meteorites, dust
Magnetic fields
Photons
Gravity fields
“Position,” the source of the economic value of the current commercial space Industry
Interstellar space, the rest of the galaxy and universe
Vast to unimaginable space

## Slide 6: Why Go There?
Exploration and science
Space solar power
Space mining
Space manufacturing
Colonization
Tourism
Asteroid defense, national defense
Unique biologics
Positional utilities

## Slide 7: Space Manufactured Products
Crystals
Semiconductors
Microencapsulation
Fibers, fiberoptics
Pharma
Human organs
Metal alloys
Equippage for space operations

## Slide 8: Humans-Mars, Visits-to-Colonization
Until recently, Humans-Mars was far more Expensive….
The Musk reusable rockets have and will reduce much the costs of space access
Nuclear batteries could power high thrust MHD, 6,000 secs of Isp, 200 day round trips, essentially solving the radiation/ GCR and micro g health issues
Need to reduce the tonnage of requisite equipage/ supplies from Earth
Mars has massive resources, Therefore ISRU, In Situ Resource Utilization, Earth Independence

## Slide 9
Benefits of ISRU
Is an absolute necessity for Colonization
Possibly enabling for serious “Commercial Space”, not just commercial execution of Government functionalities, and beyond orbital “Positional Earth Utilities”
Enables demonstration of reliability, functionality, systems performance years before the humans arrive at on planet conditions, greatly increases possibility of mission success and improves overall safety
Provides reusability, the huge cost benefits of robotic systems , cost reductions for future missions

## Slide 10
Potentially Supplied by ISRU
Habitats
Return Fuel, on planet fuel, entry, descent and landing fuel
Life support [ water, O2, atmospheric N2, Food, thermalization, pressurization, dust protection]
Radiation Protection
Devices from regolith mineral volatile extraction and synthetic biology via printing and bio-fabrication
Equipage [from printed plastics derived from H20 and CO2]

## Slide 11
Water
Very little water in the atmosphere, but estimates indicate much of the water that was ever on Mars is still there…..
Massive amount of water ice at north pole region, many Km thick, enough to put an ocean on a flat mars 350 meters deep, Melt
Major quantities of Water ice and water adsorbed on minerals in the regolith, from some 3% at the equator [ up to 8+% localized] to some 40% plus at 60 degrees North etc., Can microwave/ heat to produce water vapor, capture and store as ice in “container”
A solar “tent” could produce sufficient heat to vaporize the regolith water ice
Also available from Sulfates [ 22% H2O], Silicates etc. ,bound up chemically
Large crater near equator purportedly has an “Ice Lake” the size of Lake Huron with similar or greater depth under some regolith

## Slide 12
Oxygen
Some in the atmosphere
Much available from water
Much available from the highly oxidized regolith, some suggest that if add water to regolith produces Oxygen
Much chemically bound in various oxides
Much available from atmospheric CO2 [ CO2 From cooling or compression]

## Slide 13
Minerals/ Materials Available From the Regolith/ Atmosphere
Nickel
Titanium
Iron
Sulfur
Magnesium
Calcium
Phosphorus
Chlorine
Bromine
Aluminum
Silicon
Oxygen
Hydrogen
Carbon
Nitrogen
Sodium
Manganese
Potassium
Chromium
Deuterium

## Slide 14
[Sample] Uses for Martian CO2
Nuclear shielding
Metal fuel cells
O2 production
C for carbon nanotubes, other materials/ organics
Pressurized rockets
CH4 fuel production
In-atmosphere solar pumped CO2 laser
Polyethylene production

## Slide 15
ISRU Via Synthetic Biology
Lynn Rothschild et al [Ames Research Center]
Metals extraction from regolith via biological processes
Printing fabrication via Enzymes
Biological precipitation
Nitrogen fixing Cyanobacteria
Microbial cellulose for wide variety of products
Bio Plastics
Biocomposites
Food

## Slide 16
Food
Via Extremophiles, Genomics and Synthetic Biology – Plants for Planets. Will need to reduce CO2 partial pressure – grow in a protected atmospheric environment using sunlight or morph to take the CO2
Reprocess solids, grow mushrooms for protein, insects [ excellent source of essential fats], Cyanobacteria/ Spirulina [ CO2 + Sunlight], printed food

## Slide 17
ISRU “Benefits”
Much improved Reliability across the board including redundancies, checkout at on planet/ body conditions
ISRU produced equipage [ from devices working over long times sent via inexpensive “Slow Boats”]
Reduces up-mass in Low Earth Orbit and costs much for the Human Campaign
From NRC review of Space Tech Roadmaps “Use of Martian derived Propellants could reduce launch masses by over 60%” … “A Game Changer for Exploration”

## Slide 18
From DRA-5 “Notable Advantages of ISRU”
O2 production for ascent and consumables
Reduced initial mass in low earth orbit and reduced number of Launches
Reduced lander size and volume
Greater surface exploration capability
Life support redundancy
Lower risk via fewer launches
Lower life cycle cost

## Slide 19
Mars/ Humans ISRU Bottom Line[s]
Mars , in terms of resources, is a VERY Rich planet, especially wrt water and Carbon – the essentials, plus much else.
[ Pregame] ISRU is doable, affordable and would greatly reduce Humans-Mars mission costs & MLEO and greatly improve safety
Serious ISRU changes much the mission architecture
The technologies required are either here or available soon enough to execute in a timely fashion

## Slide 20
BTW
The ISRU arrivals, daily construction activities/ progress will be a 24/7/365 [ 5 senses going forward] Virtual Reality experience for everyone……..We can send a robotic reporter to chronicle all this.

## Slide 21
DRA-5 Conclusions
“Need to Dramatically decrease the total mass that must be launched into LEO and transported to the Martian Surface”
“Reducing launched mass is an overarching need for long term self sufficiency and acceptable operations cost”
“….Critical to decreased mass are surface nuclear power, ISRU and radiation shielding”. The latter available via ditch and bury under some 4 meters of regolith an expandable habitat

## Slide 22: Orbital Debris Cleanup
Are within a very few collisions from closing out LEO
Folks are lofting tens of thousands of new LEO satellites, having increasing trouble finding launch windows through the current debris, debris cleanup needs to be added to detect and avoid
Cleanup Issues include ownership of debris and cost, including fuel
An affordable way forward is to utilize powered tethers to fuel-lessly do the cleanup AND put in a space junk yard, repurpose/ remanufacture, including ISS eventually
Power tether from either a nuclear battery or solar PV

## Slide 23: Autonomy
The costs of humans in space are orders of magnitude greater than robotics
OSAM space operations require trusted autonomy
Trusted autonomy must operate successfully in the presence of unknown unknowns, which requires an AI that conducts issue evaluation, ideation of solution spaces, and triage/ execution
There are now three successful approaches to machine ideation. They largely mimic the operation of the human subconscious, evaluation of huge numbers of quasi-random combinatorials.

## Slide 24
Why Autonomous Systems?
Autonomous systems could, now or going forward [ compared to Human operation]:
- Know far more
- Be less Expensive
- Exclude operational human error
- Have far less latency, provide new functionalities
- Have far longer duty cycle, provide size reduction[s]
- Be faster, more efficient,
- Be more durable, and “patient”
In general, operate at far less cost and for conditions and performing functions where and in a manner that humans could not

## Slide 25: Some Observations/Projections
We have been executing in space assembly since the 1960s, in space servicing more recently and starting into in space manufacturing now that the costs of space access are decreasing
There are massive resources on Mars, much less on the moon, and then there are asteroids. ISRU is essential for colonization.
Studies indicate that, thus far, space ISRU/ space resources are critical for in space, on other bodies but the cost comparison between utilization near earth vs earth sourced is not favorable
Space servicing is successful, aided by initial design that accommodates such, the outlook is servicing becoming the usual way of doing things
Space manufacturing enabled by less expensive space access should develop well.

## Slide 26: What is Needed For Spacefaring
Solutions to space debris
Solutions to human space-related health issues
Inexpensive space access, in progress
Reliability and safety improvements
Detailed mapping of space resources
Solar and nuclear power
Solutions to legalities with respect to ownership and space debris
Trusted autonomy
Closed business cases