## Slide 1: NASA-STD-6030 Qualified Material Process Requirements for Joint Non-Metallic SDO Forum Sam Cordner April 27, 2021

## Slide 2: Quick Look
NASA 6030 Principals (6030 to be published soon)
Applicability (Human Spaceflight and critically levels)
Qualified Material Process (the basics)
There is much, much more to NASA 6030, but this is a quick look at only one of the principals.

## Slide 3: AM Certification: Governing Principles
Understanding and Appreciation of the AM process
Integration across disciplines and throughout the process
Discipline to define and follow the plan
Have a plan
Integrate a Quality Management System (QMS)
Build a foundation
  Equipment and Facility
  Training
  Process and machine qualification
  Material Properties / SPC
Plan each Part
Design, classification, Pre-production articles
  Qualify and lock the part production process
Produce to the plan – Stick to the plan

## Slide 4: NASA approvals required
NASA-STD-6030 requires the following deliverables:
  Additive Manufacturing Control Plan (AMCP)
  MUA to approve the Material Property Suite (MPS)
    Class A and B parts only
  Part Production Plan (PPP)

## Slide 5: Applicability
Adaptive technologies—where process parameters change based on active feedback during the manufacturing process—are not allowed without a tailored, point-design methodology.
  e.g. Electron beam powder bed fusion (E-PBF)

## Slide 6: Classification

## Slide 7: Summary of Methodology

## Slide 8: General Requirements
Additive Manufacturing Control Plan (AMCP)
  Critical to define implementation policies for program or project
  Describes implementation of all requirements
    Includes tailoring of requirements
  Becomes governing document in place of standards
Quality Management System (QMS)
  Critical to maintain consistent implementation policy
  Ensures you stick to your plan and tailoring
  Ensures consistent training, processes and procedures
Sub-QMP-A, B or C
Sub-QMP-A, B or C
Sub-QMP-A, B or C
AMCP
Foundational Process Controls
QMS
MPS
Data
SPC Criteria
PCRD
Data
Design
Properties
General Requirements
PPP
Design Process
ECP
Qualification Maintenance Calibration
Training Plan
Training
Definition of
Material Process
Machine 2
Machine 3
Machine “n”
Qual. of Material Process
Feedstock
Specification
AM Process
Post-AM Process
QMP-A, B or C
Machine 1
Registration
(A or B)
NASA-STD-6033

## Slide 9: Building a Foundation
Planning for AM certification does NOT start with a part
AM Control Plan should define how the foundation for certification is structured and how it operates
  Equipment and Facility Controls
  Personnel Training
  Process/Machine Qualification
  Material Properties
  Statistical Process Controls

## Slide 10: Qualified Material Process (QMP)
Begins as a Candidate QMP
Defines aspects of the basic, part agnostic, fixed AM process:
  Feedstock
  Fusion Process
  Thermal Process
Enabling Concept
  Machine qualification and re-qualification, monitored by…
  Process control metrics, SPC, all feeding into…
  Design values
Sub-QMP-A, B or C
Sub-QMP-A, B or C
Sub-QMP-A, B or C
Foundational Process Controls
MPS
Data
SPC Criteria
PCRD
Data
Design
Properties
PPP
Design Process
ECP
Qualification Maintenance Calibration
Training Plan
Training
Definition of
Material Process
Machine 2
Machine 3
Machine “n”
Qual. of Material Process
Feedstock
Specification
AM Process
Post-AM Process
QMP-A, B or C
Machine 1
Registration
(A or B)
NASA-STD-6033

## Slide 12: The QMP becomes the Foundation!

## Slide 13: Conclusions
NASA 6030 is for all additive manufacturing. There are some specifics to applicability.
Process control is what defines a good process. This control comes from several places including an AMCP, QMS, and QMP.
A test matrix to evaluate QMP has been presented.
Control what you do::Evaluate what you get

## Slide 14: Additional for the M&P Group