## Slide 1: A Unified Approach for Computational Aeroelasticity
Dr. Walter A. Silva
Aeroelasticity Branch
NASA Langley Research Center
24 June – 15 July, 2021
AIAA Online Short Course

## Slide 2: Acknowledgements
Excerpts from AIAA Short Course on Aeroelasticity
Prof. Cesnik
Prof. Strganac

## Slide 3: Outline
Mathematical Preliminaries
Unsteady Aerodynamics
Structural Analysis
Aeroelasticity (AE)
Aeroservoelasticity (ASE)
Reduced-Order Models
Case Studies
Discussion

## Slide 4: A-6F Wind-Tunnel Model Flutter (YouTube)
https://www.airspacemag.com/videos/a-6-wing-flutter-tests_1/

## Slide 5: KTH Wind-Tunnel Model Flutter
No hyperlink; separate video

## Slide 6: Mathematical Preliminaries

## Slide 7
Classification of Systems

## Slide 8: Excerpts from References
Autonomous Second-Order Nonlinear Systems:
“…we shall restrict our attention to second-order autonomous
systems…where time does not enter explicitly into the
equation of motion. This, of course, precludes time-
dependent forcing functions.”
Unit-Step and Unit-Impulse Functions:
“Whereas the unit-step function is well defined, the unit-
impulse function, mathematically speaking, is not.”
What do these statements mean? Do we understand how
these concepts apply to real-world systems?

## Slide 9
Mathematical Foundations System Classifications
Zero
Memory
Memory
Time Invariant
Time Varying
Linear
Nonlinear
Linear
Nonlinear
y=x
Saturation,
Deadband
Van der Pol,
Duffing and
N-S Eqs
Mathieu
y = m(t)x
x = A(t)x +
B(t)u
Saturation,
Deadband
as f(t)
•
2
y = mx
Notes: 12/18/98
57

## Slide 10: Linear vs. Nonlinear
Superposition (Valid for Linear Systems)
If S(a1x1 + a2x2+…) = S(a1x1) + S(a2x2) + … => Linear
x(t)
y(t)
xn(t)
x1(t)
an
a1
xn(t)
x1(t)
…
…
an
y(t)
a1
Linear System
Linear System
Linear System
Equivalent

## Slide 11: Linear vs. Nonlinear
Superposition fails for Nonlinear Systems
y(t) = x2(t)
Input: x(t) = cos(w0t)
Output: y(t) = 1/2 + 1/2 cos(2w0t)
Bias New frequency!!
(ax1 + bx2)2 = a2x12 + 2abx1x2 + b2x22
≠ (ax1)2 + (bx2)2
Check:

## Slide 12: Linear vs. Nonlinear
Linear systems cannot create new frequencies
that are not present in the input!
Linear
System
u(t)
y(t)
If
u(t) = A1*sin((2π f1)*t + ø1)
Then
y(t) = A2*sin((2π f1)*t + ø2)
Amplitudes and phases could be different but not frequency

## Slide 13: Linear vs. Nonlinear
Nonlinear systems can create new frequencies
that are not present in the input!
Nonlinear
System
u(t)
y(t)
If
u(t) = A1*sin((2π f1)*t + ø1)
Then
y(t) = A2*sin((2π f1)*t + ø2) + A3*sin((2π f2)*t + ø3) + …
Yields harmonics (integer multiple of f1) and subharmonics
(fractional multiple of f1)

## Slide 14
Confusion exists in literature
Time-invariant DOES NOT mean steady response
Time-invariant system (shift invariant)
Time-varying system
Linear and nonlinear systems can be EITHER time-
invariant or time-varying
Time-Invariant vs. Time-Varying
Notes: 12/18/98
58

## Slide 15
Time Invariant --> y(u(t1)) = y(u(t2)) (Shift Invariant)
Time Varying --> y(u(t1)) ≠ y(u(t2))
y
t
y
t
t1
t2
t1
y
t2
y
Time-Invariant vs. Time-Varying
t
t
Notes: 12/18/98
59

## Slide 16
Time-Invariant
  Mass-Spring System (water bucket on spring)
  Airplane (Why? How?)
  Pendulum
  Others?
Time-Varying
  Rocket (Why?)
  “Leaky” Mass-Spring System (leaking bucket)
  Others?
Time-Invariant vs. Time-Varying
Examples
Notes: 12/18/98
59

## Slide 17
Stationary
  Statistical properties do not change with time
Nonstationary
  Statistical properties DO change with time
Stationary vs. Nonstationary
Notes: 12/18/98
59

## Slide 18: Memory vs. Memoryless
Memory
  Future outputs influenced by past inputs and
  outputs
  Derivative and/or integral terms
Memoryless
  Present output independent of past history
y = 2x
x
y
x
y
2
4
6
6
2
4

## Slide 19: Memory vs. Memoryless Examples
Memory
  Mass-Spring System (Why?)
  Pendulum
  Any Ordinary Differential Equation
  Any Integral Equation
Memoryless
  Saturation function

## Slide 20: Deterministic vs. Stochastic
Deterministic
  Given input always yields the same output
  Repeatable
  Examples?
Stochastic
  Given input yields family of potential outputs
  Based on Probability Distribution Function
  Examples?

## Slide 21: Classify These Systems
L/NL
TI/TV
M/ML
D/St
x = A(t)x + B(t)u
x = Ax + Nxu + Bu
•
•
x + (x2 - 1)x + x = 0
••
•
saturation
Mx + Cx + Kx = F(t)
••
•
Mx + Cx + K1x + K2x3 = F(t)
••
•
Navier-Stokes eqs
Class Example

## Slide 22
Convolution

## Slide 23: Linear Time-Invariant (LTI) Continuous-Time
Impulse Response, h(t)
CT-LTI
Fundamental mathematical function
Application to discrete-time systems not
consistent amongst references and texts
h(t)
t

## Slide 24: Linear Time-Invariant (LTI) Continuous-Time
So what is convolution? Why use it?
Arbitrary motion
LTI
u(t)
y(t)
Convolution -->

## Slide 25
Convolution
t
u(t)
t
t
u(t
0
) • h(t)
•
•
•
u(t
1
) • h(t)
y
(t
)
+
Linear Time-Invariant (LTI)
Continuous-Time

## Slide 26
Convolution
How is it presented in texts?
If convoluting f and g (f*g), the flip one of the functions, say f, multiply with each other and “slide”
Why? What does this mean?
What are your memories of convolution?
Linear Time-Invariant (LTI)
Continuous-Time

## Slide 27: Linear Time-Invariant (LTI) Continuous-Time
Step Response, S(t)
CT-LTI
Fundamental mathematical function
Often easier to apply to physical systems than
impulse (Dirac)
S(t)
t
0

## Slide 28: Linear Time-Invariant (LTI) Continuous-Time
Impulse Response = Derivative(Step Response)
Convolution using Step Response (S(t))

## Slide 29: Linear Time-Invariant (LTI) Discrete-Time
Digital Signal Processing (DSP)
Continuous-time signalscontinuous time (CT), variable
Discrete-time signalsboth time and amplitude discrete
Why DSP?
Easier implementation (computer)
Better control (no CT devices susceptible to heat, etc)
Digital signals sometimes result of sampling of CT signals;
sometimes just part of a digital process

## Slide 30: Linear Time-Invariant (LTI) Discrete-Time
Sequence of Numbers
x = {x[n]}, n is integer
x[n] = xa(nT), -∞ < n < ∞
Where xa is CT signal, T is sampling period,
(1/T) is sampling frequency
Signal ONLY defined at sample points; not defined
in between.

## Slide 31: Linear Time-Invariant (LTI) Discrete-Time
x[0]
x[1]

## Slide 32: Linear Time-Invariant (LTI) Discrete-Time
Important and Fundamental Sequences
Unit Sample Sequence
Discrete-time (DT) impulse
1
…
0
DT impulse does not suffer from mathematical abstractions found in Dirac delta function (CT)!!

## Slide 33: Linear Time-Invariant (LTI) Discrete-Time
Important and Fundamental Sequences
Unit Step Sequence
Discrete-time (DT) step
1
…
0 1 2 3

## Slide 34: Linear Time-Invariant (LTI) Discrete-Time
Important and Fundamental Sequences
NOTE: or
With x[n-1] advancing forward, x[n+1] going backward,

## Slide 35: Linear Time-Invariant (LTI) Discrete-Time
Important and Fundamental Sequences
Also, u[n]
…
0 1 2 3
u[n-1]
…
0 1 2 3 4

## Slide 36: Linear Time-Invariant (LTI) Discrete-Time
Important Concept
Any sequence can be represented as a sum of
scaled and shifted unit sample responses.
For example,

## Slide 37: Linear Time-Invariant (LTI) Discrete-Time

## Slide 38: Linear Time-Invariant (LTI) Discrete-Time
So, what is the response of a system to this input, p[n]?
Is system linear? If so, we can treat each term as if it is a separate input.
Is system TI? If so, the response due to each unit sample input is the same only shifted (before the scaling).
So, what is the response of a system to the first term?

## Slide 39: Linear Time-Invariant (LTI) Discrete-Time
DT-LTI
Unit sample input
Unit Sample
Response
for all time
DISCRETE-TIME
CONVOLUTION

## Slide 40: Linear Time-Invariant (LTI) Discrete-Time
DT-LTI
DT-LTI
Linear
DT-LTI
Time Invariant

## Slide 41: Linear Time-Invariant (LTI) Discrete-Time
So response to input p[n]
is
This is convolution!

## Slide 42: Linear Time-Invariant (LTI) Discrete Convolution
DT-LTI
h(k)*2
u(t)
1
2
y(t) = ?
1
2
h(k)*1
+
+
…
Total sum = y(t)

## Slide 43: Linear Time-Invariant (LTI) Discrete Convolution (2nd method)
DT-LTI
u(t)
1
2
y(t) = ?
1
2
y(1) = U(1)*h(1)
Shift U(t) to right,
y(2) = U(1)*h(2)+
U(2)*h(1)
Shift U(t) to right,
…
U(t)

## Slide 44: Linear Time-Invariant (LTI) Step Response in Discrete-Time
Discrete-time differentiation = Difference
0
…
-
0
…
0

## Slide 45: Excerpts from References
Autonomous Second-Order Nonlinear Systems:
“…we shall restrict our attention to second-order autonomous systems…where time does not enter explicitly into the
equation of motion. This, of course, precludes time-dependent
forcing functions.”
Unit-Step and Unit-Impulse Functions:
“Whereas the unit-step function is well defined, the unit-impulse function, mathematically speaking, is not.”
Now we understand what these concepts mean so we can begin
to understand how they apply to systems!

## Slide 47: Linear Time-Varying (LTV) Discrete and Continuous
What is the benefit of time-invariance for convolution?
How does this change for time-varying systems?
Is convolution possible for time-varying systems?

## Slide 48
Transforms

## Slide 49: Linear Time-Invariant (LTI) Continuous - Transforms
Y(w) = H(w) X(w)
Transform Operation
(Fourier,Laplace)
Convolution in time = Multiplication in frequency
Deconvolution in time = ?
Note: If H(w) exists --> h(t) must exist !!

## Slide 50: Laplace Transform
Named for great French mathematician Pierre Simon de
Laplace
• Like all transforms, converts one form of a signal
into a different form
• Transforms from time domain to s-domain (or s-plane) and
back

## Slide 51: Laplace Transform (cont’d)
S-plane is the complex plane, real numbers along the x-axis ( ) and imaginary numbers along the y-axis ( )
Can use the complex variable to define locations on s-plane
Laplace transform analyzes signals in terms of sinusoids and exponentials

## Slide 52: Laplace Transform (cont’d)
• Example
• zeros: -3 + j, -3 - j
poles : -4, -1 + j, -1 - j

## Slide 53: Laplace Transform (cont’d)
• Can plot the zeros and the poles in the s-plane
-1
-4
Real
Imaginary
STABLE
UNSTABLE
-1
1

## Slide 54: Laplace Transform (cont’d)
• The s-plane
Real
Imaginary
STABLE
UNSTABLE

## Slide 55: Fourier Transform
Fourier transform of x(t) will exist if x(t) has finite energy
Additionally, should follow Dirichlet conditions:
  x(t) has finite number of discontinuities
  x(t) has finite number of minima and maxima
  x(t) is absolutely integrable

## Slide 56: Fourier Transform
t
0
0
F. T.
What does this mean?
• White light  equal amounts of energy over spectrum
White
Spectrum

## Slide 57: Fourier Transform
t
0
0
F. T.
0
t
0
t
0
0

## Slide 58: Fourier Transform
Computation of Fourier transform takes a real signal in time and generates a complex number in frequency
The complex number can be visualized in two ways: as real and imaginary components vs. frequency or as magnitude and phase vs. frequency
Recall

## Slide 59: Continuous - Transforms
Y(w) = H(w) U(w)
Transform Operation
(Fourier,Laplace)
Convolution in time = Multiplication in frequency
Deconvolution in time = ?
H(w) = Frequency Response Function

## Slide 60: Continuous - Transforms
Y(w) = H(w) U(w)
u(t)
y(t)
h(t)
y=h*u
U(w)
H(w)
F.T.
F.T.
Inverse F.T.
Multiplication of two complex numbers

## Slide 61: Discrete-Time Fourier Transform

## Slide 62: Fourier Transform: Discrete-Time
Cooley and Tukey publish landmark paper, 1965
Dramatic efficiency in solving a discrete version of the
Fourier transform
Taking advantage of symmetry and periodicity
Known as the Fast Fourier Transform (FFT)
Has enabled the real-time computation of frequency analysis

## Slide 63: Fourier Transform: Discrete-Time
Standard Fourier transform involves many mathematical
operations per computation
Number of operations is a function of the square of the
size of the data, or N2
If N = 210 = 1024, then N2 = 220 = 1,048,576
The number of operations for the FFT is N(log2N)
For N = 210, N(log2N) = 10,240!!!
FFT algorithm implemented in hardware, software
One of the most important algorithms ever created

## Slide 64: Discrete Transform
y(i)
=
h
k
=
0
N

(
k
)
u
(
i

k
)
Y(z) = H(z) U(z)
Discrete-time equivalent of Laplace transform
Z-transform

## Slide 65: Z-Transform
Laplace transform is used for continuous-time systems (differential equations)
Laplace transform  s-domain, s-plane
Z-transform is used for discrete-time systems (difference equations)
Z-transform  z-plane
Goal for both methods is to identify the poles (roots) and zeros of the system

## Slide 66: Z-Transform
S-plane arranged in a rectangular coordinate system (real vs. imaginary)
For Laplace transform, the complex variable is defined as
Z-plane arranged in a polar (circular) format (will see why later)
For Z-transform, a complex variable in polar notation is defined as

## Slide 67: Discrete Transform S-Plane to Z-Plane
0.0
2
1
3
6
4
5
1
2
3
4
5
6
S-Plane
Z-Plane

## Slide 68: Discrete-Time Frequency Analysis

## Slide 69: Frequency Analysis
Continuous-time systems can have infinite frequency range
Sampling of a continuous-time system results in a discrete-
time system
Different sampling rates (sampling frequency, time step) will
result in different discrete-time systems from the same
continuous-time system
Important to understand discrete-time sampling concepts in
order to understand system dynamics

## Slide 70: Frequency Analysis Sampling
Time step (dt) is time (seconds) between samples
- for dt=0.01 secs, each sample occurs at 0.01 seconds
Sampling frequency is the inverse of time step fs = 1/dt
- for dt=0.01 secs, fs = 100 samples /sec
- samples/sec = Hertz
Selection of time step (or sampling frequency) must be
based on frequency content of system or signal of interest
Must understand sampling, aliasing, and Nyquist frequency

## Slide 71: Frequency Analysis Sampling
Extremely Important Equation
Given Nyquist condition, the highest frequency that a particular sampling frequency can resolve is
fs > 2f  f = fs/2 (Nyquist frequency)  fn = fs/2 = 1/(2*dt)
What is the frequency resolution of a given time step?
Df = 1/(N*dt) where N = length of signal (no. of time steps)
Frequency resolution improves as N increases
Frequency resolution improves as dt increases

## Slide 72: Influence Functions, Green’s Functions

## Slide 73: Linear Time-Invariant Systems Influence Functions, Green’s Functions
f1
f2
f3
What are the deflections x1, x2, and x3
where the forces are being applied?
Kx = F, K=stiffness matrix
If K is not known, excite one force at a
time to get each column of K matrix
4 2 3
2 1 2
3 2 4
1
0
0
=
4
2
3
And so on…
Influence coefficient matrix = Static “Impulse response”

## Slide 74: Linear Time-Invariant Systems Influence Functions, Green’s Functions
To solve an Ordinary Differential Equation (ODE)
Replace F(t) with a Dirac delta function,
What is the reason for this substitution?
What is the system? Input? Output?

## Slide 75: Linear Time-Invariant Systems Influence Functions, Green’s Functions
is G(t) = Impulse Response
So, what is the solution of original ODE?
For zero initial conditions,
Solution to this equation

## Slide 76: Linear Time-Invariant Systems Influence Functions, Green’s Functions
This concept is the basis for many methods commonly used in engineering:
  Aerodynamic Influence Coefficients (AICs)
  Structural Influence Coefficients (SICs)
  Kernel Function
These are all the same concept

## Slide 77: State-Space Modeling

## Slide 78: State-Space Models
An nth-order differential equation
can be converted to a system of n first-order
differential equations by assigning

## Slide 79: State-Space Models (cont’d)
Resulting in the following set of equations
This is known as state-space form

## Slide 80: State-Space Models (cont’d)
Here’s an example for a mass-spring system
define

## Slide 81: State-Space Models (cont’d)
Setting yT = [y1 y2], in matrix form,

## Slide 82: State-Space Models (cont’d)
If you have inputs to the system
and specific outputs
Outputs related to
the states of system
Outputs not related
to states of system
(direct feedthrough)

## Slide 83: State-Space Models (cont’d)
The traditional model is defined as
With system stability defined by performing
eigenvalue analysis of A matrix (stability matrix)
Modern control theories, optimization, simulation,
and even nonlinear system theories are based on
this model

## Slide 84: State-Space Models (cont’d)
The impulse response for this system
is defined as
A goal of system identification is to identify the
system quadruple (A,B,C,D) for a given system;
Can be achieved IF impulse response is known,
directly or indirectly.

## Slide 85: State-Space Models (cont’d)
Solution of this system of equations involves the state transition matrix,
defined as the solution of
which is

## Slide 86: State-Space Models (cont’d)
Solving the differential equation,
What is this?

## Slide 87: State-Space Models (cont’d) Discrete-Time
The discrete-time version is
with impulse (pulse) response as
Each value of the discrete-time pulse response
is known as a Markov parameter. The information
Contained by the Markov parameters is central
To the theory of system identification (state-space
Realization).

## Slide 88: System Identification

## Slide 89: System Identification
Basic premise of system identification is to define a mathematical model of a system when only the input and output (sometimes only output) are known
There are several theories available in the time domain and the frequency domain
Predominantly, the majority of the theories are for linear systems
Nonlinear system identification is a more challenging problem

## Slide 90: System Identification
?
Inputs
Outputs
Class Discussion
Given what we have learned thus far, how
would you proceed to identify this system?
What questions should be asked?
Define procedures to help answer questions

## Slide 91: System Identification
Types of Identification
Parametric
  the structure or format of the equation of a
  system is known but its parameters are unknown
Nonparametric
  there is no assumed mathematical structure for the system

## Slide 92: System Identification
Examples of Identification
Parametric
Nonparametric
Inputs
Outputs

## Slide 93: System Identification
Some Terminology
White-Box Model
Light-Gray-Box Model
Dark-Gray-Box Model Generic with parameters
Black-Box-Model Generic
Inputs
Outputs

## Slide 94: System Identification
Time Domain Methods
  Often based on impulse response
  Impulse response terms known as Markov parameters
  Include use of correlation methods
  Can generate ARMA (auto-regressive moving average) and state-space models
Inputs
Outputs
State-Space Model (A,B,C,D)

## Slide 95: System Identification
Frequency Domain Methods
  Often based on filter methods
  Fourier methods usually incorporated
  Can generate frequency response functions
Inputs
Outputs
Frequency Responses

## Slide 96: System Identification Input Excitations
Time Domain
Frequency Domain
Impulse (pulse)
Sinusoid
Random
White
noise
Colored
noise

## Slide 97: Discrete-Time Markov Parameters
The values of a discrete unit-pulse response of a state-space system are known as the Markov parameters
For SISO (Single-Input, Single-Output),
Essential for system ID/system realization
If Markov parameters known, can compute A, B, C, D matrices
For MIMO systems, Markov parameters are matrices; (i,j) entries
PULSE algorithm extracts Markov parameters from input/output data
“On Markov Parameters in System Identification”, NASA TM 104156

## Slide 98: State-Space Realization (Ho-Kalman)
Given Markov parameters, find system dimension and quadruple (A,B,C,D) up to transformation (not unique)
Possibly first state-space realization methods (Ho-Kalman)
Related to multiplication of Observability and Controllability matrices:
B. L. Ho, R. E. Kalman, “Effective Construction of Linear State Variable Models from Input/Output Functions”, Regelungstechnik, vol. 14, No. 12, pp. 545-8, 1966.

## Slide 99: State-Space Realization (Ho-Kalman)
Result is a Hankel matrix, constant skew diagonals (upside down
Toeplitz matrix)
Values on the skew diagonals are the Markov parameters of the
system minus zero term (D) and values greater than index
To use Ho-Kalman, first form Hankel matrix H; factor H into its ‘O’ and
‘C’ components; use ‘O’ and ‘C’ to find A, B, and C
Rank(H)=n, keep adding data until rank does not increase

## Slide 100: Nonlinear Systems

## Slide 101: Nonlinear Systems Brief History
1600s – 1700s Newton’s Physics, Calculus
1800s Planetary motion analysis, Chaos
Early 1900s Presence of nonlinearity in
engineering devices
Lorentz’ equations
1970s Turbulence and chaos
1980s Fractals

## Slide 102: Nonlinear Systems - Complexity
Real world is nonlinear, varying from single DOF
to multiple DOF to continuous
  1 DOF: Logistic equation (predator-prey)
  2 DOF: Pendulum, Limit Cycles
  n DOF: Structures, Electronics
  continuous: Earthquakes, Turbulent Fluids,
  Nonlinear Waves (shocks)
Linear systems are a very special, limited subgroup,
the result of a simplification (linearization) of a more
complex nonlinear system

## Slide 103: Linear vs. Nonlinear
A linear system either
  Moves toward its equilibrium point
  OR blows up
A nonlinear system exhibits
  Greater complexity (responds to various equilibrium points)
  Exact (closed-form) solutions rarely available

## Slide 104: Linear vs. Nonlinear
t
t
t
t
ICs
Linear
stable
Single
Equil.
Point
unstable
Nonlinear
Multiple
Equil.
Point
Goes to ∞ as t goes to ∞
“stable”
Finite escape time
Goes to ∞ in finite time

## Slide 105: Nonlinear Systems
In addition to
  Finite escape time
  Multiple equilibrium points (equilibria)
  Limit cycles (will discuss)
Can also have
  Subharmonic, or harmonic oscillations
  Chaos (randomness from a deterministic system)

## Slide 106: Nonlinear Systems (Time Domain)
Regardless of complexity, state-space form provides a
powerful, convenient, and consistent mathematical format for modeling and analyzing nonlinear systems:

## Slide 107: Nonlinear Systems (Time Domain)
Cast into state-space form,
Pendulum

## Slide 108: Nonlinear Systems (Time Domain)
Equilibrium points (Fixed points) are a distinctive property of
nonlinear systems
A nonlinear system usually has multiple equilibrium points; a
linear system has one and only one equilibrium point
Knowing the number and type of equilibrium points of a
nonlinear system provides insight into the complex
dynamics of the system
An equilibrium point is a point in the solution space of the
system where the system is at rest

## Slide 109: Nonlinear Systems (Time Domain)
To find equilibrium points, set derivatives to zero:
So equilibrium points are
But what are the different types
of equilibrium points?

## Slide 110: Nonlinear Systems (Time Domain) Equilibrium Points
View in Phase Plane
View in Time
Start with IC
Time

## Slide 111: Unsteady Aerodynamics

## Slide 112: Background
Objective : find aerodynamic loads (forces & moments) associated with motion
  vibratory motion of the structure -- flutter and vehicle response
  motion of the flow field -- turbulence and gust response
  rotary motion of the vehicle -- rotorcraft and cascade flows (turbomachines)
  aircraft maneuvers & active control
Difficulties
  flowfield nonlinearities
    viscous flow -- drag due to friction, flow separation, & stall
    compressibility -- shock formation & oscillating shocks
  3 - dimensional flows -- aspect ratio, wing sweep, wing / body interference
  stores, nacelles, and other appendages

## Slide 113
Early (Classical) Developments
- 2D, flat plate, incompressible flow (linear equations)
- Quasisteady approximation
- Wagner’s function (step response in angle of attack)
- Kussner’s function (response to sharp-edged gust)
- Theodorsen’s function (sinusoidal airfoil response)
- Sear’s function (sinusoidal gust response)
- Analytically derived (no computers!)
Complex Geometries and Compressible Flow
- Analytical derivation of classical responses difficult
- Requires more complex aerodynamic equations
- Need computers to solve complex equations for complex
geometries
Background
Notes: 12/18/98
54

## Slide 114: Background
Assumptions for linear methods
  boundary layer ignored, attached flow assumed (inviscid)
  irrotational & isentropic (permits potential formulations) -- no shocks
  sinusoidal (harmonic) motion of structure and flow -- 1st-order effects
  superposition (linear) -- camber + thickness + oscillating flat plate
Nonlinear methods
  Assumptions vary depending on equation level
  Equation hierarchy defines complexity and related assumptions

## Slide 115: Quasisteady aerodynamics
AOA consists of Vy , Va , and ao contributions
An upwash, Vy , increases the AOA
Angular velocity about the elastic axis
leads to an AOA that varies along the wing.
Upwash, Va , at the 3/4 c is used.
Thus
Instantaneous response at condition; no history

## Slide 116: Model Comparison (Lift) & Reduced Frequency Influence
k = 0 . 1
k = 1 . 0

## Slide 117: Classic Aerodynamic Functions
 | Airfoil Motion | Gust
Step | Wagner’s Function (angle of attack or impulsive velocity) | Kussner’s Function (sharp-edged gust)
Sinusoidal | Theodorsen’s Function | Sear’s Function

## Slide 118: Wagner’s Function
Time-domain response in lift due to a step change in angle of attack. Defines the lag between the motion of the airfoil and the associated aerodynamic response (lift).
The quasi-steady approach assumes no lag -- immediate response
Wagner’s
Quasisteady
Semichords Traveled

## Slide 119: Wagner’s Function
= 1
I0, I1: modified Bessel functions of the first kind
K0, K1: modified Bessel functions of the second kind
and
Lift:
where b = semichord, r = density, U = freestream velocity, w = downwash (motion)
And is a nondimensional quantity proportional to time known as the distance travelled in semichords

## Slide 120: Wagner’s Function
What is this?

## Slide 121: Reduced Frequency
Fundamental parameter in unsteady aerodynamics
Frequency parameter
Number of oscillations undergone by airfoil during time airflow travels across the chord of the airfoil
Typically use reduced frequency
Similarity of propagation

## Slide 122: Theodorsen’s Method
Quasisteady flow (as previously derived) :
Unsteady Potential Flow (Theodorsen’s Theory ~ 1930s)
which introduces “noncirculatory” contributions
Theodorsen’s Function is C(k) = F(k) + iG(k) where k is the reduced frequency, k = bw / V

## Slide 123
Theodorsen’s Function
NACA Report 629

## Slide 124: Aerodynamic Modeling
Actual flows are:
  three dimensional
  viscous
  compressible
  nonlinear
For most applications, a significant simplification on the flow representation can be reached.

## Slide 125: Aerodynamic Modeling
Viscous, Inviscid Flows
  Viscous flow: mass diffusion, viscosity (friction), and thermal conduction phenomena are present.
  Inviscid flow:
  Examples of viscous flows: high angle of attack; blunt bodies
Flow outside boundary layer is inviscid
Thin boundary layer—viscous flow

## Slide 126: Aerodynamic Modeling
Compressible, Incompressible Flows
  Incompressible: density is constant (low speed flows)
  Mach number is a good indicator of compressibility
    M < 0.3 incompressible (approximate)
    M > 0.3 compressible (approximate)

## Slide 127: Aerodynamic Modeling
Mach Number Regimes
  By definition, the flow is locally:
    Subsonic, if M < 1
    Sonic, if M = 1
    Supersonic, if M > 1
  Four different flow regimes using Mach # as the indicator:
    Subsonic
    Transonic
    Supersonic
    Hypersonic

## Slide 128: Aerodynamic Modeling
Subsonic Flow (M < 1 everywhere)
  Usual simplifications: incompressible, irrotational, linearized.
  Disturbances propagate both down and upstream.

## Slide 129: Aerodynamic Modeling
Transonic Flow (mixed regions of M < 1 and M > 1)
  Assumptions: nonlinear, compressible
  Shock waves move due to oscillations of airfoil and oscillations in the flow
  Defined by geometry, NOT freestream Mach number!
Bow shock
Trailing edge shock

## Slide 130: Aerodynamic Modeling
Supersonic Flow (M > 1 everywhere)
  Assumptions: compressible, linearized
  Disturbances propagates downstream inside Mach cone.
Sharp nosed edge
Shock wave
Expansion wave

## Slide 131: Aerodynamic Modeling
Hypersonic Flow (high supersonic speeds)
  Assumptions: nonlinear, viscous
  Stronger shocks; thin shock layer interacts with viscous boundary layer
  High layer temperatures—chemical reactions occur
  Typically for M > 5
Shock wave
Thin, hot shock layer with viscous interactions and chemical reactions

## Slide 132: Strip Theory
3-D extension of the 2-D theory
  2-D solutions assume that the loads at each spanwise station of a wing depend only on the motion of that station.
  The wing is divided into a number of strips and the aerodynamic loads on each strip is calculated on the basis of the 2-D coefficients evaluated at the centerline of the strip.
chords parallel to the flow

## Slide 133: Strip Theory
3-D extension of the 2-D theory (cont.)
  Effective primarily for unswept wings with high aspect ratios.
  Strip theory can be adjusted to account for compressibility (Prandtl-Glauert correction) or aspect ratio effects.
  Theodorsen function C(k) is used for the unsteady circulatory loads.
  Each strip has at least two degrees-of-freedom (DOF),i.e., pitch and plunge (three DOF if control surface is present).

## Slide 134: Linear Frequency-Domain Methods
Numerical method to solve the 3-D potential flow.
Break-up lifting surface into boxes.
x
Evaluate upwash at 3/4 box chord
Boxes arranged in strips parallel to freestream velocity
Assumption:

## Slide 135: Doublet Lattice Method
Discretized problem reduces to:
and can be set up in matrix form:
    Very popular method (e.g., MSC/NASTRAN, ASTROS, etc.)
    Linearized potential flow—subsonic flow applications
    Undisturbed flow is uniform and is either steady or gusting harmonically
    Similar in concept to Finite Element Model (FEM) in structural applications
Notes:

## Slide 136: Practical Considerations
Practical considerations (from MSC/NASTRAN implementation):
  Aspect ratio of the boxes should be ~1 (range 1/3 to 3 is acceptable).
  Chord length of the boxes < 0.08 U/f, where U=uniform flow velocity, f=greatest frequency of interest (Hz), i.e., 12 boxes per minimum wavelength.
  No less than four boxes per chord.
  Boxes should be concentrated near wing edges and hinge lines or any other places where downwash is discontinous and pressures have large gradients.

## Slide 137: Unsteady Aerodynamics

## Slide 138
q
Mach no.
1.0
stable
unstable
Typically will need “some”
nonlinear aero to determine
transonic flutter “dip”.
transonic flutter “dip”
Nonlinear Unsteady Aerodynamics
Navier-Stokes Eqns
Euler Eqns
Full Potential
Transonic Small Dist.
Linearized TSD
Classical
TSD (hi freq)
Lifting Surface
(Linear, sub-,
and supersonic)
Notes: 12/18/98
61

## Slide 139: Aerodynamic Equation Hierarchy
Navier-Stokes (NS) Equations
Direct Numerical
Simulation (DNS)
Large Eddy
Simulation (LES)
Reynolds-averaged
Navier-Stokes (RANS)
Thin-Layer
Approximation

## Slide 140: Aerodynamic Equation Hierarchy
Navier-Stokes (NS) Equations
Direct Numerical
Simulation (DNS)
The full and exact solution of the NS equations
without any turbulence model approximations
Huge computational requirements ~ flow past
airfoil requires exaflop (1018 flops)
Turbulence contains wide spectrum of vortices
of equal physical importance -- limited to simple
geometries and low Reynolds numbers

## Slide 141: Aerodynamic Equation Hierarchy
Navier-Stokes (NS) Equations
Large Eddy
Simulation (LES)
Next level of simplification from DNS
Focus is on the large energy-containing scales
Smaller scales approximated with subgrid models
Much less computational requirements than DNS
DNS
LES

## Slide 142: Aerodynamic Equation Hierarchy
Navier-Stokes (NS) Equations
Reynolds-averaged
Navier-Stokes (RANS)
Stationary turbulent effects are
time averaged
Time averaging creates more
unknowns than equations (closure)
Turbulence models provide closure
FUN3D

## Slide 143: Aerodynamic Equation Hierarchy
Navier-Stokes (NS) Equations
Reynolds-Averaged
Navier-Stokes (RANS)
Thin-Layer
Approximation
Only those derivatives in the direction
normal to the wall are retained in the
shear stress and heat flux terms
CFL3D

## Slide 144: Navier-Stokes Equations
Most generic flow representation, may be considerably computationally intensive for unsteady calculations.
Thin-layer approximation: valid only for high Re—very large turbulent eddy viscosities invalidate the model.
Equations in vector form:
where:
As before in Euler Equations
Shear stresses in flow

## Slide 145
Example of Different CFD Results
Ref.: Bennett, R. M., and Edwards, J. W., “An Overview of Recent Developments of Computational Aeroelasticity,” 29th AIAA Fluid Dynamic Conference, Albuquerque, New Mexico, June 15–18, 1998.
Flutter speed index
Frequency ratio
“Comparison of experimental and calculated flutter results for the AGARD Wing 445.6 tested in air.”

## Slide 146: Aerodynamic Equation Hierarchy “Rules of Thumb”
Linear
Inviscid w/
flat plate
Nonlinear
Inviscid w/
thickness
Accuracy usually
not improved
(w/ experiment)
+
Viscous
effects
Accuracy usually
is improved
(w/ experiment)
Bottom Line: Thickness and viscosity tend to have
compensating effects, which is why Linear Methods
have proven so effective!!

## Slide 147: Aerodynamic Equation Hierarchy “Rules of Thumb”
Nonlinear
Inviscid w/
thickness
Shocks tend to be stronger and farther aft than experiment
Viscous
effects
Reduce shock strength from inviscid result, moving shock forward (boundary layer)
Computed transonic flutter boundaries tend to be “very deep” (AFW/CAP-TSD analyses)
Bottom of flutter dip is raised (softened) from inviscid result

## Slide 148: Aerodynamic Equation Hierarchy “Rules of Thumb”
Unsteady shock dynamics
Lower frequency structural motions
Higher frequency structural motions
Flow has more time to react to motions
Shock excursion over larger portion of wing chord
Larger excursion implies greater variation in pressures
which implies greater nonlinear integrated effect (forces)
Flow has less time to react to motions
Shock excursion over smaller portion of wing chord
Smaller excursion implies less variation in pressures
which implies less nonlinear integrated effect (forces)

## Slide 149: Structural Analysis

## Slide 150: Finite Element Method
Very powerful method for analyzing arbitrary structures.
The de facto industry standard.
Extensive literature available on this topic.
Several commercially available packages
  MSC/NASTRAN
  ANSYS
  I-DEAS
  ADINA
  ABAQUS
  Etc.

## Slide 151: Finite Element Method
Basic idea: the problem is solved by breaking down the domain in subdomains and by assuming a shape for the solution (Rayleigh-Ritz approximation) within each subdomain (finite element). In the limit of the subdomain refinement, the solution should converge to the exact solution.
subdomain
boundary
domain

## Slide 152: Finite Element Method
Different “subdomain” formulations (type of elements):
  1-D elements: rods, bars, strings
  2-D elements: plate, shells, shear element; triangular, quadrilateral, variable number of nodes
  3-D elements: solid (brick) elements; tetrahedron, hexahedron

## Slide 153: Finite Element Method
Four main steps in the method:
  Element formulation (in applications, choice from an existing library of elements)
    Type and order of shape functions
    Element shape
    Nodal degrees of freedom
  Assembling process: global DOF. from element DOF
  Solution
    Linear/nonlinear system solvers
    Linear: assumes small perturbation -> constant stiffness matrix
    Eigensolver: modes and frequencies
    Interface with aerodynamics/aeroelasticity
  Pre- and Post-processing

## Slide 154: Normal Modes Method
The Normal Equations are an expression of the Modal Method.
Modes are eigenfuctions/eigenvectors of the mass-spring system.
Linear assumption (small perturbation) in effect.
Note: “Normal” usually with respect to the mass matrix/distribution.

## Slide 155
Example for a cantilever beam
Normal Modes Method
Third Mode
Second Mode
First Mode
Beam Length

## Slide 156: Overview - ‘reduced order model’
The motion of the wing may be represented by a superposition of ‘modes’ . . .
  Flexure : y (span, time) = [ F ] {qy}
  Torsion : a (span, time) = [ F ] {qa}
velocities and accelerations of flexure and torsion may be represented by this expansion of modes

## Slide 157: KTH Model Mode Shape 2

## Slide 158: KTH Model Mode Shape 6

## Slide 159: KTH Model Mode Shape 7

## Slide 160: Nonlinear Structural Dynamics
Issues
  Large perturbations
  Stiffness matrix not constant across entire motion
  Material nonlinearity
  Follower forces
  Others
Options
  Nonlinear Normal Modes
  Directly coupled solution to FEM
  Local linearization at each condition of interest

## Slide 161: Aeroelasticity

## Slide 162: Aeroelasticity
Thermal
Control
RIGID BODY
Notes: 1

## Slide 163: Historical Point of Interest
  Airplane designs had aeroelastic problems from Day One !
  Samuel Langley's monoplane launched (days before the Wright Flyer) from a houseboat in the Potomac River suffered a structural failure -- possibly aeroelastic divergence
Notes: 6

## Slide 164
Some types of aeroelastic phenomena
STATIC (involves the interaction of aerodynamic and elastic forces)
  DIVERGENCE -- deformation - dependent aerodynamic forces exceed the elastic restoring capability of the structure
  CONTROL SURFACE REVERSAL -- control loss or reversal of expected response due to structural deformation (stiffness) of the primary surface
  LIFT EFFECTIVENESS ----change in magnitude and distribution of aerodynamic loads due to the structural stiffness of the aerodynamic surface
DYNAMIC (involves the interaction of aerodynamic and elastic and inertial forces)
  FLUTTER -- an oscillatory instability where one ”mode of motion” is driven to resonance by a second mode. Both modes have coalesced to the same frequency (includes ‘bending-torsion’, propeller whirl, and panel flutter)
  ‘BUZZ’ and ‘BUFFET’ -- high frequency instabilities caused by flow separations, wakes from forward structures, shock wave oscillations
  ‘DYNAMIC RESPONSE’ due to gusts, turbulence, and other such atmospheric disturbances that affect aircraft performance

## Slide 165: Aeroelastic divergence -- a static instability in which the elastic restoring forces are exceeded by the deformation-dependent aerodynamic forces. It does not depend on ‘strength’ (e.g., yield or ultimate loads); it does depend on ‘stiffness’ (e.g., [K], EI, … )
To illustrate, consider the following example . . .
where
q = dynamic pressure K = stiffness e = eccentricity = aerodynamics
With substitution for the aerodynamic loads . . .
Solving for the deformation of the structure,  :
Observe that
If “q” is the free variable, then divergence is defined as
Notes: 1

## Slide 166: FLUTTER is caused by the interaction of aerodynamic, inertial, and elastic forces
Flutter is easily illustrated by examining the behavior of a wing section limited to two degrees of freedom -- pitch and plunge.
The equations of motion are found by summing forces and moments
Notes: 10

## Slide 167: Aeroelastic Analysis
Fidelity of the structural model is key to aeroelastic analysis
  A finite element model (FEM) is essential
  A “dynamically similar” model could be used
  Measured modes may be a source for a structural model
Aeroelastic analysis software products:
  NASTRAN
  Zona Technology
  NASA
  “home grown”

## Slide 168: Aeroelastic Analysis
Aeroelastic stability analysis is performed for
  All altitudes of interest
  Mach numbers within the flight envelope
  Symmetric and antisymmetric modes
The analyst’s concern must include
  The transonic regime
  Examination of all participating modes of vibration
Two general solution categories:
  Classical methods for linear, frequency-domain unsteady aero
  Time-domain methods for nonlinear, CFD-based unsteady aero

## Slide 169: FLUTTER
••
Time domain solutions:
Response to a disturbance (initial condition) is examined.
All structures have some level of structural damping [c] that can be added to equations.
m
mr
mr
I
y
K
K
y
L
M
y



































0
0
Mass Matrix
+

••
Stiffness Matrix
Unsteady Aero
Notes: 11

## Slide 170: Classical Solution Methods
In general, the equations of motion for the aero(servo)elastic system are:
Many methods are used:
  Velocity “root - locus” plots
  Theodorsen’s method
  the “V-g” method (a.k.a. American method)
  the “p-k” method (aka British method)
We solve the “general” aeroelastic set of equations, however we must consider
  relationship between “circular” frequency and reduced frequency (k)
  harmonic motion is assumed (aero in frequency domain)
  relationship between Mach number, velocity, altitude, flow conditions
  eigenvalues are complex -- frequency and damping are found
  for “separated” equations, the solution must agree
  the presence and form of damping
  Flutter Determinant, solved iteratively (usually)

## Slide 171
Frequency domain solutions (roots) may reveal . . .
  flutter as a coalescence of aeroelastic frequencies of 2 or more modes
  or, aeroelastic divergence as a “zero frequency” mode
FLUTTER
Notes: 14

## Slide 172: FLUTTER - The V-g (Velocity-damping) chart is a popular way to present frequency domain solutions
A V-g Diagram is constructed for each altitude and Mach no., the V-g diagram shows damping for increasing freestream velocity.
Critical modes may be sensitive to damping, the path (somewhat) indicates the nature and severity of the instability.
Aerodynamic loads affect both frequency & damping, but some modes are insensitive to aerodynamics.
The number of roots depends upon the number of DOF in the system or modes of vibration used in the solution.
Notes: 16

## Slide 173: Time-Domain Solution Methods
Modeshapes from FEM splined to CFD grid for use in CFD code
Linear Structure represented by state-space modal equations of motion
Nonlinear Aerodynamics represented by flow solution (Euler, NS)
Linear Structure outputs structural states
Structural states are combined with modeshapes into physical space to define grid deformation, input to Nonlinear Aerodynamics
Nonlinear aero computes pressure distribution at each time step
Pressure distribution projected (dot product) onto each mode (Generalized Aerodynamic Forces, GAFs)
GAFs
Q
Generalized
Coordinates
Q - Dynamic
Pressure
Monolithic
CFD code

## Slide 174: Time-Domain Solution Methods
GAFs
Q
Generalized
Coordinates
Modal Space
N modes
2N states
Physical Space
Grid deformation
Pressures/Forces
Project Pressures
Onto each Mode
dS

## Slide 175: Time-Domain/Freq Solution Methods
dS
Time Domain
Frequency Domain
N modes
N GAFs
Influence Function
Response of N modes
to N modes
NxN GAFs
Example: AGARD 445.6 Wing
4 modes
4 Time-domain GAFs
16 Freq-domain GAFs

## Slide 176: Time-Domain Solution Methods
Classical Solution Methods yield ‘nmode x nmode’ GAFs!!
Time-Domain Solution Methods yield ‘nmode’ GAFs!!
Black Box -> New Q, new solution -> $$$
A change in structural damping requires a new solution
Outputs are time signals of generalized coordinates/GAFs -> no insight regarding aeroelastic mechanisms (as found in V-g-f or root locus plots)
GAFs
Q
Generalized
Coordinates
Q - Dynamic
Pressure
Monolithic
CFD code

## Slide 177
Aeroelastic Analysis & Test Process

## Slide 178: Computational Aeroelasticity Coupling Methods
There are three primary approaches for coupling CFD/CSD:
  Intimately-Coupled (or Unified) Analysis: governing equations have to be reformulated
  Tightly (or Closely) Coupled Analysis: interaction between CFD and CSD codes occurs at every time step
  Loosely-Coupled Analysis: occasional interactions between CFD and CSD codes

## Slide 179: Aeroservoelasticity

## Slide 180: Introduction (Background)
ASE : Multidisciplinary interaction of:
  The aircraft’s flexible structure
  The steady and unsteady aerodynamics
  The active control systems
ASE Interactions
  Adverse effects on vehicle stability and performance
  Favorably modify the aeroelastic response characteristics
  (HiLDA video)
Viable design option for:
  Minimum weight
  Optimized performance
  Multimission requirements

## Slide 182: ASE Design Benefits

## Slide 183: Point of Interest
Traditional approach
  Design rigid-body control system
  Design/investigate flexible-body control system
  Frequency separation allows separate designs to be combined later
High Speed Civil Transport (large, flexible)
  Closely-coupled rigid-body and flexible modes
  Traditional approach not effective
  New design paradigm
  Long fuselage leads to lags in response
  Several ASE issues (SMC, RQ, GLA,…)

## Slide 184
AE/ASE Typical Plots
MODELING
PERFORMANCE
ROBUSTNESS
Mode Shapes
Aero Paneling
S-Plane Approx
k
k
I
R
Stability
PSD

Statistical Response
t
Deterministic
Response
I
R
Nyquist Plot
M



Bode Plot


Singular Values
Notes: 12/18/98
16

## Slide 185: Equations of Motion
Structure
Controls
Aerodynamics
• Can combine structure and controls into state-space form for
use with modern control theory (optimal control, stability)
• Classical linear aerodynamics defined as discrete, tabular
functions of frequency; not in time domain, therefore, cannot
include in structure-control state-space formulation
• Use rational function approximations to solve problem

## Slide 186: Aerodynamic “Fits”
Imaginary
Real
Aero = f(w)
Doublet lattice
Kernel function
Aero(S) = f(S)

## Slide 187
P-Transform Latest technique; see references by J. Dykman, Boeing-Long Beach
Notes: 12/18/98
17

## Slide 188: Equations of Motion

## Slide 189: Gust Modeling
Two basic models of “turbulence”
  Dryden spectrum - for wind-tunnels
  Von Karman spectrum - for atmospheric flight
Based on spectra (frequency content)
Think of as additional filter that will affect the overall response of the vehicle
Measurement/quantification of turbulence an important and active effort

## Slide 190: Comments on EOMs
Final product is system quadruple (A,B,C,D) matrices
Quadruple is math model of structure, aerodynamics, and controls (including sensors and actuators)
Stability is determined by eigenvalue analysis of A matrix
Quadruple suitable for any control system design concept
Quadruple suitable for initial simulation

## Slide 191
Math Model Development
Unsteady Aero
Mode Shapes
Aero/Structural
Interface
Frequency
Domain Model
Generalized Masses
Modal Frequencies
Structural Damping
Actuator and
Turbulence Models
Open-Loop
Frequency Domain
Model
Closed-Loop Frequency
Domain Model
Aerodynamic
S-Plane
Approximation
Open-Loop State-
Space Model
Closed-Loop State-
Space Model
Design Methods
Analysis Methods
State-Space
Control Law
Transfer Matrix
Control Law

## Slide 192
State-Space Model
Bu
A
C
Cc
Bc
Ac
Bwg
Wg
Notes: 12/18/98
15

## Slide 193
Dynamic Pressure Root Locus Plot
Notes: 12/18/98
27

## Slide 194: Dynamic Pressure Root Locus Plot
Will want to see something like...
Flutter at
Q psf
Flutter suppression
System (FSS) Off
Flutter suppression
System (FSS) On
Flutter at
1.2Q psf
…without aggravating higher frequency mechanisms
and within hardware performance limits

## Slide 195: Discipline Integration Example – X-59
https://www.youtube.com/watch?v=DPd0OHrmCBc
Demonstrate low-boom overland flight

## Slide 196: X-59 Aeroelastic Modeling, Testing, and Validation
AeroElasticity (AE)
Flutter
Static/Dynamic
Deformation
Loads
Structure
Unsteady Aero
Structure
Unsteady Aero
Control System
AeroServoElasticity (ASE)
Flight Dynamic/ASE Stability
High sensitivity identified
Loads
Low-Boom Flight Demonstrator (LBFD)
AE/ASE Concerns
Long, slender fuselage
Thin wings
Large engine (mass)
Lift distribution (statically unstable)
Finite Element Model (FEM) accuracy
of critical importance
Tight Collaboration with
Lockheed-Martin (LM)
Independent verifications
  Computational
    FEM
    Loads
    Linear aero
    CFD aero
    Reduced-Order
    Models
    AE/ASE
    Thermal
  Experimental
    Proof Test (stiffness)
    Ground Vibration Test (structural dynamics)
    Structural Coupling
    Test (Control System)
  Active participation in all
  analyses and tests

## Slide 197: X-59 Aeroelastic Modeling, Testing, and Validation
Low-Boom Flight Demonstrator (LBFD)
AE/ASE Concerns
Long, slender fuselage
Thin wings
Large engine (mass)
Lift distribution (statically unstable)
Finite Element Model (FEM) accuracy
of critical importance
Transonic Aero
Static Shape
Proof Test Preparations
Image credit:Lockheed-Martin

## Slide 198: X-59 AeroServoElastic (ASE) Analyses
ASE
Stability
Sensitivity
Studies
Flight
Condition
1
Flight
Condition
2
Stable
Margin
Unstable
Unstable
Stable
Margin
Weight variations:
5%, 10%, 18%
ASE sensitivity to weight -> fuselage mode -> ASE
Close collaboration with Flight Dynamics
FEM
Image credit:Lockheed-Martin

## Slide 199: Reduced-Order Modeling

## Slide 200: Background
The development of Reduced-Order Models (ROMs) is a very active area of research
A ROM seeks to extract the essence of a complex system in order to create a simpler, more efficient, representation
There exist various types of ROMs for various applications (Structures, Aero, Controls, etc.)
Can consider linear unsteady aero methods as ROMs
Can consider CFD turbulence models as ROMs

## Slide 201: Background
Two major categories: POD and System ID
POD: Proper Orthogonal Decomposition
Separation of variables for any data set
Decomposing into “dominant” spatial and temporal components
Can use spatial and temporal components to re-create related physics
Similarities with Principal Component Analysis (PCA) and Independent Component Analysis (ICA)
Sometimes referred to as “Modal Decomposition” in reference to Fluid Dynamics
Large number of references available

## Slide 202: Background
System ID: System Identification
System ID seeks to create a mathematical representation of a “black box” using very specific types of inputs and the resultant outputs
Remainder of Tutorial will focus on AEROM, a system ID software for unsteady aerodynamics and aeroelasticity

## Slide 203: Introduction
The AEROM software, developed at NASA Langley Research Center, continues to be developed, distributed, and applied to various configurations
The software is a “wrapper” that can be easily applied to any time-accurate CFD code (nonintrusive to source code)
The software has been successfully used with the structured CFL3D and the unstructured FUN3D flow solvers
Capabilities include error minimization and rapid generation of aeroelastic root locus plots
Some history and applications of AEROM follow

## Slide 204: Initial Developments
V-g-f plots
ASE Models
Two Different Worlds
CFD grids
Aeroelastic transients
Linear Aeroelastic/ASE Methods
Easy to generate
Rapid, multiple solutions
Well integrated into vehicle
design processes
Nonlinear Aeroelastic CFD Solutions
Improved physics
Expensive, time consuming
Difficulty integrating into vehicle
design processes
Root locus plots

## Slide 205: Initial Developments
V-g-f plots
ASE Models
Two Different Worlds
CFD grids
Aeroelastic transients
Linear Aeroelastic/ASE Methods
Easy to generate
Rapid, multiple solutions
Well integrated into vehicle
design processes
Nonlinear Aeroelastic CFD Solutions
Improved physics
Expensive, time consuming
Difficulty integrating into vehicle
design processes
Root locus plots
COMBINE?

## Slide 206: Initial Developments
V-g-f plots
ASE Models
Two Different Worlds
CFD grids
Aeroelastic transients
Linear Aeroelastic/ASE Methods
Easy to generate
Rapid, multiple solutions
Well integrated into vehicle
design processes
Nonlinear Aeroelastic CFD Solutions
Improved physics
Expensive, time consuming
Difficulty integrating into vehicle
design processes
Root locus plots
COMBINE?
Volterra
Theory

## Slide 207: Volterra Theory of Nonlinear Systems
y
(
t
)
=

0
h
1
(
t
-

)
u
(

)
d

+

0
t

0
t
h
2
(
t
-

1
,
t
-

2
)
u
(

1
)
u
(

2
)
d

1
d

2
+
.
.
.
+

0
t
.
.
.

0
t
h
n
(
t
-

1
,
.
.
.
,
t
-

n
)
u
(

1
)
.
.
.
u
(

n
)
d

1
.
.
.
d

n
+
.
.
.
h
0
+
Multidimensional convolutions with multidimensional kernels
Kernels are IMPULSE RESPONSE FUNCTIONS
Question: Does an aerodynamic impulse response exist?
Initial Answer: No, or unclear, according to some texts
Fung: “Whereas the unit-step function is well defined, the unit-impulse function, mathematically speaking, is not.” (??), pg 275

## Slide 208: Conceptual Breakthrough
Classical Unsteady Aerodynamics
Origins
Impulse Response
Convolution
circa 1930s
continuous time
linear
Dirac delta function
abstract/undefined
confusion
ignored/dismissed
recognized efficiency
continuous time
linear
step response ONLY
Clearly, this function cannot be used within a CFD analysis.
BUT, frequency-domain GAFs exist, therefore, by Fourier principle, the
inverse Fourier transform of GAFs (impulse responses) must exist!
Valid for ODEs, PDEs;
Green’s function

## Slide 209: Conceptual Breakthrough
Digital Signal Processing (DSP)
circa 1960s
discrete time
linear, nonlinear
unit sample
simple, well-defined
extremely useful
easy to apply
digital efficiency
linear, nonlinear
Impulse OR step
cornerstone of DSP
[k]
k) = 1, k=discrete time
Unit sample input
Output due to this input known as Unit Sample
Response
No abstract/complicated theory
Practical, directly applicable to any discrete-time
system

## Slide 210: Eigensystem Realization Algorithm (ERA) Discrete-Time State-Space Realization Theory
Linearized
  Developed at NASA LaRC by colleague Dr. Jer-nan Juang et al.
  Multi-input/Multi-output (MIMO ), MATLAB-based, interactive
  Based on SVD of Hankel matrix of Impulse Responses (Unit Sample Responses)
  Applied extensively and successfully to experimental modal identification
  First application to the development of unsteady aerodynamic state-
  space models (2001)
Given 1st-order Volterra kernel (h(k)), compute A, B, C, and D matrices
x - states of the system
y - outputs (4 modes-->4 outputs)
u - inputs (4 modes-->4 inputs)
A,B,C,D - system matrices
Impulse (Sample) Responses = CeAtB + D

## Slide 211: Traditional Approach for Obtaining Unsteady Aerodynamics in State-Space Form
Frequency Domain
Time Domain
Doublet
Lattice
GAFs
OR
Aeroelastic
Analysis
Rational
Function
Approx.
CFD
(Flutter,
ASE Sim)
GAFs
State-Space
Unsteady
Aerodynamics
FFT
Aeroelastic
Analysis

## Slide 212: New Approach for Obtaining Unsteady Aerodynamics in State-Space Form Using ERA
Frequency Domain
Time Domain
Doublet
Lattice
GAFs
OR
Rational
Function
Approx.
CFD
(Flutter,
ASE Sim)
GAF
Imp
Resp
State-Space
Unsteady
Aerodynamics
FFT
ERA
Aeroelastic
Analysis
Aeroelastic
Analysis

## Slide 213: Time-Domain GAFs Aerodynamic Impulse Responses Do Exist!
AGARD 445.6 Wing
M=0.9
An FFT of these
Functions yields…

## Slide 214: Frequency-Domain GAFs FFT of Impulse Responses (comparison w/ linear solution)

## Slide 215: FUN3D Code
Unstructured-grid flow
solver
Langley-developed code
Aeroelastic capability
Multiple turbulence
models

## Slide 216: ROM Development Process
Unsteady Aerodynamic State-Space ROM
Walsh Functions
Structural state-space ROM

## Slide 217: ROM Development Process
Aeroelastic Simulation ROM

## Slide 218: ROM Development Process
Error Minimization (Unsteady Aerodynamics)
Low
Error
?
Yes
No
PULSE
ERA
Continue

## Slide 219: ROM Development Process
Aeroelastic Root Locus Plot Using Aeroelastic Simulation ROM
Modeled as a closed-loop
system with gain (dynamic
pressure) in MATLAB
Eigenvalues
Z-Plane
Root Locus
S-Plane
Root Locus
Frequency vs
Damping Ratio
Root Locus

## Slide 220: Applications
Supersonic Low-Boom Configuration
KTH Full-Span Generic Fighter Wind-Tunnel Model
AGARD 445.6 Aeroelastic Wing
S&C Flight Dynamics, Aero Damping
X-59 Low-Boom Flight Demonstrator (LBFD)

## Slide 221: Supersonic Low-Boom Configuration
Lockheed-Martin concept
Detailed, sized FEM
Grids for aeroelastic response and sonic boom propagation

## Slide 222: Supersonic Low-Boom Configuration
Comparison of ROM and
FUN3D Mode 4 aeroelastic
transients at M=1.7, Q=2.0 psi
Aeroelastic root locus plot with varying dynamic
pressure, indicating multiple aeroelastic flutter
mechanisms

## Slide 223: KTH Full-Span Generic Fighter Wind-Tunnel Model
Generic full-span fighter
Designed and fabricated by KTH
Tested in TDT (summer 2016)
CFD models in free air and inside
a CFD model of the TDT

## Slide 224: KTH Full-Span Generic Fighter Wind-Tunnel Model – TDT Model
Comparison of ROM and
FUN3D Mode 3 aeroelastic
transients at M=0.9, Q=1744 Pa
Aeroelastic root locus plot with varying dynamic pressure, indicating aeroelastic flutter mechanism between modes 5 and 6

## Slide 225: AGARD 445.6 Wing
Data acquired in the TDT in the 1960s, NASA reports by Dr. E. C. Yates, Jr.
45º sweep, 4% thick (very thin) airfoil data acquired at 0º AOA
Very thin airfoil -> narrow transonic range (starts at M=0.98)
Used significantly (overused? misused?) for CFD code comparisons
Measured flutter data often misrepresented in literature as “highly nonlinear” flutter boundary, ”transonic flutter dip”

## Slide 226: AGARD 445.6 Wing
Inviscid results indicate an unstable third mode, clearly visible in ROM root locus plot but not clearly visible in aeroelastic transients plot (red)
Because a root locus plot is the result as time approaches infinity, viewing only
transients from CFD code can be misleading
Viscous results indicate a stabilization of the third mode
M=1.141
M=1.141, Q=30 psf

## Slide 227
System ID for MIMO Systems for S&C
Computational Fluid Dynamics
(Kestrel or FUN3D)
Simultaneous Inputs, Single CFD Solution
System/Observer/Controller Identification Toolbox
(SOCIT)

## Slide 228
Pitch Moment Damping Walsh Functions vs. Harmonic Motion and Reference
228
SciTech 2018,
Aviation 2018,
Shelton, Silva

## Slide 229: FUN3D/AEROM Transonic Analyses: X-59
M=1.05
Mode 44 FUN3D/ROM Comparisons
Aeroelastic Root
Locus Plot
44 modes,
2% struct damping
(from single CFD
solution-AEROM)
ROM
FUN3D
BOTH
Real
Imag
Time Steps

## Slide 230: Concluding Remarks
The Short Course is concluded.
Thank you for your time and participation!
Any questions or comments?
Sincerely,
Walt Silva